## Slide 1
Status of CEPC HCAL
Haijun Yang (SJTU)
for CEPC Calo Working Group
CEPC Working Day
November 1, 2019

## Slide 2
Outline
Requirements of CEPC Calorimeters
SDHCAL based on RPC
SDHCAL based on GEM and THGEM
AHCAL based on Scintillator + SiPM
Design of Active Cooling
Summary and Future Plans

## Slide 3
Requirements of CEPC Calorimeters

## Slide 4
CEPC HCAL: Geometry and Layout
SDHCAL
AHCAL
Inner radius in X-Y plane Rin = 2300mm
Outer radius Rout = 3340mm
Inner & outer of HCAL endcap in Z-axis
are 2670mm and 3710mm

## Slide 5
PFA Calorimeters
AHCAL: Scintillator + SiPM
SDHCAL: RPC & THGEM
https://twiki.cern.ch/twiki/bin/view/CALICE/CalicePapers
SiW ECAL
ScW ECAL

## Slide 6
CEPC HCAL: Technology Options
HCAL technology options in CEPC CDR
  SDHCAL with RPC (Baseline)
  SDHCAL with THGEM
  AHCAL with scintillator + SiPM
Stainless steel as absorber
Digital HCAL requires a higher readout granularity than analogue HCAL to avoid saturation for high energy showers
  More channels with digital HCAL
Read out with multiple thresholds: Semi-digital HCAL → SDHCAL
SDHCAL with 3-threshold
results in better energy
resolution than binary
mode for Ebeam > 40 GeV

## Slide 7
SDHCAL based on RPC
PCB support (polycarbonate)
PCB (1.2mm)+ASICs(1.7 mm)
Mylar layer (50μ)
Readout ASIC
(Hardroc2, 1.6mm)
PCB interconnect
Readout pads
(1cm x 1cm)
Mylar (175μ)
Glass fiber frame (≈1.2mm)
Cathode glass (1.1mm)
+ resistive coating
Anode glass (0.7mm)
+ resistive coating
Ceramic ball spacer (1.2mm)
Gas gap
Large GRPC R&D
Negligible dead zone
Large size: 1 x 1 m2
SDHCAL prototype
Size: 1m x 1m x 1.4m
No. of layers: 48
Cell size: 1cm x 1cm
No. of channels: 440K
Power: 1mW/ch
ASIC HARDROC (64 ch)
3-threshold: 110fC, 5pC, 15pC

## Slide 8
Performance of SDHCAL
JINST 10 (2015) P10039
JINST 11 (2016) P04001
SDHCAL Efficiency (Data/MC): 96% / 97%
SDHCAL Multiplicity (Data/MC): 1.8 / 1.74
Good Data/MC agreement for
efficiency and multiplicity obtained with
cosmic muons and test beam muons.
80 GeV hadron
40 GeV muon

## Slide 9
SDHCAL: Energy Reconstruction (2)
are parameterized as functions of total number of hits(N1+N2+N3)
optimizer
.
Energy reconstruction formula:
JINST 11 (2016) P04001

## Slide 10
SHCAL: Energy Reconstruction (MVA)
Besides 4 Nhits variables, 8 new variables are built to
describe hadronic showers, and to improve the energy
reconstruction performance.

## Slide 11
SDHCAL: Energy Reconstruction (MVA)
MLP
MLP
BDTG
BDTG

## Slide 12
SHCAL: Energy Reconstruction (MVA)
Energy linearity improves from
3-4% to 1-2% level using MVA
Energy resolution improves
about 5-15% using MVA

## Slide 13
SHCAL: Energy Reconstruction (MVA)
Energy linearity improves from
3-4% to 1-2% level using MVA
Energy resolution improves
about 5-15% using MVA
JINST 14, P10034 (2019)

## Slide 14
SDHCAL: Particle Identification
CALICE-CAN-2019-001
BDT helps to improve the hadron/e/mu PID, purify TB samples.
Keep 99% of pion efficiency and to reject >99% of e/mu.

## Slide 15
SDHCAL: Particle Identification (Low Energy)
SDHCAL TB at CERN using low energy (3-11 GeV) pion beam.
Data and MC simulation for pion samples agree well

## Slide 16
SDHCAL (RPC): Energy Resolution

## Slide 17
Construction of GRPC
GRPC Construction Procedure
1.Position the walls and pipes
2.Glue walls
and pipes.
3.Draw the spacer
position sketch
4.Put the spacers
on the glass
5.Glue the spacers
6. Glue the second glass to the walls
7. Gas tight with
Silicon and test leaks
8. coating and mylar fixing
200*200*1.2mm3
120*200*1mm3
350*500*1.2mm3

## Slide 18
SDHCAL: Energy Resolution

## Slide 19
GRPC Test Platform
z
RPC Size: 120×200×1.2mm3 High Voltage: 7200V
Readout
& DAQ
Gas system
Test system &
Faraday cage

## Slide 20
SDHCAL: Gas Flow Simulation
RPC size 20cm*20cm*1.2mm
Spacer size: h=1.2mm, 2mm*4mm

## Slide 21
SDHCAL based on M-THGEM
Many options of the THGEM type detector used for MPGD based DHCAL.
Advantages:
Multi-THGEM (MTHGEM) uses a PCB multi-layer board
manufacturing technology
Compact
A higher effective gain at lower operational voltage
High concentricity of the holes and the rings, good gain uniformity
MTHGEM detector
Multi-cascade THGEM detector

## Slide 22
SDHCAL: 20cm X 20cm MTHGEM
Structure of 20cm×20cm MTHGEM detector
22
Performance
Gain
Uniformity
Stability
Foil
Structure
Detector

## Slide 23
SDHCAL: 50cm X 50cm MTHGEM
23
MTHGEM foil
Drift
Detector
Performance
Signal
Gain～200
Construction

## Slide 24
SDHCAL: GEM Detector
30cm×30cm double layer GEM
Advantages：
- assembling process is easy and fast
- uniform gas flow
- detachable
Self-stretching technique (from CERN)
detector
50cm×100cm double layer GEM
Study is ongoing
MIP Efficiency > 95%
Multiplicity ~ 1.1 – 1.3
Performance of large GEM detector is still on study.
Plan to study performance of resistive WELL-THGEM(RWELL).

## Slide 25
SDHCAL: GEM Detector Simulation
Single particle : 10 ~ 100GeV π+
HCAL layers:40
25
Hit Number vs Energy @different thresholds
Resolution vs Energy @different thresholds

## Slide 26
AHCAL based on Scintillator + SiPM
AHCAL (Scintillator + SiPM) for CEPC
Scintillator cell size: 3x3cm2, 4x4cm2, 5x5cm2
32 super modules (16+16) in barrel region
Number of layers: 40
Each active layer + readout  5mm
Absorber (steel Fe, 0.12lI)  20mm
ASIC readout chip: SPIROC2E, KLauS

## Slide 27
Test: Scintillator + SiPM
Injection moulded
SiPM or MPPC (Hamamatsu)
MIP detection eff. > 95%
scintillator
30x30x3mm3 uniformity
50x50x3mm3
Mean:32.2p.e.
Mean:8.57p.e.
30x30x2mm3
Mean:34.29p.e.
Step motor controlled
Light output 50x50x3 mm3
is too low to separate MIPs from noise.
27
50x50x3 mm3
30x30x2 mm3
30x30x3 mm3

## Slide 28
MPPC VS NDL
Company | MPPC |  |  | NDL |  | 
Type | 1251-025P | 13360-1325PE | 14160-1315PS | 1010C | 3030C | 125
Active area[] | 1 | 1.69 | 1.69 | 1 | 9 | 1
Pixel number | 1600 | 2700 | 4400 | 10000 | 90000 | 6400
Breakdown[V] | 65 | 53 | 38 | 27.5 | 27.5 | 21.5
Overvoltage[V] | 2.4 | 4 | 5 | 6.5 | 6.5 | 3
Dark counts[kHz] | 82 | 120 | 290 | 550 | 5150 | 470
Crosstalk[%] | 22.6 | 1.59 | 1.17 | 4.4 | 8 | 8.1
Gain[] | 2.83 | 5.11 | 2.5 | 1.295 | 1.3 | 1.91
Company | MPPC |  |  | NDL |  | 
Type | 1251-025P | 13360-1325PE | 14160-1315PS | 1010C | 3030C | 125
 | 1 | 1.69 | 1.69 | 1 | 9 | 1
Pixel number | 1600 | 2700 | 4400 | 10000 | 90000 | 6400
Breakdown[V] | 65 | 53 | 38 | 27.5 | 27.5 | 21.5
Overvoltage[V] | 2.4 | 4 | 5 | 6.5 | 6.5 | 3
Dark counts[kHz] | 82 | 120 | 290 | 550 | 5150 | 470
Crosstalk[%] | 22.6 | 1.59 | 1.17 | 4.4 | 8 | 8.1
 | 2.83 | 5.11 | 2.5 | 1.295 | 1.3 | 1.91
NDL-SiPM:
High fill factor
High gain
Cheap
Low breakdown
MPPC-SiPM:
Low dark rate
Low crosstalk
Expensive
High breakdown

## Slide 29
Gain and Crosstalks vs Voltage
The value of gain which can be calibrated with SPIROC2E is marked on red circle.

## Slide 30
DCR and Crosstalks vs Voltage
SiPMs from MPPC with lower DCR and crosstalk characteristics,
except type 12571-025P.
Type 13360-1325PE is a better one for CEPC-AHCAL detector cell.

## Slide 31
MIP Response of SiPMs
Company | MPPC |  |  | NDL |  | 
Type | 1251-025P | 13360-1325PE | 14160-1315PS | 1010C | 3030C | 125
Pedestal Width[ADC] | 6.172 | 3.997 | 13.51 | 3.718 | 5.596 | 3.61
Pedestal Width[fC] | 294 | 191 | 643 | 177 | 266 | 172
Overvoltage[V] | 2.4 | 4 | 5 | 6.5 | 6.5 | 3
MIP [ADC] | 542 | 719 | 395 | 107 | 450 | 135
S/N | 87.9 | 179.9 | 29.3 | 28.8 | 80.5 | 37.4
Linear range[MIP] | 26 | 40 | 61 | 200 | 200 | 118
High gain1 PC~210ADC
S/N = MIP/pedestal
Electronic: SPIROC2E
All type of SiPMs can satisfy the dynamic range requirement of AHCAL
Type 13360-1325PE can be acquired a better MIP signal from S/N.

## Slide 32
Parallel connection of detector cell
LED trigger
Judge measurement systems
SiPM1(ADC) | 625.9 | 979.7 | 703.6 | 456.1
SiPM2(ADC) | 169.4 | 259.3 | 392.1 | 368.6
SiPM mergence(ADC) | 714.8 | 1180 | 1007 | 766.7
SiPM1
Schematic
SiPM2
LED1
LED2
Parallel connection
Change the light intensity of LED
SiPM1
Mean:456.1
SiPM2
Mean:368.6
total
Mean:766.7
Change the condition of LED，the signal of merging SiPM is the sum of single SiPM.
The measurement system can work normally without scintillator.

## Slide 33
Measurement of merging cells
Target
1cm Pb
Trigger
Cosmic-ray
Schematic
Trigger
Most of gamma radiation
can be shielded by 1cm thickness Pb.
Single
Mean:27.9
Double
Mean:57.9
The signal of merging SiPM is near 2 times compared with single SiPM after shielding most of gamma radiation. It is consistent with theory.
Up
Down

## Slide 34
Comparison of Light Yields (MPPC12571-025P)
Light yield measurement with different scintillator and ESR films
20 tiles by injection molding wrapped with ESR
light yields of 20 scintillators
Non-uniformity is 10%
CALICE
RMS / Mean
Domestic: 4.1% vs CALICE: 5.6%
Domestic

## Slide 35
CEPC AHCAL: Cell Automatic Assembly System
Motivation:
  7M scint. cells for CEPC AHCAL;
  Reflective foils packaging can’t be done manually;
Recent Progress:
  Local companies provide preliminary design;
  Using robotic arm to pack;
Packaged cell
 The automatic assembly system can be used for different scintillator sizes: 3cm3cm, 4cm4cm and 5cm5cm

## Slide 36
Automatic Packing Machine
Robot arm
Label
Pushing hands
Finished product
ESR
Original product

## Slide 37
Detector Cell Gluing Experiment
Materials：
Araldite 2011 epoxy glue
3×3 PCB board
Detector cell;
A film used to brush glue
Result:
This technique is working;
The detector cell was glued on PCB board faster;
Maybe reduce to 4 glue hole;
Plan to test crosstalk and prototype.
motivation：
In order to quickly and effectively realize the integration of large area AHCAL detection unit.
Before glued
After glued

## Slide 38
CEPC AHCAL: Prototype to be constructed
Specification (to be optimized):
Active layers: 35-40 layers;
Size: about 51cm x 51cm
Detector cell: 3cm x 3cm x 3mm
Absorber: stainless steel (80cm, 5lI);
Sensor: NDL-1015, Hamamatsu S13360-3025P
Motivation：
A prototype is required for performance study
Mechanical structure for auto test system
About 100 cells / batch

## Slide 39
Estimation of HCAL Power Consumption
- HCAL Barrel, Rin = 2.3m, Rout = 3.34m, length = 2.67*2=5.34m, Nlayer=40
Area of HCAL barrel = 2*PI*[(Rin+Rout)/2]*L*Nlayer = 3782 m2
- HCAL Endcap (2), Rin = 0.35m, Rout = 3.34m, Nlayer=40
Area of HCAL endcap = 2*PI*(Rout*Rout – Rin*Rin)*Nlayer = 2772 m2
Cell Size \ channels | HCAL Barrel | HCAL Endcap | Channels (Nch) | Power AHCAL | Power SDHCAL
1cm x 1cm | 37.82M | 27.72M | 65.5M |  | 110 kW
2cm x 2cm | 9.455M | 6.93M | 16.4M |  | 52 kW
3cm x 3cm | 4.2M | 3.08M | 7.3M | 110 kW | 43 kW
4cm x 4cm | 2.36M | 1.73M | 4.1M | 88 kW | 
5cm x 5cm | 1.51M | 1.11M | 2.6M | 77 kW | 
Power Consumption (rough estimation):
AHCAL: 7mW/ch * Nch3 + 9W/DIF/m2 * 6554 (59kW)
SDHCAL: 1mW/ch * Nch1 + 5.4W/DIF/m2 * 6554 (35.4kW)

## Slide 40
Active Cooling Simulation
108 chips
Rectangular section tubes : 2x1 mm
Copper plate over: 1.5 mm
PCB plate under: 1.4 mm
symmetry
symmetry
1.5 m
0.5 m
Flow in
Flow out
Water cooling : h = 10000 W/m²/k
Thermal load : 80 mW/chip
27.147 (max) – 24.591 (min) =2.556 oC
Cooling maybe necessary if operating at continuous mode (CEPC)
A water-based cooling system inside copper tubes in contact with the ASICs to absorb excess heat.
Temperature distribution in an active layer of the SDHCAL.
For AHCAL, a water-based copper cooling system embedded in the stainless steel absorber.

## Slide 41
Active Cooling Simulation
41
ANSYS Simulation of RPC+PCB
With copper plate & water tubes
Temperature test of RPC+PCB

## Slide 42
Active Cooling Simulation
10 layers, flow rate: 1m/s
With cooling at 6th layer:
With cooling each layer:
  uniform among layers
  cooling power: ~1.53W/layer
no cooling
cooling at 6th layer
cooling at each layer
cooling pipes
PCB with resistors to mimic HARDROC ASIC heat source for cooling design and test.

## Slide 43
Cooling plates: water pipes imbedded in metal plates
  cooling ability: ~kW/m2
  safety(water is not so good)
Stainless steel
  poor heat transmission
  difficult to produce  high cost
  can work as the absorber
Aluminum
  good heat transmission
  easy to produce
  5 times the radiation length than steel
Cooling plates
Active Cooling Module
Cooling plate
PCB
RPC
Stainless steel
Cooling Test Module

## Slide 44
Summary and Future Plans
CEPC AHCAL prototype with Scintillator + SiPM is under construction.
CEPC SDHCAL performance study using CALICE TB data, and using MVA techniques to improve PID and energy reconstruction.
Active cooling simulation and design is ongoing
Thanks for your attention !

## Slide 45
Backup

## Slide 46
Schematic of CEPC Detector

## Slide 47
Outline of CEPC Calorimeters
PFA Concept
  ECAL: 30 layers, W, 24 X0 , 1 I
    10mm*10mm Si pads; 5mm*45mm scintillator strips
  HCAL: 40 layers, Fe, 5 I
    SDHCAL: 1cm*1cm; gRPC, THGEM
    AHCAL: 3cm*3cm; scintillator tiles + SiPM
Dual readout concept
  Cu/Fe, 10 I
  Scintillation fibers + quartz fibers

## Slide 48: PFA and Imaging Calorimeter
Particle Flow Algorithm

## Slide 49: Readout ASIC
MICROROC Parameters
Thickness: 1.4mm
64 Channels
3 threshold per channel
128 hit storage depth
Minimum distinguishable charge:2fC
Readout ASIC | Channels | Dynamic Range | Threshold | Consumption
GASTONE | 64 | 200fC | Single | 2.4mW/ch
VFAT2 | 128 | 18.5fC | Single | 1.5mW/ch
DIRAC | 64 | 200fC for MPGD | Multiple | 1mW/ch, 10μW/ch
DCAL | 64 | 20fC~200fC | Single | ——
HARDROC2 | 64 | 10fC~10pC | Multiple | 1.42mW/ch,10μW/ch
MICROROC | 64 | 1fC~500fC | Multiple | 335μW/ch, 10μW/ch
Considered the multi-thresholds readout, dynamic range and power consumption, MICROROC is an appropriate readout ASIC
MICROROC
Microroc Test Board

## Slide 50
CEPC HCAL Geometry
Inner radius in X-Y plane Rin = 2300mm
Outer radius Rout = 3340mm
Inner & outer of HCAL endcap in Z-axis are 2670mm and 3710mm
Y
Z
Y
X
Y
X

## Slide 51
SDHCAL based on RPC
JINST 10 (2015) P10039

## Slide 52
6mm(active area) + 5mm(steel) =
11 mm thickness
4.7 mm
4.3mm
ASICs : HARDROC2
64 channels
Trigger less mode
Memory depth : 127 events
3 thresholds
Range: 10 fC-15 pC
Gain correction  uniformity
Printed Circuit Boards (PCB) were designed to reduce the cross-talk with 8-layer structure and buried vias.
Tiny connectors were used to connect the PCB two by two so the 24X2 ASICs are daisy-chained. 11m2 has 6 PCBs and 9216 pads.
DAQ board (DIF) was developed to transmit fast commands and data to/from ASICs.
Imad Laktineh (IPNL)
Electronics Readout
Notes: 52

## Slide 53
SDHCAL based on THGEM
Several THGEM options are explored:
  Double - THGEM
  Single - THGEM
  WELL - THGEM
WELL-THGEM is optimal choice
Thinner, lower discharge
40  40 cm2 of THGEM (below) was produced
40cm×40cm THGEM

## Slide 54
SDHCAL based on THGEM
THGEM
thickness
20cm×20cm WELL-THGEM
WELL-THGEM: 55Fe (Xray ~ KeV), gain ~ 5000, energy resolution is 20%-25%
high rate ~ 1 MHz/cm2, MIP eff > 95%

## Slide 55
AHCAL: Compensation for Energy Reconstruction
Fit:
a=35.6 b=6.60.07%
a=43.7 b=9.50.07%
a=37.5 b=6.00.07%
Local Compensation improves by ~18%
Global Compensation improves by ~15%
Fit by
Local Compensation
Using least square method
Global Compensation

## Slide 56
Scintillator Test Info

## Slide 57
AHCAL: Comparison of Injection Scintillators
From CALICE
24653 counts at 423nm
3674 counts at 430nm
Emission spectra are
consistent
Peak Photon counts:
PEN / PS ~ 1 / 6
For high yield-PEN
- thin plates, large sensors.
For low yield-PEN, large size
- multiple reflections
P.e (PEN+SiPM) ~ 5
P.e (PS+SiPM) ~28
10mmX10mmX3mm
PS PEN

## Slide 58
Test: NDL-SiPM +ASIC
12.5um
Pitch | 10um | 12.5um | 15umeveloping)
Peak PDE @420nm | 31% | 32% | 35%
Gain | 2* | 3.5* | 5*
Breakdown Voltage(V) | 27.5 | 21.5 | 
Pitch | 10um | 12.5um | 15umeveloping)
Peak PDE @420nm | 31% | 32% | 35%
Gain |  |  | 
Breakdown Voltage(V) | 27.5 | 21.5 | 
NDL-10um
NDL-12.5um
LED-trigger
10um
Read-out and Calibration by Spiroc2b
Calibration by their NDL preamplifier
10um
10um
12.5um
12.5um
Self-trigger
LED-trigger
KLauS ASIC (KIP, Uni-HB)
• Low noise, low power dissipation
• Continuous readout without dead time
KLauS Chip
25 uW / channel @ duty cycle 0.5%

## Slide 59
Scintillator + NDL SiPM (Beijing)
Hamamatsu MPPC vs NDL EQR SiPM (epitaxial quenching resistors)
- Short recovery time
- High counting rate capability
NDL-SiPM
Photon Spectrum
SiPM1 | SiPM2 | SiPM3 | SiPM4 | SiPM5 | SiPM6
25.43p.e. | 25.77p.e. | 25.12p.e. | 24.06p.e. | 23.44p.e. | 24.61p.e.

## Slide 60
CEPC ECAL Layout and Structure
One cylindrical barrel + two disk-like endcaps
2 m in radius, and 5.3 m long.
8 barrel sections: 1 section → 8 staves, 1 stave → 5 modules, 1 module → 5 columns
Each endcap → 4 quadrants, 1 quadrant → 9 columns
Column: slabs integrated into supporting structures
Best possible hermeticity and minimum crack regions
Barrel stave
Endcap quadrant
Slab

## Slide 61
CEPC ECAL Baseline Design
A Si-W sandwich calorimeter
Absorber
  30 layers of W plates
    First 20 layers: 2.1mm thick each
    Last 10 layers: 4.2mm thick each
  84 mm thick in total (24 X0)
Active medium
  30 layers of Si plates
  0.5 mm thick each

## Slide 62
CEPC ECAL: Scintillator + W
Advantage: cost effective
The primary difference is in active layer thickness
  2 mm thick scintillator (vs. 0.5mm silicon)
  Scintillator: 5mm  45mm  2mm
  Cross arrangement  cell size of 5 5 mm2
Readout/Service layer: 2mm
SiPM monitoring and calibration is required
“Crossing” configuration of strips to get a high effective granularity
Scintillator: 45mm 5mm

## Slide 63
SDHCAL: Particle Identification
CALICE-CAN-2019-001
BDT helps to improve the hadron/e/mu PID, purify TB samples.
Keep 99% of pion efficiency and to reject >99% of e/mu.
~50%
~26%
~14%
~9%
~6%
~4%
~3%
~2%

## Slide 64: Optimization of SDHCAL Layers
 SDHCAL has 48 layers:
- 6mm RPC+20mm absorber (stainless steel)
 40-layer yields decent energy resolution
TB Data
MC Simulation
pion

## Slide 65
SDHCAL: RPC Construction at SJTU
1.Position the walls and pipes
2.Glue walls and pipes.
3.Draw the spacer position sketch
4.Put the spacers on the glass
5.Glue the spacers
6. Glue the second glass to the walls
7. Gas tight with silicon
and test leaks
8. Graphite coating
and mylar fixing

## Slide 66: Active Cooling System
CEPC is designed to operate at continuous mode with beam crossing rate: 2.8105 Hz. Power pulsing will not work at CEPC.
Compare to ILD, the power consumption of VFE readout electronics at CEPC is about two orders of magnitude higher, hence it requires an active cooling
  Evaporative CO2 cooling in thin pipes embedded in Copper exchange plate.
  For CMS-HGCAL design: heat extraction of 33 mW/cm2, allows operation with 6  6 mm2 pixels with a safety margin of 2
To be modelled for Mokka simulation
 Transverse view of the slab with
one absorber and two active layers.
 The silicon sensors are glued
to PCB with VFE chips, cooled by the
copper plates with CO2 cooling pipes.
Active Cooling

## Slide 67
Active Cooling Simulation and Test
Resistors: 4*6*10 per PCB
Total resistance of a group of 10 parallel-connected resistors: 470Ω
ASICs in SDHCAL: ~0.064W/chip
 ~5.5V on resistors
Requirements for the power supply:
  Voltage range: >0~5.5V
  Output power: >1.536W/PCB
  Adjustable/programmble
Resistance(Ω) | 4.7k
Power rating(W) | 0.0625(~17V)
Max operating voltage(V) | 50
Max overload voltage(V) | 100
Max operating T(℃) | 155
Min operating T(℃) | -55
Temperature coefficient | ±100ppm/℃