## Slide 1: Feasibility of next generation mu-e conversion at CiADS
Chen Liangwen
IMPCAS

## Slide 2: Location of HIAF and CiADS

## Slide 3
HIAF装置
HIAF 2018-2024
Budget: 1.5+1.2 B CNY, approved
EB1:
0.8 AGeV, 3×1010ppp 238U35+
1.75AGeV, 7.5×1010ppp 78Kr19+
2.6AGeV, 1.0×1011ppp 16O6+
EB2:
>9AGeV, 1×1012ppp U92+
~10GeV, >1×1013ppp Xe54+
~12AGeV, >5×1013ppp He2+
~24.8GeV, >1×1014 ppp H
HIAF Upgrade
全超导
磁刚度
34Tm => 86Tm
常温磁铁

## Slide 4: CiADS
Cavity name | βopt | Freq. (MHz) | Cavity type | Energy gain at βopt per cavity(MeV) | Energy range (MeV)
HWR010 | 0.10 | 162.5 | Half wave resonator | 0.84 | 2.1-6.8
HWR015 | 0.19 | 162.5 | Half wave resonator | 2.32 | 6.8-44.7
Spoke42 | 0.42 | 325 | Spoke 3-cell resonator | 4.30 | 44.7-171.2
Ellip062 | 0.62 | 650 | Elliptic 6-cell cavity | 8.54 | 171.2-346
Ellip0825 | 0.82 | 650 | Elliptic 5-cell cavity | 12.36 | 346-540

## Slide 5: Outline
CiADS and Mu-e Conversion
Neutrino production@HIAF-U
g-2@HIAF-U
The Granular Waterfall Flow Target

## Slide 6: Charged Lepton Flavor Violation
Flavor violation in the SM
  quark sector
  neutrino oscillation
  charged lepton?
?
?
Muon CLFV processes
  Highly suppressed in the SM and unobservable (<)
  Clear hints to BSM

## Slide 7: Muon electron conversion: golden channel for BSM
0909.1333
Excellent sensitivity to most physics models at or beyond direct reach by the LHC

## Slide 8: Search for Muon electron conversion
The MELC and then the MECO
Pulsed proton beam
Pion capture with high solenoid field
Muon transport with curved solenoid
Current Search for muon electron conversion based on MELC and MECO configuration
proton

## Slide 9: Search for Muon electron conversion
Low energy muon captured by atom
Muons cascade to 1s state emitting x-ray
Muon dissapearance
  Decay in orbit

## Slide 10: Search for Muon electron conversion
Low energy muon captured by atom
Muons cascade to 1s state emitting x-ray
Muon dissapearance
  Decay in orbit
  Captured by nucleus

## Slide 11: Search for Muon electron conversion
  the binding energy
  R(A) the atomic recoil energy
Mu2e signature:
A single mono-energetic electron
Electron from Decay in orbit
signature
Low energy muon captured by atom
Muons cascade to 1s state emitting x-ray
Muon dissapearance
  Decay in orbit
  Captured by nucleus
  Coherent Muon electron conversion

## Slide 12: Search for Muon electron conversion

## Slide 13: Search for Muon electron conversion

## Slide 14: Search for Muon electron conversion

## Slide 15: Search for Muon electron conversion
Radiative pion capture (RPC)
R. Torres, 2015
signature

## Slide 16: Search for Muon electron conversion
Radiative pion capture (RPC)
R. Torres, 2015
signature
Delayed signal window
Eliminated this kind of prompt background by
delayed signal time window

## Slide 17: Search for Muon electron conversion
R. Torres, 2015
signature
Radiative pion capture (RPC)
Eliminated this kind of prompt background by
delayed signal time window
good extinction
Leaked proton
Delayed signal window

## Slide 18: Search for Muon electron conversion
R. Torres, 2015
signature
Radiative pion capture (RPC)
Eliminated this kind of prompt background by
delayed signal time window
good extinction
long muon beamline ?
shorter pulse duration ： the arrival time distribution of pion will be more sharper
Leaked proton
Delayed signal window

## Slide 19: Search for Muon electron conversion
Delayed signal window
Antiproton induced background:
  Antiproton production threshold
  Low energy antiproton pass through the beam line and annihilate on materials in the detector region, leading directly or indirectly to 100MeV/c electrons

## Slide 20: Search for Muon electron conversion
Delayed signal window
Antiproton induced background:
  Antiproton production threshold
  Low energy antiproton pass through the beam line and annihilate on materials in the detector region, leading directly or indirectly to 100MeV/c electrons
  Very low kinetic energy antiprotons, cannot be suppressed by the delayed window

## Slide 21: Search for Muon electron conversion
Delayed signal window
Antiproton induced background:
  Antiproton production threshold
  Low energy antiproton pass through the beam line and annihilate on materials in the detector region, leading directly or indirectly to 100MeV/c electrons
  Very low kinetic energy antiprotons, cannot be suppressed by the delayed window
Eliminated antiproton background by
Decreasing the proton beam energy
Adding a thin absorber material in the muon beam line (also muon will be absorbed )

## Slide 22: Search for Muon electron conversion
Delayed signal window
Muon decay in orbit (DIO)
  Intrinsic background
signature

## Slide 23: Search for Muon electron conversion
Delayed signal window
Muon decay in orbit (DIO)
  Intrinsic background
signature
Eliminated this kind of prompt background by
delayed signal time window
minimizing the momentum resolution of the detector

## Slide 24: Search for Muon electron conversion
Delayed signal window
Cosmic Ray induced backgrounds
  Cosmic-ray muons interact
  Within the detector region
  and produce background
  electrons
From R. Bonventre, nufact 2019

## Slide 25: Search for Muon electron conversion
Delayed signal window
Cosmic Ray induced backgrounds
  Cosmic-ray muons interact
  Within the detector region
  and produce background
  electrons
From R. Bonventre, nufact 2019
Cosmic-ray veto system

## Slide 26: Search for Muon electron conversion
Delayed signal window

## Slide 27: Search for muon electron conversion
Mu2e with POT
COMET phase I with POT
From R. Bonventre, nufact 2019
From 1812.09018

## Slide 28: Search for Muon electron conversion
Current limit:
  TRIUMF
  < (Ti target)
  SINDRUM-II @PSI
  < (Ti target)
  < (Au target)

## Slide 29: Next search for muon electron conversion at

## Slide 30: Next generation mu2e at ?
Mu2e II
  Update to Mu2e
next generation mu2e <=
From Yuri Oksuzian, NuFact 2019

## Slide 31: Next generation mu2e at PIP-II
From D. Glenzinski, 2018

## Slide 32: Next generation mu2e at PIP-II
From D. Glenzinski, 2018

## Slide 33: Next generation mu2e at J-PARC
COMET II
PRISM

## Slide 34
Next generation mu2e at CiADS ?

## Slide 35
CiADS and PIP-II
PIP-II
By Chen W. L
800MeV, 1.6MW

## Slide 36
CiADS and PIP-II
PIP-II
By Chen W. L
800MeV, 1.6MW

## Slide 37
CiADS and PIP-II
PIP-II
CiADS
Cavity name | βopt | Freq. (MHz) | Cavity type | Energy gain at βopt per cavity(MeV) | Energy range (MeV)
HWR010 | 0.10 | 162.5 | Half wave resonator | 0.84 | 2.1-6.8
HWR015 | 0.19 | 162.5 | Half wave resonator | 2.32 | 6.8-44.7
Spoke42 | 0.42 | 325 | Spoke 3-cell resonator | 4.30 | 44.7-171.2
Ellip062 | 0.62 | 650 | Elliptic 6-cell cavity | 8.54 | 171.2-346
Ellip0825 | 0.82 | 650 | Elliptic 5-cell cavity | 12.36 | 346-540
800MeV, 1.6MW
500MeV, 2.5MW
By Chen W. L

## Slide 38
CiADS and PIP-II
PIP-II
CiADS
Cavity name | βopt | Freq. (MHz) | Cavity type | Energy gain at βopt per cavity(MeV) | Energy range (MeV)
HWR010 | 0.10 | 162.5 | Half wave resonator | 0.84 | 2.1-6.8
HWR015 | 0.19 | 162.5 | Half wave resonator | 2.32 | 6.8-44.7
Spoke42 | 0.42 | 325 | Spoke 3-cell resonator | 4.30 | 44.7-171.2
Ellip062 | 0.62 | 650 | Elliptic 6-cell cavity | 8.54 | 171.2-346
Ellip0825 | 0.82 | 650 | Elliptic 5-cell cavity | 12.36 | 346-540
800MeV, 1.6MW
500MeV, 2.5MW
By Chen W. L

## Slide 39
CiADS and PIP-II
PIP-II
CiADS
Cavity name | βopt | Freq. (MHz) | Cavity type | Energy gain at βopt per cavity(MeV) | Energy range (MeV)
HWR010 | 0.10 | 162.5 | Half wave resonator | 0.84 | 2.1-6.8
HWR015 | 0.19 | 162.5 | Half wave resonator | 2.32 | 6.8-44.7
Spoke42 | 0.42 | 325 | Spoke 3-cell resonator | 4.30 | 44.7-171.2
Ellip062 | 0.62 | 650 | Elliptic 6-cell cavity | 8.54 | 171.2-346
Ellip0825 | 0.82 | 650 | Elliptic 5-cell cavity | 12.36 | 346-540
800MeV, 1.6MW
500MeV, 2.5MW
By Chen W. L

## Slide 40
CiADS and PIP-II
PIP-II
CiADS
Cavity name | βopt | Freq. (MHz) | Cavity type | Energy gain at βopt per cavity(MeV) | Energy range (MeV)
HWR010 | 0.10 | 162.5 | Half wave resonator | 0.84 | 2.1-6.8
HWR015 | 0.19 | 162.5 | Half wave resonator | 2.32 | 6.8-44.7
Spoke42 | 0.42 | 325 | Spoke 3-cell resonator | 4.30 | 44.7-171.2
Ellip062 | 0.62 | 650 | Elliptic 6-cell cavity | 8.54 | 171.2-346
Ellip0825 | 0.82 | 650 | Elliptic 5-cell cavity | 12.36 | 346-540
800MeV, 1.6MW
500MeV, 2.5MW
By Chen W. L
1GeV proton

## Slide 41
CiADS and PIP-II
PIP-II
CiADS
Cavity name | βopt | Freq. (MHz) | Cavity type | Energy gain at βopt per cavity(MeV) | Energy range (MeV)
HWR010 | 0.10 | 162.5 | Half wave resonator | 0.84 | 2.1-6.8
HWR015 | 0.19 | 162.5 | Half wave resonator | 2.32 | 6.8-44.7
Spoke42 | 0.42 | 325 | Spoke 3-cell resonator | 4.30 | 44.7-171.2
Ellip062 | 0.62 | 650 | Elliptic 6-cell cavity | 8.54 | 171.2-346
Ellip0825 | 0.82 | 650 | Elliptic 5-cell cavity | 12.36 | 346-540
800MeV, 1.6MW
500MeV, 2.5MW
By Chen W. L
1GeV proton
CiADS-I 500MeV, 2.5MW
CiADS-II 1GeV, 10MW

## Slide 42: Mu2e@CiADS
advantage
1、 pulse width shorter ~100ns
2、 no antiproton background
disadvantage
1、 lower energy and lower muon yield efficiency
Delayed signal window
The time structure of the beam can be realized in CiADS

## Slide 43: Mu2e with different proton energy
Stopped muon rates estimation:
assume 90% duty factor
1695ns pulse space
pulse width < 200ns
Production target can stands the power
Al stopping target
  Same geometry as Mu2e
The same detector system as Mu2e
3 years running time (6e7 s)
Data taken from papers of D. Glenzinski, et al. 1612.08931,1307.1168

## Slide 44: Outline
g-2@HIAF-U

## Slide 45
缪子g-2/EDM
μ注入
π注入

## Slide 46
缪子g-2/EDM
E821@BNL vs E989@Fermilab
E821@
E989@Fermilab
E821@

## Slide 47
缪子g-2/EDM@HIAF-U可行性
Parameter | 136Xe
Nucleon on target(POT) / pulse | 136*2*1012
Pulse width (ns) | 120
Number of pulses | 5
Cycle length (s) | 4
Beam momentum (AGeV/C) | 10.23
Selection momentum (GeV/c) | ~3.1
>30 times of μ+ （3.1 GeV/c）can be provided

## Slide 48
E989@Fermilab
E821@BNL
g-2@HIAF
缪子g-2/EDM@HIAF-U可行性
E989@Fermilab vs g-2@HIAF-U
0.018 ppm
0.02ppm
0.02ppm
be compatible with
?
?
E989@Fermilab的
 | BNL | Fermilab | HIAF
单位:

## Slide 49: Outline
Neutrino@HIAF-U

## Slide 50: Energy similar with BNB neutrino source
BNB@Fermilab
EB1:
0.8 AGeV, 3×1010ppp 238U35+
1.75AGeV, 7.5×1010ppp 78Kr19+
2.6AGeV, 1.0×1011ppp 16O6+
EB2:
>9AGeV, 1×1012ppp U92+
~10GeV, >1×1013ppp Xe54+
~12AGeV, >5×1013ppp He2+
~24.8GeV, >1×1014 ppp H
HIAF Upgrade
全超导
磁刚度
34Tm => 86Tm

## Slide 51: 重离子产生π介子
相同能量的重离子能产生更多低能端π介子
π+能量 (GeV)
π+能量 (GeV)

## Slide 52: Horn based beam
NuMI beam line@Fermilab

## Slide 53: HIAF-U中微子源
Ar 18/40, 9AGeV, Be target , 10x100cm, horn#1 in NoVA
0.0A 1e6POT
0.02MA 1e6POT
0.2MA 1e5POT

## Slide 54: collection scheme

## Slide 55: collection scheme

## Slide 56: 中微子散射截面研究?
2014年

## Slide 57: Outline
The Granular Waterfall Flow Target solution

## Slide 58
“全新的概念，融合固态靶和液态靶的优势，极具潜力……”---G. Munzenberg
颗粒流散裂靶
中子出射
重力驱动密集颗粒流
束流轰击
  密集颗粒流靶：极高的热移除能力
电子束耦合原理试验

## Slide 59: 高亮度次级粒子源高功率靶的技术挑战
束流功率高，有效靶体积小——热移除、辐照损伤问题
单脉冲束流粒子数高——热冲击硬化、脆化等
次级粒子收集、输运通道对靶结构设计的限制——工作形态、稳定性问题
一种瀑布型颗粒流靶概念设计
Tests of a prototype tungsten
production target at RAL
  High melting temp, radiative cooling (~1600ºC), with 8kW beam (700w in target)
束流功率升高到100kW，靶的温度将达到3150以上。

## Slide 60: MOMENT颗粒流靶概念设计（IMP&IHEP）
Solenoid
Solenoid
一种顺束流径迹的曲型设计

## Slide 62: Conclusion
the accelerator structure of CiADS is similar with PIP-II
CiADS-I and CiADS-II could be feasible platform for next generation mu e conversion experiments
  No antiproton background
  Shorter pulse width
  Relatively low muon yields
g-2@HIAF-U feasible? Systematic uncertainty need improved
neutrino@HIAF-U
  Neutrino cross section experiment?

## Slide 63
Thanks for
your attention！

## Slide 64: backups

## Slide 65: Kick and pick
+500V
-500V
0V
0
6
12
18
Time (ns)
K
P
K
Ideal Voltage between the electrode
( K: kicked P: picked)
MEBT layout
Pick beam dynamic envelop
kick beam dynamic envelop
Beam stop and power distrbution

## Slide 66: PIP-II
From D. Glenzinski, 2018

## Slide 67: 不同停止靶

## Slide 68
From 1612.08931

## Slide 71: Stopped muon yields at CiADS
Stopped muon rates estimation:
assume 90% duty factor
1695ns pulse space
pulse width < 200ns
Al stopping target
3 years running time (6e7 s)
 | 0.5GeV | 1GeV
Stops/POT |  | 1.4e-4
Stops/kW ? | 5.8e18 | 2.2e19
100 kW sensitivity |  | 
Data taken from papers of D. Glenzinski, et al. 1612.08931,1307.1168

## Slide 72: Sensitivity estimation
The single event sensitivity
The number of stopped muon per POT for a given stopping target with proton kin energy E(p)
The muon capture fraction for a given stopping target : 0.6 for Al target
The fraction of muon captures that occur in the signal time window for a given stopping target : 0.489 for Mu2e stopping target
The total reconstruction and selection efficiency for electrons from conversion: 0.173 for Mu2e
from papers of D. Glenzinski, et al. 1612.08931,1307.1168