## Slide 1: Dual Readout calorimeter
R. Santoro
Università degli Studi dell’Insubria (COMO) and INFN (Milano)

## Slide 2: Outline
Results from previous test beams
On-going activity in preparation to the next test beam scheduled at the end of 2020
The progress in the full simulation will not be covered in this talk

## Slide 3: Test Beam 2017/18: SiPM readout
2 MADA Boards: a 32 channel digitizer with a sampling rate of 80MSpS/14-bit ADC and an FPGA based charge integration algorithm
A stack of 10 brass layers (112 cm long, X0 = 29 mm) housing 1mm diameter clear & scintillating fibres with a pitch of 1.5 mm (RM = 31 mm)
8x8 fibers
The module
The Front-end Board
The Read-Out Board

## Slide 4: Cerenkov light yield: 2017
Detector operated at nominal bias voltage (PDE = 25%)
Temperature stability correction:
  < 0.5°C during a single run (negligible)
  < 2°C during the full scan (considered )
Light yield = 28.6 0.4 ph-e/GeV
NIM-A, Vol. 899, 52 – 64 (2018)

## Slide 5: Cerenkov light yield: 2017
Detector operated at nominal bias voltage (PDE = 25%)
Temperature stability correction:
  < 0.5°C during a single run (negligible)
  < 2°C during the full scan (considered )
Geant4
0°
0.2°
Energy containment predicted by simulation is 45%
It is independent from beam energy
It is almost constant when a geometrical cut of 3mm in the center is applied in the selection
A full contained electron shower is expected to have a Light yield* = 54 5 ph-e/GeV
* Number corrected for the measured scintillating contamination
NIM-A, Vol. 899, 52 – 64 (2018)
Light yield = 28.6 0.4 ph-e/GeV

## Slide 6: Scintillating light yield: 2017
Detector operated at 0.5V over breakdown (PDE 2%)
Temperature stability correction:
  < 0.5°C during a single run (negligible)
  < 2°C during the full scan (considered )
PDE correction for temperature variation

## Slide 7: Scintillating light yield: 2017
D. Renker:
NIMA 567 (2006) 48–56
The SiPMs operated at this voltage are not saturated but they are working in a strongly non linear regime: a correction is required to restore the linearity
Detector operated at 0.5V over breakdown (PDE 2%)
Temperature stability correction:
  < 0.5°C during a single run (negligible)
  < 2°C during the full scan (considered )
PDE correction for temperature variation
Valid as a first approximation: the light uniformly illuminate the SiPMs, all photons come at the same time and spurious effects are negligible

## Slide 8: Scintillating light yield: 2017
Detector operated at 0.5V over breakdown (PDE 2%)
Temperature stability correction:
  < 0.5°C during a single run (negligible)
  < 2°C during the full scan (considered )
PDE correction for temperature variation
A full contained electron shower is
expected to have a
Light yield* = 3200 ph-e/GeV
* The light yield is scaled to the typical SiPM PDE (25%)
Once the correction is applied, even if it is not perfect, the linearity is largely improved
NIM-A, Vol. 899, 52 – 64 (2018)
The seed linearity is not yet fully restored

## Slide 9: Scintillating light yield: 2018
To operate the SiPMs at nominal over-voltage, we interposed a yellow filter between the sensors and the fiber tips
A series of preliminary measurements has been performed in the lab in order to select the proper attenuation ratio
SiPM: Photodetector efficiency (from datasheet)
Scintillating fiber: emitted light spectrum (measured)
Expected spectrum and its attenuation
Yellow filter: transmittance spectrum (measured)

## Slide 10: Scintillating light yield: 2018
NIM-A (in press): https://doi.org/10.1016/j.nima.2019.04.090
To operate the SiPMs at nominal over-voltage, we interposed a yellow filter between the sensors and the fiber tips
A series of preliminary measurements has been performed in the lab in order to select the proper attenuation ratio

## Slide 11: Lateral shower profile: 2017
Geant4
Data
In addition, this segmentation allowed to measure the electromagnetic lateral shower profile with an unprecedented granularity
Data VS Geant4
NIM-A, Vol. 899, 52 – 64 (2018)

## Slide 12: Plans for the next test beam
The main goal for this test is the assembly and qualification of a large calorimeter readout with SiPM
  As an intermediate step will read only a part of it with SiPMs
This will push for a series of new challenges
  Improve the linearity response:
    SiPMs with larger dynamic range
    New SiPMs plus filters
  Readout of an increased number of channels
    The front-end board used in the previous tests doesn’t fit any more with the new requirements
    A new strategy is under investigation (ASIC)
  New strategy is required for the assembly
    Something scalable that goes beyond the prototype
    It is important to consider solutions that take into account the coasts and the quality assurance

## Slide 13: The SiPM used in the previous test beams
The sensors used were 25 μm cell pitch (S13615-1025)

## Slide 14: New SiPMs under test
New sensors: S14160-1310PS / S14160-1315PS

## Slide 15: A first look at the SiPMs
Vbias = 42 (4 V over breakdown)
Signal amplification: 40dB
Measured Xtalk = 2%
Sensor: S14160-1315PS
Cell size =15
We tested the new SiPMs using our standard equipment (SP5600 and DT5720A from Caen) together with an automatic software tool developed to characterize SiPMs (JINST 10, C08008)

## Slide 16: A first look at the SiPMs
Vbias = 42 (4 V over breakdown)
Signal amplification: 40dB
Measured Xtalk = 2%
Sensor: S14160-1315PS
Cell size =15
Sensor: S14160-1310PS
Cell size =10
Vbias = 42.5 (4.5 V over breakdown)
Signal amplification: 40dB
Measured Xtalk = 1.8%
We tested the new SiPMs using our standard equipment (SP5600 and DT5720A from Caen) together with an automatic software tool developed to characterize SiPMs (JINST 10, C08008)

## Slide 17: Readout: Citiroc1A

## Slide 18: Citiroc1A: block scheme

## Slide 19: Citiroc1A: charge measurements

## Slide 20: Citiroc1A: trigger and timing

## Slide 21: The evaluation boards
Tested
Under Test
The qualification:
Check the multiphoton with available SiPMs to assess the single photon capability (smaller pitch means larger dynRange but also smaller signal for ph-e)
Measure the full dynamic range using both amplification branches
Measure the front-end linearity

## Slide 22: DT5702: SiPM qualification
Typical response to a fast LED
Hmamatsu SiPM:
1.3 x 1.3 mm²
50mu cell size
Multiphoton spectra with two different preamplifier settings
160 p.e. of DynRange
Signal after the shaper
High Gain branch

## Slide 23: DT5702: SiPM qualification
Vbias = 42 (4 V over breakdown)
Signal amplification: 61 a.u.
Sensor: S14160-1315PS
Cell size =15
High Gain branch

## Slide 24: DT5702: SiPM qualification
High Gain branch
Vbias = 42 (4 V over breakdown)
Signal amplification: 61 a.u.
Sensor: S14160-1315PS
Cell size =15
Sensor: S14160-1310PS
Cell size =10
Vbias = 42.5 (4.5 V over breakdown)
Signal amplification: 40dB
Even if with temporary connections, we can assess the multi-photon also with a15mu pitch sensor
The reason why we don’t see the multiphoton using the 10mu pitch is under investigation (i.e. connections, gain, bit granularity …)

## Slide 25: Dynamic range
Test performed using the DT550W and a matrix of 64 SiPMs S13615-1025 (1x1 mm2, cell size = m): same matrix used in the previous test beam
Measurement performed with a LED:
Dpp measured with the High Gain (setting 60 a.u.)
Low gain calibrated (ADC/ph-e) measuring the sensor response at different light intensities with both branches
Dyn-Range estimate ≈1600 ph-e: it fits with available number of cells
  The number increases if we reduce the low-gain amplification
  It ss crucial the measurement of the linearity: in this case with need a calibrated light intensity
High-Gain
Signal amplification: 60 a.u.
Low-Gain calibration
Signal amplification: 60 a.u.

## Slide 26: How to readout a “medium-size” calorimeter?
150 mm
60 mm
The basic principle
2 Citiroc1A (64 ch)
Timing with a TDC implemented into the FPGA (≈ 0.5 ns)
2 ADC to measure the charge
1 HV power supply (20 – 100V) with temperature compensation
Interface for readout
FERS: A5202
If the Citirorc1A qualification will fulfil our requirements we still need a compact and scalable solution for a test beam: the FERS-5200 system from CAEN could be a possible solution

## Slide 27: How to readout a “medium-size” calorimeter?
The basic principle
FERS-unit can be used in standalone or connected to the system
Up to 16 FERS-unit can be connected in daisy-chain (FERSnet)
The FERSnet data throughput is up to 200 MB/s
The FERScb is a data collector housing 4 high speed optical link (TDLink)
The connection to the host PC is performed with a 10 Gbit ethernet
The FERScb has an embedded ARM processor (Quad Core) running Linux for data processing / data compression
If the Citirorc1A qualification will fulfil our requirements we still need a compact and scalable solution for a test beam: the FERS-5200 system from CAEN could be a possible solution

## Slide 28: Test beam 2020
The prototype for the test beam
9 modules 16 x 20 tubes (2mm outer diameter) = 320 tubes
8 modules readout with PMTS
The central module equipped with SiPMs
  320 SiPMs to be readout
  5 FERS board + 1 Data collector

## Slide 29: A possible strategy for the assembly
Vertical SMD connector
A79602-001 PZN-04-VV
Front-view
Back-view
We start with an array of small front-end boards (1.8 x 1.8 mm2 each) designed to host 1 SiPM and a connector on the back side
Once the array is populated with all the components, each front-end board will be removed from the array and it will be qualified before the next step of the assembly

## Slide 30: A possible strategy for the assembly
tube
Fiber (inserted into the tube)
Front-end board + SiPM + connector
The front-end board + SiPM will be glued to the tip of the fiber
Both the functionality and optical coupling for the basic unit will be qualified
Once all tubes, equipped with the SiPMs, will be qualified the module assembly starts

## Slide 31: A possible strategy for the assembly
This approach is very preliminary and all the details has to be verified but, if feasible, it has a series of advantages
The design of the front-end board is easy and cheap: it doesn’t require any complex routing
The individual SiPM can be qualified at each step of the assembly procedure
We can guarantee a good contact between SiPMs and fibers:
  This can also be part of the quality assurance test
In principle, this strategy should be immune from cross-talk between fibres
Once all tubes are glued together, the prototype we will have on the back a forest of wires to be plugged into the FERS.

## Slide 32: Conclusion
The results from old test beams are confirming all the potentiality of this calorimeter when it is readout with SiPMs
A lot of activities are on-going in order to prepare the new test beam
The next challenge is the design of a scalable prototype looking both at the cost and performances

## Slide 33: Backup

## Slide 34: Dual-readout calorimetry
The concept is to measure the fem component event by event. This eliminates the fem fluctuation effect on calorimeter performance
The measurement is performed using two different sampling processes:
  Cherenkov light, produced by the relativistic particles, dominating in the e.m. shower component
  Scintillation light produced by the total deposited energy

## Slide 35: The history of Dual Readout Fiber Calorimeter
15 years of R&D qualified the dual-readout calorimetric technique
S. Lee, M. Livan, R. Wigmans, Dual-Readout Calorimetry, Rev. Mod. Phys. 90 (2018) 025002.

## Slide 36: Energy resolution
Electromagnetic resolution:
Copper module
NIM A735, 130-144 (2014)
Hadronic resolution:
Lead module
NIM A537, 537-561 (2014)
Lateral
Leakage

## Slide 37: Particle Identification
Different methods allow hadron/electron separation:
NIM A735, 210 (2014)
RD52 lead calorimeter:
60 GeV e-/π-
A multivariate analysis reached a particle ID capability of:
ε(e-) = 99.8%
@ R(π-) ∼ 500

## Slide 38: New SiPMs under test
New sensors: S14160-1310PS / S14160-1315PS

## Slide 39: Citiroc1A: charge measurements (II)
Two techniques implemented to measure the amplitude:
Track & Hold and Peak Detector

## Slide 40: Signal Grouping
This board allows to investigate the SiPM performances when the signals are grouped analogically (from 1 to 9 SiPMs)
Each SiPM is individually biased
Same FEE used in the test beam
From one SiPM to 8 SiPM
 | 1 SiPM | 4 SiPM | 8 SiPM
R = resolving power (ph-e) | 24.5 | 16.6 | 10.0
Space granularity (mm2) | 4.5 | 18 | 36
 | 1 SiPM | 4 SiPM | 8 SiPM
R = resolving power (ph-e) | 24.5 | 16.6 | 10.0
Space granularity (mm2) |  |  |