## Slide 1: A dedicated SiPMs array for GRD of GECAM
孙希磊,安正华,张大力
高能所
第十三届全国粒子物理学术会议2021.08.16

## Slide 2: Contents
Introduction
Status of GECAM
Detectors solution
SiPMs array design
Performance
Radiation damage
Summary

## Slide 3: Multi-messenger astronomy
GW170817A
4π FOV eyes for X/gamma rays
GECAM

## Slide 4: GECAM Gravitational wave high-energy Electromagnetic Counterpart All-sky Monitor
姿控舱
载荷电子学舱
载荷探测器
Characteristics
  FOV： 100% all-sky
  Sensitivity：~2E-8 erg/cm2/s
  Localization：~1 deg
  Energy range：8 keV – 4 MeV
  GRB Broadcast: Near real-time
Detectors
Payload electronics
Spacecraft electronics
Attitude control
Power module
GECAM-A
GECAM-B
GECAM satellite (160 kg for each)
600 km
Solar battery

## Slide 5: X/gamma-ray telescopes
GECAM
SVOM/GRM
Fermi/GBM
Swift/BAT
SVOM/ECLAIRs
5
20
200
Energy Band (keV)
5 000
20 000
10
Field of View (FOV)
50
all-sky (%)
100
Konus-Wind （no localization）
~2021
2004
~2021
2008
2020
INTEGRAL/SPI-ACS （no local.&spec）
1994
2002
HXMT/HE
2017
Launch time

## Slide 6: Launched at Xi Chang
2020.12.10

## Slide 7: Status on orbit
Due to the issues of power supply system, GECAM-B can observe about 11 hours/day (FoV is about 70% of all-sky area), while GECAM-A has not started to observe yet.

## Slide 8: The first GRB published on GCN
https://gcn.gsfc.nasa.gov/gcn3/29331.gcn3
2021.01.19

## Slide 9: First GRB event via Short Message of Beidou Navigation Satellites
2021.01.20

## Slide 10: SiPMs based detectors
GRB
Detector layout of each satellite
  25 GRDs, 3 inch, 15 mm thickness
  8 CPDs，16 cm2/cpd
  223°FoV， ~1 deg position error
  8 keV-4 MeV，75% efficiency@8keV
  Compact, HV-free,
Hemispherical compound eye design
Detectors solution for microsatellite
Constraints of microsatellites payload
Dimension <50 cm
Weight <50 kg
Power <50 W
Why microsatellites?
Cheap
Short period
Two satellites launched by one rocket
damsel-fly

## Slide 11
GRD Structure
Domestic crystal
Silicone pad
Reflective film
SiPM Array

## Slide 12: SiPM Characteristics
 | SensL | Hamamatsu | FBK
Type | MicroFJ-60035 | S14160 | NUV-HD
PDE (%) | 51 (Vbr+5V) | 50 (Vbr+2.7V) | 56 (Vbr+5V)
Dark count rate (kHz/mm2) | 70 (Vbr+5V) | 166 (Vbr+2.7V) | 150 (Vbr+5V)
Gain | 6.0X106 (Vbr+5V) | 2.5X106 (Vbr+2.7V) | 3.5X106 (Vbr+4.5V)
Crosstalk probability (%) | 20 (Vbr+5V) | 7 (Vbr+2.7V) | 10 (Vbr+5V)
Break-down voltage (V) | 24.5 | 37 | 26
ΔTVop(mV/℃) | 21.5 | 34 | 20
Compact size
Large dynamic range
Single-photon sensitivity
High photon detection efficiency
Insusceptibility to magnetic fields
Solid, robust
However
Optimization design for arrays
Low temperature -20oC
High light yield and fast crystals
Radiation damage
DCR ~100 kHz/mm2

## Slide 13: SiPMs array design
SiPMs Array design
Arranged evenly in a circular shape
Reflective film to improve photon collection efficiency
-20 0C, to suppress the dark noise rate
PreAmp design
Parallel for 16 chips, Sum in 4 groups
High gain and low gain
Independent power supply in two groups
Temperature feedback for supply voltage

## Slide 14: Waveform output

## Slide 15: Energy Spectrum and resolution
VS PMT 6233
preliminary
preliminary

## Slide 16: Low temperature performance
preliminary
preliminary

## Slide 17: Energy Spectrum of 5.9 keV X-ray
preliminary

## Slide 18: Uniformity performance
preliminary

## Slide 19: SiPM Full-array/Semi-array performance
preliminary

## Slide 20: Radiation damage on orbit
Average equivalent Al thickness 21.5 mm
Equivalent 10 MeV proton fluence
1.5E+09 (cm-2) 3y
2.5E+09 (cm-2) 5y
DCR threshold current will increase

## Slide 21: Baseline fluctuation increase
preliminary

## Slide 22: Threshold increase on-orbit
25 keV/y increment
preliminary
preliminary

## Slide 23: Characterization of SiPMs with neutron

## Slide 24: Current increases with the radiation
3-year radiation dose
6.0x10^9 n/cm2
-20 ℃ 27.5V
Current ~0.2 mA
0.32 mA/day
3-year
1-year
-20 ℃
preliminary

## Slide 25: Current increase on-orbit
27.5 V
28.0 V
28.2 V
preliminary

## Slide 26: Summary
GECAM has been launched
Power supply problem, one satellite part time running, 70% of all sky
Near real-time downlink capability
A dedicated SiPMs array designed for GRD
Performs well except for radiation damage issues
Threshold increase 25 keV/year @-20 ℃, 27.5 V

## Slide 27
Thanks for your attention

## Slide 28: Annealing effect and low temperature suppress
preliminary