## Slide 1
Development of the CMS-HGCAL silicon module center in Beijing
张华桥 (高能所)
17 Aug 2021@HEP-CPS, China

## Slide 2: CMS (compact muon solenoid) experiment
最重的探测器
中国
RPC/CSC
GEM/Trigger/HGCal
14 TeV

## Slide 3: CMS endcap calorimeter phase II challenges
Considering these two requirement within the limited given budget…
CMS High Granularity Calorimeter
(HGCal)
CMS @ HL-LHC: ~1x1016 1 MeV neq cm-2 @ 3ab-1
and up to 2 MGy absorbed dose in endcap calorimeters
140-200 pile up in HL-LHC
JINST 12（2017） P10003
Charged tracks：
Tracker（70%）；
photons：
ECAL（20%）；
Neutral hadrons ：
HCAL (10%)
CMS-TDR-019

## Slide 4: CMS High Granularity calorimeter
advantage： radiation hard, one readout per cm3
Excellent energy, position, time res.：5D Calorimeter
Similar idea
France/Prague/Japan/England
Other future HEP experiments
Years of R&D，
Application Not yet approved
CMS HGC
Approved to be built 2015-2025

## Slide 5: CMS HGCAL: 50-layer sampling calorimeter
Active Elements:
Hexagonal modules based on Si sensors in CE-E and high-radiation regions of CE-H
Scintillating tiles with SiPM readout in low-radiation regions of CE-H
Key Parameters: (updated from TDR)
HGCAL covers 1.5 < ｜h｜ < 3.0
Full system maintained at -30oC
~640m2 of silicon sensors
~370m2 of scintillators
6M Si channels, 0.5 or 1.1 cm2 cell size
  Data readout from all layers
  Trigger readout from alternate layers in CE-E and all layers in CE-H
~31000 Si modules including spares
Electromagnetic calorimeter (CE-E): Si,Cu/CuW/Pb absorbers,28 layers,25.5 X0 & ~1.7l
Hadronic calorimeter (CE-H): Si & scintillator, steel absorbers, 22 layers, ~9.5l
r = 0.28 m
r = 2.62 m
2 m
h = 3
h = 1.5
mass  200 T
each endcap

## Slide 6: CMS HGCal Silicon active layer
120 μm, 200 μm, 300 μm for different radiation level
640 m2 silicon/31000 module(3 times as CMS silicon tracker)
Working under -30 degrees
Very compact layers to integrate active materials
sensor
PCB
module

## Slide 7: Tasks of silicon MAC
6 MACs: 3 in US, 3 in Aisa
  Beijing IHEP host a MAC
Each MAC will on avarage produce ~5200 Modules
  More than 100 m2 silicons and 1M readout channels
Part of HGC team at IHEP
May 2021
Beijing

## Slide 8: IHEP HGCal lab infrastructure: cleanroom
140m2 dedicated cleanroom（Class 1000） ready：
  Temperature：20oC to 22oC
  Humidity：35% to 55%
  Compressed/vacuum/dry air pipe installed
CMS/HGCal management visit IHEP MAC: 2019/09
绑定区

## Slide 9: Operation of cleanroom
Continuous monintoring
Cleanness of June in HGC lab:
  Better than class 1000
Tempeture and Huminity are under control (even some of variation due to work/tune of clean room)

## Slide 10: IHEP HGCal lab infrastructure: equipment/training done
Gantry with assembly tools
Pick up
Dispense
OGP training
Pull tester
Mini gantry training
Module test
Cosmic ray test
Bonder and test

## Slide 11: Componant checks
Optical gauge products ZIP 635
  Automate meansurement without contact
划痕识别
Microscope:
  Quick visual checks
OGP ZIP 635
Flatness of PCB
Scratches on sensor
Bonding check
Microscope
Shape of PCB
Silicon sensor probe station MPI TS200

## Slide 12: Module assembly (1)
Module assembly is done on 1.25m*1.25m gantry
  Integrate vacum, high presure gas, vision system, dispensor
  Automated and cordinated by dedicated software
  Calibrated with ~10 micron precision
Gantry Repeadility: 1 𝝁 m
Flatness of gantry fixture

## Slide 13: Module Assembly (2)
First 8 inch module successfully assemblied at IHEP
Dispense on baseplate
10𝝁m
24𝝁m
Thickness control
Gantry/fixture
Dispense on sensor

## Slide 14: Wire bonding
Connect senor to electronics
  ~ 20 millions wires
BJ855 + Dage 4000
High speed and good pull strength

## Slide 15: Encapsolution
Protect wire from moisture and mechanics with DOWSIL 186 glue
Done with mini-gantry + dispensor + centrifuge
Automated procedures

## Slide 16: Module testing (1)
Single module test-stand(3 versions) + Cosmics setup
  Pedestal, nosie, charge injection, leakage current, MIP…
Themal cycling testing box is under design
TS: Hexacontroller + trophy board + ZYNQ
Older version of test stand

## Slide 17: Module testing (2): First 8 inch module
Test leakage, Pedestal, Noise, etc.
Module IHEP001
Total leakage
Sensor IV from CERN
Sampling scan
Charge injection scan
Pedestal Map
Noise Map
Noise before/after bonding

## Slide 18: HGCal production database
HGCAL Database: an essential part of HGCAL construction
  Record data of all steps in module production
  GUI being developed: transmit information between MAC and CERN
  Sensors, PCBs, baseplates, tooling; production testing results; shipping

## Slide 19: Summary
The Module Assembly Center at IHEP are almost ready
  Infrasture and main equipment are ready and qualified
  First 8 inch module is produced (key requirement for MAC qualification)
    Including 130 nm radiation hard ASICs (temporary export licence)
    Testing shows very good performance
    Shipped back to CERN for beam test in coming September
  More details about the Si Module in Feng Wang’s poster
Moving to production stage (possible delay since 2020/6)
THU,FDU,ZJU joined HGC(MAC) efforts since 2020.
Thanks funding support from NSFC, MoST, IHEP,THU…
2021/9: MAC site qualification
2022/10: 5% production done
2023/10: 50% production done
2024/7: 100% production done
2027: ready for CMS data taken

## Slide 20
郭佳林
苑超辰
余涛哲
王储
刘勇
张华桥
华慧玲
陶军全
王泽炳
顾煜栋
王峰
程华杰
参与第一块模块制作的部分成员合影：2021/6
Thanks