## Slide 1
Testbeam schedule
Zhijun Liang
(IHEP, Chinese Academy of Sciences)
Notes: Annual strategy planning session for the joint Key Lab for Particle Detectors and Electronics.
You can present an overview of the CEPC Detector design, the R&D program, and go over the key technologies to be pursued during the next five years for CEPC. Aim for about 30‘+10’ approximately.

## Slide 2
Introduction
Goal: Measurement the spatial resolution in beam test
Requirement
    Beam type: electron/pion/proton
    Beam energy >2GeV
    Rate >1kHz
Timeline
    Schedule 1~2 test beam every year from 2020 to 2023
    2020 : Beam test for 1st MPW chip
    2021: Beam test for 2nd /3rd MPW chip
    2022: Beam test for prototype

## Slide 4
First test beam for MOST2
Expect to have first beam test on summer 2020
    Aim to test 1st MPW chip
    Minosa telescope for tracking (position information)
    3~4GeV , 10kHz electron beam
    Test 2~3 chips each time
    Compare performance before and after irradiation
Typical setup in DESY testbeam
Typical setup in DESY testbeam

## Slide 5
First test beam for MOST2: laser test
To prepare the beam test , we need to do laser test
    Test trigger system, synchronize the laser trigger signal with the chip
    and simulate MIP response.
    Two pulse laser (infra-red laser )
      Laser Pulse Frequency can vary from 100Hz ~100kHz

## Slide 6
First test beam for MOST2: X ray tests
X ray irradiator in IHEP
    Can reach 1MRad in one afternoon

## Slide 7
First test beam for MOST2: IHEP beam test
Two beam line available in IHEP
    E2 line: 2.5GeV， 10~20Hz, electron beam, 104~109 electrons per bunch
    E3 line: 1~2GeV, 1~4Hz, electron/pion/K, single particle
Plan to use E3 line for some beam test

## Slide 8
Test beam for prototype
Two possibilities
3~4GeV , 10kHz electron beam in DESY
Standalone tracker prototype
tracker prototype + Minosa telescope combined tracking

## Slide 9
Summary
Expect First beam test in DESY in summer 2020
To prepare for it :
Laser test
IHEP beam test
X ray irradiation
Proton irradiation
Timeline
    Schedule 1~2 test beam every year from 2020 to 2023
    2020 : Beam test for 1st MPW chip
    2021: Beam test for 2nd /3rd MPW chip
    2022: Beam test for prototype