## Slide 1: CEPC injection extraction hardware R&D status
Jinhui Chen, X.H. Cui, D. Wang, Yiwei Wang, Lei Wang, Yuwen Wu, Hua Shi
Injection group
2019-12-30
CEPC day，Dec. 30, 2019 at IHEP in Beijing

## Slide 2: Outline
1
Overview of CEPC Inj./Ext. systems
2
Inj./Ext. systems layout preliminary design
3
Hardware design consideration
4
Summary

## Slide 3
Overview of the CEPC injection and extraction systems

## Slide 4: CEPC injection and extraction systems
DR injection and Extraction system(e+)
Booster LE injection system (e+,e-)
Booster Extraction system1 (e+,e-)
Collider off-axis injection system (e+,e-)
Booster Extraction system2 (e+,e-)
Booster HE injection system (e+,e-)
Collider swap out injection system (e+,e-)
Collider swap out extraction system (e+,e-)
Collider beam dump system(e+,e-)
There are 9 injection and extraction sub-systems in CEPC accelerator complex, including:
Off-axis injection
(in W and Z mode)
On-axis injection
(only in Higgs mode)
Linac
DR
Booster
Collider
120GeV
1.1GeV
10~120GeV
dump
①
⑨
④
②
⑥
③
⑧
⑦
⑤

## Slide 5: Injection Schemes Considerations
Top-up injection schemes for low emittance rings:
  Off-axis injection (need larger DA)---accumulating injection
    Pulsed local bump injection
    Pulsed septum field injection
      multi-pole magnet injection
      Nonlinear kicker injection
  On-axis injection (need smaller DA)
    Transverse swap-out injection
    Longitudinal accumulating injection
  For the CEPC, from the Linac to the damping ring then to the booster and the collider rings, the beams are injected and extracted all by on-axis scheme.
  In the collider rings，the both off-axis accumulating injection schemes are applicable for W and Z mode due to larger DA. On-axis swap-out injection scheme is the baseline one for Higgs mode for smaller DA. In this mode, the beams are accumulated by off-axis injection in the booster ring.

## Slide 6: Injection components design considerations
Injection and extraction components: Kicker and septa
Lambertson magnet is the first choice for the septa, since there is height difference between the machines. Lambertson is more reliable than other types of septa with typical septum width of from 2mm to 10mm.
Which type of Kicker to choose is usually determined by the injection scheme, the waveform of pulse and required kick strength.
The waveform of kicker pulse is determined by injection scheme, filling pattern and revolution period.
The width of septum, kick strength and length of injection straight section should be considered together.
A reasonable injection and extraction region layout design is very important for hardware design. This part is not available in CEPC CDR.
In the past 3 months， the preliminary injection layout design was done. So far, we just figured out what kind type of the components needed in all subsystems. And we just proposed a hardware R&D plan in the coming years.

## Slide 7
CEPC injection and extraction systems layout preliminary design

## Slide 8: Damping Ring injection and extraction
On-axis bunch-by-bunch injection
Injection and extraction systems are totally occupied 2 long straight sections.
Storage Beam
Injection Beam
Septum Plate 6mm
Lambertson: length=0.5m, deflection angle=100mrad, B=0.72T
thickness of septum sheet=6mm Leakage field=<5E-4(0.8mm) Beam-Stay-clear(HxV)=25x15mm
Fast kicker: pulse width<250ns, repetition rate=100Hz, length=0.25m, deflection angle=1.5mrad, B=0.02T, Beam-Stay-clear(HxV)=32x18.8mm (slotted pipe kicker)
7.6mm
7.6mm
10ms
125ns
1.1GeV，75.4m
250ns
Inj.& ext. straight sections
Q
Q
1.25m
4.5m
0.5m
0.25m
ϴv=1.5mrad
2.5m
21.2mm
Side view
Q
Q
ϴH=100mrad
25mm
150mm
Top view
Lambertson
kicker
17.45mm?
21.95mm
Q
Q

## Slide 9: Parameters of Hardware of DR
 | Injection | extraction
Energy（GeV） | 1.1 | 1.1
Bunch number | 2 | 2
Bunch spacing（ns） | 125 | 125
Injection（extraction）mode | Bunch by bunch | Bunch by bunch
Kicker repetition rate (Hz) | 100 | 100
Kicker pulse width (ns) | <250 | <250
Kicker rise（fall）time (ns) | <125 | <125
Timing delay(ns) | <125 | <125
Kick angle (mrad) | 1.5 | 1.5
Kicker Integral magnetic field strength (Tm) | 0.006 | 0.006
Length of kicker（m） | 0.25 | 0.25
Kick strength（T） | 0.024 | 0.024
Kicker Beam-Stay-clear(HxV)（mm） | 32x18.8 | 32x18.8
Kicker good field region (HxV)（mm） | 38x22？ | 38x22？
Kicker field uniformity（%） | 1 | 1
Septa deflection angle（mrad） | 100 | 100
Septa Integral magnetic field strength （Tm） | 0.36 | 0.36
Septa board thickness（mm） | 6 | 6
Septa Circulating Beam-Stay-clear(HxV)（mm） |  | 
Septa Injected beam-stay-clear（HXV）（mm） |  | 
Septa good field region (HxV)（mm） |  | 
septa field uniformity（%） |  | 
Kicker: Slotted pipe kicker
Septa: horizontal Lambertson magnet

## Slide 10: Booster LE injection
On-axis bunch-by-bunch injection
50ns,100Hz
Storage Beam
Injection Beam
Septum Plate 10mm
10mm
10mm
Kicker: vertical strip-line kicker driven by DSRD pulser
Septa: horizontal Lambertson magnet
Q
Q
22.5m
196m
2m
1m
ϴV=0.11mrad
171m
30mm
Side view
Q
Q
ϴH=12.7mrad
12.7mm
300mm
Top view
Lambertson
kicker
11.19mm
30.22mm
Q
Q
Q

## Slide 11: Booster HE extraction for CR off-axis injection
Train by train or bunch-by-bunch extraction
Storage Beam
Injection Beam
Septum Plate 10mm
10mm
10mm
200ns
40~2000ns
200ns
1kHz
Kicker: horizontal out-vacuum delay-line dipole kicker(coating ceramic vacuum chamber) driven by PFN-based solid-state pulser
Septum: vertical Lambertson magnet
Q
Q
24m
196m
15m
0.7m
ϴH=0.2mrad
156m
30mm
Side view
Q
Q
ϴV=9.5mrad
71mm
300mm
Top view
Lambertson
Dipole kicker
0.07mm
33mm
Q
Q
Q

## Slide 12: Collider ring off-axis injection
200ns
40~2000ns
200ns
1kHz
Storage Beam
Injection Beam
Septum Plate 2mm
5mm
3mm
Dipole kicker: horizontal out-vacuum delay-line kicker+coating ceramic chamber+PFN-based solid-state pulser
NLK kicker: horizontal out-vacuum delay-line NLK kicker+coating ceramic chamber+PFN-based solid-state pulser
Septa: Vertical Lambertson magnet
Q
Q
0.7m
35m
0.7m
ϴH=0.1mrad
10mm
Side view
Q
Q
ϴV=28mrad
?mm
300mm
Top view
Lambertson
Dipole kicker
?mm
10mm
kicker
pulsed local bump scheme
Q
Q
35m
0.7m
ϴH=0.1mrad
10mm
Side view
Q
Q
ϴV=28mrad
?mm
Top view
Lambertson
NLK
?mm
13.5mm
pulsed multipole injection scheme

## Slide 13: On-axis swap-out injection layout
Storage Beam
Injection Beam
Septum Plate 10mm
5mm
5mm
Off-axis injection is used in the process of the booster high-energy re-injection. Both puled multipole injection and pulsed bump injection are suit.
On-axis swap out injection is applied in CR. A set of dipole kicker can serve both injection and extraction process.
Booster
E- CR
Side view
Booster
E- CR
Top view
LMS
LMS
LMS
LMS
LMS
LMS
LMS
LMS
Kicker
Kicker
Kicker
NLK
NLK
Kicker
down
up
down
up
out
out
in
1360ns,1kHz
Dipole kicker: horizontal ferrite core out-vacuum kicker+coating ceramic chamber+LC resonance pulser
Inj. NLK: horizontal NLK or Pulsed sextupole+coating ceramic chamber+LC resonance pulser
Septum: Vertical Lambertson magnet
NLK or Pulsed sextupole magnet+ ceramic vacuum chamber
Dipole kicker+ ceramic vacuum chamber
0.333ms,1kHz
1360ns,1kHz

## Slide 14: Dump extraction
Q
Q
?m
?m
35m
0.7m
ϴH=0.11mrad
125m
25m
20mm
Side view
Q
Q
ϴV=26mrad
?mm
450mm
Top view
Lambertson
kicker
?mm
23.85mm
Train by train or bunch-by-bunch extraction
Storage Beam
Injection Beam
Septum Plate 10mm
5mm
5mm
200ns
40~2000ns
200ns
1kHz
Dipole kicker: horizontal out-vacuum delay-line kicker+coating ceramic chamber+PFN-based solid-state pulser
Septa: Vertical Lambertson magnet

## Slide 15: Booster Ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 10 | 120 |  | 10 | 80 | 10 | 45.5
Function | Injection （both） | Extraction （off-axis） | Inj./Ext. （on-axis） | Injection （off-axis） | Extraction （off-axis） | Injection （off-axis） | Extraction （off-axis）
Bunch number | 242（in half ring） |  | 7（in half ring） | 1524（uniform） |  | 6000 | 
Min. bunch spacing （ns） | 680 |  | 23800 | 220 |  | 25 | 
Bunch number per train× train number | - |  | - | - | - | 80×75 | 
Train spacing （ns） | - |  | - | - | - | 2460 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Bunch by bunch | Train by train
Kicker repetition rate (Hz) | 100 | 1000 |  | 100 | 1000 | 100 | 1000
Kicker pulse width (ns) | 1360 |  |  | 440 |  | 50 | <6900
Kicker flat top（ns） | - |  |  | - |  | - | >1980
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <25 | <2460
Timing delay(ns) | <680 |  | <23800 | <220 |  | <2460 | <4400
injection（extraction）period (s) | 2.42 | 0.242 | 0.007 | 15.24 | 1.5 | 60 | 0.075
Kick angle (mrad) | 0.11 | 0.2 | 0.1 | 0.11 | 0.2 | 0.11 | 0.2
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04 | 0.004 | 0.05 | 0.004 | 0.03
Beam pipe aperture Φ（mm） | 55 |  |  |  |  |  | 
Considering the compatibility of three operating modes:
Function | LE-Injection （both） | HE-Extraction （off-axis） | HE-Inj./Ext. （on-axis）
Kicker repetition rate (Hz) | 100 | 1000 | 1000
Kicker pulse width (ns) | 50 | 440~2420(Adjustable) | 1360
Kicker flat top（ns） | - | 0~1980(Adjustable) | -
Kicker rise（fall）time(ns) | <25 | <220 | <680
injection（extraction）period (s) | 60 | 1.5 | 0.007
Kick angle (mrad) | 0.11 | 0.2 | 0.1
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04
Beam pipe aperture Φ（mm） | 55 | 55 | 55
50ns,100Hz
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 16: Collider ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 120 |  |  | 80 |  | 45.5 | 
Function | Injection （off-axis） | Injection （on-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump）
Bunch number | 242（in half ring）- 7 |  |  | 1524（uniform） |  | 12000 | 
Min. bunch spacing （ns） | 680 |  |  | 220 |  | 25 | 
Bunch number per train× train number | - |  |  | - |  | 80×150 | 
Train spacing （ns） | - |  |  | - |  | 245 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Train by train | 
Kicker repetition rate (Hz) | 1000 |  |  | 1000 |  | 1000 | 
Kicker pulse width (ns) | 1360 |  |  | 440 |  | <2460 | 
Kicker flat top（ns） | - |  |  | - |  | >1980 | 
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <245 | 
Timing delay(ns) | <680 | <23800 | <680 | <220 |  | <4400 | 
injection（extraction）period (s) | 0.242 | 0.007 | 0.242 | 1.5 |  | 0.15 | 
Kick angle (mrad) | 0.1 | 0.2 | 0.2 | 0.1 | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.04 | 0.08 | 0.08 | 0.027 | 0.05 | 0.015 | 0.03
Beam pipe aperture HxV（mm） | 75×56 |  |  |  |  |  | 
Function | Injection （on-axis） | Injection （off-axis） | Extraction （dump）
Kicker repetition rate (Hz) | 1000 | 1000 | 1000
Kicker pulse width (ns) | 1360 | 440~2420(Adjustable) | 440~2420(Adjustable)
Kicker flat top（ns） | - | 0~1980(Adjustable) | 0~1980(Adjustable)
Kicker rise（fall）time(ns) | <680 | <220 | <220
injection（extraction）period (s) | 0.007 | 1.5 | 1.5
Kick angle (mrad) | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.08 | 0.04 | 0.08
Beam pipe aperture HxV（mm） | 75×56 | 75×56 | 75×56
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
Considering the compatibility of three operating modes:
200ns
40~2000ns
200ns
1kHz

## Slide 17: Alternative scheme of RF region beam separating system
k1
k2
k4
k3
165us
165us
k1
k2
k3
k4
165us
CW=6.06kHz, 50%
In Higgs mode，e- /e+ beams only fill half ring respectively. So, it is possible to separate beams by kickers.
Compared with electrostatic separator, kicker magnet is stronger and contributes lower beam impedance.
4 sets of kicker locate at both sides of RF region, K1 and k4 applied for e+ beam,K2 and K3 for e- beam;
The waveform of kicker pulsers is square wave with duty cycle of 50%, pulse width of 165 us and frequency of 6.06 kHz;
The phase difference between K1 (K3) and K2(K4) is π.
RFC
RFC
K2
K1
 | Kicker | Septa
Intergrated strength BL [T*m] | 0.1624 | 1.4
Strength B [Guass] | 203 | 1000
Effective length Leff [m] | 8 | 14
Half width of good field region Hgf/Vgf [mm] | 10.1/3.8 @ 5E-4 | 18.9/3.8 @ 5E-4
Half width of beam stay clear Hbsc/Vbsc [mm] | 9.6/3.6 | 9.2/3.6
Septum width width [mm] | - | 10
Delay-line kickers
DC septas
Last e+ Bunch
First e- Bunch
k1
Top view
Yiwei Wang

## Slide 18
Hardware design consideration for CEPC injection and extraction systems

## Slide 19: Main types of hardware
 | Sub-system | Kicker Type | Kicker waveform | Septa Type
1 | Damping ring inj./ext. | Slotted-pipe kicker | Half-sine/250ns | Horizontal LMS
2 | Booster LE inj. | Strip-line kicker | Half-sine/50ns | Horizontal LMS
3 | Booster ext. for CR off-axis inj. | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS
4 | Collider off-axis inj. | Delay-line NLK kicker | Trapezoid /440-2420ns | Vertical LMS
5 | Booster ext. for CR on-axis inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS
6 | Booster HE inj. | NLK or Pulsed sextupole | Half-sine/0.333ms | Vertical LMS
7 | Collider swap out inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS
8 | Collider swap out ext. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS
9 | Collider beam dump | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS
10 | RF region beam separating | Delay-line dipole kicker | CW square / 165us,50% | Horizontal Copper septa

## Slide 20: Lambertson septa design
DS
US
The similar hardware was developed in HEPS, CSNS, BEPC
Higher reliability and stability
The width of septum wall might be in the range from 2mm to 20mm.

## Slide 21: Slotted-pipe kicker design for DR
Outer body (316L)
Busses (FOC)
insulation support (ceramic)
HV feedthrough
Cooling water hole
+
-
To vacuum pump
  Similar design was done in HEPS project(The HEPS Booster kicker)
  E=1.1GeV，Total kick angle: θ=1.5mrad
  Kick strength=0.024T，length of kicker=0.25m，distance between two electrodes=44mm，pulse width<250ns
  U=dɸ/dt=0.024*0.044*0.25/(100*10-9)=2640V。
250ns

## Slide 22: Strip-line kicker design for booster LE inj.
Kick strength
  Total kick angle: θ=0.11mrad
  E=10GeV, d=55mm, g=1 =>U*L>30.25kV∙m
  Total strip-line kicker electrode length L=1m =>U>30.25kV(or ±16kV)
Here, θ is kick angle(rad)；E is beam energy(eV)；U is applied pulse voltage for both electrodes(V)；l is strip-line length；d is the distance between the electrodes，g is the geometry factor, determined by the shape of the electrode. w is the strip-line width.
Kick speed
  Min bunch spacing - τ=25ns
    Electrode length l<3.75m => l= 1m
    Electrical pulse Width 6.7ns< tp <43.3ns =>Flat-top ttop >6.7ns, Rise/fall Time tr/tf <18.3ns
50ns,100Hz

## Slide 23: Strip-line kicker design for booster LE inj.
1000mm
Strip-line kicker
fast pulser
Strip-line kicker and DSRD based short pulsed PS
The similar hardware was developed in HEPS-TF progress.
Feed through
D shape blades
Outer body
Cooling water tube
End cover
4ns
V=17kV,
FWHM=5ns,
Tr(10-90%)<2.6ns,
Tf(90-10%)<3.2ns,
Bottom width(3%-3%)<10ns
PFL=0.3m

## Slide 24: Distributed parameter (delay-line) dipole kicker
Features:
Out-vacuum kicker with metallic coating ceramic vacuum chamber
Solid-state adjustable pulse width PFN based Pulser
The structure of delay-line kicker is complicated; the kind of kicker helps to achieve ideal trapezoid waveform.
PFN
Delay-line kicker magnet
By IHEP，1978
CEARN,SPS
200ns
40~2000ns
200ns
1kHz
Solid-state switches
need a R&D progress for us

## Slide 25
Lumped parameter dipole kicker magnet
Features:
Out-vacuum kicker with metallic coating ceramic vacuum chamber
Solid-state LC discharge half-sine Pulser
It is easier than last type one.
C-type ferrite blocks
metallic coating ceramic vacuum chamber
1360ns,1kHz
C
Ls
LM
Inductive adder based on IGBTs

## Slide 26: Why use nonlinear kicker injection?
Peter Kuske, Proposal for a Transparent off-axis Injection scheme for BESSYII
The advantages of NLK injection:
Off-axis injection, able to accumulate beam
Less disturbance to the stored beam for TOP-UP injection
Need smaller DA
Nonlinear Kicker Injection
Pulsed Local Bump Injection
KEK Pulsed sextupole
BESSYII NLK

## Slide 27
Pulsed sextupole and NLK
Pulsed sextupole magnet:
metallic coating ceramic vacuum chamber + Solid-state LC discharge half-sine Pulser .
Out-vacuum lumped parameter NLK:
metallic coating ceramic vacuum chamber + Solid-state LC discharge half-sine Pulser
Out-vacuum distributed parameter NLK:
metallic coating ceramic vacuum chamber + Solid-state adjustable pulse width PFN based Pulser
It need to push the accelerator physics group to study if NLK is better choice for CEPC off-axis injection.
0.333ms,1kHz
  New proposed
Kang wen
200ns
40~2000ns
200ns
1kHz
Pulsed sextupole magnet
lumped parameter NLK
？
Distributed parameter NLK
Distributed parameter dipole kicker

## Slide 28: Challenge of new beam separating system
Kicker pulser requirements are special:
  Flat-top dropping
  Amplitude long term stability
overshoot
Top-drop
Tail
Amplitude drift
165us
165us
165us
CW=6.06kHz,50%
Ideal
waveform ：
Practical
waveform：
Delay-line kicker model
Septa: horizontal vacuum out DC Cu septum magnet（septum wall=10mm）
Dipole kicker and pulser: ？？
compensate topology
septa
controlling technique
242,1.5MHz
Lumped dipole kicker
  High average power
  High repetition rate
5MW
Energy recycling
CW square wave
High repletion rate short wave

## Slide 29: Hardware R&D Plan
Component | description | Number(set) | schedule
Vacuum chamber | Coated ceramic vacuum chamber | 1 | 24 Mon.
Dipole kicker | Vacuum out distributed parameter dipole kicker magnet | 1 | 24 Mon.
NLK | Vacuum out distributed parameter NLK magnet | 1 | 12 Mon.
Trapezoid pluser | Solid-state pulse width adjustable trapezoid pulser | 1 | 36 Mon.
CW pulser | continuous square wave pulser | 1 | 36 Mon.
Year | 2019 | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  | 
Quarter | 4th | 1st | 2nd | 3rd | 4th | 1st | 2nd | 3rd | 4th | 1st | 2nd | 3rd | 4th | 1st | 2nd | 3rd | 4th
Vacuum chamber |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dipole kicker |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Trapezoid pluser |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CW pulser |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 30: Summary
There are 9 injection and extraction sub-systems in CEPC accelerator complex.
Very preliminary injection layout design was done.
We just figured out what kind of components needed in all sub-systems so far. We still need more input parameters for more detail design.
Hardware R&D plan in the coming years was just proposed .

## Slide 31
END
Thank you for attentions!!!

## Slide 32
Backup slides

## Slide 33: Layout of the accelerator complex
The CEPC accelerator complex consists of a Linac, which including a small damping ring for positron beams, several transport lines, a booster ring and 2 storage rings, all 3 of which are in a single tunnel.
1.2km
10-120GeV
120GeV
120GeV
e+
e-
100km
Damping ring
Dump
Dump