## Slide 1: Design Status of CEPC Control System
Presented by Gang Li
Feb. 14th, 2020

## Slide 2: Outline
Characteristics and Challenge of CEPC Control System
Feedback from 2019 CEPC IAC
Investigation and Research on key technology of control system
Summary

## Slide 3: Characteristics and Challenge of CEPC Control System
Super scale--CEPC VS BEPCII, CSNS or HEPS
  Linac: 1.2/1.4Km
  Ring: 100Km
A large number of Controlled Equipments
  Discrete distributed in the Linac and Ring
Quantity of controlled devices’ PV
  Hundreds of thousands

## Slide 4: Feedback from 2019 CEPC IAC
Data rate, traffic in the network
  Interface between the detectors and accelerator

## Slide 5: Investigation and Research on key technology of control system
Distributed control system
Based on Ethernet
Data processing
  Hardware: Control Network(VLANs)
  Software: PVA Gateway

## Slide 6: Investigation and Research on key technology of control system
Control Network
  Commercial products(Huawei,Ruijie, etc)
  Distance：40Km
  Transmission rate：100Gbit/s，30Gbit/s
  The rate of signal in optical fiber: ~0.7*c
    Delay time: 200µm*2
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 7: Investigation and Research on key technology of control system
Software
  VLAN(Virtual Local Area Network)
  Archivers
  CA/PVA Gateway
  …
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 8: Investigation and Research on key technology of control system
Software
  Data Archiver
    Channel Archiver(CA)
    Archiver Appliance(CA/PVA)
  Archive millions of PVs
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 9: Investigation and Research on key technology of control system
Software
  CA/PVA Gateway
    Reduce the resource load on IOCs
CA/PVA Gateway
M*N->M+N
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 10: Investigation and Research on key technology of control system
Software
  CA/PVA Gateway
    Access control restrictions to requests from the clients
Accelerator
Detectors
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 11: Investigation and Research on key technology of control system
Localization controller
  PLC controller
    SUPCON(浙江中控)
    HollySys(和利时)
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 12: Investigation and Research on key technology of control system
Localization controller(SUPCON PLC)
  2019.7/2019.12, technology exchange
  Reliability
  Availability
The prototype PLC at Lab
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 13: Investigation and Research on key technology of control system
Interact with Detectors
  Software signal
  Hardware signal
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 14: Investigation and Research on key technology of control system
Requirement information of controlled devices
Notes: 周长100Km，直径31.85Km，光速3*10e8，在光纤中速度约2*10e8

## Slide 15: Summary
More detailed requirements should be further clarified, with the progress of CEPC TDR
EPICS：Cooperate closely with EPICS community
AI/machine learning in control system
Thanks a lot!