## Slide 1: Progress of Mechanics system
Haijing Wang
CEPC DAY, 2020/2/14

## Slide 2: Overview
Progress since 2019/06/28 (Last report on CEPC day):
  Supports
  Movable collimators
  MDI mechanics
    Installation scenarios
    Remote vacuum connection
    Cryostat support system

## Slide 3: Supports
Over 80% of the length is covered by magnets of about 138 types, each magnet needs to be supported.
Accelerating tubes, vacuum tubes, instruments…, all need supports.
We has began the cooperation on design with members of CIPC

## Slide 4: Supports
Common girders for quadrupoles and sextupoles are also in consideration
Pre-aligned units can save workload in tunnel and reduce the relative misalignment
Long and thin, hard to design in stiffness
No change for the supports in Booster and Linac
Booster
Collider

## Slide 5: Tunnel mockup
Total length: 40 m
A tunnel mockup is designed for the interface checking of the equipment locations, installation, alignment and transportation. It includes part of arc section and part of RF section.
The relative locations between magnets in each ring is the same as the lattice design.

## Slide 6: Transport vehicles
Over 80% of the tunnel length is covered by magnets. Efficiency of transportation and installation must be considered.
Transport vehicles are designed for the magnets transportation and coarse positioning.
Accuracy of coarse positioning: better than 0.5 mm.
Vertical driven unit
Chassis
Balance weight
Horizontal driven unit
Load support
  * Cooperate with Beijing North Vehicle Group Corporation.

## Slide 7: Transport vehicles
Transportation and coarse location of magnets in Collider
Transportation and coarse location of magnets in Booster
Flexible load support for “long” devices and “short” devices
  * Cooperate with Beijing North Vehicle Group Corporation.

## Slide 8: Movable collimators
Located in straight section between two dipoles, the length is 800 mm.
Five horizontal collimators in each ring are designed in the TDR stage.

## Slide 9: Movable collimators
Highest Von Mises Stress by synchrotron radiation: 81 MPa
Synchrotron radiation: 7700W @120GeV, 30MW.
Preliminary thermal-static analyses by synchrotron radiation have been done. Material: Glidcop-Al15.
Cooling method | Loads | Highest temperature（℃）
Copper & water | Surface load | 286
Copper & water | Volume load (Damping of X ray) | 148
Laminated material & water | Surface load | 146
Highest temperature by synchrotron radiation: 148 ℃
Photon energy damping in
Copper @ 300 KeV

## Slide 10: Movable collimators
* From Carsten Niebuhr, IAS MDI Workshop, Hongkong, 16.-17.01.20
Laminated material with copper and graphene film
Y: Highest temperature;
X: Thickness of membrane of high thermal conductivity
Laminated materials with metal and high-thermal-conductivity membrane is considered for severe heat load.

## Slide 11: Movable collimators
Two inner profiles are designed, gradual rectangle and gradual ellipse with movable stoppers in them.
RF fingers are at the edges of the stoppers to decrease impedance.
Gradual rectangle profile
Gradual ellipse profile
 |  | Energy loss (no RF fingers) (W) |  | 
 |  | Higgs | W | Z
Gradual rectangle profile | Stopper open | 66 | 267 | 933
 | Stopper closed | 39 | 160 | 560
Gradual ellipse profile | Stopper open | 8 | 32 | 112
 | Stopper closed | 19 | 76 | 266
  * From Y Liu et al., Impedance and Collective Instabilities for Collider, Booster and damping ring in CEPC, this workshop

## Slide 12: MDI mechanics
IP chamber & pixel support by Q. Ji
Connection interface of detector and accelerator
SC magnets, cryostat and their support
First vacuum pump @±6.5m

## Slide 13: MDI mechanics
Installation scenario of MDI
  Assume the IP chamber and the detectors, the yoke have been installed.
  The remoted vacuum connection methods will be used.
  The support system of cryostat is under studying.
  The idea of Lumical being moved to the detector part has been discussed.
Pre-alignment of SC magnets and installation of accelerator components
The connection and alignment of one side
The similar procedure at the other side

## Slide 14: MDI mechanics
An alternative scenario
  The baseline of SuperKEKB before the validation of RVC.
From K. Kanazawa of KEKB, the 18th KEKB Accelerator Review Committee, 2013
  This scenario is connecting one end of IP chamber with cryostat outside the detector .
  But unlike the asymmetry of SuperKEKB MDI, this scenario can't cut out the remote vacuum connection at the other end of IP chamber.
Not advisable

## Slide 15: MDI mechanics
Another alternative scenario
  The method like DAFNE. Being considered by FCC and BINP.
A. Bogomyagkov, et al., Mechanical design of the FCC-ee interaction region, FCC week (24 –28 June 2019) Brussel
A.Bogomyagkov, MDI issues of BINP Super TauCharmfactory, Report on IAS 2020.(Hongkong, 2020).
This scenario is connecting both ends of IP chamber outside the detector like
DAFNE.
The two cryostats can be well pre-aligned but it is impossible to move the whole assembly into the detector without changing the size of detector hole.
Not advisable

## Slide 16: MDI mechanics
Lists to be done:
  Vacuum connection method. Leak rate requirement: ≤2.7e-11Pa.m3/s
  Support system. Alignment error requirement: ≤30 μm, at least ≤50 μm.
  3D layout of all the components, find and solve the space problems.
  The vacuum tubes and cooling methods.
  Integration of accelerator and detector, and the installation and replacement scenarios.

## Slide 17
 | Distance from yoke boundary to connection location (m) | Alignment requirements of SC/ deformation of cryostat (μm)
BEPCII | ~2.3 (has manual operation space) | Tested deformation: 960
SuperKEKB | ~3.5 (the longer side) [1] | Analyzed deformation: 900 [2]
FCC-ee | ~4.37 [3] | Alignment error: ≤50 [4]
CEPC | ~3.8-6.1 * | Alignment error: ≤50
[1] Hiromi linuma, SuperKEKB status. Report, Nov, 2013。
[2] Hiroshi Yamaoka, et al, The mechanical and vibration studies of the final focus magnet-cryostat for SuperKEKB. Proceedings of IPAC 2014, Dresden, Germany.
[3] M. Koratzinos, Overview of MDI at FCC-ee, Report on IAS 2020.(Hongkong, 2020).
[4] Future Circular Collider Study. Volume 2: The Lepton Collider (FCC-ee). Conceptual Design Report. V0.20, 8 Nov, 2018
*: The distance needs to be discussed further. The current design is based on the shortest version.

## Slide 18: MDI mechanics-Remote vacuum connection
Bellows
Spline flange
flange
Pneumatic annular
Long tools
Support
Spline gear
Locking gear
Flange
Screw thread
Limit pin
Spline flange
Spline gear
RVC Design
Dimensions:
Transversal: Max. ϕ264mm
Longitudinal: ~223mm
  * Cooperate with Shenyang Huiyu vacuum technics co., Ltd.

## Slide 19: MDI mechanics-Remote vacuum connection
Flange
Flange
Sealing membrane
bellows
Guiderods and limits
Tubes
Flange
Inflatable seal design
Dimensions:
Transversal: Max. ϕ112mm
Longitudinal: ~120mm
  Experience from CSNS: leak rate requirement: ~10-7 Pa.m3/s level, four levels higher then CEPC requirement.
  Best obtained: ~10-9 Pa.m3/s level
Improved methods
  Precision machining of sealing membrane and flange.
  Different materials of sealing membrane and flange.
  Using edge sealing instead of membrane sealing.
  …

## Slide 20: MDI mechanics-Remote vacuum connection
 | RVC design | Inflatable seal design
Sealing methods | Pneumatic clamping with auxiliary locking | Pneumatic clamping
Advantages | Successful experience from SuperKEKB; Having auxiliary locking Independent on operating distance to some extend (rotating long tools ). | Small and simple; Bellows at accelerator side; Independent on operating distance totally.
Disadvantages | Big and complex; Bellows at IP chamber side; | Difficult on leak rate requirement; Without auxiliary locking
An improved design of inflatable seal
Three MDI installation scenarios Remote vacuum connection is inevitable.
Remote vacuum connection design is relatively independent on other devices.
We will concentrate the leak rate problem of inflatable seal design by the improvement methods, and also take the RVC design as the baseline since it has successful experience from SuperKEKB.

## Slide 21: MDI mechanics-Remote vacuum connection
The design review was hold on July 23,2019
…,所提出的MDI远程真空连接方案原理可行、结构方案合理，通过评审。
Total valuation: 960,000 RMB

## Slide 22: MDI mechanics-Support system
Support system of SC magnets
  The alignment accuracy of SC magnets: ≤30 μm, at least ≤50 μm.
  Movement mechanism: high precision track & rack.
  Adjusting mechanism: motor driven wedges jacks for vertical direction, motor driven screw jacks
Cryostat
Adjusting mechanism
Support bed
Movement mechanism
  * Cooperate with Beijing Institute of Space Mechatronics

## Slide 23: MDI mechanics-Support system
Max deformation owing to gravity: 190 um
Under 1 ℃ environment temperature variation, Max deformation varies 48 um
The current design of cryostat is 5 meters long with18 mm thick stainless walls. The weight of the cryostat is about 2 tons.
Only the cryostat itself is considered in the calculation above.
If the yoke length gets larger, the deformation will be even larger, which is proportional to the 4th power of length.
If the weight of components inside the cryostat and the magnetic field forces are considered, the deformation will be much larger.
  Detailed analyses of the cryostat & support assembly should be done, including the deformation and vibration, considering gravity, temperature, magnetic field force.

## Slide 24: MDI mechanics-Support system
Modal analyses: order 1- order 6
1st: Vertical wiggling
2nd: Horizontal wiggling
3rd: Horizontal bending
4th : Horizontal bending
5th : Vertical bending
6th : Vertical bending

## Slide 25: MDI mechanics-Support system
9th : Rotating
7th
8th
10th
FCC said the just considered the rotating modal order.
We think we can only ignore the 7th, 7th, and 10th modal orders. At least the first Eigen frequency must not be ignored.
We have the same ideal as SuperKEKB.
Needs discussion further.

## Slide 26: MDI mechanics-Support system
We are considering to pre-align the SC magnets to “certain location” to compensate the effect of loads. It needs complex stiffness design and has risk, especially for the stability and repeatability.
The magnetic field forces in Z, H, and W operations are different. The pre-alignment should fulfill all the cases.
The design will be adjusted with detector design, dynamic design and alignment design.
We will learn the successful experience from other facilities.
N. Ohuchi, IPAC2018
SSW measurement of SuperKEKB
Max. center misalignment is 0.69 mm
“Every alignment errors are able to corrected by the corrector magnets.
No clear alignment solution right now!

## Slide 27: Summary
The common girder design is being considered as a alternative support method for quadrupoles and sextupoles in Collider.
A 40 meters mockup of arc-section has been designed for interface checking, installation, alignment and transportation.
Transport vehicles for the magnets transportation and coarse positioning has been designed.
Preliminary structure design, FEA and impedance calculation has been done for the movable collimators.
For the MDI region, the design of the remote vacuum connection methods have been done, and the support system of SC magnets is under design.

## Slide 28: Thanks