## Slide 1: Design status of CEPC mechanics
Haijing Wang
The 2020 Workshop of CEPC, Shanghai
Oct. 26-28, 2020

## Slide 2: Outline
Overview
Design status for the accelerator
  Magnet supports
  Transportation and installation
Design status for the IR
  MDI layout
  Integration and alignment scheme
  Remote vacuum connector
  SC magnet supports
Movable Collimators
  Structure design and FEA
  Considerations for severe thermal loads
Lists to be done

## Slide 3: Magnet supports
Over 80% of the length is covered by magnets of about 138 types.
Adjustment Ranges of magnets |  |  | 
X | ≥±20 mm | Δθx | ≥±10 mrad
Y | ≥±30 mm | Δθy | ≥±10 mrad
Z | ≥±20 mm | Δθz | ≥±10 mrad
Booster
Collider

## Slide 4: Magnet supports
Plenty of supports to be designed.
We has began the cooperation on design with members of CIPC

## Slide 5: Magnet supports
Optimization for dipole supports
Magnet group people will check if the deformation is workable.
No. of supports | Max. deformation (um)
3 | 19
4 | 7
5 | 5
Other magnet girders will be renewed too.
  Simple & flexible structure.
  Small deformation & good stability
  Low cost
  * Cooperate with Keye co., Ltd

## Slide 6: Transportation and installation
Transportation and coarse location of magnets in Collider
Transportation and coarse location of magnets in Booster
Flexible load support for “long” devices and “short” devices
  * Cooperate with Beijing North Vehicle Group Corporation.

## Slide 7: Transportation and installation
Plinth installation and grouting
  Pre-machined plinth.
  Specialized tooling to improve efficiency.

## Slide 8: MDI layout
Vacuum layout
  Inner diameter at IP: 28 mm
Be
Al
Cu
IP chamber
Y-shape
chamber
Cryostat chamber
Paraffin cooled
Water cooled
IP
IP BPM
Lumical
Water cooled
Vacuum connection
No forced cooling
RF bellows
Semi-symmetry layout to avoid SR

## Slide 9: MDI layout
IP chamber by Q. Ji
Connection interface of detector and accelerator
SC magnets, cryostat and their support
First vacuum pump @±6.5m

## Slide 10: MDI Layout
10
Difficulties:
    Avoid SR
    Limited longitudinal space: IP chamber, vacuum connector, Y-shape chamber, BPM, Lumical…
    Limited transversal space: all the structure should be within detection angle.
BPM
Lumical
Remote vacuum connector

## Slide 11: Integration and alignment scheme
 | Distance from yoke boundary to connection location (m)
BEPCII | ~2.3 (has manual operation space)
SuperKEKB | ~3.5 (the longer side)
FCC-ee | ~4.37
CEPC | ~3.8-6.1 *

## Slide 12
Before and after BESIII push-in
Accelerator foundation is fixed. It is good at:
  Beam stability.
  Integration of detector before push-in.
Detector foundation is fixed. It is good at:
  Detector stability
Maybe we can find balanced approach (very long distance with only beam pipes near MDI)
Before Beast(II) push-in
Detector push-pull arrangement of ILC
Integration and alignment scheme

## Slide 13
Alignment scheme
Integration and alignment scheme
From X. Wang
Alignment scenario:
  Pre-align the SC magnets using vibrating wire system to “certain location” to compensate the effect of loads.
  Align the SC magnets in two cryostats using optical system.
  Measure misalignment using SSW and adjust by corrector magnets meet the alignment requirements.
  Details are under study.
N. Ohuchi, IPAC2018
SSW measurement of SuperKEKB
Max. center misalignment is 0.69 mm
“Every alignment errors are able to corrected by the corrector magnets.
VWS is a candidate pre-alignment method, accuracy of magnet centers: ≤10 μm

## Slide 14: Remote vacuum connector
Difficulties:
    Longitudinal space: Bellows should absorb deformation when baking. Add Z-direction support, length has been decreased to 83mm.
    Minimize thermal loads: The thermal loads mainly includes SR power and HOM power. Avoid SR power by layout design, and decrease HOM power by RF finger.
    Cooling: It is hard to dissipate the heat at RF finger which is thin, low thermal conductivity and far from the coolant. FEA
Totally 4 mechanisms have been designed, one is focused on now.
    Transversal space: All the structure should be within detection angle.
    Leak rate requirement: Ultra-high vacuum. Leak rate requirement: ≤2.7e-11Pa.m3/s

## Slide 15: Remote vacuum connector
Improved inflatable seal
Two layers of edge sealing
Replace the sealing membranes by two layers of edge sealing.
RF finger
Dimensions:
Transversal: Max. ϕ174mm
Longitudinal: ~83mm
Low vacuum

## Slide 16: Progress of remote vacuum connector
Sealing methods | Within detection angle | Leak rate estimation | Remarks
RVC | NO |  | Successful used in S-KEKB
Remote chain | Yes |  | Eliminated
Inflatable seal* | Yes |  | Experience from CSNS
Improved inflatable seal | Yes |  | Mainly focused on
* Our experience:
    Single-layer  double layer, leak rate can be improved from 1e-6 Pa.m3/s to 8.5e-10 Pa.m3/s.（From D. Zhu）
    Replace membrane sealing by edge sealing
From J-parc

## Slide 17: Progress of remote vacuum connector
Leak rate estimation of improved inflatable seal
  Theoretical derivation (Roth’s model)
  Flow conductance: 10-11~10-12 m3/s.
  Can fulfill the leak rate requirement when the pressure in low vacuum region is lower then 1 Pa level.
  Roughly estimation.
Next step
  Consider the effect of flatness
  Match the FEA with simple tests.
  Deduce the leak rate by analogy and FEA.
  Prototype.
From X. Tang

## Slide 18: Progress of remote vacuum connector
RF finger is thin, low thermal conductivity and far from the coolant.
Maybe the materials can be replaced?
 | CDR H | CDR Z | CDR High Luminosity Z
Power density (W/cm2) | 0.135 | 1.36 | 4.4
Highest temperature (℃) | 44.5 | 248.8 | 755
Structure | Material | Thermal conductivity W/(m·K)
Bellows | 316L | 15
Flange | 316LN | 
Squeezing finger | Inconel 625 | 9.8
Sliding finger | BeCu | 118
Coolant

## Slide 19: SC magnet supports
Key points
  Stability (static and modal)
  Accuracy
  Easy-operating
  Dimensions
Deformation analyses
Modal analyses

## Slide 20: SC magnet supports
High stiffness for stability Flexibility for high accuracy.
Studies on support stiffness is on-going.
Motor driven wedges jacks for high stiffness and accuracy.
Auxiliary support, high damping material/structure are also in consideration
High stability
From Y. Wang
Confliction

## Slide 21: Movable collimators
Located in straight section between two dipoles, the length is 800 mm.
SR power: 7700W @120GeV, 30MW
Loss-Factor: 0.045V/pC
Ploss: 18.8w(Higgs)/76.1w(W)/265.8w(Z)
From Y. Liu
Highest temperature: 148 ℃
From P. Zhang

## Slide 22: Considerations for severe thermal loads
GF-Cu composite
SR power: GF (Graphene film) –Cu composite
Beam deposition: Aborting system
GF-Cr composite
Disregistry of C-Cu &C-Cr
Y: Highest temperature;
X: Thickness of membrane of high thermal conductivity
From P. Zhang
Carsten Niebuhr, IAS MDI Workshop, Hongkong, 16.-17.01.20

## Slide 23: Lists to be done
Detailed design of optimization the magnet supports.
Further estimation the leak rate of the remote vacuum connector.
Detailed design of SC supports.
More detailed integration scheme with detector.
Alignment scheme.
Detailed design of movable collimators and further consideration of severe thermal loads
…

## Slide 24: Back ups

## Slide 25: Remote vacuum connector
Bellows
Spline flange
flange
Pneumatic annular
Long tools
Support
Spline gear
Locking gear
Flange
Screw thread
Limit pin
Spline flange
Spline gear
RVC Design
Dimensions:
Transversal: Max. ϕ264mm
Longitudinal: ~223mm
  * Cooperate with Shenyang Huiyu vacuum technics co., Ltd.

## Slide 26: Remote vacuum connector
Pneumatic peanut ring
Bevel gears
Chains
Bi-direction screw
Support
Universal joint
Pneumatic tube
Bellows
Dimensions:
Transversal: Max. ϕ177mm
Longitudinal: ~215mm
Remote chain seal

## Slide 27: Remote vacuum connector
Flange
Flange
Sealing membrane
bellows
Guiderods and limits
Tubes
Flange
Inflatable seal
Dimensions:
Transversal: Max. ϕ174mm
Longitudinal: ~67mm
  Experience from CSNS: leak rate ~10-7 Pa.m3/s level, four levels higher then CEPC requirement.