## Slide 1: TDAQ and online computing
David Newbold(UKRI), Chris BEE(Stony Brook/BNL),
Zhen-An LIU(IHEP)*
Plenary Session CEPC Workshop 2020
SJTU/Shanghai, Oct. 28 2020

## Slide 2: Outlook
Overview on the TDAQ activies
Focus on the talks and discussions in the TDAQ two sessions in this workshop
Some key outcome points and potential action
Summary

## Slide 3: Overview on TDAQ activities
Experiments Experience Studies by invited talks(at previous workshops)
  Data Acquisition for the PANDA Experiment at FAIR by Wolfgang Kuehn(U.Giessen)
  Overview of CMS Trigger by Simon Bologna（U Bristol）
  The LHCb Triggerless readout system for LHC Run 3 and beyond by Federico Alessio(CERN)
  ATLAS Solution for Phase 2 Storage and Networking by Fabrice Le Goff (CERN)
  Data Acquisition for the ATLAS Inner Tracker beyond 2026 by Jens Dopke
  DUNE DAQ Plans by Pengfei Ding(FNAL)
  LHCb VELO Readout by Karol Hennessy(U. Liverpool)
  ATLAS experience with FPGA(TDAQ’s perspective by Weimin Qian(RAL)
  Real-time analysis with LHCb by Saur Miroslav(UCAS)

## Slide 4: Overview on TDAQ activities(2)
Progress on CEPC TDAQ R&D(prior to now)
  Hardware Development at IHEP by Jingzhou Zhao(IHEP)
  Readout of JadePix-1, A prototype CMOS Pixel Sensor for CEPC Vertex Detector by Jia Tao(IHEP)
  Discussion of CEPC DAQ (EB and networking) by Fei LI(IHEP)
  xTCA development/applications on Belle II/CMS Experiment and perspective to CEPC TDAQ by Z.A.LIU (IHEP )

## Slide 5: It’s time
Turning from consideration of work outside CEPC to discussion of issues and practical steps specific to CEPC detector
  Better understanding the detectors
  Start TDAQ R&D activities

## Slide 6: New iteration of understanding of the sub-detectors(this workshop)
Update the Data Volume and channel count under different machine running modes
  Higgs
  W
  Z
New assumptions about readout bandwidths and readout implementation and power consumption
Any zero suppression or compression they might carry out at the front end
  No
  YES, then how

## Slide 7: Collect Clearer requirements to TDAQ at this workshop
Needs for control and timing signals in FEE
  Clocks, Synch,BC0,L1A,SC,…
Any views/preferences on readout style(triggered or trigger-less readout)
  Trigger sequential readout
  Continuous sequential readout
  Non-sequential readout

## Slide 8: Morning/Afternoon for Time Zone
Morning
  Requirement from the LumiCal, Suen Hou (IPAS)
  Requirement from the Vertex Detector, Wei Wei (IHEP)
  Requirement from the TPC, Huirong Qi (IHEP)
  Requirement from both ECAL & HCAL, Yong LIU (IHEP)
Afternoon
  Requirement to from Drift chamber, Franco Grancagnolo (INFN-Lecce)
  Requirement from DR Calorimeter, Roberto Ferrari (INFN)
  Requirement from Muon detector, Paolo Giacomelli (INFN-Bo)
  Requirement from Silicon Tracker, Jens Dopke (STFC RAL)

## Slide 9: Vertex Detector by WeiWei(IHEP)

## Slide 10: Trigger/triggerless readout?

## Slide 11: Silicon Tracker by Jens Dopke(STFC/RAL)
Good progress with prototype
BW:10Gb/s/link* 4k links=40Tb/s
Suppression: 1/(5-10), <10Tb/s

## Slide 12: Clear Requirement to TDAQ
Both Trigger based mode and triggerless mode
Slow control requirement expected
FE Chip
FE Chip
FE Chip
FE Chip
Local aggregation
On Module Condensing
Local Support Aggregation
Condensing
O(1) Gbps
O(10) Gbps

## Slide 13: Drift Chamber by Francesco Grancagnolo (INFN-Lecce)

## Slide 14: Maximum total Volume in trigger mode

## Slide 15: Total Data Volume after reduction

## Slide 16: TPC by Huirong Qi
Total Channel:840k,6.5K chips

## Slide 17: TPC by Huirong Qi
Total data volume:13.8GB/s
Trigger option unclear yet

## Slide 18: ECAL by Yong Liu(IHEP)

## Slide 19: HCAL by Yong Liu(IHEP)

## Slide 20: ECAL/HCAL by Yong Liu(IHEP)
Requirements to TDAQ still unclear

## Slide 21: DR Calo by Roberto Ferrari(INFN)
?

## Slide 22: DR Calo by Roberto Ferrari(INFN)
Requirement to TDAQ to be considered

## Slide 23: LumiCal by Suen Hou(IPAS)

## Slide 24: LumiCal by Suen Hou(IPAS)

## Slide 25: Summary of the Requirement
.

## Slide 26: Further action
We gather the updated requirements from all sub-detectors as in last page, we will review them carefully for consistency, and to inform what future work is needed on TDAQ.
Some quick comments on each of the detector system see backup slides

## Slide 27: Invited Special Technology on readout
Pixel readout technologies and the challenges for the future
  By Maurice Garcia-Sciveres (LBNL)

## Slide 28: Invited Special Technology on Software trigger
ATLAS HLT tracking optimisation

## Slide 29: Good example of Offline selection to online HLT

## Slide 30: Good example for Resource estimation

## Slide 31: Invited Special Technology on TCDS
Precision timing distribution systems and their current performance
  By Eduardo Mendes(CERN)

## Slide 32: How a precise timing distribution could be realized

## Slide 33: Versatile Link for low-jitter

## Slide 34: Implementing the Versatile link in the experiment

## Slide 35: Higher Phase-determinism IP

## Slide 36: Timing compensation and monitoring

## Slide 37: Discussions on Stradegy of DCDS/TDAQ Rearch & Design
Accelerator interface with DCTD
  Machine Clock/Synchronization Signals
  BC0, revolution,…
  TDAQ status feedback
Readout Structure
  IHEP Experience and Application in Belle II and CMS
  Which platform one prefer?
    Micro-TCA(MTCA) or
    Customized ATCA or
    xTCA (ATCA-PICMG3.8/MTCA.4) or
    Other standard?

## Slide 38: Discussions on DCDS/TDAQ(cont.)
Online networking and computing
Hardware/Firmware Technologies
  Common hardware(backend readout)
  FPGA/GPU/… based processor
  Common Firmware
  Software DEV platform
Prototypes development
  Welcome for R&D
  How to collaborate
Demo System development
  Components
  Key modules R&D
  Task sharing
Other more issues？

## Slide 39: Highlight/key points
We learn that constraints from Vertex detector are probably the most significant
Other detectors are less constrained, but the data rates may still be very large, and present a significant data concentration problem
Common philosophy/ideas/standards are now needed for control and readout of on-detector electronics, to prevent from any divergence
Agreeing these common standards will make early R&D and prototyping possible and optimally for everyone. (more refers to backup slides)

## Slide 40: Potential next actions
Start to consider timing and control strategy
  Must avoid divergence of thinking in different groups / detectors
Start to consider online software strategy
  Produce first estimate of required resources (mostly human)

## Slide 41: Summary
Very productive sessions
  Updates on the requirements to TDAQ
  Better understanding
More Detailed Key Technologies presented
Fruitful discussion with common understanding
Potential next work/actions are proposed

## Slide 42: backups

## Slide 43: Summary and thinking of Lumical
Event rate 2.6kHz @ 10e34
80k channels @8b -> 210MB/s
(Lumi goes up to 10e36???)
ZS factor 1%
-> 21MB/s
Could trigger from strip detector
L1 -> 100kHz?
L2 -> 10kHz?
HLT -> 1kHz?
Stand alone -> but data rates not huge
(Separate DAQ stream?)

## Slide 44: Summary and thinking of Vertex
Peak hit occupancy: 120MHz / chip in W mode
Dominated by inner layer (outer layer 10x smaller)
Event-driven readout - what does this mean?
Can handle both triggered and trigger less readout
Triggered -> 160Mb/s/chip; max 3us latency
Triggerless -> 4Gb/s/chip
5000 chips total
Preference: no output to trigger, receives trigger
(But the latency?)
Say 1000 @ 4Gbps for inner layer -> 4Tb/s (!!!)
Speaker estimates ~8Tb/s
-> No pixels in trigger
-> Trigger required
Triggered data rate is low
-> Read out on L1, but latency is a serious challenge
Room for compromise on buffer depth?

## Slide 45: Summary and thinking of TPC
Raw data rate 13.8GB/s -> small
Readout time 100us?
Does not seem compatible with inclusion in the trigger

## Slide 46: Summary and thinking of Calo
Order 10GB/s for both options ECAL
0.3 - 1GB/s for HCAL
Triggerless fully possible…
But what about readout link count?
What about latency?
Main problem will be data concentration
(-> more latency!)

## Slide 47: Summary and thinking of Calo
IDEA
200kHz event rate assumption (FCCee)
56k channels, 400ns drift time
2Gs/s per channel at 12b
Post-ZS raw data rate 1TB/s (TRIGGERED)
60GB/s after clustering - could improve with timing information
Can be self-triggering (note the 400ns)

## Slide 48: Summary and thinking of DR Calo
300kW!
40GB/s at 100kHz triggered
“Very conservative”
More reasonable, 1.3GB/s (trivial)
Untriggered? What is trigger output?
1TB/s noise hits!
No discussion of trigger outputs so far
(What is the raw-raw rate? Looks like 400 * 1.3GB/s = 500GB/s? This is quite large)

## Slide 49: Summary and thinking of Muon
2.5MB/s for 100kHz triggered -> very small
(1.5M ch)
Preshower 300MB.s
(7.5M ch)
Untriggered readout probably possible, yet to be investigated

## Slide 50: Summary and thinking of Silicon
50m^2 silicon, 150k sensors
Can run triggerless or triggered
SLOW CONTROLS?
Material vs redundancy
4k data links * 10Gb/s = 40Tb/s
Buffer size for triggered is 80 hits / chip
- Seems fine at Z pole
2Tb/s raw

## Slide 51
Potential next actions:
Understand what data is available from calo / muons
Define basic trigger selections, investigate selectivity, trigger rates, etc.
  Understand whether fast tracking information is useful / necessary
  ‘Lightweight L1’
Look at whether implementation in 3us is feasible
Tabulate data rates from detector for LL1, start to look at consequences
  Data rates from detector
  Necessary modularity and concentration of readout
  Power and cost of electronics on and off detector
    Order of magnitude estimates only
Tabulate data volumes and rates to storage
  Do we need a further pass of data selection, or
  Assume a ‘keep everything’ strategy after LL1?
  Perhaps a first pass of further RoI selection / zero suppression?
  What level of monitoring / prompt reconstruction is needed?
Start to consider timing and control strategy
  Must avoid divergence of thinking in different groups / detectors
Start to consider online software strategy
  Produce first estimate of required resources (mostly human)

## Slide 52: TDAQ Coverage
Detector Readout
Hardware Trigger
Software/High Level Trigger
Event Building and Storage with Online Control
Fast Control/TCDS/machine interface
Slow Control/future trend

## Slide 53: Strategy
  Investigate other experiments
    Trigger based System/Triggerless System
    Trigger based readout/triggerless readout
    If Trigger less
      Continuous Sequential readout/non-sequential readout
  International Exchange/collaboration
  Further understanding with the Bandwidth of Detector Systems
  Determine the requirements from Detector Readout
    Trigger/triggerless readout
    If triggerless: Continous sequential/non-sequential readout
  TCDS
    Time Stamp (BCN/BX, L1, …) for both trigger/triggerless
  Hardware readout Structure(VME/xTCA/PXI,…)
  Networking and Online

## Slide 54: More Key points to think
Early decisions on trigger and readout mode are important
They fundamentally affect design of detector
Some kind of fast trigger is needed for vertex (at least)
Is this guaranteed by design constraints?
3us implies hardware, is this a fixed parameter?
Only first thinking about trigger signals from calo / muons
- Seems feasible to do trigger less readout of both
- Implications need some study
Do we need tracks in the trigger system?
Drift chambers seem possible to read out triggerless
Not clear whether tracking is doable or whether it is necessary
Is it possible to make vertex detector RoI choices based on call / muons alone?
We have a DATA CONCENTRATION problem in some sub detectors
Potentially inefficient use of data links without significant aggregation
What about slow controls? Timing?
Can we aim for a ‘fully integrated / redundant’ control system?
Can we aim for a common readout protocol?
For some systems (vertex, silicon), timing and control needs vary according to run mode