## Slide 1: CEPC optics correction with magnet’s errors and influence to DA
Yuanyuan Wei, Bin Wang, Yiwei Wang, Chenghui Yu, Yuan Zhang
The Institute of High Energy Physics, Beijing
CEPC Day March 27 2020, IHEP

## Slide 2
The magnet’s error effect
The correction scheme
The correction results
  50mm IR quadupole misalignment
  100mm IR quadupole misalignment
Algorithm upgrade
Summary
To do list
Outline

## Slide 3: Lattice
E=120GeV
=363.11
=365.22
= 0.36m
= 0.0015m
=599m
=4023m
= 1.21nm

## Slide 4: Magnet’s error effect
  Horizontal misalignments in quadrupoles
  ΔDx and Δx
  Vertical misalignments in quadrupoles
  ΔDy and Δy
  Horizontal misalignments in sextupoles
  beta beat and tune shift
  Vertical misalignments in sextupoles
  ΔDy and coupling
Component | x (mm) | y (mm) | z (mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 100 | 100 | 100
Sextupole | 100 | 100 | 100
Component | Field error
Dipole | 0.01%
Arc Quadrupole | 0.02%
  Bending field errors
  ΔDx and Δx
  Quadrupole field errors
  beta beat and tune shift

## Slide 5: Correction scheme
COD correction with sextupoles off
Turn on the sextupoles and perform COD correction again.
Dispersion correction (DFS)
Beta beating correction (LOCO)
Coupling and vertical dispersion correction (Local coupling parameter correction）.

## Slide 6: COD correction
BPMs placed at quadrupoles (~1500, 4 per betatron wave)
Horizontal correctors placed beside focusing quadrupoles（~1500）
Vertical correctors placed beside defocusing quadrupoles（~1500）
Orbit correction is applied using orbit response matrix and SVD method.

## Slide 7: COD correction
IR=50mm 981 seeds
IR=100mm 955 seeds

## Slide 8: Dispersion correction
Dispersion free steering principle (DFS): orbit manipulation by knob correctors.
M
rbit vector
vector
: Weight factor
A: Orbit response matrix
B: Dispersion response matrix

## Slide 9: Dispersion correction
decreased from 29mm to 4.3mm
Factor 7 improvement
decreased from 102mm to 2.3mm
Factor 44 improvement
IR=50mm 943 seeds
IR=100mm 736 seeds
decreased from 31mm to 2.2mm
Factor 14 improvement
decreased from 42.7mm to 5.9mm
Factor 7 improvement

## Slide 10
Beta-beating correction
Correct the beta functions with sextupoles on.
Based on AT LOCO: model based correction
  Establish lattice model Mmod, multi-parameter fit to the orbit response matrix Mmeas to obtain calibrated model:
  Parameters fitted: K, KS …
  Use calibrated model to perform correction and apply to machine.
  Application to correct beta-beating, dispersion and coupled response matrix.

## Slide 11
1/5 quadrupoles,1/2 IR quadrupoles (~600 out of 3000 quadrupoles) strengths are changed to restore beta functions along the ring.
Beta-beating correction
decreased from 5.1% to 1.3%
decreased from 11.8% to 1.1%
IR=50mm 496 seeds
IR=100mm 99 seeds
decreased from 4.3% to 1.4%
decreased from 14.3% to 1.5%

## Slide 12: Correction results
Observable | Before correction | After correction
Hori. disp. | 30.9 mm | 2.2 mm
Vert. disp. | 42.7 mm | 5.9 mm
Hori. Beta-beating | 4.3% | 1.4%
Vert. Beta-beating | 14.3% | 1.5%
Observable | Before correction | After correction
Hori. disp. | 29.0 mm | 4.3 mm
Vert. disp. | 102.1 mm | 2.3 mm
Hori. Beta-beating | 5.1% | 1.3%
Vert. Beta-beating | 11.8% | 1.1%
Component | x (mm) | y (mm) | z (mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 100 | 100 | 100
Sextupole | 100 | 100 | 100
Component | x (mm) | y (mm) | z (mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 50 | 50 | 50
Sextupole | 100 | 100 | 100

## Slide 13: Coupling correction
Neglecting beam-beam effects
Local coupling parameter matching was developed for BEPCII.
Both coupling and vertical dispersion are controlled.
Using the trim coils of the sextupoles (~1000), which providing skew-quadrupole field, to perform emittance tuning for CEPC.
The vertical orbit distortion due to a horizontal deflection at a BPM is:
++
, ：only related to the decoupled linear optics
: local coupling parameters
: response matrix
: skew-quadrupole vector

## Slide 14
ex = 1.2170.005 nm
ey = 0.043 0.002 pm
ey/ex = (0.0035 0.0002)%
IR=50mm 491 seeds
IR=100mm 154 seeds
ex = 1.2190.010 nm
ey = 0.078 0.002 pm
ey/ex = (0.0064 0.0002)%

## Slide 15
DA and MA
Tracking by Wang bin
IR=50mm 226 seeds satisfy
DA_x > 10 && DA_y > 15 && min_del > 0.0135
IR=100mm 25 seeds satisfy
DA_x > 10 && DA_y > 15 && min_del > 0.0135

## Slide 16
Algorithm upgrade
More variables fitted in LOCO to improve the beta beating correction.
Fit dispersion at the same time with beta beating correction.
Constraint the strength of skew component in coupling correction.
Iterate the dispersion, beta beating and coupling correction.
IR=100mm
20 seeds test with upgraded algorithm

## Slide 17: Summary
The optics correction is very challenging for the relaxed tolerance of the imperfections.
Passing rate can be increased with upgraded algorithm.
More finer correction of optics is necessary for satisfying the DA and MA requirements.

## Slide 18: To do list
.
Optimize the correction strategy to achieve finer tuning of optics with more iteration and more variables included in fitting.
Introduce extra knobs to compensate the optics at IP.
Introduce more types of imperfections.
Study off-momentum correction.

## Slide 19: Thanks for your attention