## Slide 1: CEPC instability studies for high luminosity H and Z
Na Wang, Yudong Liu, Yuan Zhang
CEPC day, March 27, 2020, IHEP

## Slide 2: Main beam parameters
Parameter [unit] | Higgs-CDR | Higgs-High Lum | Z-CDR | Z-39MW
Beam energy [GeV] | 120 |  | 45.5 | 
Lmax/IP (1034cm-2s-1) | 2.9 | 5.2 | 32.1 | 101.6
IP x/y (m) | 0.36/0.0015 | 0.33/0.001 | 0.2/0.001 | 
Emittance (H/V) [nm] | 1.21/0.0031 | 0.89/0.0018 | 0.18/0.0016 | 
Beam current [mA] | 17.4 | 17.8 | 461.0 | 1081.4
Bunch number | 242 | 218 | 12000 | 15000
Bunch Population [1010] | 15 | 17 | 8 | 15.0
Momentum compaction | 1.1110-5 | 0.9110-5  | 1.1110-5 | 
Natural bunch length z (mm) | 2.7 | 2.2  | 2.4 | 
Natural energy spread | 1.010-3 |  | 3.810-4 | 
Betatron tune x/y | 363.10/365.22 | 391.11/393.22  | 363.10/365.22 | 391.11/393.22
Synchrotron tune | 0.065 | 0.066 | 0.028 | 
Radiation damping [ms] | 46/46/23 | 47.6/47.6/23.8 | 843/843/436 | 849/849/424

## Slide 3: Rough estimations
Estimations with analytical formulae give rough requirements on broadband and narrowband impedances.
Parameter [unit] | Higgs-CDR | Higgs-High Lum | Z-CDR | Z-39MW
Beam current [mA] | 17.4 | 17.8 | 461.0 | 1081.4
Bunch number | 242 | 218 | 12000 | 15000
Bunch Population [1010] | 15 | 17 | 8 | 15.0
Threshold on broadband ¦ZL/n¦eff [mΩ] | 8.8 | 7.7 | 0.9 | 0.5
Threshold on broadband ky [kV/pC/m] | 65.6 | 63.2 | 20.1 | 11.5
Threshold on narrowband | 3.5 | 3.4 | 1.110-3 | 5.010-4
Threshold of narrowband Zy | 2.3 | 2.3 | 1.810-3 | 8.210-4
No showstopper for Higgs!

## Slide 4: Instability for Z (1)
Microwave instability and bunch lengthening
  Rarely induce beam losses, but may reduce the luminosity due to the deformed beam distribution and increasing of the beam energy spread.
Parameter | Z-CDR | Z-39MW
σl0 [mm] | 2.4 | 
σl with ZL [mm] (σl/σl0-1) | 5.1 (113%) | 6.2 (150%)
e/e0-1 | 15% | 50%
CDR
CDR
39MW
39MW
10nC

## Slide 5: Instability for Z (2)
Transverse mode coupling instability
  Fast instability, normally with beam losses.
  Considering bunch lengthening due to the impedance or beamstrahlung, the current threshold increases
Without bunch lengthening
With bunch lengthening
CDR
39MW
CDR
39MW

## Slide 6: Instability for Z (3)
Transverse resistive wall instability
  The coupled bunch instability can be driven by the resonance at zero frequency of the transverse resistive wall impedance.
  Growth time of the most dangerous mode vs. damping factors
  => High-Lumi Z needs more efficient feedback damping!
 | Z-CDR | Z-39MW
Instability growth time [ms] | 4.3 (~12 turns) | 1.8 (~5 turns)
Radiation damping [ms] | 843 | 
Bunch by bunch feedback [ms] | 1.7(~5 turns) | 

## Slide 7: Instability for Z (4)
CBI due to RF HOMs
  With 120 2-cell SC RF cavities and a HOM frequency spread larger than 0.5MHz, all the HOMs are below the threshold of feedback damping.
  For High-Lumi with 1-cell cavities, the amplitude of the HOMs will be roughly reduced by a factor of ~2 (Discussion with JiYuan Zhai), the threshold will decrease by a factor of ~2  No significant changes

## Slide 8: Instability for Z (5)
Electron Cloud
  With bunch spacing of 20ns, the electron cloud density is above the instability threshold even the SEY is suppressed to 1.1 by NEG coating!
  Possible mitigations:
  1) Antechamber, 2) Photon absorber, 3) Solenoid, 4) Cleaning electrode
YuDong Liu

## Slide 9: Instability for Z (6)
Beam ion instability
  Induce emittance blow-up and a positive tune shift along the bunch train.
  Filling pattern: CDR {Ntrain=150, Bunch spacing=25ns, Gap=270ns}
  High-Lumi {Ntrain=150, Bunch spacing=20ns, Gap=280ns}
  Faster growth rate for High-Lumi Z  Effectiveness of feedback on fighting ion instability need to be checked
Build-up of the ions along the bunch train
Parameters | Z-CDR | Z-39MW
Lsepωion/c0 | 0.6 | 0.6
ρion,ave[m-3] | 2.7E11 | 4.0E11
τe [ms] | 0.2 | 0.1
τH [ms] | 7.2 | 5.4
y | 0.009 | 0.008

## Slide 10: Instability for Z (7)
Cross talk with beam-beam observed for CDR parameter
  Less stable region obtained with impedance included in the beam-beam simulation.
  The effect can get more severe for High-Lumi Z!
Only one working point is stable without impedance.
The beam-beam interaction gets more unstable with longitudinal impedance due to the X-Z coupling.
Possible mitigations:
  Beam parameter optimization
  Impedance reduction
Yuan Zhang

## Slide 11: Summary
No showstopper for High-Lumi Higgs
Instability gets stronger for High-Lumi Z, main showstoppers are
  The design current is far above the threshold of MWI, in addition to the coupling with beam-beam, the beam will get more unstable in horizontal  further optimizations on beam parameters and impedances are required (overall consideration on beam-beam, MWI, TMCI, …).
  Electron cloud instability needs further modifications on the vacuum designs.
  Transverse resistive wall instability needs more efficient feedback damping.

## Slide 12: Backup slides

## Slide 13: CEPC-CDR vs FCC-ee: Higgs
 | CEPC-CDR | FCC-ee | Luminosity contribution | Limit for CEPC
Number of IPs | 2 | 2 |  | 
Energy (GeV) | 120 | 120 |  | 
Circumference (km) | 100 | 100 |  | 
SR loss/turn (GeV) | 1.73 | 1.72 |  | 
Half crossing angle (mrad) | 16.5 | 15 |  | 
Piwinski angle | 3.48 | 5.8 | A: 1/1.67 | Limited by E
Ne/bunch (1010) | 15 | 18 | B: 1.44 | Beam-beam effect
Bunch number | 242 | 328 | C: 1.35 | SR power
Beam current (mA) | 17.4 | 29 |  | 
SR power /beam (MW) | 30 | 50 (30) |  | 
Bending radius (km) | 10.7 | 10.76 |  | 
Momentum compaction (10-5) | 1.11 | 0.73 |  | 
IP x/y (m) | 0.36/0.0015 | 0.3/0.001 | D: 1.34 | DA, error tollerance
Emittance x/y (nm) | 1.21/0.0024 | 0.63/0.0013 | E: 1.88 | Cell length, magnet number
Transverse IP (um) | 20.9/0.06 | 13.7/0.036 |  | 
x/y/IP | 0.018/0.109 | 0.016/0.118 |  | 
VRF (GV) | 2.17 | 2.0 |  | 
f RF (MHz) (harmonic) | 650 | 400 |  | 
Nature bunch length z (mm) | 2.72 | 3.15 |  | 
Bunch length z (mm) | 4.4 | 5.3 |  | 
HOM power/cavity (kw) | 0.46 (2cell) | ? |  | 
Energy spread (%) | 0.134 | 0.165 |  | 
Energy acceptance (DA) (%) | 1.35 | 1.7 |  | 
Energy acceptance by RF (%) | 2.06 | 2.3 |  | 
Beamstruhlung lifetime /quantum lifetime (min) | 80/80 | 18 |  | 
Lifetime (min) | 26 | 12 |  | Limited by injection system
Lmax/IP (1034cm-2s-1) | 2.93 | 8.5 (5.1) | 2.9 (1.74) | 
How to increase Luminosity: B, D, E
From Dou Wang

## Slide 14: CEPC high lum. Higgs parameter after CDR
 | Higgs | W | Z（3T） | Z（2T）
Number of IPs | 2 |  |  | 
Beam energy (GeV) | 120 | 80 | 45.5 | 
Circumference (km) | 100 |  |  | 
Synchrotron radiation loss/turn (GeV) | 1.68 | 0.33 | 0.035 | 
Crossing angle at IP (mrad) | 16.5×2 |  |  | 
Piwinski angle | 3.78 | 8.5 | 27.7 | 
Number of particles/bunch Ne (1010) | 17.0 | 12.0 | 8.0 | 
Bunch number (bunch spacing) | 218 (0.76s) | 1568 (0.20s) | 12000 (25ns+10%gap) | 
Beam current (mA) | 17.8 | 90.4 | 461.0 | 
Synchrotron radiation power /beam (MW) | 30 | 30 | 16.5 | 
Bending radius (km) | 10.7 |  |  | 
Momentum compact (10-5) | 0.91 |  |  | 
 function at IP x* / y* (m) | 0.33/0.001 | 0.33/0.001 | 0.2/0.001 | 
Emittance ex/ey (nm) | 0.89/0.0018 | 0.395/0.0012 | 0.13/0.003 | 0.13/0.00115
Beam size at IP sx /sy (m) | 17.1/0.042 | 11.4/0.035 | 5.1/0.054 | 5.1/0.034
Beam-beam parameters x/y | 0.024/0.113 | 0.012/0.1 | 0.004/0.053 | 0.004/0.085
RF voltage VRF (GV) | 2.4 | 0.43 | 0.082 | 
RF frequency f RF (MHz) (harmonic) | 650 (216816) |  |  | 
Natural bunch length z (mm) | 2.2 | 2.98 | 2.42 | 
Bunch length z (mm) | 3.93 | 5.9 | 8.5 | 
HOM power/cavity (2 cell) (kw) | 0.58 | 0.77 | 1.94 | 
Energy spread (%) | 0.19 | 0.098 | 0.080 | 
Energy acceptance requirement (%) | 1.7 | 0.90 | 0.49 | 
Energy acceptance by RF (%) | 3.0 | 1.27 | 1.55 | 
Photon number due to beamstrahlung | 0.104 | 0.050 | 0.023 | 
Beamstruhlung lifetime /quantum lifetime* (min) | 30/50 | >400 |  | 
Lifetime (hour) | 0.22 | 1.2 | 3.2 | 2.0
F (hour glass) | 0.85 | 0.92 | 0.98 | 
Luminosity/IP L (1034cm-2s-1) | 5.2 | 14.5 | 23.6 | 37.7
*include beam-beam simulation and real lattice
From Dou Wang

## Slide 15: CEPC high lum. Z parameter after CDR
 | CEPC-CDR | CEPC-30MW | CEPC-39MW | FCC-ee
Number of IPs | 2 | 2 | 2 | 2
Energy (GeV) | 45.5 | 45.5 | 45.5 | 45.6
Circumference (km) | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 0.036 | 0.036 | 0.036 | 0.036
Half crossing angle (mrad) | 16.5 | 16.5 | 16.5 | 15
Piwinski angle | 23.8 | 27.9 | 33.0 | 28.5
Ne/bunch (1010) | 8.0 | 12.0 | 15.0 | 17
Bunch number | 12000 | 14564 (20.6ns+10%gap) | 15000 | 16640
Beam current (mA) | 461 | 839.9 | 1081.4 | 1390
SR power /beam (MW) | 16.5 | 30 | 38.6 | 50
Bending radius (km) | 10.7 | 10.7 | 10.7 | 10.76
Momentum compaction (10-5) | 1.11 | 1.11 | 1.11 | 1.48
IP x/y (m) | 0.2/0.001 | 0.2/0.001 | 0.2/0.001 | 0.15/0.0008
Emittance x/y (nm) | 0.18/0.0016 | 0.18/0.0016 | 0.18/0.0016 | 0.27/0.001
Transverse IP (um) | 6.0/0.04 | 6.0/0.04 | 6.0/0.04 | 6.4/0.028
x/y/IP | 0.004/0.079 | 0.004/0.093 | 0.004/0.098 | 0.004/0.133
VRF (GV) | 0.1 | 0.10 | 0.10 | 0.1
f RF (MHz) (harmonic) | 650 | 650 | 650 | 400
Nature bunch length z (mm) | 2.42 | 2.42 | 2.42 | 3.5
Bunch length z (mm) | 8.5 | 10.0 | 11.8 | 12.1
HOM power/cavity (kw) | 1.94 (2cell) | 2.29 (1cell) | 3.15 (1cell) | ?
Energy spread (%) | 0.08 | 0.1 | 0.115 | 0.132
Energy acceptance (DA) (%) | 1.5 | 0.6 | 0.7 | 1.3
Energy acceptance by RF (%) | 1.7 | 1.7 | 1.7 | 1.9
Lifetime by rad. Bhabha scattering (hour) | 2.9 |  |  | 1.13
Lifetime (hour) | 2.5 | 2.0 | 1.8 | 1.0
Lmax/IP (1034cm-2s-1) | 32.1 | 74.5 | 101.6 | 230
Single cell cavities for Z are essential to control the HOM power.
From Dou Wang

## Slide 16
CEPC Impedance budget (@z=3mm)
Components | Number | Z¦¦/n, mΩ | kloss, V/pC | ky, kV/pC/m
Resistive wall | - | 6.2 | 363.7 | 11.3
RF cavities | 240 | -1.0 | 225.2 | 0.3
Flanges | 20000 | 2.8 | 19.8 | 2.8
BPMs | 1450 | 0.12 | 13.1 | 0.3
Bellows | 12000 | 2.2 | 65.8 | 2.9
Pumping ports | 5000 | 0.02 | 0.4 | 0.6
IP chambers | 2 | 0.02 | 6.7 | 1.3
Electro-separators | 22 | 0.2 | 41.2 | 0.2
Taper transitions | 164 | 0.8 | 50.9 | 0.5
Total |  | 11.4 | 786.8 | 20.2
The broadband impedances are dominated by the RW, flanges and bellows.
The loss factor is mainly contributed by the resistive wall and the RF cavities.
More components, such as the collimators, absorbers and kickers, should be included.

## Slide 17
Vacuum chamber in FCC (FCC-cdr_volume_2)
Beam pipe in FCC-ee is a circular vacuum chamber of 35 mm radius with a rectangular antechamber on each side.
The SR absorbers will be installed inside the chamber winglets every 4~6 meters (num~10000).
antechamber
SR absorbers
pumping slots

## Slide 18
Growth time of the RW ~7 turns