## Slide 1: CEPC alignment precision Wang xiaolong 2020.3.3

## Slide 2
Outline
CEPC alignment precision requirement
Alignment control network
Component fiducialization
Component pre-alignment
Tunnel installation alignment
Alignment environment requirement

## Slide 3
Component alignment precision requirement
Provide by physics group
Component | Transversal/mm | Vertical/mm | Longitudinal/mm | Pitch /mrad | Yaw /mrad | Roll /mrad
Arc Dipole | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Arc Quadrupole | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Arc Sextupole | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
IR Quadrupole | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
IR SCQ | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
IR Sextupole | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
Error sources
Alignment control network error
Component fiducialization pre-alignment error
Field measurement error
Installation adjustment error
RF、injection、Linac alignment requirement reference to the arc region components

## Slide 4
Alignment control network
  Control network：provide an unified location reference frame for CEPC alignment and control the error accumulation of survey and alignment；
  3 levels control network
  Surface control network
  Backbone control network
  Tunnel control network
  Surface control network
    CEPC global absolute position & shape control, high precision constraint datum for tunnel control network.
    Composed of 14 permanent points
    10 internal points are in CEPC tunnel, a part of the tunnel control network.

## Slide 5
Instruments
LEICA GS10
AR20
LEICA Wild NL
LEICA NA2 + EpsNas
+ LGO
LEICA AT403
Tape
水平：3mm+0.5ppm
垂直：6mm+0.5ppm
每公里往返精度：±0.2mm
1:200000
点位测量精度：±15 µm + 6 µm/m

## Slide 6
  Plumbing point
  Instrument height measurement
  GNSS measurement
  Level measurement
  Best-fit,GNSS to level,establish CEPC coordinate system。
Control point accuracy：10mm；
Check measurement：
Total station,auxiliary control network,check the base lines
Tunnel control network accuracy is related to the distance between the adjacent permanent points.CERN simulation result shows 8mm for 5km and 12mm for 10km.
Surface control network measurement

## Slide 7: Backbone control network
  Strengthen the tunnel control network，reduce error accumulation.
  Straight line triangulation network，short line 300m，long line 600m.
  Simulation
  Use surface control network as known point to constrain backbone control network adjust.
  Simulation condition: angle 1 sec.distance 1mm+1ppm，station 42
  The biggest error between adjacent permanent points is 8mm.
徕卡TS60
测量范围:1.5m~>3500m
点位测量精度：0.6mm+ 1ppm
测角精度：0.5’’

## Slide 8: Tunnel control network
Provide position reference for component installation & alignment
tunnel control network along CEPC tunnel will be evenly distributed with an interval of 6 meters .
  4 control points each section.
Instruments：laser tracker &level
  Tunnel control network measurement
  Laser tracker measurement
徕卡AT960
powerlock：自动锁定靶球
数据采集速率：1000点/秒
AIFM:绝对测距
角度精度：15 µm + 6 µm/m
距离精度：0.5µm/m
动态锁定：10µm

## Slide 9: Tunnel control network
  Level measurement
  Level route：adopt subsection round trip measurement , 4 quadrants , each quadrant measure one closed route. Linac and BT is one route。
  Front and back sight distance is both 18m。
  Secondary leveling specification
水准路线长度 | 109550 X2米=219公里
测量效率 | 2公里/1组/天
4组共需 | 28天
测段往返差 | 每千米偶然中误差
mm | 1mm

## Slide 10: Tunnel control network
Tunnel control network precision
BEPCII SR 237.53m ，control point precision is better than 0.08mm.(2006,2008,2010,2012)
CSNS RCS 240m，RMS precision is 0.07mm.
CEPC RMS precision is 0.07mm.
BEPCII

## Slide 11
Component fiducialization is to draw the beam center to its fiducials, then the fiducials coordinates can be transferred to CEPC global coordinate system and used for component tunnel alignment
Component fiducialization
  Geometric measurement：laser tracker、 Articulated arm 、CMM、photogrammetry
  Magnetic field measurement：rotate coil、vibrating wire
  Non-contact measurement：level, transit square
  Attitude measurement： electronic gradienter
测量臂
范围：0~4m
精度：±0.023~ ±0.1mm
Camera
摄影测量

## Slide 12
Mechanical center extraction fiducialization accuracy is limited to component fabrication accuracy and consistency accuracy of mechanical center and magnetic center.
X
Y
Dipole Magnet
Fiducialization Datum Planes
Component fiducialization
Transversal /mm | Vertical /mm | Longitudinal /mm
0.05 | 0.05 | 0.08-0.15

## Slide 13
Magnetic center extraction fiducialization accuracy is limited to component fabrication accuracy and rotate center measurement accuracy.
Rotate coil：micron level precision
Component fiducialization
Transversal /mm | Vertical /mm | Longitudinal /mm
0.014 | 0.014 | 0.05
Cooperate with CMM

## Slide 14
Components on the same girder are aligned in advance.
The girder can be aligned as one unit in tunnel。
Can get higher alignment accuracy of the components on one girder.
Can save tunnel installation time.
XX=-(LMB+Z) sin(θB/2)+X cos(θB/2) + XBE
YY=Y
ZZ=(LMB+Z) cos(θB/2)+X sin(θB/2) + ZBE
Pre-alignment

## Slide 15
It is desirable to make geodesic sites on all magnets at the same height.
激光跟踪仪
Pre-alignment cell
Pre-alignment—Laser tracker

## Slide 16
Laser tracker pre-alignment accuracy | Items related to accuracy | Error estimation /mm
0.082mm | Component fiducialization | 0.05
 | Offset of adjustment and fix | 0.05
 | Measurement of laser tracker | 0.035
 | Deviation caused by component re-assembly | 0.010
 | Deviation caused by transportation | 0.02
Pre-alignment

## Slide 17
Pre-alignment—Laser tracer
三个7m*7m 工位, 高度4.3m
预期实现7μm点位测量精度
精度：0.2μm+0.3μm/m
多路激光测距，交汇测量点空间三维坐标

## Slide 18
Laser tracer pre-alignment accuracy | Items related to accuracy | Error estimation /mm
0.075mm | Component fiducialization | 0.05
 | Offset of adjustment and fix | 0.05
 | Measurement of laser tracer | 0.007
 | Deviation caused by component re-assembly | 0.010
 | Deviation caused by transportation | 0.02
Pre-alignment

## Slide 19: pre-alignment-Vibrating wire
Measure each component magnetic center
Adjust every component to the center line
measure the position relation of wire and fiducials with WPS and laser tracker
The error of scanning the magnetic center is better than 10 microns
The error of measuring the wire position is 6 microns
Vibrating wire system
Pre-alignment cell

## Slide 20: pre-alignment accuracy
Vibrating wire system | Items related to accuracy | Error estimation /mm
0.066mm | Vibrating wire measurement | 0.010
 | Offset of adjustment and fix | 0.05
 | WPS measurement | 0.006
 | Measurement of fiducials | 0.035
 | Deviation caused by component re-assembly | 0.01
 | Deviation caused by transportation | 0.02
The error of components

## Slide 21
Use tunnel control network and laser trackers to perform tunnel components alignment.
Measure the tunnel control network and through best-fit to determine the laser tracker position in CEPC global coordinate system.
Using laser tracker measure the component fiducial points to obtain the component position.
Adjust the component to the required tolerance.
Tunnel installation alignment
Fiducialization /mm | Control network /mm | Measurement /mm | Adjustment & fix /mm | Totall /mm
0.05-0.15 | 0.07 | 0.05 | 0.05 | 0.11—0.18

## Slide 22
Laser tracker and control network rough alignment
Laser-based alignment system
set laser-based alignment system beside the detector
Use laser tracker and control network align the laser-based alignment system parallel with the beam
Use laser-based alignment system as a reference align components to the designed position.
Laser-based alignment system precision:30m offset 0.02mm
激光准直系统
跟踪仪
MDI alignment

## Slide 23
SM and Cryomodule will be inserted into detector, fiducials exposed outside are too few to effectively control the component .
Need to research an inner measurement system to monitor SM and detector position relation.
MDI alignment

## Slide 24
隔振：独立隔振地基，（1）在频域1Hz~100Hz内，振动速度要求低到12μm/s以下。（2）振动频率在1~100Hz的水平和垂直振动，在1秒内的均方根振幅均小于25nm。
温度：波动度±0.1℃，全场均匀度1℃，调节范围18℃~26℃，且在调节范围下均需满足波动度和均匀度要求；
湿度：湿度调节范围30%-60% (%RH) ，湿度波动度±5% (%RH) 。
风速：距地面1.2m工作面风速≤0.3m/s；
噪音：室内噪音≤60dB；
Alignment environment requirement
Fiducialization & pr-alignment
GB51076-2015电子工业防微振工程技术规范
中国计量科学研究院精密测量实验室的建设标准
HEPS
NSLS-II

## Slide 25
直线、环隧道地面平整度：任意2米范围内，高差不超过1毫米。
地面不均匀沉降：要求小于10微米/10米/年。
隧道温度波动度要求小于±0.1℃
风速：工作区域风速≤0.3m/s；
Alignment environment requirement
Tunnel alignment

## Slide 26
Thank You !