## Slide 1
Thunderstorm Activity at LHAASO observatory
Xuejian Chen, Peihan Wang
Xunxiu Zhou, Daihui Huang, Axikegu, Lin Chen
Southwest Jiaotong University
The second LHAASO collaboration meeting in 2021 & LHAASO Project status meeting

## Slide 2
Outline
1. The introduction of thunderstorm activity
2. The thunderstorm activity at LHAASO
3. Thunderstorm 20210610
4. Summary and next step

## Slide 3
1.The introduction of thunderstorm activity
Thunderstorms are common weather phenomena at high altitudes
The strength of atmospheric electric fields could be up to 1000 V/cm or even higher
Thunderstorms can inflict immense death and property damage worldwide

## Slide 4
The lighting during thunderstorm
Positive ground lighting
Negative ground lighting
Lightning in the cloud
Intercloud lightning
Lightning outside the cloud

## Slide 5
The EFM-100c at LHAASO observatory
The data of electric field:
Time (hour: minute: second)
Polarity of field (‘+’ or ‘-’)
Intensity of field
Scale: ±1000 V/cm

## Slide 6
2.The thunderstorm activity at LHAASO
Data selection
The maximum strength of the near-earth atmospheric electric field is larger than 500 V/cm and lasts for at least 8 minutes,or it is higher than 900V/cm at least 4 minutes.

## Slide 7
Thunderstorm day and number
199 thunderstorms, 148 thunderstorm days
Thunderstorms mainly occur from June to September, Proportion: 75%

## Slide 8
Thunderstorm duration
Most thunderstorms last less than 2h
The thunderstorm 20210624 lasted 6.3 hours

## Slide 9
Thunderstorms mainly occur at 14-21 o'clock, Proportion: 78%
Daily distribution of thunderstorms
There are also a few thunderstorms in the middle of the night

## Slide 10
The polarity variations of thunderstorm fields
Most thunderstorms have electric field polarity reversal, Proportion: 88%

## Slide 11
Lighting and the variation of electric field
The number of lightning increases with distance
Intensity variations of electric field decreases with distance

## Slide 12
3.Thunderstorm 20210610
Number of variations in polarity：42
1.6 km lightning:11

## Slide 13
Lighting and the variation of electric field
The number of lightning decreases first and then increases with distance
Intensity variations of electric field decreases with distance

## Slide 14
Near-by Lighting
Parameter | 2019-10-2021-09 | 2021-06-10 | Proportion
(1) 1.6 km Lightning | 40 | 11 | 27.5%
(2) 3.2 km Lightning | 68 | 5 | 7.3%
(3) ¦ΔE¦ > 2000V/cm | 30 | 12 | 40.0%
(1)(3) | 23 | 10 | 43.4%
(2)(3) | 5 | 1 | 20.0%
Thundercloud is close to the ground
Strong variation of near-earth thunderstorm electric field

## Slide 15
Distance - ΔE

## Slide 16
rise
release
Charge center rise
Lighting < 4.8 km

## Slide 17
Lightning ：6.4-12.8km
0
Altitude
1
2
3
6.4-12.8km is the positive power center
Different ΔE corresponds to different lightning types

## Slide 18
Lightning ：14.5-19.3 km
Before and after 19:00, the electric field changes are opposite.
Time | Statistics
Before 19：00 | 117 lightning
 | ΔE<0 : 116 lightning
After 19：00 | 32 lightning
 | ΔE>0 : 29 lightning

## Slide 19
The structure of thundercloud
0
6.4
1.6
12.8
8.0
14.5
9.6
19.3
3.2
4.8
11.3
Charge structure of thundercloud before 19:00
Charge structure of thundercloud after 19:00
Altitude

## Slide 20
Electric field calculation model
R
H
Real electric charge
Induced charge
2.
3.
If : R=5 Km is a constant
The model of thundercloud

## Slide 21
Calculation verification
Distance | ΔQ | Number |  | 
1.609 | 40.84 | 11 | 449.24 | 805.8
3.219 | 29.96 | 5 | 149.8 | 
4.828 | 68.92 | 3 | 206.76 | 
6.437 | 54.87 | 1 | 54.87 | 379.65
8.047 | 14.21 | 2 | 28.42 | 
9.656 | 29.6 | 2 | 59.2 | 
11.265 | 16.2 | 7 | 113.4 | 
12.875 | 30.94 | 4 | 123.76 | 
14.484 | 16.72 | 4 | 66.88 | 2775.78
16.093 | 22.36 | 20 | 447.2 | 
17.703 | 19.34 | 43 | 831.62 | 
19.312 | 17.44 | 82 | 1430.08 | 

## Slide 22
Summary and next step
2. The thunderstorm 20210610 was analyzed in detail and get a simple charge structure of thundercloud.
3. More thunderstorm events need to be analyzed.
1. The thunderstorm electric fields and lightings at LHAASO observatory were studied.
Thanks!