## Slide 1: Study of ENDA with Sand Cubes at YBJ
Presenter: Dixuan Xiao
Tibet University
the ENDA Group
The second LHAASO Collaboration meeting,
Shanghai, Oct 15, 2021

## Slide 2: Outline
Algorithm upgrade
Sand cube test at YBJ
Summary and next steps

## Slide 3
With old algorithm, number of detected neutrons was much less than expected.
New algorithm at FPGA program of FADC
  Remove trigger condition “pulse shape is higher than threshold at least continuous three bins”
  Change pulse shape sampling time window from 500μs into 2 μs to reduce complication
1. Algorithm upgrade

## Slide 4
single neutron pulse height distribution
FADC count
New algorithm decreases threshold of detector and then increases neutrons.
Detector #1

## Slide 5
neutron distribution of triggered events
neutrons
events
We took data of 16 full days acquired from the old algorithm( Apr. – May, 2021) and another 16 days from the new algorithm( Jul. – Aug, 2021).
The new algorithm can record more neutrons in triggered events.

## Slide 6
FADC problems
Solved problems by ourselves
  New algorithm
  After WR time is wrong (01/01/1970), sometimes program can not recover by itself and FADC firmware has to be restarted.
  When thunderstorm, some of channels stop work.
  Wrong measurement of pulse height due to short cable problem inside FADC
Remained problems:
  10MHz noise
  Big noise causing that threshold can not be tuned down more
  Absolute time measurement has a fluctuation of 1.7ms in coincidence with KM2A
  Shower arrival time difference between pre-8 and post-8 detectors.

## Slide 7: 2. Sand cube test at YBJ
We are building 1m3 SandCube under detectors:
To protect media (hadron target) from rain;
To improve knowledge about media because we can know more precisely about ingredient of sand than one of soil.
Make M-C simulation with GEANT4

## Slide 8
near sand cubes
on sand cubes

## Slide 9
Comparison: single neutrons
single neutron pulse height distribution
FADC count
Detector #1
Time in one day (hour)
Detector #1
Sum of Counting rate (per min) in 5 days
single neutron detection is not different between with/without sand cubes

## Slide 10
Comparison: triggered events
neutrons
events
We took data of 5 days when detectors mounted on sand cube( 23rd- 27th, Sept) and another 5 days near sand cubes( 6th-10th, Oct).

## Slide 11
Comparison: ratio between with/without sand cubes
neutrons
Neutrons<12, background + smaller showers, ratio increases slightly to 1.05;
Neutrons>=12, bigger showers, still poor statistics
events

## Slide 12: 3. Summary and next steps
Algorithm had been upgraded, and the new algorithm solves problem of lack neutrons.
Sand cubes have been added for test. More statistics is waited for.
Difference between with-sand-cube and without-sand-cube will be compared with simulation.

## Slide 13: Backup