## Slide 1: R&D progress on Linac and damping ring
Jingru Zhang
On behalf of CEPC linac team
Institute of High Energy Physics, CAS

## Slide 2: Outline
1
Linac baseline design
2
R&D activities
3
Summary

## Slide 3: Linac baseline design
The requirements of the booster to the linac
Parameter | Symbol | Unit | Value
e- /e+ beam energy | Ee-/Ee+ | GeV | 10
Repetition rate | frep | Hz | 100
Bunch numbers per pulse |  |  | 1
e- /e+ bunch charge |  | nC | >1.5
Energy spread (e- /e+ ) | σE |  | <2×10-3
Emittance (e- /e+ ) | εr | nm | <40

## Slide 4: Linac baseline design
Key technologies of 10 GeV S-band linac baseline
  Electron gun
  SHBs
  Buncher
  S-band accelerating structure
  Pulse compressor
  Positron source
  Big hole accelerating structure
  DR 650MHz RF cavity
  LLRF
  Phase reference line
  ……

## Slide 5: Accelerating structure
S-band accelerating structure design
  Motivation: It is almost 290 3m long S-band (2860MHz) accelerating structures
  Goal: About 30 MV/m @1μS (without beam) accelerating gradient is expected

## Slide 6: Accelerating structure
Chart: Frequency （MHz）
work frequency | 1.02
Chart: Cell number
Cold test result
  The phase shift and the cumulative phase shift are less than 1 deg
  The VSWR is 1.02 at working frequency
  The bandwith ±≥2MHz （VSWR≤1.2）

## Slide 7: Accelerating structure
High power test
Analyzing Magnet
Modulator &klystron
accelerating structure

## Slide 8: Accelerating structure
High power test
  Developed automatic practice technology
  Online monitoring and interlock protection of dark current are added, which provides an effective monitoring and protection
离子泵1状态
离子泵1状态
真空计状态
自动老练参数配置
调制器状态
测试台联锁状态
Control platform user interface
J.D. Liu

## Slide 9: Accelerating structure
High power test
  Database records the waveform when breakdown happen
  Optimization of practice algorithm to improve practice efficiency

## Slide 10: Accelerating structure
The relationship of the modulator high voltage vs. output power of the klystron
  When the modulator voltage is 37kV, The klystron output is 34.1MW
  With SLED, the maximum power benfore the accelerating structure is 154MW

## Slide 11: Accelerating structure
Practice steps
  Pulse width 1uS, voltage to 40kV，2uS, to 40kV，With SLED, set the voltage goal 37kV
April 28 to May 26
  Practice goal is 37kV
  Automatice practice mode

## Slide 12: Accelerating structure
With SLED, the relationship of the gradient and the input power
  Pin the input power to the SLED
  V the averge accelertiang gradient
  L the total length od the structure, 3m
  R the average shunt impedance, 64MΩ/m，
  α attenuation of unit length, 0.48
  M Energy multiplication factor, 1.8

## Slide 13: Accelerating structure
June 8, 2020，Process test and acceptance were carried out
  The maximum output power is 153MW
  The maximum gradient is 33MV/m
测试期间在调制器高压37kV运行情况，其中蓝线为连锁保护总信号（5V保护，0V正常），红线为脉冲调制器高压设定值，绿线为调制器高压采样值

## Slide 14: Pulse compressor
Pulse compressor
  It is used to improve the peak power from the klystron and saving cost
  The input power is 80 MW
  The pulse width will be compressed from 4uS→0.8uS
  TE113 mode is selected
  The frequency tuned by temperature control
  It is including mode converter and spherical cavity
Mode 1
Mode 2
E-field distribution of the two degenerated polarized modes

## Slide 15: Pulse compressor
Mode converter
  The TE10 mode input from Port 1 will be converted into two degenerated TE11 modes at Port 3
  There are two degenerated TE113 modes in the spherical cavity, The phase difference of the two modes is about 90°
  The input port S11 is -62.7 dB
  The S41 is -71dB for port 4 is for vacuum
Port 1
Port 2
Port 3
Port 4
Vacuum model
Electromagnetic field
S11 / VSWR | -62.7 dB/1.0016
S21 | -42.9 dB
S31(1) | -3.02 dB
S31(2) | -3.02 dB
Phase difference of two modes | 89.89°
S41(1) | -70.9 dB
S41(2) | -71.0 dB
X. He

## Slide 16
Thermal stress analysis
  Wall thickness: 20mm
  The maximal temperature rise is on the coupling hole of 2.5 ℃ (the water cooling flow set as 50 L/min)
  The frequency tunable range of ±1 MHz is enough for all the frequency shift resulted from the input power, vacuum pumping, air pressure, etc.
Temperature
Deformation
Stress
Parameter | Value
SLED water temperature | 30 ℃
Room temperature | 25 ℃
Filling time | 730 ns
Klystron output power | 80 MW
Pulse width | 4 μs
Pulse repetition rate | 100 Hz
CEPC parameter
Pulse compressor
Accordingly, if we use the water temperature to tune the frequency, the temperature need to be ±3.6 ℃ change

## Slide 17
Parameter | value
Frequency | 2856 MHz
Mode | TE113
Q0 | ~146000
VSWR | ≤1.1
Coupling factor | ~6.9
Tuning rang | ≥±1 MHz
Input power | 80MW
Repetition fre. | 100Hz
Pulse width | ~4µs
Pulse width after compress | ~0.83µs
Peak power gain | ≥7dB
Energy gain factor | ~1.6
Working temperature | 30±0.1oC
The parameters
  The simulated Q factor is 94% of the theoretical one
  The energy gain factor is ~1.6
Simulated compressed pulse
For input signal:
Pulse compressor

## Slide 18: Pulse compressor
Simulated resonant spherical cavity with coupling hole（Eigenmode solver）
  f0=2855.9986 MHz, 2855.9994 MHz,
  Q0=139583, 139551
Cavity diameter
  364.58mm
Electric field distribution of the twoTE113 polarized degenerate mode
Simulation model

## Slide 19: Pulse compressor
The whole pulse compressor
  The Frequency solver results： Coupling Coefficient 7.47， f0=2856.0267 MHz， Q0=144785（the same as the Eigenmode solver results
Electric field distribution of the twoTE113 polarized degenerate mode
S21 curve

## Slide 20: Pulse compressor
Detune calculation
  Copper rod
    Diameter of 12 mm
    insertion depth of 210 mm
  Frequency solver result: frequency changes from 2856.02 → 2871.56 MHz（△15.54 MHz），The Eigenmode solver result, from 2856.03 → 2871.41 MHz（△15.38 MHz）, the two solvers have got the same result
  S11= -46.85 dB（VSWR=1.0091），S21= -0.0188 dB
Cross section view

## Slide 21: Pulse compressor
Vacuum pumping speed and vacuum level
  The pumping speed of the ion pump is 100 L/s
  Considering the material as fine fabricated OFHC, the deflation rate will be：1×10-10 Torr.L/s/cm2
  The simulation shows that the vacuum level inside the cavity is all below 3×10-8 Torr, which meet the requirements （＜ 5×10-8 Torr ）
Baiqi Liu
Simulation model
Simulation result
Vacuum distribution

## Slide 22: Pulse compressor
Mechanical technological design
  Copper block material, milling process
    High cost
    Waste material
  Copper plate, spinning Process √
    Need mould design
    Mass production will reduce costs

## Slide 23: Damping Ring RF cavity
Damping ring
D, Wang
DR V2.0 | Unit | Value
Energy | GeV | 1.1
Circumference | m | 75.4
Storage time | ms | 20
Bending radius | M | 3.565
Dipole strength B0 | T | 1.03
U0 | keV | 36.3
Damping time x/y/z | ms | 15.2/15.2/7.6
0 | % | 0.05
0 | mm.mrad | 376.7
z，inj | mm | 5.0
Nature z | mm | 7.5
inj | mm.mrad | 2500
ext x/y | mm.mrad | 530/180
inj /ext | % | 0.2/0.05
Energy acceptance by RF | % | 1.0
fRF | MHz | 650
VRF | MV | 2.0

## Slide 24: Damping Ring RF cavity
Input coupler and doorknob for DR 5 cell cavity
Electromagnetic field distribution
S11
O.Z. Xiao

## Slide 25
Coupling factor simulation
The coupling ring is perpendicular to the direction of the magnetic field, and the coupling degree is 6.4
Coupling degree ~ 5 at rotation angle ~ 28 degrees
coupling loop angle（degree） | coupling degree
0 | 6.4
20 | 5.8
40 | 3.8
Damping Ring RF cavity
H. Shi

## Slide 26
cavity parameters
Diameter of the tuner
  94
Tuning rang (1.2MHz)
  649.635kHz (-30mm)
  650.829kHz (+30mm)
 | Unit | Value
Beam tube aperture | mm | 44
Total length | mm | 1383.66
Cell length | mm | 5*230.61
Outside diameter | mm | 345
-mode frequency | MHz | 649.993
Q0 |  | 31665
R/Q | Ω | 1316
Shunt impedance | MΩ | 20.8
Accelerating voltage | MV | 1.2 (2.0)
Accelerating gradient | MV/m | 1.04 (1.73)
Dissipated cavity power (20% margin) | kW | 45 (120)
Damping Ring RF cavity

## Slide 27
The diameters of neck tubes of tuner and vacuum ports are 94mm
2 pump ports near the ceramic of coupler and 1 pump port for each tuner with flanges CF35 are considered. The inner diameters of these pump ports are 38mm
The aperture plates are installed near the vacuum ports
Damping Ring RF cavity
vacuum

## Slide 28: Damping Ring RF cavity
vacuum
  Two 100L/s ion pump in the No.1 & N0.5 cavities, one 15L/s is in the coupler
  The vacuum pressure distribution in the cavity is uniform, 3.0e-7 ~ 3.5e-7 Pa
  The vacuum at the coupler position is about 3.4e-7 Pa
  The vacuum at the tuner position is about 5.2e-7 Pa
B.Q. Liu
Vacuum degree distribution
Ion pump distribution

## Slide 29: Damping Ring RF cavity
Machenical design
Cavity
Tunner
Coupler
X.D. Weng

## Slide 30: Damping Ring RF cavity
5-CELL腔体
5-CELL腔体由5个腔体，两端端盘和中间耦合盘组成。
整个腔体关于中心轴对称，所以共有3中规格腔体，CELL-1腔体×2、 CELL-2腔体×2、 CELL-3腔体×1。
CELL-1腔体接离子泵，CELL-2腔体接调谐器，CELL-3腔体接耦合器。
每个CELL腔布置CF100窗口接真空泵、调谐器和耦合器，另外体均每个CELL腔布置两个CF35用作PICK-UP窗口。
端盘、腔体、耦合盘均设计水冷结构。

## Slide 31: Damping Ring RF cavity
端盘、耦合盘水冷结构
端盘水冷结构
耦合盘水冷结构
端盘和耦合盘的冷却均采用内部交叉水道的结构。
水道尺寸为φ12mm，进水水嘴尺寸为φ12×1，接卡套接头。

## Slide 32: Damping Ring RF cavity
腔体水冷结构
腔体为薄壁筒体，无法做内部水冷结构，因此选择外围盘管进行冷却。
为保证水冷管与腔体的良好接触和热传导，在筒体外表面开槽将水冷管埋进腔体并钎焊。
水冷盘管
开槽埋管

## Slide 33: Damping Ring RF cavity
调谐器结构介绍
调谐杆外径为84
调谐行程±30mm
调谐范围：
649.635kHz (-30mm)
650.829kHz (+30mm)
外导体水冷使用双层管结构，调谐杆水冷使用螺旋水道结构
调节螺纹副使用双螺母结构，主螺母传动，副螺母消隙
调节螺纹副
轴承
波纹管
调谐杆
外水冷
内水冷
主螺母
副螺母

## Slide 34: Damping Ring RF cavity
耦合器结构介绍
门钮转换器
陶瓷窗
外导体
内导体
耦合环
门钮与内导体连接形式
轭流结构

## Slide 35: Summary
The accelerating structure has completed. Through the expert test and acceptance, the design goal is achieved.
The sphereral pulse compressor RF design has completed. The machanical design has started.
The DR ring 5 cell cavity is designing.

## Slide 36
Thank you !