## Slide 1
Youlian Lu
Heat transfer analysis of CEPC beampipe
2020.8.29

## Slide 2
Contents
Introduction of the beampipe
Heat transfer analysis of beampipe
Heat transfer analysis of vertex detector
Summary

## Slide 3
1.Introduction of the beam pipe
Ver：BP20200829
The detector has not given the design requirements.
——Form Liu Yudong
Objective
To obtain the best cooling parameters and working temperature.
Provide basis for structure design.
Heat flux
Only High-order mode heat
Total heat load in high Luminosity Z：3476.6W
The central Be pipe
The extending Al pipe
Vertex detector
Coolant: water
LumiCal
Coolant: paraffin
Heat flux: 50~200mW/cm2
Coolant: Air
Structure

## Slide 4
Sub-sectional cooling structure
2. Heat transfer analysis of beampipe
2.1 Two kinds of heat exchange structures
Paraffin inlet
Paraffin inlet
Paraffin inlet
water inlet
water outlet
paraffin inlet
Integrated cooling structure

## Slide 5
2. Heat transfer analysis for beampipe
2.2 Integrated paraffin cooling of Be and extending pipes(2019.10)
High order heat is too large.
Cannot meet the engineering requirement.
 | Δp | Δt | Maximum temperature |  |  | 
 |  |  | Be | Al | Cu | SS304
Synchronous photothermal load +Higgs | kPa | ℃ | ℃ | ℃ | ℃ | ℃
 | 66 | 3.7 | 41.8 | 72.9 | 100.3 | 96.1
Synchronous photothermal load +Z |  | 38.9 | 76.3 | 211.4 | 322.2 | 305.3
Heat flux
Temperature distribution
——From Liu Yudong
Cu
Be
u=0.5zm/s
Tin=23℃
Al
Cu
Al
Calculation model and condition
Coolant: paraffin
Four inlet, four outlet
Viscous model: Laminar
Cu
Structure
——From Bai Sa
1.Synchronous photothermal load :151.6W,
Width is 0.36 mm
2.High-order mode heat: Higgs@782W, Z@11060W
uniform distribution
Δp：Pressure drop
Δt: Temperature difference between inlet and outlet of cooling medium

## Slide 6
2. Heat transfer analysis for beampipe
2.3 Sub-sectional cooling for Be and extending pipes
(1) 2019.12
Max.t of transition section of SS316L: 31.3℃
The total heat flux is very low.
Meeting the engineering requirement.
Oil: Δp=3.8kPa, Δt=2.2℃ H2O: Δp=6.6kPa,Δt=0.7℃
——From Bai Sa and Liu Yudong
Coolant：water
Two inlet, two outlet
tin=23℃
Flow rate: 1.7L/min
Total Heat:
Al
Al
Be
Cu
Cu
SS304L
SS304L
Coolant：water
Two inlet, two outlet
tin= 23℃
Flow rate: 1.7L/min
Total heat:
Coolant：paraffin
Two inlet, two outlet
tin=23℃
Flow rate: 0.85L/min
Total heat:
Thermal load on the wall of the beam pipe:
1.Synchronous radiant heat: 25.24W
0 ~259mm: 0W
259 ~620mm: 24.5W, Width is 0.36 mm
620 ~ 700mm: 0.74W, Width is 0.36 mm
2.High-order mode heat :168 W
Structure
Heat flux
Calculation model and condition
Temperature distribution
Vacuum wall diameter：Φ28 Φ28 Φ31
Viscous model: Laminar

## Slide 7
Al pipe/water:0.5m/s | 
Maximum temperature | Water Δt
℃ | ℃
40.8 | 0.14
Calculation condition:
length: 95mm
Inner wall diameter of inner pipe: Φ30mm
Inner pipe thickness: 2mm
Outer pipe thickness: 2mm
Gap: 2mm
Inlet temperature:23℃
Synchronous radiant heat: 500W/cm2
Synchronous radiant heat Width is 0.36 mm
Heating time: 0.5s
transient calculation
Calculation model
Heat transfer results
Fix the ends
Temperature distribution of Al pipe
Maximum stress of Al：31.9MPa
Maximum strain of Al pipe：0.49mm
Thermal stress analysis
2. Heat transfer analysis for beampipe
2.3 Sub-sectional cooling for Be and extending pipes
(3) 500W/cm2 synchronous radiant heat on 95mm Al pipe(2020.5)
The strain of Al pipe is too large.
Synchronous radiant heat is unexpected.
Heat flux

## Slide 8
2. Heat transfer analysis for beampipe
(2) ver.2020.5
Coolant: water
Two inlet, two outlet
tin= 23℃
Flow: 3.4L/min
Coolant: paraffin
Four inlet, four outlet
tin= 23℃
Inlet velocity: 2.2L/min
Coolant: water,
Two inlet, two outlet
tin= 23℃
Inlet velocity: 3.4L/min
Max.t of detector installation position: 27.8℃
Max.t of transition section of SS316L: 80.3℃
Max.t of outer Be: 25.5℃
The heat flux has increased a lot.
No cooling in the ends leads to high temperature.
Vacuum wall diameter：Φ28 Φ40
——From Liu Yudong
2.3 Sub-sectional cooling for Be and extending pipes
Structure
Al:453.26W
Be:136.72W
Al:453.26W
Heat flux
Calculation model and condition
Temperature distribution
Viscous model: Laminar
High order mode heat : 1043.2 W

## Slide 9
2. Heat transfer analysis for beampipe
(4) Ver.2020. 7
——From Liu Yu Dong
2.3 Sub-sectional cooling for Be and extending pipes
Be
Al
Al
Coolant: water,
Inlet temperature: 23℃
Inlet velocity: 3.4L/min
Coolant: water,
Inlet temperature: 23℃
Inlet velocity: 3.4L/min
Coolant: paraffin,
Inlet temperature: 23℃
Inlet velocity: 2.2L/min
Structure can be cooled in Z model.
Max.t of transition section of inner Al: 48.1℃
Max.t of detector installation position: 27.2℃
Max.t of outer Be: 25.7℃
paraffin: Δp=19.5kPa, Δt=5.6℃
water: Δp=19.4kPa, Δt= 3.3℃
Calculation model and condition
Heat flux
Structure
Only high order mode heat
Z model: 1031.5 W
High Luminosity Z: 3476.6W
Temperature distribution in Z model
Viscous model: Laminar

## Slide 10
2. Heat transfer analysis for beampipe
2.3 Sub-sectional cooling for Be and extending pipes
Meets the requirements of engineering application.
But the temperature of detector installation position is higher than our expectation.
paraffin: Δp=19.5kPa, Δt=14℃
water: Δp=19.4kPa, Δt= 6.3℃
(4) Ver.2020. 7
Temperature distribution in High Luminosity Z
Max.t of transition section of inner Al: 81.2℃
Max.t of detector installation position: 33℃
Max.t of outer Be: 28.9℃

## Slide 11
2. Heat transfer analysis of beampipe
2.4 Optimization of key parameters
Be Pipe: Simple three-tier structure
Critical pressure calculation formula：
where：E——modulus of elasticity
t ——thickness
μ——Poisson's ratio
R——(R1+R2)/2
 | E | μ
Be | 303Gpa | 0.1
Al | 68.2GPa | 0.32
 | thickness | R1 | R2 | Pcr
 | mm | mm | mm | Mpa
Be | 0.5 | 14 | 14.5 | 3.3
 | 0.35 | 15 | 15.35 | 0.94
Al | 0.5 | 14 | 14.5 | 0.82
 | 0.35 | 15 | 15.35 | 0.23
Critical pressure results
0.35mm Al can bear only 0.23MPa.
Making a step of Be to enlarge the interface thickness, which will increase the critical pressure of Al.
Pressure loss design : Δp≤20KPa
(BEPCII: Δp=8KPa )
(1) Critical pressure
Be
Al
Al

## Slide 12
2 Heat transfer analysis of beampipe
Pressure loss change as Velocity
According to pressure drop and heat transfer: u=0.8m/s
2.4 Optimization of key parameters
(2) Velocity for Be pipe
Inlet: u=0.8m/s
Calculation model
(3) Gap thickness for Be pipe
Pressure drop under different gaps
gap | u | dp
mm | m/s | kPa
0.5 | 0.8 | 17
0.4 | 0.8 | 29.6
0.3 | 0.8 | 46.7
Gap thickness: 0.5mm
Inlet: u=0.5~0.8m/s
Calculation model
gap | u | Δp
mm | m/s | kPa
0.5 | 0.5 | 10.5
 | 0.8 | 17
 | 0.95 | 20.1

## Slide 13
Mass contrast
Heat transfer calculation results
power | gap | velocity | dp | Maximum temperature |  | dt
 |  |  |  | Inner Be | Outer Be | 
W | mm | m/s | KPa | ℃ | ℃ | ℃
87.9 | 0.2 | 0.3 | 21.3 | 27.5 | 26.8 | 4
 |  | 0.5 | 35.4 | 25.9 | 25.2 | 2.4
 | 0.25 | 0.4 | 18.2 | 26 | 25.2 | 2.4
 |  | 0.5 | 22.7 | 25.6 | 24.7 | 1.9
 | 0.3 | 0.5 | 15.8 | 25.4 | 24.3 | 1.6
412.6 | 0.3 | 0.5 | 15.8 | 34 | 29.1 | 7.4
 |  | 0.75 | 23.8 | 31.5 | 26.7 | 5
 |  | 1 | 35.1 | 30.5 | 25.4 | 3.7
 | Density | thickness | Thickness *density | Mass ratio
 | Kg/m3 | mm |  | 
paraffin | 810 | 0.5 | 405 | 1
water | 1000 | 0.3 | 300.0 | 0.74
 |  | 0.25 | 250.0 | 0.62
 |  | 0.2 | 200.0 | 0.49
(a) Water cooling
Water isn’t adopted in cooling Be pipe, because:
Water corrodes Be.
Water density is higher than paraffin.
Be reflector in CSNS is used water cooling.
Reduce the gap thickness.
inlet: t=23℃; 0.3~0.5m/s
Calculation model
2.5 Exploration of coolant for Be pipe
2.Heat transfer analysis of beampipe
Z model: Better heat transfer effect！Less mater mass!
High Luminosity Z: difficult

## Slide 14
(b) Cryogenic gas cooling
Inlet, u=10~15m/s
Calculation model
2.5 Exploration of coolant for Be pipe
Power |  | pressure (gage pressure) | velocity | tin | Δp | Maximum temperature |  | Δt
 |  |  |  |  |  | Inner Be | Outer Be | 
W |  | MPa |  | ℃ | KPa | ℃ | ℃ | ℃
87.9 | N2 | 0 | 10 | -50 | 2 | 110.2 | 69.6 | 135
 |  | 0.1 | 15 | -15* | 4 | 56.9 | 19.9 | 46.6
 | He | 0 | 10 | -50 | 3.5 | 128.6 | 124.5 | 176.3
 |  | 0.1 | 15 | -35** | 4.2 | 29.5 | 23.4 | 60.6
412.6 | N2 | 0.1 | 15 | -50 | 4 | 233.2 | 96 | 191.6
Temperature distribution of outlet section
N2(*)
He(**)
Z model: Cryogenic gas cooling is feasible. But it is difficult to realize in engineering.
High Luminosity Z: Difficult
Results
2 Heat transfer analysis of beampipe
Formula of convective heat transfer coefficient in circular tube:
It is suitable for forced convection heat transfer without phase transition.

## Slide 15
3.1 Detector position and heat transfer requirement
Air inlet
Air outlet
Vertex detector
Heat transfer condition:
Heat flux: 50mW/cm2~200mW/cm2
Coolant： Air
Working temperature：40℃ or 60℃？
3. Heat transfer analysis for vertex detector
4-Φ12
4-Φ12

## Slide 16
3.2 Detector heat source
High heat flux: 50mW/cm2~200mW/cm2
The heat flux is higher than conventional air cooling.
 | Carbon fiber quantity | Chip quantity on a single carbon fiber | Total number of chips | Single chip |  |  | Total area | Total heat |  | 
 |  |  |  | length | width | area |  |  |  | 
 |  |  |  |  |  |  |  | 50mW/cm2 | 100mW/cm2 | 200mW/cm2
 |  |  |  | mm | mm | cm2 | cm2 | W | W | W
First | 9 | 19 | 171 | 25.6 | 12.8 | 3.277 | 560.3 | 28.0 | 56.0 | 112.1
Second | 18 | 20 | 360 | 25.6 | 12.8 | 3.277 | 1179.7 | 59.0 | 118.0 | 235.9
Third | 24 | 20 | 480 | 25.6 | 12.8 | 3.277 | 1572.9 | 78.6 | 157.3 | 314.6
Total | 51 | 59 | 1011 | 25.6 | 12.8 | 3.277 | 3312.8 | 165.6 | 331.3 | 662.6
Total heat
For air cooling, 1W thermal power classically needs 3000mm2 cooling area.
1W/3000mm2=3.33e-4W/mm2=3.33e-2W/cm2=33.3mW/cm2
(散热器常规风冷的风速一般在5m/s以上)
（For conventional air cooling, air velocity is generally above 5m/s in radiator air cooling.）
3. Heat transfer analysis for vertex detector

## Slide 17
3.3 Air velocity in the vertex cavity
For the air velocity that can be provided under the beam tube structure is only 0.7m/s.
Due to the tight space, the air velocity required for cooling cannot be provided.
Air velocity is inversely proportional to area
Φ12
Duct inlet
Sectional area contrast
Beam pipe
Velocity in the detector cavity
Time | Pipe inlet area |  |  |  |  | Vertex cavity cross section |  |  |  |  | 
 | ID | Velocity | Number | flow | Sectional area | OD | ID | Sectional area | Effective area | Area ratio | Actual average velocity
 | mm | m/s |  | m3/h | mm2 | mm | mm | mm2 | mm2 |  | m/s
2020.5 | 6 | 15 | 8 | 12.2 | 226.1 | 120 | 30.7 | 1.06E+04 | 1.03E+04 | 45 | 0.3
2020.7 | 12 | 15 | 4 | 24.4 | 452.2 | 118 | 30.7 | 1.02E+04 | 9.91E+03 | 22 | 0.7
3. Heat transfer analysis for vertex detector

## Slide 18
3.4 Air cooling analysis of single silicon strip in the third layer(2020.5)
A
A profile
Silicon strip
Flexible circuit board(Kapton):
698mm*16.8mm*0.07mm
Carbon fiber：698mm*16.8*0.2mm
Exothermic layer(Si)：
25.7mm*12.8mm*0.05mm*10plates
material | density | Specific heat | conductivity
 | kg/m3 | J/(kg.k) | W/(m.K)
Si | 2419 | 713 | 149
kapton | 1417 | 1260 | 0.2
carbon fiber | 1810 | 710 | 0.52
Material property
3. Heat transfer analysis for vertex detector
(1) Calculation model
Silicon strip distribution
Chip length(10 plates)：257mm
carbon fiber length：698mm
Air flow direction
Calculation model with air
Because of symmetry, using half to simulate.
structure
tin=20℃，0.3~0.5m/s

## Slide 19
Heat flux | Δt |  | Maximum temperature | 
mW/cm2 | 0.3m/s | 0.5m/s | 0.3m/s | 0.5m/s
 | ℃ | ℃ | ℃ | ℃
200 | 76.5 | 48.2 | 537.9 | 489.5
100 | 38.2 | 24.1 | 276.7 | 251.8
50 | 19.1 | 12.1 | 146.6 | 134.5
Only air cooling can’t take away the heat.
The outlet temperature of air is high.
3.4 Air cooling analysis of single silicon strip in the third layer(2020.5)
(2)Results
Cooling the ends of carbon fiber
3. Heat transfer analysis for vertex detector
Temperature distribution

## Slide 20
Heat flux | Maximum temperature | 
 | Only air cooling | Air cooling + Ends cooling
mW/cm2 | ℃ | ℃
200 | 537.9 | 525.6
100 | 276.7 | 271.2
50 | 146.6 | 144.8
3.5 Air cooling + ends cooling for single silicon strip in the third layer(2020.5)
Results
The temperature can be decreased by end cooling, but it is limited by the thermal conductivity and cross-sectional area of the material.
Chip length(10 plates)：257mm
carbon fiber length：698mm
Air flow direction
0.3m/s
t=20℃
t=20℃
3. Heat transfer analysis for vertex detector
Increasing carbon fiber conductivity
Calculation model

## Slide 21
3.6 Air cooling + ends cooling for single silicon strip in the first layer(2020.7)
3. Heat transfer analysis for vertex detector
Choose the shortest silicon strip to analysis. The shortest, the easiest for ending cooling.
Inner side:
9plates
No Natural convection
(because no air cooling here)
outside:
10plates
Natural convection
(1) Calculation model
carbon fiber length：267mm
t=20℃
t=20℃
h?, t=20℃
Range of natural convection heat transfer coefficient: h=1~10W/(m2.K).
Determine the parameter of h: h=f(u)
Determine the velocity around the first layer
Simply calculation: Adding natural convection on the surface instead of air cooling.
Many influencing parameters in calculation
t=20℃, h=?
Single silicon strip
Silicon strip distribution

## Slide 22
Inlet:1.5m/s
outlet
Average velocity:
(2) Determine the velocity of the first layer(2D)
3D: u=1.5m/s
4-Φ12，u=15m/s
2D: u=1.5m/s
Determination of inlet velocity
Velocity distribution
0.5m/s
0.7m/s
1.0m/s
3.6 Air cooling + ends cooling for single silicon strip in the first layer(2020.7)
3. Heat transfer analysis for vertex detector
The average velocity next to the first layer is 0.5m/s.
Calculation model(2D)

## Slide 23
(3) Determine natural convection heat transfer coefficient
Calculation model
tin=20℃
u=2.17m/s
Air average velocity: 0.5m/s
Natural convection heat transfer coefficient: h=10W/(m2.K)
Section profile
inlet
outlet
Calculation condition
Carbon fiber thickness:0.25mm
Carbon fiber length: 267mm
Heat source: 50mW/cm2
Carbon fiber conductivity | Air cooling | Natural convection | 
 | Average velocity: 0.5m/s | t=20℃ | 
 |  | h=5 | h=10
W/(m.K) | ℃ | ℃ | ℃
0.52 | 115.3 | 185.2 | 117
200 | 53.7 | 74.2 | 54
Air cooling VS Natural convection
3.6 Air cooling + ends cooling for single silicon strip in the first layer(2020.7)
3. Heat transfer analysis for vertex detector
Silicon strip in the first layer

## Slide 24
(4) Influence of carbon fiber thermal conductivity on heat transfer
Increasing conductivity of carbon fiber can greatly reduce the chip temperature.
Calculation condition
Carbon fiber thickness: 0.1mm
Carbon fiber length: 267mm
Heat source: 50mW/cm2
3.6 Air cooling + ends cooling for single silicon strip in the first layer(2020.7)
3. Heat transfer analysis for vertex detector
t=20℃
t=20℃
Outer face: h=10W/(m2.K), t=20℃
Inner face: no convection
Calculation model
λ=0.52W/(m.K)
t1
t2
t3
t1-t2=122.8℃
t2-t3=13.5℃
Increasing the thickness of carbon fiber
The maximum temperature of chip
VS carbon fiber conductivity
But the temperature has not fallen to what we expected.

## Slide 25
(5) Influence of carbon fiber thickness on heat transfer
3.6 Air cooling + ends cooling for single silicon strip in the first layer(2020.7)
3. Heat transfer analysis for vertex detector
Calculation condition
Carbon fiber length: 267mm
Carbon fiber conductivity: 200W/(m.K)
The ends temperature: 20 ℃
Heat source: 50mW/cm2
Unilateral natural convection: h=10W/(m2.k),t=20℃
The detector maximum temperature can be reduced to less than 55℃ when carbon fiber thickness is 0.25mm and it’s conductivity is 200W/(m.k).
Detector preferred temperature: ≤40℃
Adding high conductivity coating
The maximum temperature of chip
VS carbon fiber thickness

## Slide 26
4.5.2 Influence of different factors on vertex detector heat transfer
(6) Influence of graphene conductivity on heat transfer
Adding high conductivity coating
graphene：0.05mm
Adding high conductivity coating it’s possible to reduce the detector temperature the range of 40~50℃.
Calculation condition
Carbon fiber length: 267mm
Carbon fiber conductivity: 200W/(m.K)
The ends temperature: 20 ℃
Heat source: 50mW/cm2
Unilateral natural convection: h=10W/(m2.k),t=20℃
The maximum temperature of chip
VS graphene conductivity
3.6 Air cooling + ends cooling for single silicon strip in the first layer(2020.7)

## Slide 27
5. Summery
(1) Beampipe
（a） Paraffin cooling for Be and water cooling for extending AL pipe
Be pipe: Paraffin cooling can satisfy the engineering requirement, but the temperature of detector installation position is a little higher than our expectation.
Extending Al pipe: cooling well!
（b） Coolant Exploration for Be
Water: Good cooling medium. Water eroding on the thin Be tube remains to be studied.
Cryogenic gas: Feasible in Z mode. But it is difficult to realize in engineering.
(2) Vertex detector
A series of cooling optimization has been done, but the purpose is still not achieved. Cooling is very difficult.

## Slide 28
Thanks for your attention!