## Slide 1: Progress of CEPC Control System ----Timing System
Presented by Gang Li
Aug. 26th, 2020

## Slide 2: Outline
Timing System of CEPC
EVG/EVR V.S White Rabbit
Summary

## Slide 3: Timing system of CEPC
Important subsystem of CEPC Control System
Trigger signal
Time&Frequency reference
Etc
定时系统：
产生一系列精确的时序信号，使加速器的特定设备在重复周期内按照一定的时序工作，确保束团注入到高频俘获区（bucket）内，使束流强度达到预设值。
向束流测量和谱仪亮度测量等设备发送触发信号和时钟参考信号，为数据获取，提供时间基准。

## Slide 4: EVG/EVR VS White Rabbit
EVG/EVR Timing System
  Trigger
  RF reference
  Precise timestamping
EVG/EVR：Broadcast
Site：APS、SLS，BEPCII，CSNS，SSRF，etc
Support
  Commercial products
  EVG/EVR of SSRF
  Homemade I/O and delay board
White Rabbit Timing System
  Precise timestamping
  Trigger
  RF reference
Master/Slave: Bi-directionality
Site：CERN、GSI、ESRF、Spring-8、 HIAF、CiADS、SHINE、LHAASO、CSNS、German Stock Exchange，etc
Support
  OpenHareware+Commercial products
  V.S

## Slide 5: White Rabbit Timing System: Precise timestamping
8
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 6: White Rabbit Timing System:Trigger
White Rabbit materials from ：
https://indico.cern.ch/event/913576/
https://www.ohwr.org/projects/white-rabbit/wiki/overview
https://www.ohwr.org/projects/white-rabbit/wiki/jun2018meeting
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Many applications worldwide

## Slide 7: White Rabbit Timing System:Trigger
Synchrotron operation
  f (t) – RF in accelerating cavities
  Beam Instrumentation diagnostics
  B(t) – magnetic field in bending magnets
  I(t) – current provided by power converters
Beam Inst.
Diagnostics
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
I(t)

## Slide 8: White Rabbit Timing System:Trigger
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch
FPGA
FPGA
FPGA
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch
FPGA

## Slide 9: Support and monitoring
WR Switch
19
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM
White Rabbit Timing System:Trigger

## Slide 10: White Rabbit Timing System: RF transfer
11

## Slide 11: White Rabbit Timing System: RF transfer
11
  A prototype tested in operation: <10 ps jitter, ESRF
  A prototype: <100 fs jitter and <10 ps reproducibility over reboots, CERN

## Slide 12: Summary
A lot of experience about EVG/EVR has been/will be accumulated through BEPCII, CSNS projects/HEPS projects
White Rabbit technology is accepted and adopted by more and more new projects or upgrading projects
Thanks a lot!
Notes: h