## Slide 1: CEPC injection and extraction system hardware design progress
Jinhui Chen, Lihua Huo, Lei Wang, Yuwen Wu, Hua Shi
Injection group
2020-8-26

## Slide 2: Outline
1
Overview of CEPC inj./ext. systems
2
Damping Ring injection & extraction kicker design
3
Booster low energy injection kicker design
4
Summary

## Slide 3
Overview of the CEPC injection and extraction systems
10-120GeV
120GeV
120GeV
e+
e-
100km
Damping ring
Dump
Dump

## Slide 4: Main types of injection hardware
 | Sub-system | Kicker Type | Kicker waveform | Septa Type
1 | Damping ring inj./ext. | Slotted-pipe kicker | Half-sine/250ns | Horizontal LMS
2 | Booster LE inj. | Strip-line kicker | Half-sine/50ns | Horizontal LMS
3 | Booster ext. for CR off-axis inj. | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS
4 | Collider off-axis inj. | Delay-line NLK kicker | Trapezoid /440-2420ns | Vertical LMS
5 | Booster ext. for CR on-axis inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS
6 | Booster HE inj. | NLK or Pulsed sextupole | Half-sine/0.333ms | Vertical LMS
7 | Collider swap out inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS
8 | Collider swap out ext. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS
9 | Collider beam dump | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS
10 | RF region beam separating | Delay-line dipole kicker | CW square / 165us,50% | Horizontal Copper septa

## Slide 5
Damping ring injection & extraction kicker design
Designed by Huo Lihua, Wang Lei

## Slide 6: DR Kicker design parameters
parameter | DR-injection &extraction kicker | Unit
name | DRK | -
Quantity | 2 | -
Type | Slotted-pipe kicker | -
Deflect direction | Vertical | -
Beam Energy | 1.1 | GeV
Deflect angle | 1.5 | mrad
Magnetic effective length | 0.25 | m
Magnetic strength | 0.024 | T
Integral magnetic strength | 0.006 | T·m
Clearance region(H×V) | 44×44 | mm
Good field region(H×V) | x=±10，y=±10？ | mm
Field uniformity in good field region | ? | -
Repetition rate | 100 | Hz
Amplitude repeatability | ±0.5% | -
Pulse jitter | ≤5 | ns
Bottom width of half sine pulse | < 250 | ns

## Slide 7: Magnet physics design
Slotted-pipe kicker
2D model by Opera
Umax=3200V
Imax=2326.5A
Inductance=194nH
250ns

## Slide 8: Field uniformity
x=0, y=(-10,10):Un.=±1.6%
x=0, y=(-5,5):Un.=±0.9%
x=2, y=(-10,10):Un.=±1.65%
x=4, y=(-10,10):Un.=±1.8%
x=6, y=(-10,10):Un.=±2.1 %
y=8, x=(-10,10):Un.=±2.5%
y=10, x=(-8.8,8.8):Un.=±2.5%

## Slide 9: Preliminary engineering design
Outer body (316L)
electrodes
Auxiliary hole
To vacuum pump
HV feedthrough
HV feedthrough
To be improved :
the HV end structure
Ground end structure
Canceling Auxiliary hole？
HV feedthrough and connector

## Slide 10: Mechanical Dimensions
Φ200mm
44mm
210mm
250mm

## Slide 11: Kicker pulser
SIC 1200V SBD
IGBT
LC resonance discharge circuit (IGBT+SBD)
Imax=2326.5A(2500A)
L=194nH(250nH)
C=25nF
Tw=π√LC=248.4ns
Z=√L/C=3.16Ω
U=7357V(8000V)
IGBT quantity=10*4=40

## Slide 12
Booster Low Energy Injection kicker design
Designed by Huo Lihua, Shi Hua, Wang Lei

## Slide 13: DR Kicker design parameters
parameter | Booster Low Energy injection kicker | Unit
name | BSTLEIK | -
Quantity | 2 | -
Type | Strip-line kicker | -
Deflect direction | Vertical | -
Beam Energy | 10 | GeV
Deflect angle | 0.11 | mrad
Length of Strip-line kicker electrode | 1000 | mm
Gap between two electrodes | 55 | mm
Odd mode impedance | 50±1 | 
Even mode impedance | <65 | 
Clearance region(H×V) | 55×55? | mm
Good field region(H×V) | x=±1.1，y= (-0.85, 2.1)？ | mm
Integral field uniformity | ? | -
Amplitude of electrical pulse（into 50Ω） |  | kV
Repetition rate | 100 | Hz
Amplitude repeatability | <2% (RMS) | -
Pulse jitter | ≤1 | ns
Bottom width of electrical pulse（3%-3%） | < 50 | ns

## Slide 14: Strip-line kicker design for booster LE inj.
Kick strength
  Total kick angle: θ=0.11mrad
  E=10GeV, d=55mm, g=1 =>U*L>30.25kV∙m
  Total strip-line kicker electrode length L=1m =>U>30.25kV(or ±16kV)
Here, θ is kick angle(rad)；E is beam energy(eV)；U is applied pulse voltage for both electrodes(V)；l is strip-line length；d is the distance between the electrodes，g is the geometry factor, determined by the shape of the electrode. w is the strip-line width.
Kick speed
  Min bunch spacing - τ=25ns
    Electrode length l<3.75m => l= 1m
    Electrical pulse Width 6.7ns< tp <43.3ns =>Flat-top ttop >6.7ns, Rise/fall Time tr/tf <18.3ns
50ns,100Hz

## Slide 15: Geometry design
Zeven=87
Zeven=94
Zeven=68
(Vane width=90mm)
To achieve highest geometric factor(g=0.9884) the blade width should be w=90mm, when d=55mm.
Blade thickness=3mm? shape?
Odd mode impedance Zodd=50Ω
Even mode impedance Zeven=68 
Field uniformity:
    X(-8.8~+8.8mm)，0.4%
    Y(-16.2~+16.2mm)，~1.1%
90mm
55mm

## Slide 16: Preliminary engineering design
Outer body (316L)
electrodes
HV feedthrough
HV feedthrough
Cooling Water hole
Cooling Water tubes
To be improved :
the shape of electrodes
the ends of electrodes
Electrode supporting
HV feedthrough and connector

## Slide 17: Mechanical Dimensions
1100mm
260mm
1000mm
55mm
1100mm
260mm

## Slide 18: Summary
Slotted-pipe kicker is adopted for damping ring injection and extraction system. Preliminary magnet design was done , but there are still some details should be considered to improved.
The booster low energy injection system need a very fast kicker with 50ns bottom width. The strip-line kicker is best choice for it. Preliminary magnet design was done , but there are some details should be considered to improved too.

## Slide 19
END
Thank you for attentions!!!