## Slide 1: CEPC SCRF in TDR (Response to IAC and IARC recommendations)
Jiyuan Zhai
CEPC Day, October 19, 2020

## Slide 3: IAC Response 3
Is the accelerator TDR on track? What should be improved and how to achieve the improvement?
The IAC was pleased to see the advancements on the work performed up to now toward the TDR. The quality of the work performed, how most important issues were addressed, even if not already solved, and the design work on-going to increase the luminosity performances at Higgs and Z were highly appreciated.
Several improvements on the design parameters over the CDR have been presented including: • higher luminosity at H (5.2 x 1034 vs 2.9 x 1034) • “High-Lumi” for Z (102 x 1034 vs 32 x 1034) • assuring compatibility for top-pair production at the appropriate energy (~365 GeV) • higher energy injection into the booster with a longer linac • capability to handle 50 MW SR power • compatibility with SppC collider layout All of them expand the capability of the project with a moderate increase of the cost.
Response:
TDR design of CEPC SRF system is aiming to fulfill requirements of all the above improvements over CDR.
SRF layout, configuration, parameters, specifications and cost will be upgraded accordingly (try to converge in the end of 2020. re-baseline time? approval procedure?).

## Slide 4: IAC Recommendation 8 and IARC 11-2
IAC Recommendation 8: Define the new parameters as a “new baseline”, to make all systems consistent with them. A proper documentation database and an approval procedure for new baselines must be established, to achieve coherence through the entire project. All related parameters including RF and the injector should match the new baseline. … TDR … “goal” and time frame must be clearly stated consistently.
IARC answers to the charges: Separate types of RF cavities should be optimized for each energy using bypass lines.
IARC Recommendations 11-2: Optimization to produce the required performance for the higher luminosity Z running is essential. Using single-cell cavities in the collider ring also for the Higgs running gives cavity performance requirements not yet regularly achieved anywhere in the world. A scheme with bypasses is more realistic.
Response:
Collider ring cavity by-pass scheme and counter-phase scheme recently proposed to solve the outstanding problems (HOM and beam loading) of SRF system operation in high luminosity Z mode (30 MW) and the 50 MW power upgrade.
Booster ring cavity HOM issues stand out for high luminosity Z, but will be within control.
New RF layout and parameters optimization at each energy with the new schemes is ongoing and will be presented in CEPC2020 workshop. Booster SRF issues and other issues will also be addressed.

## Slide 5: New RF Section Layout for CEPC
120 m
288 m
48-176 m
300 m
160 m
RF section length at IP2/IP4: ~ 2 km (similar to CDR)
150 m
S
S
H/W/tt use common cavities (2-cell for H/W, 5-cell for tt) for two beams. (Less than) Half filled to avoid collision in RF section. If fully filled, bunch spacing should be more than 4 km (< 25 bunches per beam).
Z uses separate high current 1-cell cavities for two beams and by-pass H/W/tt cavities.
Allow seamless mode switching with unrestricted performance of each mode until the power limit (baseline and upgrade). Low risk.
A few percent more cost to unleash CEPC potential and more flexible operation.
Could have 80 more separate 1-cells (thus 40 less 2-cells) for W and further Z optimization while keep the total cell number for a reasonable H cavity gradient.
If consider ttbar switch to other modes, more bypass is needed. Booster bypass?

## Slide 6: CEPC SRF Parameter Comparison
 | BEPCII 500 MHz 4.2 K | BEPC3 500 MHz 4.2 K | CEPC CDR H 30 MW 3E34 | CEPC CDR Z 16.5 MW 32E34 | CEPC 1-cell H 30 MW 3E34 | CEPC TDR Z 30 MW 100E34 | CEPC TDR H 30 MW 3E34 | CEPC TDR W 30 MW 10E34 | CEPC Ultimate Z 50 MW 167E34
Beam current (mA) | 400 (600) | 900 | 2 x 17.4 | 460 | 2 x 17.4 | 838 | 2 x 17.4 | 2 x 87.7 | 1400
Cell number | 1 | 1 | 2 |  | 1 | 1 | 2/1 | 2/1 | 1
Cavity number / ring | 1 | 2 | 2 x 120 | 60 | 2 x 120 | 60 | 2x(90+60) | 2x(90+60) | 60
Eacc (MV/m) | 6 (1.5 MV) | 10 (2.5 MV) | 19.7 | 3.6 | 40 | 9.4 | 19.7 | 4.2 | 9.4
Q0 @ 4.2 K / 2 K | 1E9 | 1E9 | 1.5E10 | 1.5E10 | 3E10 | 1.5E10 | 1.5E10 | 1.5E10 | 1.5E10
Total wall loss (kW) |  |  | 6.1 | 0.1 | 6.1 | 0.35 | 6.1 | 0.27 | 0.35
Input power (kW) | 110 | 150 | 250 | 275 | 250 | 500 | 250/125 | 250/125 | 835
Cavity# / klystron | 1 | 1 SSA | 2 |  | 2/1 | 1 | 2/1 | 2/1 | 1
Klystron power (kW) | 250 | 150 SSA | 800 | 800 | 800 | 800 | 800 | 800 | 1200
Total KLY number | 2 | 4 | 120 |  | 60+120 | 120 | 90+120 | 90+120 | 120
HOM damper | Absorber | Absorber | Hook+ Absorber |  | Hook+ Absorber | Absorber | Hook+ Absorber | Hook+ Absorber | Absorber
HOM power (kW) | 8* | 20 | 0.6 | 1.9 | 0.23 | 2.4 | 0.46 / 0.23 | 1.5 / 0.75 | 4
* Bunch length 15 mm, cavity cell HOM loss factor 0.1 V/pC, tapers 0.06 V/pC, absorbers 0.26 V/pC.

## Slide 7: IAC Recommendation 9 and IARC 11-1
IAC Recommendation 9: Clarify the timetable with appropriate milestones, including prototyping. Not every technical detail and drawing will be necessary at the completion of the TDR.
IARC Recommendations 11-1: It is important to make a clear distinction between long-term R&D, such as high-Tc coating of cavities, peripheral development, such as Centrifugal Barrel Polishing, and high-priority items to produce industrial-scale production required for CEPC construction. Given limited resources, particularly of staff, priority must be given to the latter.
Response: CEPC SRF system TDR R&D and Industrialization Plan
2019-2020:
SRF system TDR design and optimization
High Q, high gradient cavity, high power components and other key technology R&D
650 MHz high Q short cryomodule prototyping
PAPS SRF facility construction
2021-2022:
SRF system TDR design re-baseline, engineering design
650 MHz high Q short cryomodule operation and improvement
1.3 GHz high Q full cryomodule prototyping
650 MHz high current cryomodule design (and prototyping?)
PAPS SRF facility commissioning, operation and upgrade
Industrialization in synergy with other SRF projects in China

## Slide 8: IAC Recommendation 10
In order to build up international involvement in the project, draw up a list of components likely to require a second source, and identify potential international suppliers.
Response:
In-kind contribution: high-lumi and high power Z cavity cryomodules, ttbar cavity cryomodules (RF source, cryogenics …)
Import components:
Feedthroughs, HOM antennas and pickup antennas, KYOCERA, Japan
All metal gate valves (RF-shielded, class-10 clean, 2 K), VAT, Switzerland
All metal angle valves (class-10 clean, 2 K), ULVAC, Japan
Vacuum gauges, RGA, leak detector, PFEIFFER, INFICON, Germany
Vacuum pumps, LEYBONBL, Germany
Ceramics for input coupler windows, MOGAN, Germany
OFHC copper material for input coupler windows, LUVATA, Finland
Cryogenic step motors, PHYTRON, Germany
Piezo actuators, PI, Germany
Flux gates, BARTINGTON, UK

## Slide 9: IAC Recommendation 11
Build international and domestic collaborations in several critical areas, e.g., MDI, SC-RF, polarization, beam dynamics (beam-beam, dynamic aperture, etc.), C-band linac, and RF sources.
Response:
CEPC SRF domestic collaboration
  Organization: CEPC SRF Collaboration kick-off soon. Members: IHEP, PKU and 5 companies.
  Activities: Already have collaborations on CEPC SRF technology and various SRF projects.
  Future collaborations: SHINE and other CW SRF FEL projects in China.
CEPC SRF international collaboration
  Organization: TBD
  Funding: apply for international team program (CAS Lu Jiaxi etc.) to support personal exchanges.
  Activities: ILC/SuperKEKB (KEK), INFN-LASA, JLAB: SRF system design, technology and infrastructure, annual SRF collaboration meeting with KEK, personal exchanges.
  Future collaborations: FCC-ee (CERN, Univ. Rostock), EIC (JLAB, BNL), PIP-II and LCLS-II-HE (FNAL), DESY, CEA-Saclay etc.