## Slide 1: Si Tracker TDAQ Input
Jens for the CEPC SiTrackerz
Pretty ad-hoc – need to gather more details
All of the content is from others, all the mistakes are mine

## Slide 2: Questions recap (slightly changed order)
Any zero suppression or compression they might carry out at the front end
Your need for control and timing signals
The total data volume and channel count for their sub-detector under different machine running modes
Your current assumptions about readout bandwidths and readout implementation and power consumption
Any views / preferences on readout style(triggered or trigger-less readout)
  Continuous sequential readout
  Trigger sequential readout
  Non-sequential readout

## Slide 3: “Simple” responses
Zero suppression:
  Naturally done within each frontend, only actual hits (including noise) will make it out, baseline is hidden
  Data transmission however should be more condensed
Control/Timing:
  Current interface could in theory come down to one command link per <N>-chip assembly (Up to one ladder, depending on redundancy needs)
  Needs to be rugged, current best operation is with additional links for clock (and trigger, if used)
  25us turnaround time for local time counter, event index (need to clarify), support for event tag with trigger information (when triggered)
  i.e. 1-3 links into detector per <large-ish object>, could deliver multiple of these from 1 fibre
    This means “only” O(1k) links into detector, depending on module grouping and worry about redundance…

## Slide 4: Complex responses
Keeping a low profile (in services)
  Per-chip links at reasonable speeds O(1Gbps)
  O(150k) chips, assuming local aggregation (with buffers), implies a total link bandwidth of O(40 Tbps) for the whole detector (Module aggregation 4-to-1)
    At reasonable link speeds (10Gbps) that is currently about 4k links (Can always dream of more here)
  This is link bandwidth – Guessing we need to zero-supress further within the detector (i.e. de-randomising buffers at end-of-ladder) to reduce from O(10k) frontend links down to O(<1k)
    This will add complexity (<reliability), material may be on par due to reduced number of high-speed transceivers…
Total bandwidth required (guesstimates, sadly):
  Currently massive overheads in prototype hit formats: 96 bit per hit
  Triggerless, can do about 100 modules at full link bandwidth in Z-mode, innermost layer
    Assuming 1e-4/cm^2/event, 16cm^2 per module, 640Mbit/s links with 96bit per hit.
    Data format could be reduced by about a factor of 2 but aggregation brings in overheads (module IDs or such)

## Slide 5: More complexity
Triggerless data is currently not fully time-ordered
  Needs event sorting outside
  On-detector complexity weighs against material and reliability
Triggered data is “prettier” and could reduce the total link count needed – but then it must be triggered 
Power consumption:
  0.6W/chip - 0.15W/cm^2 – 100kW just FE
  This is only the frontend chip and currently without any link aggregation or de-randomisation, expect extra power at end-of-ladder
    Currently O(2W) for a single high-speed link (bi-directional)
    I’d expect a similar order of magnitude for a fast buffer/de-randomiser

## Slide 6: Further details
Need prototypes – we are at 0.5 prototypes so far (chips exist), and while things are easy enough to estimate (finger in the air type), it is hard to make firm statements without any prototypes
Currently working towards a prototype ladder, that could then (in theory) be used to (gu)es(s)timate where we are and how far we can push

## Slide 7: Preferences (personal)
Triggered versus untriggered isn’t easy
Returned data arguments:
  I come from a triggered world, which is hard enough to understand (Bunch-crossing IDs should be long, Trigger IDs should be long & command defined – life would/should then be easy)
  Untriggered data will need more processing/ordering and thus should be self-explanatory when arriving at your favourite readout system (same is true for triggered, but often easier to de-mystify)
Command links:
  In an untriggered system, almost no need for synchronisation
  1-to-many command links much easier to get working here (Should reduce link count in the end)

## Slide 8: BACKUP - Current understanding
1e-4 tracks/cm^2/event
  Assuming 2 hits per track
  Scaled that to all modules – very unfair, outer layers should have less, but then I am not too deep into simulation to know whether that’s is true
1.28Gbps link speed per chip at the moment (data link), assumed 640 Mbit/s (shown to work already) for earlier slides
O(49k) pixels over 2x2cm^2
96 bit hit format – could be reduced by about a factor 2