## Slide 1: CEPC High luminosity Higgs lattice impacts on the hardwares
Yiwei Wang
for the CEPC Accelerator Physics Group
CEPC day, 25 Nov. 2020

## Slide 2: Outline
  Design of the high luminosity Higgs lattice
  Impacts on hardwares

## Slide 3: The way to a high luminosity Higgs lattice
  The high luminosity lattice (comparing with CDR) is mainly achieved by squeezing the beam size at IP while keep adequate beam lifetime.
    Squeezing the beta function at IP
    Reduction of the emittance
    get enough transverse dynamic aperture and momentum acceptance

## Slide 4
Overall parameters for Higgs mode
Parameters design by D. Wang et al
 | Higgs (CDR) | Higgs (high)
Number of IPs | 2 | 2
Beam energy (GeV) | 120 | 120
Circumference (km) | 100 | 100
Synchrotron radiation loss/turn (GeV) | 1.73 | 1.8
Crossing angle at IP (mrad) | 16.5×2 | 16.5
Piwinski angle | 3.48 | 4.87
Number of particles/bunch Ne (1010) | 15.0 | 16.3
Bunch number (bunch spacing) | 242 (0.68s) | 214
Beam current (mA) | 17.4 | 16.8
Synchrotron radiation power /beam (MW) | 30 | 30
Bending radius (km) | 10.7 | 10.2
Momentum compact (10-5) | 1.11 | 7.34
 function at IP x* / y* (m) | 0.36/0.0015 | 0.33/0.001
Emittance ex/ey (nm) | 1.21/0.0024 | 0.68/0.0014
Beam size at IP sx /sy (m) | 20.9/0.06 | 15.0/0.037
Beam-beam parameters x/y | 0.018/0.109 | 0.018/0.115
RF voltage VRF (GV) | 2.17 | 2.27
RF frequency f RF (MHz) (harmonic) | 650 (216816) | 650 (217500)
Natural bunch length z (mm) | 2.72 | 2.25
Bunch length z (mm) | 4.4 | 4.42
HOM power/cavity (2 cell) (kw) | 0.46 | 0.48
Energy spread (%) | 0.134 | 0.19
Energy acceptance requirement (%) | 1.35 | 1.7
Energy acceptance by RF (%) | 2.06 | 2.5
Beamstruhlung lifetime (min) | 80 | 41
Lifetime (hour) | 0.43 | 0.34
F (hour glass) | 0.89 | 0.88
Luminosity/IP L (1034cm-2s-1) | 2.93 | 5.0

## Slide 5: Design of high luminosity lattice
Optimization of the quadrupole radiation effect
  Interaction region: longer QD0/QF1
  ARC region: longer quadrupoles
Reduction of dynamic aperture requirement from injection
  Straight section region: larger x at injection point
Maximization of bend filling factor to minimize the synchrotron radiation loss per turn
  ARC region: sextupoles in two rings changed from staggered to parallel; The left drifts are used for the bends.
  RF region: shorter phase tuning sections
Optimization of high order chromaticity for arc region
  ARC region: new sextupole layout
  To make the lattice robust and provide good start point for DA
  Interaction region: reduction of L* without changing the front-end position of the FD cryo-module

## Slide 6: High luminosity lattice
Achieved (w/o error):
Goal (w/ error):
Achieved (w/o error):
Goal (w/ error):
  CDR: L=
  βy*=1.5mm, εx=1.2nm, L*=2.2m, 1024 FODO cells
J. Wu,
Y. Zhang,
Y. W. Wang
  CDR: L=
  βy*=1mm, εx=0.64nm, L*=1.9m, 1160 FODO cells
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 7
Superconducting magnets
in the interaction region
 | Higgs (CDR) | Higgs (high lumi.)
SC QD0 and QF1 | L*=2.2m, d=0.6m, QD0: 2.0m, 136T/m QF1: 1.48m, 111T/m | L*=1.9m, d=0.3m, QD0: 2.5m, 142T/m, 96T/m QF1=1.5m, 56T/m
SC anti-solenoids | maximum 7.2T | maximum 7.2T
SC sextupoles | VSIRD: 0.6m, 1635 T/m^2 HSIRD: 0.8m, 1882 T/m^2 VSIRU: 0.6m, 1562 T/m^2 HSIRU: 0.6m, 1999 T/m^2 | VSIRD: 0.6m, 1511 T/m^2 HSIRD: 0.8m, 2099T/m^2 VSIRU: 0.6m, 1935 T/m^2 HSIRU: 0.6m, 1413 T/m^2 (safety factor 50% for strength )

## Slide 8
Normal conducting magnets
Main magnets in the ARC | Higgs (CDR) Quantity, length and field | Higgs (high lumi.) Quantity, length and field
Dipoles (dual aperture) | 2320, 28.686 m, 373 Gs | 2944, 21.7 m, 390 Gs (Quant +27%, total length -4%)
Quadpoles (dual aperture) | 2320, 2 m, 8.4 T/m | 2944, 3 m, 10.6 T/m (Quant +27%, total length 90%)
Sextupoles (single aperture) | SF: 896, 0.7 m, 506 T/m^2 SD: 896, 0.7 m*2, 506 T/m^2 | SF: 1024, 0.7 m, 1100 T/m^2 SD: 1024, 0.7 m*2, 1129 T/m^2 (Quant +14%, total length 14%)

## Slide 9
Mechanical systems
ARC period (CDR)
345m, 5cells, 10bends, 10 quads, 4 sextupoles,
staggered sextupoles in two rings
ARC period (High lumi)
600m, 11cells, 22bends, 22 quads, 8 sextupoles,
parallel sextupoles in two rings, more sensitive to alignment error

## Slide 10
Other systems
  Beam instrumentation: Quantity of BPMs increased with 27%
  SC RF system: voltage from 2.17 GV to 2.27 GV
  Separating system(bend + static separator, or kicker + septum)
  Magnet Power supply: Quantity of sextupoles power supply increased with 14%
  Vacuum system: aperture need to be check
  Injection and extraction
  civil construction
  Synchrotron radiation lines
  Beam dump system
  …

## Slide 11: Summary
  The high luminosity lattice (comparing with CDR) is mainly achieved by squeezing the beam size at IP while keep adequate beam lifetime.
  The impacts on the technical systems are estimated for several systems which are most impacted.

## Slide 12: Backup

## Slide 13
  A possible scheme of the RF region*
*talk of Jiyuan ZHAI, CEPC SCRF system and R&D, 14:00 Accelerator section, october 26, 2020

## Slide 14: ARC region for other modes
  For the arc region, the phase advance of each cell will be changed from 90/90 to 60/60 and the additional sextupoles need to be installed for the Z mode (Ref: FCC-ee CDR).
    H/W/tt modes: 5 cells/period, 42 sextupoles in 35 cells
    Z mode: 7 cells/period, 12 additional sextupoles (+29%) in 35 cells
    35 cells of H/W/tt mode
    35 cells of Z mode
SF
SD
SD
SF
SD