## Slide 1: Necessary R&D issues of CEPC control system
Presented by Li Gang
CEPC Day, Nov.25, 2020

## Slide 2: Challenge, opportunities and risks
CEPC: A super large scale project
Controlled device: Hundreds of thousands
EPICS PV: Tens of millions
With the development of technology, the control system is iterative
ICS(Integrated control system): All in control
Software Platform
  EPICS, TANGO, FERA, DOOCS/TINE，etc
Hardware
  ATCA/uTCA
  PLC
  etc

## Slide 3: EPICS architecture of software and hardware

## Slide 4: Timing system
Trigger signal
RF reference
Timestamp
定时系统：
产生一系列精确的时序信号，使加速器的特定设备在重复周期内按照一定的时序工作，确保束团注入到高频俘获区（bucket）内，使束流强度达到预设值。
向束流测量和谱仪亮度测量等设备发送触发信号和时钟参考信号，为数据获取，提供时间基准。

## Slide 5: Timing system: EVG/EVR VS White Rabbit
EVG/EVR Timing System
  Trigger
  RF reference
  Precise timestamping
EVG/EVR：Broadcast
Site：APS、SLS，BEPCII，CSNS，SSRF，etc
Support
  Commercial products
  EVG/EVR of SSRF
  Homemade I/O and delay board
White Rabbit Timing System
  Precise timestamping
  Trigger
  RF reference
Master/Slave: Bi-directionality
Site：CERN、GSI、ESRF、Spring-8、 HIAF、CiADS、SHINE、LHAASO、CSNS、German Stock Exchange，etc
Support
  OpenHareware+Commercial products
  V.S

## Slide 6: Timing system: White Rabbit
White Rabbit materials from ：
https://indico.cern.ch/event/913576/
https://www.ohwr.org/projects/white-rabbit/wiki/overview
https://www.ohwr.org/projects/white-rabbit/wiki/jun2018meeting
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Many applications worldwide
  A prototype tested in operation: <10 ps jitter, ESRF
  A prototype: <100 fs jitter and <10 ps reproducibility over reboots, CERN

## Slide 7: Timing system R&D
Prototype of White Rabbit timing
  Learning and tracking the development of White Rabbit Technology
  RF over Ethernet (RF reference,D3S)
  Delay compensation
  Integrated into EPICS
  WHIST: White RabbIt Synchronisation and Timing, ESRF

## Slide 8: BOFB R&D
The stability of beam orbit
  Misalignment
  Ripple of Power supply
  Vibration of the earth
  Temperature drift
  Etc

## Slide 9: The structure of BOFB
Process
Power Supply
BPM
Fast Correctors
Vacuum Chambers

## Slide 10: Domestic PLC R&D
A lot of PLC will be used in control system of CEPC
BEPCII: Allen-Bradley PLC, Siemens PLC
CSNS&HEPS: Yokogawa PLC, Siemens PLC
SUPCON PLC (2019.7/2019.12, technology exchange )
  Integrated into EPICS

## Slide 11: Data Archiver R&D
Archive millions of PVs
  Channel Archiver(CA)
  Archiver Appliance(CA/PVA/PVX)

## Slide 12
R&D:Post Mortem and Online Performance Analysis System
The post-mortem system the role of organizing the collection and analysis of transient data recorded around a beam or power abort by all relevant CEPC equipment systems. By periodically acquiring the time-correlated data from all relevant system, the system can also used for the online performance analysis.

## Slide 13
R&D: Deep learning based accelerator early fault detection system
Fig. 1 The diagram of the early fault detection system
Fig. 2 The prototype of the early fault detection system for CSNS accelerator

## Slide 14
R&D: Web and database based high level applications

## Slide 15: Summary
EPICS：Cooperate with EPICS community
Cooperate with CSNS and HEPS in IHEP
Thanks a lot!