## Slide 1: Optical data transmission for silicon pixel detector readout
Xiaoting Li
Electronics Group of Experimental physics Center
11 Nov. 2020

## Slide 2: Outline
Introduction of optical data link
Research status and development
My research status
Summary

## Slide 3: Optical data link
Communications between detector (pixel-array chips) and counting room (FPGAs)
Up link (data link):
  Transmitter: (on detector)
    Receive parallel data from a pixel array
    Serialize (SerTx) and drive (SerLd) the high-speed data to a laser diode (LD)
  Receiver: (off detector)
    Receive and transfer optical signals to electrical
    An FPGA receives and processes the electrical signals
Down link (control link):
  Similar to the up link but with different direction
  Reference clock and slow control
Custom ASICs (rad-hard requirement):
  SerTx (GBTX)
  SerSc
  SerLd (GBLD)
  SerTIA (GBTIA)
Up link
Dn link

## Slide 4: Outline
Introduction of optical data link
Research status and development
My research status
Summary

## Slide 5: Research status and development – Serializer
Name | Year | Designer | Technology | Encoder | TX_DR (Gbps) | Power (mW) | Total Jitter (ps)
GLink | 1992 | CERN | Silicon Bipolar |  | 1.6 | 1900 | --
GOL | 2001 | CERN | 0.25μm CMOS |  | 1.6 | 400 | 107
LOCs1 | 2010 | SMU | 0.25μm CMOS SOS | ---- | 5.0 | 463 | 62
GBT | 2010 2016 | CERN | 0.13μm CMOS | Reed-Solomon | 4.8 | 330 | 52.4
LpGBT | 2014 | CERN | 65nm CMOS | RS | 4.8 | 20 | --
LOCs2 | 2014 | SMU | 0.25μm CMOS SOS | ---- | 8.0×2ch | 1250 | 25
LOCx2 | 2016 | SMU | 0.25μm CMOS SOS | Cyclical Redundancy Check | 5.0×2ch | 950 | 42
LOCx2-130 | 2018 | SMU | 0.13μm CMOS | CRC | 4.8×2ch | 440 | 52
---- | 2018 | SMU | 0.18μm CMOS | RS | 3.2 | 135 | 60.2
New LpGBT | 2019 | CERN | 65nm CMOS | RS | 10 |  | 
---- | 2018 | RAL | 65nm CMOS | 64b66b | 10 | -- | BER 10-16
Transmitter (serializer part) on detector
CERN: Conseil Européenn pour la Recherche Nucléaire
SMU: Southern Methodist University
RAL: Rutherford Appleton Laboratory, Harwell Oxford
5 Gbps
10 Gbps
20 Gbps…
DR of a single channel
130/250 nm
65 nm
65 or smaller

## Slide 6: Research status and development – Laser driver
Laser driver (array driver) on detector
Name | Year | Designer | Technology | Data Rate (Gbps) | Imod （mA） | Ibias （mA） | Power （mW） | Tj （ps） | TID （rad）
GBLD | 2009 2012 | CERN | 0.13 μm CMOS | 5 | 2-24 | 2-48 | ---- | 25 | ----
VDC | 2010 | OSU | 0.13 μm 8RF-DM CMOS | 5×4chA | 12 | 2 | ---- |  | 46M
GBLD | 2013 | CERN | 0.13 μm CMOS | 7.5 | 2-24 | 2-48 | ---- | 22 (best) | 100M
LOCld1 LOCld2 | 2013 2015 | SMU | 0.25 μm CMOS SOS | 8 8×2ch | 7.8-10.6 | 2-15 | 200/ch (Im-Ib: 6.4-6 mA) | ＜30 | pass
GBLD10 | 2015 | CERN | 0.13 μm CMOS | 10 | 0-12 | 0-43 | 85 | E- 13.68 O- 28.42 | 500M
GBLD10+ | 2016 | CERN | 65 nm CMOS | 10 | 0-12 | 0-43 | 31 | E- 22 ---- | ----
LDQ10 | 2017 | SMU | 65 nm CMOS | 10×4chA | 0-8 | 0-12 | 32.5/ch (4-6 mA) | E- 15.47 O- 17.97 | 300M
VLAD/lpVLAD | 2017 | SMU | 65 nm CMOS | 10×4chA | ---- | ---- | 34/ch, 22/ch （6-2 mA） | O- 48, 37 | 350M
VLAD14 | 2019 | SMU | 65 nm CMOS | 14×4chA | ---- | ---- | 55/ch （6-2 mA） | O- 14.8 | ----
---- | 2019.7 | CCNU | GSMC 0.13 μm SOI CMOS | 10 (Sim) | 2-8.6 | 1-3 | 51.2 (5-2 mA) | ---- | ----
OSU: Ohio State University 4chA: 4-channel array
E: Electrical O: Optical
Im-Ib: Imod-Ibias
Array

## Slide 7: Research status and development – LD & PD
Laser Diode / PIN Diode
  VCSEL (Vertical Cavity Surface Emitting Laser)
    TOSA/ROSA module
    VCSEL array
    Fiber connector: FC, SC, ST, LC…
Connections of ASIC chips and LD/PD
TOSA (LC)
LC connector
MTP-LC connector
PCB #3
array
array
MTP…
Connector
PCB #2
Bonding wire
PCB #1
Alignment
Optical 90-degree turn
Custom
  3D print interface
  3D wiring on silicon substrate
  …

## Slide 8: Outline
Introduction of optical data link
Research status and development
My research status
Summary

## Slide 9: My research status
CEPC MOST2 project (180-nm CIS CMOS technology, Two MPWs: 2019.6, 2020.2)
  160 Mbps in trigger mode and 4 Gbps in triggerless mode
Research works (130/55-nm CMOS technology, Two MPWs: 2015, 2017, 2019, 2020)
  4 Gbps (upgraded to 5.12Gbps) serializer ASICs in 130 nm
  10 Gbps serializer ASIC in 55 nm
Future research
  Low power, radiation-tolerant,
  high-speed serializer ASIC

## Slide 10: My research status – MOST2 project
CEPC MOST2 project (2019.6, 2020.2)
  40-MHz systerm clock, 512R×1024C array, 25μm pitch, 120 MHz/Chip, 32 bits, 8b10b encoder
  160 Mbps in trigger mode and 4 Gbps in triggerless mode
  A 64-rows×192-cloclums prototype ASIC was fabricated in two MPWs
Chip status
  TaiChuPix1:
    Pixel analog, Periphery and SER were fully functional proved
    Found and located several bugs
  TaiChuPix2:
    Modified major bugs
    Optimized pixel readout
    Added 8b10b encoder and chip-to-chip interconnection attempts
    A full signal chain (light to PC) was functional proved @ 160Mbps
    More detailed tests are ongoing
    Beam tests and TID test are preparing
TCP1: 5×5 mm2
TCP2: 5×5 mm2
TCPix2: X-ray tube at 8keV, 50uA

## Slide 11: My research status – MOST2 project
Test status of SER block
  TaiChuPix1:
    Working well at 2.56 Gbps
    Large jitter introduced at 4 Gbps
  TaiChuPix2:
    Will start soon later
TCPix1: Eye diagram @ 2.24Gbps (TB2_#1) @ 3.36Gbps @ 4.48Gbps
Tj: 141.63 ps
Rj: 5.39 ps
Dj: 64.77 ps
ISI: 45 ps
Tj: 123.27 ps
Rj: 4.84 ps
Dj: 54.26 ps
ISI: 51 ps
Tj: 147.14 ps
Rj: 5.35 ps
Dj: 70.90 ps
ISI: 66 ps
PLL test

## Slide 12: My research status – research works
2.56 Gbps
Tj: 51.66 ps
Rj: 2.28 ps
Dj: 19.22 ps
ISI: 15 ps
4.096 Gbps
Tj: 51.23 ps
Rj: 2.43 ps
Dj: 16.68 ps
ISI: 16 ps
PLL tests
Research works (2015, 2017, 2019)
  4-Gbps 32:1 serializer (without encoder)
    Laboratory test was finished, and met the design expectation
    Preparing for the radiation tests
    Optimize and upgrade to 5.12 Gbps (2.4×2.4 mm2), preparing for test
    (Funded by State Key laboratory of Particle Detection and Electronic 2019.1-2019.12)
Simulation @ 6Gbps
LVDS_RX
MUX
PLL
CMLdriver
32:1 SER 32:2 SER

## Slide 13: My research status – research works
Research works (2020)
  10-Gbps 32:1 serializer in 55 nm
    5-GHz PLL was taped-out in July 2020
    10-Gbps serializer is under design
Future researches
  Low power, radiation tolerant serializer for integrating into pixel array ASIC. (Study on key techniques of high-speed low-power and radiation-tolerant data transmission ASIC for silicon pixel detector, NSFC 2020 of youth)
Related researches in the electronic group
  Encoding and decoding techniques based on digital design flow in 130-nm process (Jie Zhang)
LCPLL: 0.9×2.35 mm2 Simulations
SER10：about 2×2 mm2 A simulation before driver

## Slide 14: Outline
Introduction of optical data link
Research status and development
My research status
Summary

## Slide 15: Summary
Thank you!
Generally introduced the optical data transmission for silicon pixel detector readout
Collected and compared several researches of serializer and laser driver. Researches trend to higher speed single-channel data rate and smaller size of the process.
Presented some recent works on serializer and future works aiming for low power and rad-hard

## Slide 16
A side view of ASICs and Multi-channel optical interface
3D wiring on silicon substrate