## Slide 1: Low Energy Muon Beam Facility at PSI
Xiaojie Ni :: Paul Scherrer Institute
2020 EMuS & MOMENT General Meeting

## Slide 2: Outline
Low Energy Muon Beam Basics
  PSI Overview
  Low Energy μ+ Beam and Setup
Applications of Low Energy µ+
  Semiconductors
  Magnetism
  Superconductivity
  Particle Physics Aspects
Improvements of Low Energy µ+ Beam

## Slide 3: Paul Scherrer Institute
Synchrotron
(SLS)
Neutron Spallation Source
(SINQ)
Muon Source
(SµS)
Proton Accelerator
SwissFEL
 Basel
Zürich 
Germany 
Aarau/Bern 
PSI West
PSI East
Notes: Hier sehen Sie das PSI aus der Vogelperspektive.
Wie Sie sehen, umfassen unsere Forschungsthemen eine sehr breite Palette:
  von der Materialforschung über die Energieforschung, der Nanotechnologie bis zur Biologie.
Auf der westlichen Aare-Seite sehen Sie unsere drei bisherigen Grossforschungsanlagen: die Synchrotron Lichtquelle Schweiz SLS, die Neutronenquelle SINQ, und die Myonenquelle SµS (gesprochen: S mü S), dazwischen das Zentrum für Protonentherapie zur Behandlung von bestimmten Krebserkrankungen.
Auf der Ostseite, im Wald, wird derzeit unsere vierte Grossforschungsanlage, der SwissFEL, gebaut. Mehr dazu später.
Diese Anlagen betreibt das PSI nicht nur für sich selbst, sondern für Forscher aus der Schweiz und dem Ausland, aus der Akademie und der Industrie.

## Slide 4: Muon Instruments at PSI: SμS (Swiss Muon Source)
HAL-9500
High Field and Low Temperature
9.5 T
< 20mK
GPS
General Purpose Surface Muon Instrument
Shared Surface Muon Beam
Muon on Request (MORE)
Muon Energy: 4.2 MeV (μ+)
0.6 T
1.6 K
LTF
Low Temperature Facility Retired Dec. 2018 Will be replaced by FLAME in 2021
3 T
0.02-4 K
LEM
Low Energy Muon
Instrument
Muon Energy: 0.5-30 keV
0.3 T
2.5 K
DOLLY
Muon Energy: 4.2 MeV (μ+)
0.5 T
0.25 K
GPD
General Purpose Decay Channel Instrument (for Pressure Studies)
Muon Energy: 5-60 MeV (μ+/ μ‒)
0.5 T
0.3 K
2.8 GPa
piE1
μE1
μE4
piE3
piM3.3
piM3.2
News:
MIXE (Muon Induced X-ray Emission)
Alex Amato et al.
RF-μSR
Zaher Salman et al.
FLAME
Hubertus Luetkens et al.

## Slide 5: Low Energy μ+ Beam and Setup for LE-μSR
~ 13000 LE-+/s; accelerate up to 20 keV
~2.2 • 108 +/s
- UHV system, 10-10 mbar
- some parts LN2 cooled
Polarized Low Energy Muon Beam Energy: 1-30 keV DE, Dt: 400 eV, 5 ns Depth: 1 – 300 nm Polarization ~100 % Beam Spot: 12 mm (FWHM)
at sample: up to ~ 5200 m+/s
Beam spot at sample
Spin-rotator (E x B)
Conical lens
Start detector
(10 nm C-foil)
Sample cryostat
e+ detectors
electrostatic mirror
Einzel lens
(LN2 cooled)
moderator
Einzel lens
(LN2 cooled)
“surface” m+ beam, ~4 MeV
Spin
Rates are for 6-cm target E and 1.8 mA proton current (2019)

## Slide 6: Low Energy μ+ Beam and Setup for LE-μSR
Muon Spin
Muon Momentum
Moderator low energy μ+
source
Typical re-acceleration voltage at the moderator: 15kV

## Slide 7: Low Energy μ+ Beam and Setup for LE-μSR
Muon Spin
Muon Momentum
Mirror
energy filter
Un-moderated fast µ+
Moderated slow µ+
Mirror at the same high voltage as the moderator. Typically 15kV

## Slide 8: Low Energy μ+ Beam and Setup for LE-μSR
Muon Spin
Muon Momentum
Spin-Rotator / Separator
E-Field
B-Field
In-plane spin rotation of ± 90° easily possible

## Slide 9: Low Energy μ+ Beam and Setup for LE-μSR
Muon Spin
Muon Momentum
Trigger
implantation time
A. Hofer, PhD Thesis (98) K.S. Khaw, et al., JINST 10, P10025 (15).
Trigger Detector or M-Counter

## Slide 10: Low Energy μ+ Beam and Setup for LE-μSR
Muon Spin
Muon Momentum
Sample Cryostat
Konti flow cryostats: 4 - 320 K at sample plate
LowTemp cryostat: 2.4 - 300 K with sample plate, 2.2 - 300 K without sample plate
Furnace: -50 - 300°C (can be cooled by LN2)
Sample size: Ideally 25x25 mm2 or ∅ = 25 mm, mosaic of four pieces of 10x102mm

## Slide 11: Low Energy μ+ Beam and Setup for LE-μSR
Magnets with APD Positron Spectrometer
B
B
WEW: 0-0.34 T
AEW: 0-300 G

## Slide 12
Applications of Low Energy µ+
Selected Examples

## Slide 13: Semiconductors
Possible muon charge states:
“bare” µ+ = Mu+ (diamagnetic)
µ+ + e- = Mu0 (paramagnetic)
µ+ + 2 e- = Mu- (diamagnetic)
Muon sites:
Bond center (BC): MuBC(+,0)
Tetrahedral interstitial site (T): MuT(0,-)
Measurements performed at T=220K:
MuBC0 fully transformed to MuBC+
MuT is used as sensor for free hole carriers.
Charge-Exchange Cycles
Direct Observation of Hole Carrier-Density Profiles and Their Light-Induced Manipulation at the Surface of Ge
T. Prokscha, et al. Physical Review Applied 14, 014098 (2020)

## Slide 14: Magnetism
Engineering the magnetic order in epitaxially strained Sr1-xBaxMnO3 perovskite thin films
L. Maurel et al., APL Materials 7, 041117 (2019)
FIG. 2. Temperature dependence of the transverse fraction fTTF of the muons normalized to the fraction at 300 K, determined from wTF LE-μSR measurements for 10-nm-thick Sr1-xBaxMnO3 films on (a) LSAT and (b) TSO. The arrows indicate the magnetic order temperature (see text).

## Slide 15: Superconductivity
Proximity-Induced Odd-Frequency Superconductivity in a Topological Insulator
Jonas A. Krieger et al., Physical Review Letters 125, 026802 (2020)
FIG. 1. (a) (top) Schematic showing the μSR geometry where the applied field is parallel to the surface and perpendicular to the muon spin and momentum directions. The lines depict the expected magnetic field depth profile due to screening of the applied field inside the heterostructure with (solid gray) and without (dotted black) proximity induced superconductivity in the Bi2Se3layer. (bottom) Calculated muon implantation profiles at different implantation energies using Trim.SP [25]. (b) Measured local mean field as a function of implantation energy above (black squares) and below (red circles) the superconducting transition temperature. The black horizontal line represents the applied field value, Bext, and the blue line is a fit to the theoretical model.

## Slide 16: More LE-μSR applications
Surface dynamics of polymers
Formation of hydrogen impurities in semiconductors at low energies
300μ
Current effects on magnetism and superconductivity in a thin LSCuO wire
Photo-induced effects in semiconductors
Magnetic properties of thin films and monolayers of single molecule magnets
Superconductivity and Magnetism in LCO/LSCO Superlattices
doping
Tc
TN
Superfluid density in high and low Tc heterostructures, superconduc-tivity and magnetism in electron-doped cuprates
Strain effects on magnetic transition in multi-ferroics
http://www.psi.ch/en/low-energy-muons/lem-publications
Topological Insulators, combination with ARPES
Proximity effects in normal/superconducting/magnetic heterostructures

## Slide 17: Particle Physics
A. Antognini, et al. PRL 108, 143401 (12).
K.S. Khaw, et al. PRA 94, 022716 (16).
Atomic Muonium is an ideal system in which to study bound state QED free of finite-size effects and in which hadronic corrections are strongly suppressed compared to hydrogen.
The Muonium 1s-2s transition offers a clean determination of the muon mass, which in turn is required for a precise interpretation of (g-2) and to determine the weak interaction Fermi coupling constant GF, and others.

## Slide 18: Particle Physics
Intense beam of metastable Muonium
G. Janka et al., Eur. Phys. J. C 80, 804 (2020).
Fig. 1 The experimental setup installed at the end of the LEM beamline, lengths at the bottom are not to scale. To the right there is an example of the time distribution of particles reaching the Stop-MCP in coincidence with the Tag-MCP . The paths of M and μ+ are not parallel for visualization reasons

## Slide 19
Improvements of Low Energy µ+ Beam

## Slide 20: Limitation
The insufficient low-energy muon rate at the sample:
Study of subtle proximity effects in magnetic/superconducting heterostructure samples are restricted due to limited statistical precision.
Study of hydrogen-like muonium states in semiconductors needs high statistics to observe the muonium precession frequencies.
Essential for all experiments requiring high statistical precision.
The large beam spot size at the sample:
About 80% of the muons stop in an area of 20×20 mm2, and only 40-50% in 10×10 mm2, due to the large phase space of the muon beam. Measurements on 55 mm2 sized samples are currently not possible because of the <10% fraction of the beam stopping in this small area, making the signal-to-background ratio unacceptably low.

## Slide 21: Improvements
A new target E
2. To replace the last triplet by a solenoid
 | Current μE4 | After replacing
Standard 40 mm TgE | 5740 | 8772
Slanted 40 mm TgE | 7555 | 10668
30-40 % for μE4
Low-energy muon rate

## Slide 22: Improvements
Collimator
Beam spot size
1-cm collimator
55 mm2 Fraction:
< 10 % 30-40%

## Slide 23: Improvements
Collimator
Beam spot size
1.5-cm collimator
12 kV transport | LEM rate (mAs) | Asymmetry | FoM (A2×R)
Without collimator | 905 | 0.056 | 2.8
1.5-cm collimator | 390 | 0.092 | 3.3
Sample: 10x5 mm2

## Slide 24: Acknowledgments
LEM-Team: Thomas Prokscha (Head) Zaher Salman Andreas Suter Hans-Peter Weber (Technician)
Andrin Doll (Postdoc) Xiaojie Ni (Postdoc)
Maria Inès Mendes Martins (PhD student from 10.2020)
Luping Zhou (Guest PhD student, 09.2019-09.2020)
Jonas A. Krieger (PhD student, graduated 07.2020)

## Slide 25: Proton Accelerator (Overview)
Cockcroft-Walton
A proton energy of 870 keV is obtained from the 60 keV extraction voltage at the ion source and the 810 keV DC acceleration of the Cockcroft-Walton accelerator

## Slide 26: Proton Accelerator (Overview)
Injektor 2 (1st Cyclotron)
Injection Energy 870 keV (4.3% of light speed)
Extraction Energy 72 MeV (37.1% of light speed)
Energy spread (FWHM) ca. 0.2 %
Beam Emittance ca. 2 pi mm x mrad
Beam Current 2.5 mA DC
Accelerator Frequency 50.63 MHz
Time Between Pulses 19.75 ns
Bunch Width ca. 0.3 ns
Magneticfield (Stiffness T x m, middle) 0.36 (1.25, 0.33 T)
Mass of Sektor Magnets 4 x 180.000 kg
Radius at Injection 400 mm
Radius at Extraction 3500 mm
Mass of Resonators 3 x 5.000 kg + 1 x 3.000 kg

## Slide 27: Proton Accelerator (Overview)
Main Cyclotron
Injection Energy 72 MeV
Extraction Energy 590 MeV
Extraction Momentum 1.2 Gev/c
Energy spread (FWHM) ca. 0.2 %
Beam Emittance ca. 2 pi mm x mrad
Beam Current 2.2 mA DC
Accelerator Frequency 50.63 MHz
Time Between Pulses 19.75 ns
Bunch Width ca. 0.3 ns
Extraction Losses ca. 0.03 %

## Slide 28: Beam Power of Accelerators World Wide
from M.Seidel, GFA, PSI

## Slide 29: Proton Accelerator (Overview)
Muon Source (Target M)
.

## Slide 30: Proton Accelerator (Overview)
Muon Source (Target E)

## Slide 31: Proton Accelerator (Overview)
Neutron Spalation Source (SINQ)

## Slide 32: Generation of Thermal μ+ at a Pulsed Muon Beam J-PARC (RIKEN-RAL)
Mu
Mu
Mu
K. Nagamine, et al., PRL 74, 4811 (1995). P. Bakule, et al., Nucl. Instr Meth. B 266, 335 (2008).

## Slide 33: Generation of Thermal μ+ at a Pulsed Muon Beam J-PARC (RIKEN-RAL)
K. Nagamine, et al., PRL 74, 4811 (1995). P. Bakule, et al., Nucl. Instr Meth. B 266, 335 (2008).
Advantage:
high LE-µ+ yield
Disadvantage:
Only ½ of the asymmetry
Tricky Laser system

## Slide 34: Generation of Slow Positive Muons from Solid Rare-Gas Moderators
PRB 36R, 8850 (87).

## Slide 35: Generation of Polarized Epithermal μ+
≈100 μm Ag at T=6K
 500 nm
s-Ne, Ar,
s-N2
„Surface“
Muons
 4 MeV
 100% pol.
T. Prokscha et al., Appl. Surf. Sci. 172, 235 (2001).
T. Prokscha et al., Phys. Rev. A58, 3739 (1998).
E. Morenzoni et al,. J. Appl. Phys. 81, 3340 (1997).
D. Harshmann et al., Phys. Rev. B36, 8850 (1987).
motivated by experiments for positron moderation

## Slide 36: Low Energy μ+ Beam and Setup for LE-μSR
0.6m
Scintilators
APD assembly
Wave length shifting optical fibers
A. Stoykov, R. Scheuermann, et al., Physica B 404, 986 (09). See also https://www.psi.ch/en/lmu/position-sensitive-detection-psd-of-muons-and-positrons

## Slide 37: Low Energy Muonium Production
mesoporous
thin film
SiN membrane 3x3 array 50-nm-thick 5.6 x 5.6 mm2
Cu nose used as e+ absorber to increase the asymmetry
2 times higher Mu yield at RT
High Mu yield also at low-T, important for the 1s-2s experiment
A. Antognini, et al. PRL 108, 143401 (12).
K.S. Khaw, et al. PRA 94, 022716 (16).

## Slide 38: Semiconductors – µ+ to Measure Charge Carrier Profiles Example 1: p-doped Ge
“fast” precession
“slow” precession
= γµ Bext
Measurements performed at T=220K:
MuBC0 fully transformed to MuBC+
MuT is used as sensor for free hole carriers.
T. Prokscha, et al. in preparation.
Charge-Exchange Cylces
Simulation of TF measurements (B=10mT)

## Slide 39: Muon Production – Example: Target E at PSI
Rotating Graphite Target (1 Hz)
Radiation Cooled, Tavg = 1700K
Thickness t=40 mm; h=6 mm;  450 mm
Radiation Losses 30%
590 meV p beam
rotation axis
Pions / Muons
t
h
solenoids
quadrupoles
T.Prokscha et al NIM-A (2008)
2200 μA ≈ 1.4∙1016 p/sec @ 590MeV →
≈ 107 – 108 μ+/sec, ≈ 100% polarized
Surface Muons: ≈ 4 MeV
μE4 beamline at PSI: 4 ∙ 108 μ+/sec
p + C  π+ π- p n …
µ+
Graphit
π+ → μ+ + νµ