## Slide 1
Electronics of the μSR Spectrometer
Hao Liang
Fanshui Deng, Miaoqing Zhuang, Yingge Zhang，Enqi Fu，Xiunan Sun，Changchang Zhao， Xuejian Li
State Key Laboratory of Particle Detection and Electronics, USTC

## Slide 2
Content
Introduction of electronics system
Front-end electronics
Multi-channel TDC based on single FPGA
Test Result and Progress
Summary
DAQ software

## Slide 3: Introduction of electronics system
Electronics system
Front-end electronics（FEE）
Multi-channel TDC based on single FPGA
01
Beam monitor
Pulsed muon beam
Scintillator detector
front-end
Sample
Discriminator
TDC module based on FPGA
Computer
Data analysis
Timing discriminator
Start
Stop

## Slide 4: Introduction of electronics system
01
Requirements
128 channels PMT readout
Count Rate > 40
Time resolution < 1ns
Sturcture
Front-end Electronics(FEE)
  8ch in each FEE
  Total 16 FEE board
Time to Digital Converter(TDC)
  32ch in each TDC
  4 TDC Module
  1 Fanout & Test Module
DAQ via Ethernet

## Slide 5: Introduction of electronics system
01

## Slide 6: Front-end electronics
02
Features
Timing Discriminator
LVDS signal fanout
Self-test

## Slide 7: Front-end electronics
02
Timing Discriminator
  Change CFD to LED
    Non-delayline CFD
      Best time resolution
      Best integration density
      Increased deadtime

## Slide 8: Front-end electronics
Deadtime reduced to 7ns
Time resolution remains better, ~300ps
02

## Slide 9: Front-end electronics
02
Self-testing circuit
On-board FPGA realize SPI bus, Communicate with TDC module, accept commands and
Generate self-test signal

## Slide 10: Multi-channel TDC based on single FPGA
Work with 4 FEE(LED)
Data transmit via Ethernet or USB
32ch FPGA based TDC
4 modules total
03

## Slide 11: Multi-channel TDC based on single FPGA
03
TDC
(54bit)
Start
Stop[1]
Stop[2]
Stop[3]
Stop[N]
·
·
·
Trigger
Channel coding
(7bit)
Channel configure
Time window configure
Self-checking、calibration、threshold control
To front board
Error’s detector
Configure
FIFO
(61bit)
Data packing
(64bit)
USB 2.0
Gigabit network
Ethernet
USB

## Slide 12: Multi-channel TDC based on single FPGA
03
8flip-flop
(rising edge)+
8flip-flop(falling edge)
Start
Clk0
Clk1
Clk2
Clk7
·
·
·
8flip-flop
(rising edge)+
8flip-flop(falling edge)
Clk0
Clk1
Clk2
Clk7
·
·
·
Stop
Hit arithmetic
(4bit)
Hit arithmetic
(4bit）
16bit counter
Enable
Time tag
(26bit)
Trigger counter
(8bit)
FIFO
(20bit)
Trigger
Readout FIFO
(54bit)
TDC internal structure (1ch)

## Slide 13: Multi-channel TDC based on single FPGA
03
Features
Number of channels:32
Clock frequency:200Mhz
Resolution:312.5ps
Type:Multi-stop
Counting range:5ns—262us
Counting rate:488Khz
Dead time:5ns

## Slide 14: Multi-channel TDC based on single FPGA
03
Fanout & Test Module
Fanout 4 start signal to each TDC
Generate Self-test signal to each TDC

## Slide 15: DAQ Software
04
QT based
Data can be saved as Nexus structure
Online monitor

## Slide 16: Test Result and Progress
05
Timing accuracy test results of front end electronics
Timing accuracy test results of TDC
Test results

## Slide 17
Electronics system test—Precision and linearity
Inc 200ps | 1 | 2 | 3 | 4 | 5 | 6 | 7
Expectation | 25.085ns | 25.273ns | 25.472ns | 25.713ns | 25.894ns | 26.110ns | 26.372ns
FWHM | 356.3ps | 364.8ps | 404.7ps | 404.0ps | 419.4ps | 424.3ps | 425.7ps
Inc 200ps | 8 | 9 | 10 | 11 | 12 | 13 | 14
Expectation | 26.553ns | 26.709ns | 26.946ns | 27.146ns | 27.268ns | 27.461ns | 27.763ns
FWHM | 401.8ps | 404.2ps | 383.1ps | 361.4ps | 365.7ps | 328.6ps | 355.9ps
Inc 200ps | 15 | 16 | 17 | 18 | 19 | 20 | 21
Expectation | 27.931ns | 28.123ns | 28.271ns | 28.461ns | 28.706ns | 28.872ns | 29.125ns
FWHM | 390.3ps | 387.5ps | 411.5ps | 412.5ps | 432.0ps | 428.7ps | 404.3ps
Inc 200ps | 22 | 23 | 24 | 25 | 26 | 27 | 28
Expectation | 29.250ns | 29.401ns | 29.579ns | 29.818ns | 30.090ns | 30.188ns | 
FWHM | 408.3ps | 381.0ps | 388.1ps | 383.8ps | 364.0ps | 378.7ps | 
Test result with CFD FEE

## Slide 18: Test Result and Progress
05
16FEEs+4TDC modules under testing

## Slide 19: Test result
New Result with LED-FEE

## Slide 21: summary
All electronics modules nearly ready
Result of electronics test and beam test shows that Readout Electronics meet the requirements