## Slide 1: LBNF Hadron Monitor
Jilei Sun, Anxin Wang, Ye Yuan, Jingyu Tang
2020 EMuS/MOMENT General Meeting
Dongguan, 11 December, 2020

## Slide 2: Outline
Introduction
Progress on the SEM Hadron Monitor
  Heat issues simulation
  Vacuum requirement
  Sag measurement
HM Prototype
Summary

## Slide 3: Introduction
Located downstream of a 200 m long decay pipe and just upstream of the beam absorber
  Beam-based alignment of the target and focusing horns
  Monitoring the neutrino beam during the normal operation by monitoring the residual protons that did not interact in target
  Exposed to severe radiation without shielding
  Radiation hardness is essential
Hadron Monitor

## Slide 4: Roles Played by the Hadron Monitor
Role 1: Beamline Alignment – Must Have
  Low intensity, direct proton beam to the hadron monitor
  Requires 70 microradians pointing resolution
    Translates to 14 mm rms at hadron monitor
  10^12 protons/pulse; 6 mm rms; 120 GeV or 60 GeV
Role 2: Target and Baffle Alignment – Must Have
  Low intensity proton beam scanned across target/baffle to hadron monitor
    Beam position determined by upstream BPMs
    Beam absorption determined by total intensity at hadron monitor
    Intensity measurement must be insensitive to beam movement from scan
  10^10  10^12 protons/pulse; < 7.5 cm rms; 120 GeV
  10^10  10^12 protons/pulse; < 15 cm rms; 60 GeV

## Slide 5: Roles Played by the Hadron Monitor
Role 3: Alignment of Horns – Would be Nice
  Low intensity proton beam scanned across horn alignment “fin”
    Beam position determined by upstream BPMs
    Beam absorption primarily determined by losses recorded in ionization chamber
    Backup measurement by total intensity at hadron monitor
  10^12 protons/pulse; 6 mm rms; 120 GeV or 60 GeV
Role 4: Monitoring during Operation – Would be Nice
  Beam that makes it through the target hits the hadron monitor
    Mostly protons
  10^12 protons/pulse; 7.5 cm rms; 120 GeV
  10^12 protons/pulse; 15 cm rms; 60 GeV

## Slide 6
 | Protons Per Pulse @HM | Proton Beam Spot Size @HM (rms) | Beam Energy (GeV) | Pulse Duration (μs) | Cycle Time (s)
Role 1: Beamline Alignment | 1.00E+12 | 6 mm | 60/120 | 1.6 | 10
Role 2: Target and Baffle Alignment | 1E10 / 1E12 | 75 / 10 mm | 120 | 1.6 | 10
 | 1E10 / 1E12 | 150 / 10 mm | 60 |  | 
Role 3: Alignment for Horns | 1.00E+12 | 6 mm | 60/120 | 1.6 | 10
Role 4: Monitoring during Operation | 1.00E+12 | 75 mm | 120 | 10 | 1.2
 | 1.00E+12 | 150 mm | 60 |  | 
Parameters of Different Operation Mode

## Slide 7: Progress on the SEM Hadron Monitor
Original idea was multi-wires
  Signal was too weak when used for target and baffle alignment
 | Protons Per Pulse @HM | Proton Beam Spot Size @HM (rms) | Beam Energy (GeV) | Pulse Duration (μs) | Cycle Time (s) | Signal estimation 0~3σ (μA) Wire D=100μm
Role 1: Beamline Alignment | 1.00E+12 | 6 mm | 60/120 | 1.6 | 10 | 665~7.4
Role 2: Target and Baffle Alignment | 1E10 / 1E12 | 75 / 10 mm | 120 | 1.6 | 10 | 0.5~0.006 / 400~4.4
 | 1E10 / 1E12 | 150 / 10 mm | 60 |  |  | 0.3~0.003 / 400~4.4
Role 3: Alignment for Horns | 1.00E+12 | 6 mm | 60/120 | 1.6 | 10 | 665~7.4
Role 4: Monitoring during Operation | 1.00E+12 | 75 mm | 120 | 10 | 1.2 | 8.5~0.09
 | 1.00E+12 | 150 mm | 60 |  |  | 4~0.05

## Slide 8: Multi-Strip Scheme
Have ~1000 times stronger signals than wires

## Slide 9: Mechanical consideration for the multi-strip
Vacuum chamber ( Material: Aluminum Alloy (LY12))
  Uniform plate at the beam-in side: 24 mm thick
  Rib plate at the beam-out side: plate thickness 10 mm; rib 30 mm
  Minimize the influence of the electrons from chamber wall
  Max. deformation: ~ 1 mm
Beam-in side, max. deformation 1.17 mm
Beam-out side, max. deformation 1.08 mm

## Slide 10: Heat Issues Simulation
Dimension of the vacuum chamber: 840 mm×840 mm×100 mm
  Strip: Ti with 100μm thickness
  Chamber outside surfaces convection coefficient: 5 W/(m^2∙K)
  Titanium emissivity: 0.5

## Slide 11: Heat Issues Simulation
  Thermal load was from a MARS Monte Carlo with the following inputs (Done by FNAL)
  Proton beam power: 2.4 MW
  Proton beam momentum: 120 GeV
  Target: 2 m long graphite (the water-cooled fin-type, not the RAL helium-cooled type)
  At larger radius than the target core: 12 cm long “wings” (equivalent of the 12 cm long bafflette in the RAL design)
Power density as a function of radius at the HM location: Al, Ceramic, Steel
Model when thermal load applied

## Slide 12: Maximum temperature 33.4 ℃, when initial temperature and ambient set to 20 ℃.
Heat Issues Simulation

## Slide 13: Vacuum Requirement
  Mean Free Path calculation
  If we take the secondary emission yield is 1%, and the distance between the planes of strips is D=1 cm, then the mean free path should be greater than D/0.01 = 1 m to prevent the influence of residual gas ionization.
  At 10^-3 Pa (~10^-5 torr), the mean free path is approximately 10 m for most gasses.
𝜆=(KB 𝑇)/(𝜋𝜎^2 𝑝)

## Slide 14
5e-6 Torr
10 L/s
30 L/s
300 L/s
Vacuum Requirement
Pumping rate calculation
  Chamber size: 1000 mm*1000m cm*100 mm, aluminum
  Pipe size: 10 m length, 5 cm diameter, stainless steel
  Leak rate: 7e-10 torr.L/(s.cm-2) for Al and 2e-10 torr.L/(s.cm-2) for SS
  30 L/s will satisfy the requirement

## Slide 15: Sag measurement
Titanium strip
  Expansion coefficiency ：（9.41~10.03）×10-6/℃（0-100℃）
  Temperature rise: 20 ℃ ( 20 to 40℃)
  Initial length: 1000 mm
  Linear expansion: 0.2 mm
  Tension is necessary
Sag of the horizontal strips need to be considered
  If the measurement accuracy better than 1%
  Gap size between strips: 1 mm
  Sag should be less than 10 μm

## Slide 16: Test stand setup
Screw
Slider
Connecting board
Strip fixer
Heater
Ti strip
Tension meter
Slideway
Infrared thermal sensor
Quartz heater
Tension meter:
2N ~ 500 N

## Slide 17: 3D imaging system for sag measurement
Measuring the displacement by tracking the speckle images on the foil with 2 cameras.
Camera: 2.3 megapixel, pixel size 5.86μm*5.86μm
System measurement accuracy: 0.02 mm
Painting spray on the foil for tracking
System setup in Test 1

## Slide 18: Test stand Improving
Drawbacks were found in Test 1&2
  Strip fixer sag also
  Stiffness factor of the tension meter is too high, which made the system very sensitive to the thermal expansion if there was no spring tensioning on the strip.
Strip fixer

## Slide 19: Test stand Improved
Leaf spring tensioning applied
Strip fixer sits on a slider, no more sag happens
Motor driven slider for accurate control
Motor driven
Leaf spring tensioning

## Slide 20: Sag Measurement - Test 3
10 μm
50 μm
100 μm
Easily to be wrinkled
3 type of strips were tested

## Slide 21: 10 μm strip failed
  Deformed because of the thermal stress
Initial position
Deformed position

## Slide 22: Test result of the 50 μm strip
Chart: Tension (N)
| 25 | 26.5 | 28 | 29.9 | 31.7 | 33.5 | 35.300000000000011 | 37.1 | 38.9 | 40.700000000000003 | 42.4 | 44.1 | 45.8 | 47.5 | 49.1 | 50.9 | 52.6 | 54.4 | 56.1 | 57.8 | 59.5
40 degrees | 0.0172 | 0.0106 | 0.0146 | 0.0165 | 0.0163 | 0.013 | 0.012 | 0.0129 | 0.0131 | 0.0105 | 0.0115 | 0.0133 | 0.0126 | 0.0096 | 0.009 | 0.0074 | 0.0055 | 0.0032 | -0.0007 | -0.0012 | -0.0094
60 degrees | 0.0228 | 0.0223 | 0.0211 | 0.0195 | 0.019 | 0.0151 | 0.0127 | 0.0099 | 0.0112 | 0.0086 | 0.0078 | 0.0072 | 0.0064 | 0.0052 | 0.0043 | 0.0017 | 0.0004 | 0.0001 | 0.0007 | -0.0004 | -0.0036
80 degrees | 0.0112 | 0.0098 | 0.009 | 0.0098 | 0.006 | 0.0011 | 0.0015 | -0.0007 | -0.0016 | -0.004 | -0.0042 | -0.0044 | -0.0029 | -0.001 | 0.0001 | -0.0022 | -0.0048 | -0.0078 | -0.0087 | -0.0083 | -0.0141
  The sag of the horizontal strip can be controlled at 10 μm level while tension applied
  Sag goes lower while increase the tension

## Slide 23: Learned from Test 3
50 N tension (~11 pounds) looks like enough, sag should be less than 10 μm
Thinner is not better for the strip, thicker strip will have less deformation caused by the thermal stress, 50 ~ 100 μm would be a good choice
For the prototype manufacture, annealing to relieve the stress of the strip before cutting will be necessary

## Slide 24: HM prototype
3D model
Leaf spring

## Slide 25
Vacuum maintenance with prototype
  600 L pump + 10 m tube
  < 1e-5 pa

## Slide 26: Prototype beam test
Proton beam parameters: 100 MeV, up to 500 μA, beam size 40 mm maximum
HM wall thickness 20 mm + 30 mm
Suitable test current is 1 μA considering the thermal issue

## Slide 27: Summary
Multi-strip type hadron monitor was intensively studied to fulfill the LBNF requirements
Heat, Vacuum, Sag issues were considered, which are all at an acceptable level
A prototype is now finished manufacturing, further beam tests is in organization and will be done next month hopefully

## Slide 28
Thanks for your attention!
谢谢！