## Slide 1: The muon beamlines for the simplified scheme
Luping Zhou
2020/12/12

## Slide 2
Surface muon beam for EMuS:
Simplified-scheme / Baby-scheme design
Vertical muon beamline
Outline
EMuS

## Slide 3
surface muon
Muon from accelerator
The muSR (Muon Spin, Relaxation, Resonance...) technology based on the surface muon:
Injecting surface muons into materials
various complex environments (high temperature, high pressure, strong magnetic field, etc.)
unique advantage in the research of neutron-absorbing materials
unique advantages in the research of external field-sensitive spin glass systems, heavy Fermi systems, and quasi-crystal systems (ZF-μSR).
It is widely used in local dynamic and static magnetic field measurement of magnetic materials, and it is a powerful supplement to neutron scattering technology.
International muon sources
Pulsed type
Continuous-wave type
ISIS
J-PARC/MUSE
TRIUMF/CMMS
PSI/SμS
Development Trend of International Muon Source
EMuS

## Slide 4
ISIS
J-PARC/MUSE
PSI/SμS
TRIUMF
Pulsed type
Continuous-wave type
International Muon Sources
EMuS

## Slide 5
International surface muon beamlines
EMuS

## Slide 6
EMuS surface muon beamlines
EMuS
Baby-scheme
Baseline-scheme
2 scenarios have been designed

## Slide 7
I. Baby-scheme / Simplified-scheme
EMuS

## Slide 8
2017-2018
2019
2020
EMuS
Development

## Slide 9
24*24*2 (rotated 10 degrees) graphite target (2g/cm^3) has been employed
The trunk beamline remain unchanged
SM1 has been changed to obtain better phase spaces for “time splitting” (2.5m drift)
Modular beamline is used as terminal line (doublet*2 for transmission and phase spaces + triplet*1 for focusing)
In SM2, the beam center deviates from the optical axis due to the “space splitting”, corrections are employed
EMuS
Introduction

## Slide 10
25kW 1.6GeV proton beam: 9.766×10^13 /s
FLUKA4, Proton simulated: 1×10^11
Within the acceptance ellipses:
20<p<40: 6345
27.8<p<29.8 (Δp/p=7%): 1526 (equaling to 14.9×10^5 μ+/s)
EMuS
Acceptance / Phase spaces
25cm from the surface of the target

## Slide 11
The optical design of Trunk line remain unchanged since 2019
The momentum slits have been adjusted for the new target
Q5-entrance
Q5-exit
EMuS
Trunk line

## Slide 12
 | momentum slits settings - X [mm] |  | SM1A Beam Spot |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | fitting [mm] |  | RMS [mm] |  | FWHM [mm] |  | emittance [pi.mm.mrad] |  | flux [E+05 mu+/s] |  | pol-z | momentum [MeV/c] |  | IP^2 [E+05 mu+/s]
 | Q5f | Q5e | sigmaX | sigmaY | x | y | x | y | x | y | sample | total |  | center | FWHM | 
nocoll | -- | -- | 11.86 | 13.63 | 12.26 | 13.43 | 30 | 34 | 367 | 660 | 3.23 | 6.98 | -0.89 | 28.55 | 2.2 | 2.56
coll1 | ±60 | ±65 | 11.99 | 13.58 | 11.85 | 13.28 | 31 | 32 | 353 | 662 | 3.05 | 6.54 | -0.92 | 28.55 | 2.2 | 2.58
coll2 | ±50 | ±50 | 11.74 | 13.64 | 11.54 | 13.32 | 32 | 29 | 344 | 670 | 3.05 | 6.34 | -0.93 | 28.55 | 2.2 | 2.64
coll3 | ±80 | ±80 | 11.91 | 13.55 | 12.03 | 13.36 | 31 | 32 | 354 | 661 | 3.25 | 6.86 | -0.90 | 28.55 | 2.2 | 2.63
Comparison of different slits settings for momentum collimation
Although the beam flux on the sample is 7% less compared with other collimation settings, the “coll2” has the highest polarization rate and IP^2
EMuS
Momentum collimation

## Slide 13
SM1
SM1A
SM1B
SM2A
SM2B
SM2
SM1
SM1B
SM1A
SM2A
SM2B
SM2
EMuS
Optics

## Slide 14
Making full use of the long target
acceptance (H*V, pi.mm.mrad): 6000*3000
trunk line triplet-4
SM2
SM1
3800*4354 [π·mm·mrad]
2000*4430 [π·mm·mrad]
EMuS
Space splitting

## Slide 15
EMuS
Positrons
Positrons in SM1 beamlines will be deflected by the Wien Filter. The subsequent focusing structure and slits will scrape the remaining positrons, and no additional collimator is needed.

## Slide 16
Electric kicker, gap=20cm, E=1MV/m,
Magnetic kicker, gap=20cm, B=0.088T
In order to separate two pulses, both electric kicker and magnetic kicker have been tried.
Separation angles are same
Magnetic kicker magnet was chosen for the separation due to the large emittance.
EMuS
Time splitting

## Slide 17
SM2A
SM2B
Collimator-y
Collimator-x
π phase shifts are employed for collimations
Four sets of slits are applied for SM1A/SM1B/SM2A/SM2B to ensure that each line can tune the beam spot without affecting other lines
optics
Monto-Carlo Simulation
EMuS
Beam spots controlling

## Slide 18
SM1A
SM1B
SM2A
SM2B
EMuS
Beam spots (Ø30)

## Slide 19
 |  | rms emittance [pi.mm.mrad] |  | spot size [mm] |  | intensity [1E+05 /s] |  | polz
 |  | x | y | rms | fwhm | sample | total | 
SM1A | Ø30 | 397 | 593 | 12.49*11.26 | 33*32 | 2.83 | 5.74 | better than -0.9
 | Ø20 | 135 | 294 | 7.98*7.56 | 19*22 | 0.71 | 1.44 | 
SM1B | Ø30 | 495 | 694 | 11.90*11.37 | 33*26 | 2.23 | 4.29 | 
 | Ø20 | 360 | 475 | 9.08*8.37 | 23*21 | 0.89 | 1.99 | 
SM2A | Ø30 | 514 | 432 | 12.33*12.33 | 30*34 | 1.15 | 2.48 | ~ -0.88
 | Ø20 | 228 | 201 | 8.60*8.30 | 26*24 | 0.28 | 0.67 | 
SM2B | Ø30 | 348 | 817 | 12.48*11.67 | 34*30 | 2.09 | 4.3 | 
 | Ø20 | 238 | 458 | 8.85*8.56 | 22*22 | 0.8 | 1.9 | 
EMuS
Simplified scheme beam spots parameters
For all end stations, 2E+05 mu+/s under 25kw proton beam could be expected (FLUKA 3)

## Slide 20
Example: SM2B
SM2B Ø30: the largest emittance
Most of the particles will be lost at the entrance of the spectrometer
2A-Q7 exit
2A-sample
EMuS
Beam info in μSR Spectrometer tube

## Slide 21
EMuS
Ø30 on Target

## Slide 22
II. Vertical beamline (Baseline-scheme)
EMuS

## Slide 23
Baseline has four surface muon lines:
the vertical beam can operate independently and is not affected by other beamlines
three lines based on the main target cannot run simultaneously with decay muon beamlines
EMuS
Introduction

## Slide 24
EMuS
Phase spaces
proton
θ
dump
θ = 55°
f: fluka
g: g4beamline
and
Coordinate transformation
The phase space distributions in the two directions tends to be consistent
Vertical muon beam

## Slide 25
Limitations:
The acceptance is limited by the capture solenoid ---- the apertures of first triplet are limited to 30cm
Symmetrical achromatic dispersion cannot be used. Due to space constraints, the bending angle is 60 degrees + 30 degrees
EMuS
Optics

## Slide 26
Vertical slits for beam spot
Most of the positrons will be scraped
Defocus, the rest of positrons will lost here
EMuS
Positrons

## Slide 27
EMuS
Momentum Collimation

## Slide 28
sample
 | slits [mm] |  |  |  |  | spot size [mm] |  | flux [1E+05 /s, 25kW] |  | RMS emittance [pi.mm.mrad] | pol-z | p [MeV/c] | 
 | H-1 | H-2 | H-3 | V-1 | V-2 | RMS | FWHM | sample | total |  |  | center | FWHM
Ø30 |  |  |  | z=7900 width=±30 | z=10700 width=±30 | 10.49*11.42 | 26*29 | 1.42 | 2.57 | 282*987 | -0.94 | 28.62 | 1.88
Ø20 | z=12250 width=±35 | z=12400 width=±33 | z=12850 width=±35 | z=7900 width=±20 | z=10700 width=±20 | 7.75*8.07 | 17*19 | 0.42 | 0.92 | 143*540 | -0.96 | 28.62 | 1.88
Vertical beamline beam spots & envelopes
EMuS

## Slide 29
Baseline horizontal lines / end stations
EMuS
Decay muon beamlines
BS-SM3
BS-SM1
BS-SM2
Presentation by Yang Hong

## Slide 30
Summary
EMuS
Simplified scheme:
Both space splitting and time splitting have been employed in order to make full use of long target as well as two pulses
Four end stations could supply surface muons with the intensity of 2E+05 /s (25kW, except sm2a). The polarization could reach -0.9
SM1A&SM2A will be constructed firstly
Baseline scheme:
Vertical muon beamline:
The intensity of vertical beamline could reach ~1.5E+05 under 25kW proton beam with a thin target
The polarization could reach -0.95

## Slide 31
Thank you
EMuS

## Slide 32
backup
EMuS
SM1-momentum
Cloud mu+
Momentum bite: 13%
Large proportion cloud mu+
Wide range momentum spectrum

## Slide 33
backup
EMuS
SM1-Chromatic aberration effect

## Slide 34
backup
EMuS
束斑类型 | G4beamline中准直器位置与大小 [mm] |  |  | 束斑性质 |  |  |  |  |  | 
 |  |  |  | 束斑大小[mm] |  | 流强 (105 μ+/s) |  |  | 极化 | 
 | X | Y | 固定准直器 | 束斑RMS | 束斑FWHM | 总流强 | 圆内流强 | 正方形内流强 | 极化度 | 纯净度
30*30 | z=3300 x=210; z=3100 x=-220; z=3800 x=-225 | z=3100 y=260 y=-290 | z=1002.55 x=±50; z=1002.55 y=32 y=-68; z=3402.55 x=220 x=-230； | 11.8*10.5 | 30*28 | 5.7 | 3.2 | 3.8 | -0.73 | 87%
20*20 | z=3300 x=205; z=3100 x=-212; z=3800 x=-225 | z=3100 y=240 y=-270 | z=1002.55 x=±50; z=1002.55 y=32 y=-68; z=3402.55 x=220 x=-230； | 8.72*8.84 | 22*22 | 2.6 | 1.1 | 1.4 | -0.74 | 86%
10*10 | z=3100 x=-210 x=200; z=3300 x=205; z=3800 x=-225 | z=3100 y=205 y=-241 | z=1002.55 x=±50; z=1002.55 y=32 y=-68; z=3402.55 x=220 x=-230 | 6.1*7.7 | 10*12 | 0.63 | 0.14 | 0.18 | -0.78 | 88%

## Slide 35
backup
EMuS

## Slide 36
backup
EMuS
束斑类型 | 准直器位置及大小(mm) |  | 束斑性质 |  |  |  |  |  | 
 |  |  | 束斑尺寸 (mm) |  | 流强 (105 μ+/s) |  | RMS发射度x*y(π·mm·mrad) | 极化 | 
 | X | Y | FWHM | RMS | 总流强 | 圆内流强 |  | 极化度 | 纯净度
phi25 |  |  | 26*22 | 12.75*12.60 | 7.6 | 3.1 | 890*888 | -0.76 | 86.6%
phi20 | z=2000, -50<x<50; z=6800, -50<x<50; z=2550, x>-10 | z=2000, -50<y<50; z=6800, -50<y<50; | 20*18 | 7.79*7.15 | 2.5 | 1.4 | 454*392 | -0.77 | 87.2%
Phi15 | z=2000, -30<x<30; z=6800, -40<x<40; z=2550, x>-10 | z=2000, -40<y<40; z=6800, -40<y<40; | 16*14 | 6.49*6.02 | 1.1 | 0.6 | 248*378 | -0.78 | 88.4%
phi10 | z=2000, -20<x<20; z=6800, -40<x<40; z=2550, x>-10 | z=2000, -30<y<30; z=6800, -40<y<40; | 10*10 | 6.50*4.78 | 0.6 | 0.2 | 209*171 | -0.79 | 89.5%