## Slide 1: Status of data and MC comparison in WCDA-1
Wu hanrong, Lin Sujie, LiuWei, Guo yiqing, Hu hongbo
2021-04-25 Guang Zhou

## Slide 2
Outline
Data Sample
MC Sample
MC and data comparison
    hits level
    events level
4. Conclusions

## Slide 3
MC Sample---CORSIKA
Shower MC Code： Corsika7.640
Energy range： 0.01TeV-0.1TeV, 0.1TeV-1TeV , 1TeV-10TeV, 10TeV-100TeV,
100TeV-1000TeV
Particle type： Proton, Helium, CNO, MgAlSi, Iron
index： -2.71, -2.64 , -2.68, -2.66, -2.59
direction： 0< zenith < 60， 0 < azi < 360
energy threshold of Secondary particle ： e+-,gamma: 0.3 MeV；强子,muon：50MeV
Sample statics：
TeV | 0.01-0.1 | 0.1-1 | 1-10 | 10-100 | 100-1000
Proton | 190000000 | 6.0x1e7 | 4.6x1e7 | 7.4x1.6 | 2.6x1e6
Helium |  | 5.7x1e7 | 2.6x1e6 | 1.9x1e6 | 9.6x1e5
CNO |  | 9.0x1e7 | 4.6x1e6 | 2.7x1e6 | 8x1e5
MgAlSi |  | 9.6x1e7 | 8.6x1e6 | 2.5x1e6 | 8.8x1e5
Iron |  |  | 6.2x1e6 | 2.5x1e6 | 1.0x1e6

## Slide 4
MC Sample---G4wcda && reconstruction
Detector MC： g4wcda4.1+4.2
Area： 2000m X 2000m
Usage times： 100次
Attenuation length： 15m
PMT collection efficiency： 0.8
Reconstruction version： Rb
Noise rate： ~20kHz
Charge resolution： 0.36
Noise spectrum：

## Slide 5
Data and mc compasion
Basic hits compasion
  noise------simulation reality
  Hit signal------energy、position
  Hit time-----direction
Events compasion

## Slide 6
Date Selection
standard day:
20191122 && 20200630 (after uni-trigger)
2. Nfit>150
3. zenc<50
4. Core form Distance to center of pool < 50m

## Slide 7
Noise check of data and MC
1. Data: 20191122，noise rate ~20kHz
MC noise rate 20kHz
Residual distribution: 1ns/bin, 20*1e3*900*1e-9=1.8e-2(/eve:nts/s)  data is consistent with MC

## Slide 8
Hits comparison
-----Charge and Tchi from data and simulation
Mc and Data Inconsistensy with about ~20% (Npe>0.5)

## Slide 9
Events comparison
-----Nhit from data and simulation
Mc and Data Inconsistensy with about 10%~20% (Nhit>60)

## Slide 10
Events comparison
---direction and position from data and simulation

## Slide 11
Events comparison
----Compactness of BKG and Gamma from data and simulation

## Slide 12
Energy spectrum from crab using WCDA-1 data
From WCDA-CPC paper

## Slide 13
Events comparison
-----Nhit and compactness (uni-trigger)

## Slide 14
Events comparison
----- zen and position(uni-trigger)

## Slide 15
Energy spectrum from crab
(from Su-jie Lin’s PPT)

## Slide 16
Full Simulation
g4wcda MC code is ready(4PMTs is merged)
Mass production is in progress

## Slide 17
conclusions
The consistency of data and MC are checked from hits and events level, scaled event rate is well consistent
energy spectrum from Crab using WCDA-1 data consistent with other experiment
To do Full Simulation

## Slide 18
Cut: zenc<45 && 阵列中心<30m && nhit30 [500,800]
Rate_data = 7.4
Rate_mc = 4.5 (Gaisser)
Rate_mc = 3.8 (Horandel)
Data/MC(Gaisser) = 7.4/4.5 = 1.64
Data/MC(Horandel) = 7.4/3.8 = 1.95
画图cut:
Zenc < 45 && 阵列中心<50 m
MC整体抬高64%
Peak 处 MC比数据高约 ~30%
Scaling 前：
9.0cm光阴极时，rate比值（【60,800】）：
data/MC=1.39 （Gaisser），
data/MC=1.49（Horandel）.
Scaling 后：
Data/MC=0.84(Gaisser)
Data/MC=0.9 (Horandel)

## Slide 19
PMTR5912官方数据：
1. 赤道宽度202mm+-5
2. 光阴极不小于190mm；
3. 玻壳厚度3mm；
高博测量

## Slide 20
MC
reduce
dat