## Slide 1: Status about WCDA data reconstruction and analysis
Min Zha, Zhiguo Yao, Bo Gao, Wei Liu, Jinyan Liu, ShiCong Hu, Guanman Xiang, Yanjing Wang, Chuandong Gao
Guangzhou 2021 LHAASO general meeting

## Slide 2: outline
Data status
Reconstruction status
Some related results
Summary and outlook

## Slide 3: Timeline of WCDA
wcda-u = wcda-1+ wcda-2:
  20200312-20210228
Phase 1: ~40 KHz
  2020/03/12: nfee trigger
  ES.*P110MN40*.dat;
Phase 2: ~45 KHz
  2020/05/25: npmt trigger
  ES.*P110MND45W*.dat;
Phase 3: ~65 KHz
  2020/06/08/: pattern trigger
  ES.*.P110MC15*.dat;
  12X12 PMTs = 60 m X 60 m area trigger
Phase 4: ~ 90 KHz
  2020/11/01 - 2021/02/28
  wcda-1 cleaning + wcda-2 shielding
  Raw data: 12 T /day
Phase 5: ~ 35kHz
  2020/03/05 – now
  WCDA full array running with 1PE @20inch + 0.3 pe@8inch

## Slide 4: Reconstruction version From Mi to Me
Charge calibration data would be produced in period;
  qcal_r20200528.root
  8-inch and 20-inch PMT cross-calibration
Time calibration
  Hardware time calibration
  Offline time calibration
    tcal_20200622v2f.root
    Using CR showers to correct edge or local phenomena
  Arrival time difference between pools
  Water depth data
    Wcal_latest.root
Reconstruction procedure:
  noise filter;
  The location of shower core was determined;
  The arrival time of PMT was corrected for curvature and sampling effects;
  Shower plane fitted in plane;

## Slide 5: Time calibration from hardware
And relative QT curve measured from hardware
At this moment this group of parameters are used
WCDA-1
WCDA-2

## Slide 6: 4 kinds of output data
Original raw data
  15T： 20210226 as example
  Es*P110*.dat
Reducedata/
  noise filter data 5.2 T/day
  Es*P110*.reduced.root
  Transfer to IHEP
Sampdata/
  specific data sample around the sources(crab)
    224 G/day
  Es*P110*.samp.root
  specific sources could be added, for example Mrk421
Recdata/
  reconstruction data 940 G/day
  2 trees: wcdaevent + wcdaeventheader
  Es*P110*.rec.root
recgdata/
  potential gamma events 1.4 G/day
  Es*P110*.recg.root
reduced data: 180 ns time window
prelimary Q/P data: Nq25t30/cxpe >6 and density ratio in /out >1
Sampdata: < 7 deg
Level 1: with very limited noise, these database could be re-reconstruced within very high speed such as 1 month data can be finished within 1 day with 2000 CPUs
Sampdata: < 7 deg, it is used to tune the new code and algorithm, 1-month crab data can be finished within 2 hours.

## Slide 7: recdata .vs. recgdata 全部重建事例 .vs. 类伽马事例
Data
  20200801-20200815
/eos/daocheng/user/w/wcdarec/prod/recdata/Mi/
/eos/daocheng/user/w/wcdarec/prod/recgdata/Mi/
Cut：ndet>100,compactness>15
gamma-like event database is very easy to be transferred to everyone and everywhere!
Notes: Nq25t30/cxpe >6 && density ratio in /out >1  recgdata

## Slide 8: Full WCDA array water condition

## Slide 9: PMT efficiency

## Slide 10: Reconstruction data quality check

## Slide 11: Passing leve-1 check
if(poolused_ != 3) continue;
if(ndetused_ < 1700) continue;
if(nhit_median_ < 350) continue;
if(nhit_median_ > 450) continue;
if(theta_median_ < 0.4) continue;
if(theta_median_ > 0.5) continue;
if(phi_median_ < 3.) continue;
if(phi_median_ > 3.3) continue;
if(tlive_ > 1e5) continue;
if(xc_median_ < 10.) continue;
if(xc_median_ > 40.) continue;
if(yc_median_ > -52.) continue;
if(yc_median_ < -65.) continue;

## Slide 12: A daily Check-list in txt file
Each reconstruction file has a tag

## Slide 13: Some related results
Database: 20190401 – 20210228 @ WCDA-1 only
Version: Rb/Rc -> Me
WCDA-1 crab @202006-202102
Poinging error <0.1 deg;
Angular resolution consistent with CPC-CRAB result;

## Slide 14
201906-202002 : Rc
Crab
Mrk421
Some sourcer results see the talk given by Chuandong Gao

## Slide 15: --continued
WCDA-U (WCDA-1 + WCDA-2) database
Before detector update
Version: Mi

## Slide 16: --continued
WCDA-U (WCDA-1 + WCDA-2) 20210101- 20210131
after detector update with WCDA-2 shielding
WCDA-u 32 sigma
Nhit: 230 + C>23.
Center: (0.05, 0.02)
psf: (0.22, 0.23)
WCDA-2: 18 sigma
Nhit: >170 + C>1.7
Center: (0.01, 0.11)
psf: (0.38, 0.54)
WCDA-1: 25 sigma
Nhit: >170 + C>17
Center: (0.02, -0.02)
psf: (0.17, 0.22)

## Slide 17: Pointing error and Angular resolution@ WCDA-U
4 month: 53 sigma

## Slide 18: Moon shadow @ 202011

## Slide 19: Summary and outlook
WCDA array is entering into full array stage, with reconstruction version update, the crab observation result from individual pools is reasonable;
3 different reconstruction databases are ready.
  WCDA-1 only data from 20190401 – 20210228
  WCDA-U data without shielding 20200314 – 20201031
  WCDA-U data with shielding 20201101 – 20210304
    It is under production and will be finished within one week;
Next step
  WCDA full array data reconstructionstarting from 20210305
    8-inch and 20-inch PMT cross-calibration at charge and arrival time?
    Optimization on Angular resolution?
    Optimization on Q/P separtion?
  20 sigma /day -------------------------------- No.1 target
  Continue physics analysis on existed reconstruction database;
  Full array MC studying;

## Slide 20: backup

## Slide 21: Gamma Response Energy
Looks like individual pool has best performance around 4 TeV
联合的median energy

## Slide 22: Result from offline calibration (20201101-20201130)
WCDA-1: 20 sigma
nq05t30: >100 + C>15
Center: (0.002, -0.002)
psf: (0.24, 0.31)
WCDA-2: 18 sigma
nq05t30: >250 + C>15
Center: (0.03, -0.06)
psf: (0.31, 0.21)

## Slide 23: Pools enviormental parmaters
WCDA-1
WCDA-3
WCDA-2

## Slide 24: 2nd Correction based CR showers
WCDA-1
WCDA-2

## Slide 25
 |  |  | Nearest TeVCat Src | 
Ra [˚] | Dec [˚] | Sig | Distance [˚] | Name
184.62 | 79.75 | 5.89 | 9.94 | -
14.95 | 64.34 | 6.05 | 3.74 | -
336.86 | 60.62 | 5.93 | 0.26 | RG 106.3+02.7
308.10 | 41.31 | 7.96 | 0.15 | PSR J2032+4127
305.51 | 40.57 | 6.17 | 0.41 | VER J2019+407
166.16 | 38.11 | 23.59 | 0.10 | Markarian421
304.80 | 36.94 | 9.29 | 0.14 | VER J2019+368
83.72 | 21.94 | 47.75 | 0.10 | Crab nebula
288.63 | 10.54 | 6.45 | 0.57 | -
287.09 | 6.43 | 10.20 | 0.20 | MGRO J1908+06
287.89 | 4.71 | 5.02 | 0.40 | SS433 w1
284.37 | 2.31 | 6.91 | 0.31 | HESS J1858+020
282.39 | -1.83 | 5.96 | 1.13 | -
280.94 | -3.43 | 8.24 | 0.57 | -
280.24 | -5.15 | 6.62 | 0.70 | -
279.32 | -6.54 | 6.93 | 0.18 | MAGIC J1837-073
278.83 | -8.76 | 5.17 | 0.63 | -
276.59 | -13.52 | 6.71 | 0.34 | LS 5039