## Slide 1: PROGRESS OF LOW EMITTANCE BOOSTER DESIGN
Daheng Ji, Dou Wang
2020,12,28

## Slide 2: Outline
Review of last report
Further error study based on TME 0
Update of lower emittance booster design
Error study based on FODO 1

## Slide 3: Review of Last Report（2020.09.23）
Sawtooth effect @180GeV （ ✔ ）
Effect of earthfield @10GeV （ ✔ ）
Impacts/solution of Detector Stray Field （ ✔ ）
Dynamic simulation with errors during ramping and table ramping scheme （ ✔ ）
CDR design (FODO 0): error effect and correction of linear optics （ ✔ ）
Booster error study based on lower emittance lattice (TME 0) （ ✘）

## Slide 4: Review of last report Low emittance lattice design based on TME (0)
D. Wang, Y. M. Peng, C. H. Yu
Cell length: 110m
dis. supressor
arc cell
Straight sec.
DA optimization
Phase for arc cell
Phase for straight section
SD position
Phase for matching section
Interleave sextupole scheme
Exact geometry match for three rings
-- error=0.17m

## Slide 5: Review of last report Error effect and correction for linear optics (TME 0)
 | FODO 0 | TME 0
Emittance X (nm) | 3.57E-09 | 1.29E-9
Tunes | [263.2016/261.2193] | [319.2507/129.2806]
Quad amount | 2110 | 2528
Quad Strength (K1L rms） | 0.0383 | 0.0828
Sext amount | 512 | 2912
Sexts Strength (K2L rms) | 0.1795 | 0.1512
H Corrector | 1053 | 896
V Corrector | 1054 | 1632
BPM | 2108 | 2528
FODO 0 (CDR)
TME 0

## Slide 6: Review of last report Low emittance lattice design based on TME 0
Error set and correction process is same as FODO Lattice
Beam parameter and DA recovery not good
  Strong focusing?
  1/4 resonance?
  Correctors and BPMs arrangement?
  …
RMS | FODO 0 (CDR) | TME 0
Orbit (mm) | 0.0575/0.0525 | 0.4065/0.2389
Beta Beating(%) | 0.294/0.353 | 3.940/5.439
Delta Dispersion(m) | 0.005/0.007 | 0.0156/0.0229
FODO 0 (CDR)
TME 0

## Slide 7: Further error study based on TME 0
Correction optimization:
  Tune change
  Set H correctors on BEND
  BPM position optimization
  Dispersion function in orbit correction
  Dispersion weight in correction
  Singular value scan
  …
FODO 0 (CDR)
TME 0
RMS | FODO 0 | TME 0 | TME 0 opt.
Orbit (mm) | 0.0575/0.0525 | 0.4065/0.2389 | 0.2216/0.1784
Beta Beating(%) | 0.294/0.353 | 3.940/5.439 | 2.79/3.833
Delta Dispersion(m) | 0.005/0.007 | 0.0156/0.0229 | 0.0039/0.0052
TME 0 opt.

## Slide 8: Lower emittance booster design update
Emittance: 3.57nm  (1.29nm~1.9nm)
Coupling requirement: 0.5%  1.4%
Injection for higher lum. H mode
Off-axis injection for CDR Higgs
Difficulty transfer from Collider to booster
CDR
New-TME
New-FODO
Two kinds of low emittance lattice
TME (cell length=108m)
FODO (cell length=70m~80m)
D. Wang, Y. M. Peng, C. H. Yu

## Slide 9: TME design update (TME 1)
Combined magnet: B+Q
Emittance = 1.45 nm@120GeV
Energy spread = .00168
fine tuning is going on…
D. Wang, C. H. Yu, Y. M. Peng…

## Slide 10: Alternative design based on FODO
90/ 90 FODO cell
FODO length: 70m~80m
Noninterleave sextupole scheme
Similar structure as CDR
arc cell
dis. supressor
Straight sec.

## Slide 11: DA optimization for FODO lattice
80m FODO (emit=1.9nm)
70m FODO (emit=1.29nm)
6*FODO5,
FODO,
6*FODO5,
FODO,
6*FODO5,
FODO,
6*FODO5
45 phase in short straight section
7*FODO5,
7*FODO5,
7*FODO5,
7*FODO5
45 phase in short straight section
Before opt
Before opt
After opt
After opt
Insert proper phase section to weaken/cancel some dispersive nonlinear term – enlarge off-momentum DA
FODO 1.1
FODO 1.2

## Slide 12: Error study based on FODO 1.1
Lattice | FODO 0 | TME 0 | FODO 1
Emittance X (nm) | 3.57E-09 | 1.29E-9 | 1.29E-9
Tunes | [263.201/261.219] | [319.250/129.280] | [353.180/353.280]
Quad amount | 2110 | 2528 | 2816
Quad Strength (K1L rms） | 0.0383 | 0.0828 | 0.0407
Sext amount | 512 | 2912 | 896
Sexts Strength (K2L rms) | 0.1795 | 0.1512 | 0.4091
H Corrector | 1053 | 896 | 1408
V Corrector | 1054 | 1632 | 1408
BPM | 2108 | 2528 | 2816
w/ Correction | FODO 0 | TME 0 | TME 0 opt. | FODO 1
Orbit (mm) | 0.0575/0.0525 | 0.4065/0.2389 | 0.2216/0.178 | 0.1693/0.1236
Beta Beating(%) | 0.294/0.353 | 3.940/5.439 | 2.79/3.833 | 1.52/2.50
Delta Dispersion(m) | 0.005/0.007 | 0.0156/0.0229 | 0.0039/0.0052 | 0.0045/0.0032
The sensitivity is between FODO 0 and TME0
The correction effect is consistent with the sensitivity
DA should be further optimized

## Slide 13: Key issue
Shortage of computing resourcesAccuracy/Iteration speed/Seeds
  Memory
    ((1408(HC)+1408(VC))*2816(BPM)*2*2816(Q))*8/1024/1024/1024=332.75GB
    ((100(HC)+100(VC))*2816(BPM)*2*2816(Q))*8/1024/1024/1024=23.63GB
  Matlab
1 loop: 2~3 weeks…

## Slide 14: Summary
TME 0 was proved too sensitive and abandoned now
Lower emittance booster design updates two versions of the new design: TME 1 and FODO 1
  TME 1 is in the process of design optimization
  FODO 1 has started error simulation
    Optics/DA result is acceptable, but not good enough
Shortage of computing resources limits the progress of iteration.

## Slide 15
Thanks

## Slide 17: Low emittance lattice design based on TME （0）
Cell length: 110m
dis. supressor
arc cell
Straight sec.
DA optimization
Phase for arc cell
Phase for straight section
SD position
Phase for matching section
Interleave sextupole scheme
Exact geometry match for three rings
-- error=0.17m
D. Wang, Y. M. Peng, C. H. Yu