## Slide 1: The Collaboration with CERN Control Group
Presented by Gang Li
CEPC Day, Dec.28, 2020

## Slide 2: Collaboration has a future
CEPC: A super large scale project
Controlled device: Hundreds of thousands
EPICS PV: Tens of millions
Control system: All in control
The design of control system is iterative, with the development of technology

## Slide 3: Collaboration has a future
Hardware Platform
  COTS (commercial off-the-shelf): ATCA/uTCA, PLC, etc
  Co-developed or self-developed products: WhiteRabbit, etc
Software Platform
  EPICS
  FESA
  TANGO
  Etc

## Slide 4: Collaboration: Timing system-WR
Trigger
RF reference
Timestamp
定时系统：
产生一系列精确的时序信号，使加速器的特定设备在重复周期内按照一定的时序工作，确保束团注入到高频俘获区（bucket）内，使束流强度达到预设值。
向束流测量和谱仪亮度测量等设备发送触发信号和时钟参考信号，为数据获取，提供时间基准。

## Slide 5: Timing system: White Rabbit Fieldbus
White Rabbit materials from ：
https://indico.cern.ch/event/913576/
https://www.ohwr.org/projects/white-rabbit/wiki/overview
https://www.ohwr.org/projects/white-rabbit/wiki/jun2018meeting
CERN and GSI initiative for control & timing
Fieldbus
  Ethernet
  Determinism & Reliability
  Synchronization
Initial specs: links ≤10 km & ≤2000 nodes
Many applications worldwide
  A prototype tested in operation: <10 ps jitter, ESRF
  A prototype: <100 fs jitter and <10 ps reproducibility over reboots, CERN

## Slide 6: Ethernet
WR
node
WR
node
WR
node
WR
node
WR
node
WR
node
WR
node
WR
node
WR
node
WR
node
WR
node
WR
node
Add/ Remove nodes dynamically
WR switch
WR switch
WR switch
WR switch
WR
node
WR
node
WR
node
WR switch
WR switch: 18 ports
Bandwidth: 1 Gbps
Up to 2000 nodes
Copper or fiber medium
Up to 10 Km fiber links
WR
node
other GbE switch
other
node
other
node
other
node
Non WR devices
Timing system: White Rabbit fieldbus
Ethernet Features (VLAN) & Protocols (SNMP)

## Slide 7: Deterministic & Reliable
Reliability is the ability of a system to provide its services to clients under both routine and abnormal conditions.
Topology Redundancy
Data Resilience with Forward Error Correction schemes
Determinism is the guarantee that packet transmission delay between two stations will never exceed a certain boundary.
WR switch
WR switch
WR switch
FEC
Timing system: White Rabbit fieldbus

## Slide 8: Synchronization Offset Adjustment with Enhanced Precision Time Protocol
WR switch
System Timing Master
Timing Master
WR Switch
WR
node
WR
node
WR switch
WR switch
WR
node
WR
node
WR
node
WR
node
WR
node
Timing Master
WR Switch
PTP synchronizes the local clocks with the master clock by measuring and compensating the delays introduced by the link.
Common notion of time
Timing system: White Rabbit fieldbus

## Slide 9: White Rabbit: Trigger

## Slide 10: White Rabbit: RFoWR

## Slide 11: White Rabbit: Component

## Slide 12: White Rabbit: Component costs

## Slide 13: White Rabbit VS standard PTP

## Slide 14: Collaboration: What and Who and How
WR Switch
  COTS
WR Node
  Some of COTS
  Some of customized devices
更鼓，信科太
  WR Switch
SHINE and IMP
  Customized Node
CERN
  all
CERN and Company
  Send young people to CERN
  Participate in workshop and international meeting
  Prototype based on product from 更鼓 or 信科太
  Apply for fund

## Slide 15: Collaboration: Conference and workshop
International conference and workshop
  https://icalepcs.org/conferences.html
https://ohwr.org/project/white-rabbit/wikis/Workshops

## Slide 16: Reference
https://ohwr.org/project/white-rabbit/wikis/WRpresentations
https://www.ohwr.org/projects/white-rabbit/wiki/jun2018meeting
https://indico.cern.ch/event/913576/

## Slide 17: Summary
WR: CERN and others
EPICS：Cooperate with EPICS community
Thanks a lot!