## Slide 1
Test Beam opportunity on
Beijing Synchrotron Radiation Facility (BSRF)
YongSheng Huang (黄永盛）, Zhijun Liang (梁志均）, MengZhao Li (李梦朝）,Bo Liu(刘波)
IHEP, Chinese Academy of Sciences

## Slide 2
Motivation
  Due to pandemic, many CEPC testbeams scheduled at DESY were cancelled
  Test beam facility in IHEP Hall 10 can be alternative option
  However Limited by event rate, and operation time (~2 months per year)
  Beijing Synchrotron Radiation Facility (BSRF) stations can be alternative
  Out-of-phase electrons may go through BSRF station
  Advantage of BSRF:
  Long operation period (~10 months per year)
  Potential to have high event rate and high energy electrons
Electron orbit

## Slide 3
Setup at BSRF Station
  1B3 station (18m away from BEPC ring)
  1W2B station(~30m away from BEPC ring)
  4W1A station (40m+ away from BEPC ring)
Setup at 1B3 station
Setup at 4W1A station

## Slide 4
Detector at BSFC testbeam
IHEP-IME
2×2 LGAD
HPK 5×5 LGAD
Single channel readout
  Three detectors are used, data taking with Oscilloscope
   One IHEP-IME 2×2 LGAD. Area: 3mm×3mm, time resolution: 39ps
  Two HPK 5×5 LGAD. Area: 6.5mm×6.5mm, time resolution: 60-70ps
  One HPK 15×15 LGAD. Area: 20 mm ×20 mm, low signal level
HPK 5*5
HPK 5*5
IHEP-IME
2*2 LGAD
Beam
(X ray
/electrons?)
17mm
17mm

## Slide 5
IHEP-IME 2×2 LGAD
HPK 5×5 LGAD
HPK 5×5 LGAD
Detector signal at BSFC testbeam
  Two type of signal: Coincidence and non-coincidence events
Typical Coincidence events
(Coincidence signal
in 2~3 LGAD detectors)
Typical non-coincidence events
(signal only in 1 LGAD
no signals for others LGADs )
IHEP-IME 2×2 LGAD
HPK 5×5 LGAD
HPK 5×5 LGAD
  high rate , Period: ~6ns
  Consistent with BEPC cycle
6ns

## Slide 6
Detector signal at BSFC testbeam
2 MIP
Beta tests
Collected charge of Coincidence signal
consistent with MIP signal in beta test
6keV X ray
BSRF
IHEP-IME LGAD
IHEP-IME LGAD
BSRF
Beta test
Collected charge of non-Coincidence
Similar to 6keV X ray

## Slide 7
Trigger rate
  Triggering on IHEP-IME LGAD (upstream detector)
  Adding more layers of steel to absorb X ray
  Trigger rate decrease, and then became stable at ~50Hz/cm2
  Coincidence events ratio increased
HPK
HPK
IHEP-IME LGAD
Beam
(X ray
/electrons?)
17mm
17mm
Steel
2 LGAD coincidence ratio
3 LGADs coincidence ratio
Steel thickness(mm)
Steel thickness(mm)
Trigger on IHEP-IME LGAD

## Slide 8
BSRF Station | 1B3 | 4W1A
Coincidence events rate （Hz/cm2） | ~50 | ~1.5 Hz/cm2
Distance to BEPC ring (meter) | 18 | ~43
Event rates
  Coincidence events rate (MIP-like event rate) is higher in station closer to BEPC ring

## Slide 9
Time of flight– identifying MIP-like particle
HPK 5*5
IHEP-IME
2*2 LGAD
beam
28.3cm
Steel
  In coincidence events, what is MIP-like particle ?
  Is that low momentum proton or pion (secondary particles) ?
  Or high energy electrons ?
Measured flight time=936 ps, σt=97ps
Expected flight time = 943 ps
Consistence with speed of light （electron like)
Exclude proton below 1GeV
Exclude pion below 0.2 GeV
Distance
=28.3cm

## Slide 10
Beam profile
  Beam spot size:~0.5cm * 5cm (estimated from burn mark )
  Beam spot size is consistent with of the shutter shape
Shutter in 1B3 station
Burn mark in 1B3 station

## Slide 11
Potential of using 1B3b station for detector test beam
  1B3a was used for XRD spectrum (material structure study)
  1B3b is now borrowed temporarily
  Test beam potential study (last week)
  Accelerator colleague will use 1B3b for next 1~2 months for vacuum study （插入件在X辐照下放气实验）
  Has potential to build test beam facility for longer term at 1B3b
  Use CEPC vertex detector chips to build beam telescope
  Build a magnetic to sperate X ray from electron beams, also measure the momentum of electrons
1B3a
1B3b
1B3a
1B3b

## Slide 12
Summary
  Found MIP-like particles in three BSRF stations (likely to be high energy electrons)
  The largest MIP-like event rate is about 50Hz/cm2
  BSRF stations has potential to become a good test beam facility

## Slide 13
 | DESY | IHEP Hall 10 E3 beam line | BSRF
Momentum | 1-6 GeV | <1 GeV secondary beam | 1~2.5 GeV (to be measured)
Particles | electrons | Protons/ Pions/ /Electrons | Electrons ? (to be confirmed)
Trigger rate | 250Hz/cm2 --4000 Hz/cm2 | 0.6 Hz/cm2 (design) <0.1 Hz/cm2 (measured) | ~50 Hz/cm2
Operation period | ~10 months/ year | ~2 months/ year | ~10 months/ year
Beam spot Size | 4cm2 | ~80cm2 | ~2.5cm2 Depending on shutter shape
Comparisons

## Slide 14
Coincidence signal at BSFC test beam
IHEP-IME 2*2 LGAD
HPK 5*5 LGAD
BSRF
Beta test
BSRF
Beta test
2 MIP ?
Collected charge of Coincidence signal
consistent with MIP signal in beta test
2MIP like signal in large area LGAD
HPK
HPK
IHEP-IME LGAD
Beam
17mm
17mm
Steel

## Slide 15
Non-Coincidence signal at BSFC test beam
HPK
HPK
IHEP-IME LGAD
Beam
17mm
17mm
Steel
Collected charge of non-Coincidence
First peak is similar to 6keV X ray
The origin of the second peak is unknow, it disappeared after putting more Steel
Similar to
6keV X ray
IHEP-IME 2*2 LGAD

## Slide 16
DESY test beam facility

## Slide 17
IHEP Hall 10

## Slide 18
Timing resolution in beta test
  IHEP and Beijing Normal U. developed IHEP-NDL LGAD sensors
   Can reach 25 pico-second(ps) , similar performance compared to HPK sensors
  IHEP and Institute of micro-electronics (IME) developed IHEP-IME sensors
   IHEP team (Mei Zhao …) designed, IME fabricated
CEPC timing detector : R & D status
IHEP-NDL sensor
IHEP-IME sensors
8 inch wafer

## Slide 19
CEPC timing detector :IHEP Test beam 2020
  Timing detector team (3 postdocs and 4 students) participate IHEP test beam
   Tuning the beam, taking shifts, commissioning the detectors
  Postdoc: Bo Liu, Yunyun Fan, Xuan Yang
  Students: Mengzhao Li, Shuqi Li, Han Cui, Chengjun Yu

## Slide 20
Outlook: Testbeam with ATLAS HGTD module
Time resolution: 45ps
Position resolution: ~1mm
Area : 6.5mm*6.5mm --> (2cm*4cm)

## Slide 21
Detector signal at BSFC testbeam
  Collected charge in non-coincidence signal is consistent with ~10keV X ray signals
  Collected charge in coincidence signal events is consistent with MIP signal in beta test
  Found two-MIP like signal in HPK LGAD in BSRF beam tests
  Two MIP particles hitting one LGAD detector at the same time ?
2 MIP
BSRF
tests
Beta
tests