## Slide 1: FPGA Helix Tracking Algorithm with STT
Wolfgang Kühn, Yutie Liang, Zhen’an Liu
Jingzhou Zhao
IHEP Beijing, IMP Lanzhou, Uni-Giessen
29.12.2020

## Slide 2
Outline
1. Introduction
2. Tracking Algorithm
T0 extraction from tracking
Tracking at FPGA
5. Summary and Outlook

## Slide 3
Introduction to the PANDA STT
4636 Straw tubes
23-27 planar layers
15-19 axial layers (green) in beam direction
4 stereo double-layers for 3D reconstruction,
with ±2.89 skew angle (blue/red)
From STT : Wire position + drift time

## Slide 4
Tracking Algorithm -- Road Finding
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Tube_ID
Layer_ID
Hit: Seg_ID (3 bits) + LayerID (5 bits) + Tube_ID (6 bits) + Arrival time
1: Start from inner layer
2: Attach neighbour hit to tracklet layer by layer
Boundary between two segments.
Number of neighbor:
4 in axial layer; 6 in stereo layer

## Slide 5
Known : xi , yi , di
Question: To determine a circle,
x2 + y2 + ax + by + c = 0
Method: Minimize the equation
E2 = ∑(xi2 + yi2 + a xi+ b yi + c)2 (1/di)2
Sx = ∑xi …
Sxx = ∑xixi …
Sxxx = ∑xixixi …
Tracking Algorithm -- helix parameters calculation
1) Circle para.
2) Track quality.
x
y
xc, yc, R

## Slide 6
Pz reconstruction
1: The radius, the position of the helix center in the XY plane are determined.
2: Φ = kZ + Φ0
z
y
x
One cylinder the helix lies in.
Based on Pt determined before
One straw tube
Track need to be tangent to the crossing ellipse.
Crossing points
(ellipse)
Gianluigi Boca and Panda Collaboration, Panda STT TDR, 2012

## Slide 7
Known : zi , Φ i , di
Question: To determine a line,
Φ + kz + Φ0= 0
Method: Minimize E2 = ∑(Φi + kzi + Φ0)2 (1/di)2
Pz reconstruction

## Slide 8
Extract T0 from Tracking
T0 shifted by:
-50 ns:
-20 ns:
10 ns:
20 ns:
Extracted T0:
-47.0±4.0 ns
-19.8±2.1 ns
9.4±2.5 ns
19.0±2.3 ns
T0 shift = Ʃdi /N / const (N: number of hits
di: signed distance of circle to track)

## Slide 9
Tracking Strategy with experimental data -- 20 MHz
Hits are sorted according to their arrival time.
In case of T0 provided:
Start from T0  Collect hits in 220 ns window 
Run tracking algorithm  Assign track to right event
In case of T0 not provided:
Do tracking and T0 extraction at the same time

## Slide 10
Tracking Strategy with experimental data -- Phase I
Hits are sorted according to their arrival time.
In case of T0 provided:
Start from T0  Collect hits in 220 ns window 
Run tracking algorithm  Assign track to right event
In case of T0 not provided:
Take the earliest time of a segment of hit as T0 .  do one more iteration to optimize.

## Slide 11
11
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
9.0
0.0
#0 T0 = 9.0 ns
#1 T0 = 35.7 ns
#1 T0 = 95.3 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
9.0
0.0
37.2
9.4
#0 T0 = 37.2 ns
#1 T0 = 9.4 ns
#1 T0 = 98.3 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
9.0
0.0
37.2
114.5
9.4
38.2
#0 T0 = 38.2 ns
#1 T0 = 114.5 ns
#1 T0 = 115.3 ns
#1 T0 = 128.0 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
0.0
37.2
114.5
140.9
116.6
9.0
9.4
38.2
#1 T0 = 116.8 ns
#1 T0 = 116.6 ns
#1 T0 = 119.0 ns
#1 T0 = 140.9 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
0.0
37.2
115.3
9.0
9.4
38.2
114.5
140.9
141.1
150.9
8.4
35.9
114.1

## Slide 12
PC as data source and receiver.
Ethernet.
Optical link
FPGA
FIFO
Tracking algorithm
Ethernet via
Optical Link
Setup and Test
FIFO

## Slide 13
Performance at FPGA
For one event with 100 hits (6 tracks): 7 μs
Hit reading
Road finder
Pt extraction
Pz extraction
(100 cc)
(50 cc X 6)
(120 cc X 2 X 6)
(60 cc X 2 X 6)

## Slide 14
Tracking at FPGA
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 15
Performance test

## Slide 16
Summary and Outlook
σ_pt : ~ 3.2% σ_pz : ~ 4.2% .
7 μs/event (6 tracks)
Tracking strategy in case of W/O T0.
From Virtex 4 to Kintex 7 in future.

## Slide 17
Thank you

## Slide 18
自触发前端电子学及数据推动结构
时钟分配系统 – 全局时间戳对齐事例
Level 1 (L1) 网络层–由高性能计算节点组成，运行丰富的特征提取算法。提取径迹级别物理信息，如动量、能量、粒子类别。
Level 2 (L2) 网络层– 利用L1网络层输出进行高层次信息提取，抽取事例级别的物理信息，如母粒子的质量，用以压低本底。
项目研究内容—无硬件触发数据获取系统
梁羽铁

## Slide 21
The Latency

## Slide 22
20 MHz
1600 ns revolution time
400 ns gap
TMean between 2 events: 50 ns
Drift time: ~200 ns
Event Structure -- pile-up
Event pile-up

## Slide 23
Block diagram of algorithm in VHDL

## Slide 24
Performance test
24
N_gen: number of generated tracks
with at least 3 hits in STT
|P_rec - P_gen| < 6 sigma

## Slide 25
Performance at different event rate
25
Number of fake tracks per event increases at high event rate.

## Slide 26
Square Root Operation
C++ VHDL
Xc: 0.7286 0.7278
Yc: 161.153 161.138
R: 161.155 161.167 (0.01%)
Zi:
C++ VHDL
29.4 ±5.0 29.23 ±5.1
17.0 ±8.1 16.93 ±8.1
384 bins in the range of 1 ~ 4, error ~ 0.4%
Linear extrapolation, precision improves
z(cm)
Φ

## Slide 27
The Missing Event at Event-based simulation
Tracks in this event are not well reconstructed.
In this case, it is hard to extract a T0.
27

## Slide 28
Tracking at FPGA -- 20 MHz
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 29
Tracking Strategy
1) Start from 0
2) hits in 220 ns window
3) run tracking algorithm
4) extract T0 of next event
5) go back to 2)
Two time-based simulations:
1 GeV single muon
DPM
HK 22.7
8.4
35.9
114.1

## Slide 30
Performance at FPGA
For one event with 100 hits (6 tracks): 7 μs
Hit reading
Road finder
Pt extraction
Pz extraction
(100 cc)
(50 cc X 6)
(120 cc X 2 X 6)
(60 cc X 2 X 6)
HK 22.7

## Slide 31
#0 T0 = 8.3 ns
#2 T0 = 31.7 ns
#1 T0 = 28.0 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
8.3
0.0
#0 T0 = 8.5 ns
#2 T0 = 34.6 ns
#1 T0 = 36.3 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
8.3
0.0
34.6
8.5
#0 T0 = 9.7 ns
#2 T0 = 35.9 ns
#1 T0 = 112.4 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
8.3
0.0
34.6
112.4
8.5
35.9
#1 T0 = 128.0 ns
#1 T0 = 137.2 ns
#1 T0 = 146.1 ns
#1 T0 = 127.2 ns
#0 T0 = 65.7 ns
#1 T0 = 116.0 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
8.3
0.0
34.6
112.4
128.0
116.0
8.5
35.9
#1 T0 = 138.4 ns
#0 T0 = 67.8 ns
#1 T0 = 116.6 ns
#1 T0 = 128.0 ns
#1 T0 = 147.4 ns
#1 T0 = 158.1 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
8.3
0.0
34.6
112.4
128.0
116.0
128.0
138.4
8.5
35.9
#1 T0 = 128.1 ns
#1 T0 = 147.4 ns
#1 T0 = 167.0 ns
#1 T0 = 139.2 ns
#0 T0 = 97.0 ns
#1 T0 = 117.1 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
8.3
0.0
34.6
112.4
128.0
116.0
128.0
138.4
139.2
147.4
8.5
35.9
HK 22.7

## Slide 32
To Improve the Momentum Resolution -- using a 2nd iteration
Pt(input) 1st iteration 2nd iteration
0.2GeV/c : 0.195 ±0.0068 0.195±0.0068
0.5GeV/c : 0.5 ±0.0212 0.5 ± 0.0164
1.0GeV/c : 0.99 ±0.0595 1.0 ± 0.0317
2.0GeV/c : 1.85 ±0.213 2.0 ± 0.073
Pt(GeV/c)
Pt(GeV/c)
1st iteration
2nd iteration
x
y
xc, yc, R

## Slide 33
5
4
8
6
7
2
3
1
..
..
..
9

## Slide 34
PZ reconstruction

## Slide 35
Pz reconstruction
1: The radius, the position of the helix center in the XY plane are determined.
2: Φ = kZ + Φ0
z
y
x
One cylinder the helix lies in.
Based on Pt determined before
One straw tube
Track need to be tangent to the crossing ellipse.
Crossing points
(ellipse)
Gianluigi Boca and Panda Collaboration, Panda STT TDR, 2012

## Slide 36
Pz reconstruction
Known : zi , Φ i , di
Question: To determine a line,
Φ + kz + Φ0= 0
Method: Minimize E2 = ∑(Φi + kzi + Φ0)2 (1/di)2

## Slide 37
Pz reconstruction
Pt = 0.5 GeV/c
Pz(input)
0.25 GeV/c : 3.7 %
0.50 GeV/c : 4.0 %
1.00 GeV/c : 4.3 %
Pt = 1.0 GeV/c
Pz(input)
0.5 GeV/c : 3.1 %
1.0 GeV/c : 3.8 %
2.0 GeV/c : 4.2 %
Pt = 2.0 GeV/c
Pz(input)
1.0 GeV/c : 3.7 %
2.0 GeV/c : 4.8 %
4.0 GeV/c : 5.2 %