## Slide 1: Introduction of new TME booster lattice
Ji Daheng, Wang Dou
On behalf of CEPC AP group
CEPC day, IHEP, Jan. 22th, 2021

## Slide 2
 | Higgs (CDR) | Higgs
Number of IPs | 2 | 2
Energy (GeV) | 120 | 120
Circumference (km) | 100 | 100
SR loss/turn (GeV) | 1.73 | 1.8
Half crossing angle (mrad) | 16.5 | 
Piwinski angle | 3.48 | 4.87
Ne/bunch (1010) | 15.0 | 16.3
Bunch number | 242 | 214
Beam current (mA) | 17.4 | 16.8
SR power /beam (MW) | 30 | 30
Bending radius (km) | 10.7 | 10.2
Momentum compaction (10-6) | 11.1 | 7.34
IP x/y (m) | 0.36/0.0015 | 0.33/0.001
Emittance x/y (nm) | 1.21/0.0024 | 0.68/0.0013
Transverse IP (um) | 20.9/0.06 | 15.0/0.037
x/y/IP | 0.018/0.109 | 0.018/0.115
VRF (GV) | 2.17 | 2.27
f RF (MHz) (harmonic) | 650 (217500) | 
Nature bunch length z (mm) | 2.72 | 2.25
Bunch length z (mm) | 4.4 | 4.42
Energy spread (%) (SR/BS) | 0.1/0.134 | 0.1/0.19
Energy acceptance requirement (%) | 1.35 | 1.7
Energy acceptance by RF (%) | 2.06 | 2.5
Lifetime due to beamstrahlung (min) | 80 | 41
Lifetime (min) | 25 | 21
F (hour glass) | 0.89 | 0.88
Lmax/IP (1034cm-2s-1) | 2.93 | 5.0
CEPC high lum. Higgs parameters
Horizontal DA requirement of collider ring due to injection
X. H. Cui

## Slide 3: Booster lattice design based on TME （TME0）
Cell length: 110m
dis. supressor
arc cell
Straight sec.
DA optimization
Phase for arc cell
Phase for straight section
SD position
Phase for matching section
Interleave sextupole scheme
Exact geometry match for three rings
-- error=0.17m
D. Wang, Y. M. Peng, C. H. Yu

## Slide 4: Error effect and correction (TME 0)
 | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | 100
Longitudinal shift Z (μm) | 100 | 150 | 100
Tilt about X/Y (mrad) | 0.2 | 0.2 | 0.2
Tilt about Z (mrad) | 0.1 | 0.2 | 0.2
Nominal field | 1e-3 | 2e-4 | 3e-4
 | Accuracy (m) | Tilt (mrad) | Gain | Offset w/ BBA(mm)
BPM(10Hz) | 1e-7 | 10 | 5% | 30e-3
 | FODO 0 (CDR) | TME 0
Emittance X (nm) | 3.57E-09 | 1.29E-9
Tunes | [263.2016/261.2193] | [319.2507/129.2806]
Quad amount | 2110 | 2528
Quad Strength (K1L rms） | 0.0383 | 0.0828
Sext amount | 512 | 2912
Sexts Strength (K2L rms) | 0.1795 | 0.1512
H Corrector | 1053 | 896
V Corrector | 1054 | 1632
BPM | 2108 | 2528
Error correction process is almost same as CDR
Orbit correction
Optics correction with dispersion control
RMS | FODO 0 | TME 0 | TME 0 opt.
Orbit (mm) | 0.0575/0.0525 | 0.4065/0.2389 | 0.2216/0.1784
Beta Beating(%) | 0.294/0.353 | 3.940/5.439 | 2.79/3.833
Delta Dispersion(m) | 0.005/0.007 | 0.0156/0.0229 | 0.0039/0.0052

## Slide 5: Error sensitivity- Bare Lattice+Q Shift 3um &1um

## Slide 6: TME design update (TME 1)
Overall idea: uniform distribution for the Q
Combined magnet: B+Q, B+S
Emittance = 1.45 nm@120GeV
Energy spread = .00168
p = 2.21×10-5
Interleave sextupole scheme
Phase advance/cell: 100/28
D. Wang, C. H. Yu, Y. M. Peng…
B+S
TME 0
TME 1

## Slide 7: Booster parameter update based on TME
Injection
Extraction
Consistent with new CEPC high lum. parameter at 4 energy modes.

## Slide 8: DA comparison
DA tracking by SAD.
FODO0 (CDR)
FODO 1.2
TME 0
TME 1
3.56nm
1.29nm
1.3nm
1.45nm
1.9nm
FODO 1.1

## Slide 9: Error effect and correction (TME1)
Less Q and S
Lower power consumption for Q and S
Lower error sensitivity
Lattice | FODO 0 （CDR） | FODO 1 | TME 0 | TME1
Emittance X (nm) | 3.57 | 1.29 | 1.29 | 1.44
Tunes | [263.201/261.219] | [353.180/353.280] | [319.250/129.280] | 230.231/87.181
Quad amount | 2110 | 2816 | 2528 | 1090+1440(B+Q)
Quad Strength (K1L rms） | 0.0383 | 0.0407 | 0.0828 | 0.0190
Sext amount | 512 | 896 | 2912 | 1440+1440(B+S)
Sexts Strength (K2L rms) | 0.179 | 0.4091 | 0.1512 | 0.02
H Corrector | 1053 | 1408 | 896 | 898
V Corrector | 1054 | 1408 | 1632 | 1632
BPM | 2108 | 2816 | 2528 | 2530

## Slide 10: Error sensitivity- Bare Lattice+Q Shift 3um &1um TME 0 vs TME 1
TME 1 error sensitivity much better than TME 0

## Slide 11: Error effect and correction (TME1)
RMS | FODO 0 (CDR) | FODO 1 | TME 0 opt. | TME1
Orbit (mm) | 0.0575/0.0525 | 0.1693/0.1236 | 0.2216/0.178 | 0.156/0.077
Beta Beating(%) | 0.294/0.353 | 1.52/2.50 | 2.79/3.833 | 0.0274/0.102
Δ Dispersion(m) | 0.005/0.007 | 0.0045/0.0032 | 0.0039/0.0052 | 0.00055/0.011
Most of Orbit/Optics correction effect is very good
The correction result of vertical dispersion is not good, which can be solved by parameter optimization
DA tracking is still in progress,

## Slide 12: Summary
New TME design (TME 1) booster reduces the number of independent magnets by using combined magnets.
Improves the uniformity of component distribution and reduces the strength of Q&S
Error sensitivity and simulated correction analysis show excellent robustness
The results of more seeds and DA Tracking are still in the calculation, and we hope to further determine the advantages of TME structure
The results of further design optimization are still in progress