## Slide 1
Status from the LDT simulation
03/22/2021
Ryuta

## Slide 2
Geometry Setting
・Barrel part : “default”
unless specified.
・Z max value
Ω[sr] = 2p(1-cos(q))
Using a formula:
Ω/4p = (100-80%)/2  cos(q)=0.8  Zmax=1800mm/tan(q) = 2400 mm
solid angle of a cone with half-angle q
・Radiation length value input
-- Coverage (of barrel part) ~ 80%
-- Change to 0.00001752 (X/X0/cm) for He:C3H8=6:4, as discussed during last Friday’s discussion

## Slide 3
Momentum resolution
・R1.8m <-> R1.5m
-- for R1.5m, DCH: 300-1500mm, 10cm cell size, 120layers. SET position is also shifted as well. (IV)
・R1.8m:
-- Change the Rmin-Rmax of DCH, while the others including SITs settings are kept the same. (I)
-- Change the Rmin-Rmax of SIT, with DCH (Rmin = 900 mm, Rmax = 1800mm ) (II)
-- Change the Rmin-Rmax of SIT/DCH (III)

## Slide 4
Momentum resolution (I)
-- Only change the range of DCH
 | DCH R
Black | 300-1800 mm
Red | 600-1800
Breen | 900-1800

## Slide 5
Momentum resolution (I’)
-- Only change the range of DCH
but cut from the outer side
 | DCH R
Black | 300-1800 mm
Red | 300-1500
Breen | 300-1200

## Slide 6
Momentum resolution (II)
-- Keep Rmin of DCH as 900mm
-- Change the range of SITs
 | SIT R
Black | 78-298 mm
Red | 78-598
Breen | 300-898

## Slide 7
Momentum resolution (III)
-- Change both of SIT/DCH
 | SIT R
Black | 78-298 mm, DCH:300-1800
Red | 78-598, DCH:600-1800
Breen | 300-898, DCH:900-1800

## Slide 8
Momentum resolution (IV)
-- Change to R=1500mm
R=1500mm
R=1800mm
Would need to check the dependency of SET position, as well as this results.

## Slide 9
Next
・ Number of hits layers vs injection angle ( cos(q) )
・ Effect of Gas mixture ratio (as shown in last slide by Lizi )
・ Comparison of “a”, “b” terms, with different setup (i.e. R1.5m)
・ Something others, such as SET position dependence.