## Slide 1: Progress of prototype of electrostatic separator for CEPC Bin Chen CEPC MOST2 Project 2021 Annual Meeting (Apr 22) 2021

## Slide 2: Outline
  Prototype development of electrostatic separator
    Design improvements
    Manufacturing process
    Installation process
    Precision High Voltage Power Supply
    Factory test
  Next plan
  Summery

## Slide 3
Prototype development of electrostatic separator
  A separator unit including: 1. Vacuum chamber (5 straight through chambers, 2 cone tubes and 2 pump chambers); 2. a pair of electrodes; 3. 2 ground electrodes; 4. 4 groups of insulation metal-ceramic support; 5. 4 groups of high voltage feedthrough; 6. 2 sets of vacuum system (including ion pump, sublimation pump and gauge); 7. support platform.
  structure drawing of Electrostatic Separator

## Slide 4: Prototype development of electrostatic separator
  Design improvements

## Slide 5: Prototype development of electrostatic separator
  Coolant loop in electrode plate
In order to improve the cooling efficiency, the cooling circuit of the plate was improved.
Two groups of high voltage feedthrough are added.
The coolant feed pipe and high voltage feed pipe adopt the same pipe. Coolant comes in at one end and goes out at the other.

## Slide 6: Prototype development of electrostatic separator
  HV metal-ceramic support
  The ceramic parts are made of 95% alumina ceramics.
  The ceramic ends are metallized , and the pure titanium flanges are welded for fixation, which has the advantage of high mechanical strength.

## Slide 7: Prototype development of electrostatic separator
  HV metal-ceramic support
  The electric field design of ceramic-metal-vacuum triple point is the key point.
  The electric field on the edge of the electrode is less than 80kV/cm, which belongs to the safe range in vacuum.
R13.87

## Slide 8: Prototype development of electrostatic separator
  HV metal-ceramic support
  The electric field of the triple point is less than 70kV/cm, which is belongs to the safe range. According to general experience, the average field intensity of flashover in atmosphere is about 3kV/cm, and it is greater than this value in vacuum. We take the insulation distance of ceramic surface as 50cm, which can reach 150kV.
Vacuum
UHV tank
（metal）
Triple point
Ceramic
Metal

## Slide 9: Prototype development of electrostatic separator
  High voltage feedthrough
  The insulating part is made of alumina ceramic, both ends are metallized, and the sleeve is sealed with pure titanium flange.
  The coolant loop is machined on the main electrode for adequate cooling.

## Slide 10: Prototype development of electrostatic separator
  High voltage feedthrough
  The maximum electric field (@±135kV) appears on the edge of the electrode, which is less than 80kV/cm. The electric field at the triple point is less than 78kV/cm, which is safe in vacuum. Ceramic surface creepage distance is also in the safe range.

## Slide 11: Prototype development of electrostatic separator
  Manufacturing process - UHV tank
  The vacuum chamber is polished and the leak detection is completed

## Slide 12: Prototype development of electrostatic separator
  Manufacturing process – Electrode
  Titanium rod
main electrode plate
Ends of electrode
Titanium mounting flange

## Slide 13: Prototype development of electrostatic separator
  Manufacturing process – Electrode
Electrode probe
  Electrode probe outside insulated sleeve (Teflon)

## Slide 14: Prototype development of electrostatic separator
  The welding procedure – Electrode
  Welding the electrode probe with the installation flange, and check for leakage after welding.
  The installation flange with probe is welded to the cover of the electrode plate.

## Slide 15: Prototype development of electrostatic separator
  The welding procedure – Electrode
  The installation flange of supports is welded to the cover of the electrode plate.
  The main electrode plate and the cover are welded together, leakage detection.

## Slide 16: Prototype development of electrostatic separator
  The welding procedure – Electrode
  The main electrode plate was welded with the titanium rod.
  The curved plate at both ends of the electrode is welded to the titanium rod, and the angle of the curved surface is corrected after welding.

## Slide 17: Prototype development of electrostatic separator
  The welding procedure – Electrode
  The curved plate at both ends is welded with the main electrode plate, and corrected after welding.
  The whole electrode plate is polished

## Slide 18: Prototype development of electrostatic separator
  The welding procedure – Electrode
  The main electrode plate and the cover plate was welded together, then leak detection and water pressure test.

## Slide 19: Prototype development of electrostatic separator
  The welding procedure – Electrode
  The main electrode plate was welded with the titanium rod
  The electrode probe was welded to the mounting flange on the main electrode plate and the leak detection was performed.

## Slide 20: Prototype development of electrostatic separator
  Ceramic processing
  Ceramic processing is a major problem encountered in this project, and it is also the main factor leading to the delay of the project schedule.
  The ceramic sintering, glazing, metallization and welding of the support parts were carried out smoothly.

## Slide 21: Prototype development of electrostatic separator
  high voltage /coolant feedthrough ceramic column processing encountered many problems
  (1) cracking: Ceramic root cracking occurs in the process of sintering, After many tests, sintering success.
  (2) drop the glaze: Ceramics deglaze in the process of glazing.
  (3) welding: after ceramic metallization, there is leakage after welding with titanium ring. After modifying the titanium ring, the welding is successful.

## Slide 22: Prototype development of electrostatic separator
  Installation process
  Because the space in the vacuum chamber is very small. There are many components to be installed inside and the structure of the components is complex. So the overall installation of the equipment needs extra care. The installation steps are as follows:

## Slide 23: Prototype development of electrostatic separator
  Installation process
  1. Install main electrode plate 1, adjust and fix the position of the main electrode plate 1, as shown in the figure

## Slide 24: Prototype development of electrostatic separator
  Installation process
  2. The cavity body is reversed 180°, the main electrode plate 2 is installed, adjust and fix the position of the main electrode plate.

## Slide 25: Prototype development of electrostatic separator
  Installation process
  3. The overall cavity is reversed by 180°, and the position of the electrode plate 1 is adjusted and fixed.

## Slide 26: Prototype development of electrostatic separator
  Installation process
  Main Plate mounting bracket and moving trolley
Chamber rotary tooling

## Slide 27: Precision High Voltage Power Supply
Including : two HV supplies of maximum 150kV– one positive and one negative polarity.
Voltage margin for conditioning
An imported high-voltage power supply was ordered in November 2019.
A domestic high voltage power supply was ordered in March 2020.
 | Unom | Inom | Residual ripple | Stability
Heinzinger import | 150kV | 1.5mA | 1ⅹ10-4 | 1ⅹ10-4
Wisman domestic | 150kV | 4mA | 1ⅹ10-4 | 1ⅹ10-4

## Slide 28: Precision High Voltage Power Supply
  To generate the high voltage, the rectified mains voltage is converted to rectangular alternating current of approx. 20 kHz and fed into a high-voltage transformer. Afterwards the voltage is multiplied and rectified in a subsequent multi-stage converter cascade. The generated high voltage is corrected in a high-voltage filter.
Topology of high voltage power supply

## Slide 29: Precision High Voltage Power Supply
威思曼分压器RVD

## Slide 30: Precision High Voltage Power Supply

## Slide 31: Precision High Voltage Power Supply

## Slide 32: Prototype development of electrostatic separator
  Factory test

## Slide 33: Prototype development of electrostatic separator
  Factory test
  System vacuum leak detection
vacuum leakage rate ≤2x10-13Pa.m3/s

## Slide 34: Prototype development of electrostatic separator
  Factory test
  The system was vacuum baked for a week (up to 150 ℃)

## Slide 35: Prototype development of electrostatic separator
  Factory test
  The system was vacuumed after baking
vacuum pressure: 1.3x10-8Pa

## Slide 36: Prototype development of electrostatic separator
  Factory test
  High voltage test
  The voltage was increased to 108kV. Due to the arc occurred at the air side of feedthrough, two power supplies failed to use. The damaged power supplies have been returned to the factory for repair

## Slide 37: Prototype development of electrostatic separator
  Factory test
  Reason: 1. The insulation performance decreases due to the high air humidity (70%) of the test site; 2. The ceramic surface is polluted during assembly, resulting in a decline in insulation performance.
  Improvement scheme : 1. Carry out cleaning and sandblasting of ceramic parts; 2. carve annular groove on the outer surface of ceramic parts to increase the creepage distance; 2. Electrode probe is coated with insulation bushing and sealed to block the creepage path on the air side of the HV feedthrough.

## Slide 38: Prototype development of electrostatic separator
  Factory test results
 | Parameters | Target | Test results
1 | vacuum leakage rate | ≤1x10-10Pa.m3/s | 2×10-13Pa·m3/s
2 | Nominal vacuum pressure | ≤5x10-8Pa(烘烤后) | 1.3×10-8Pa 3.9×10-8Pa
3 | Maximum conditioning voltage | ±135KV，稳定工作8小时无故障打火，真空度≤5x10-8Pa | －108KV ＋97.6KV

## Slide 39
  Project next plan
  After the improvement by Feedthrough, the separator will be delivered to the IHEP for testing.
The electrostatic separator will be further experimented with high voltage, and the cooling system and high order mode absorption will be optimized.
Finally, finishing high voltage testing of the prototype, to achieve the final indicators.

## Slide 40
Summary
  Improved the cooling loop of the electrodes.
  The structure of the insulation metal-ceramic support and of high voltage feedthrough is optimized and the electric field simulation is carried out.
  All the components of the separator have been machined.
  The overall installation of the separator was completed
  The factory test shows that the vacuum reaches the target
  Due to the arc of the high voltage test, two power supplies failed to be used. After the improvement by Feedthrough, the separator will be delivered to the IHEP for testing.

## Slide 41
Thank You!