## Slide 1: The Scintillating Glass AHCAL Simulation
Yukun Shi
USTC

## Slide 2: Background and motivation
Circular electron positron collider
  The CEPC is designed as the Higgs factory
  The baseline detector option for the CEPC is guided by the particle flow algorithm(PFA)
Design of the CEPC Accelerator
CEPC baseline detector

## Slide 3: Background and motivation
The high granularity AHCAL composed of millions channels plays an important role in the PFA reconstruction
The scintillating glass has large density comparing to the plastic scintillator, thus it can improve the AHCAL resolution
Scintillating Glass
HCAL resolution is the 2nd largest factor contributing to the BMR(Yuexin Wang)

## Slide 4: Simulation Setup
Stand Alone Geometry
  Prototype Transverse size:
  40 sampling layers
    Scintillating Glass
    Steel
    PCB
  Birks effect isn’t considered
  Incident particle: Klong(10 to 80GeV)
  Leakage cut: shower start before layer5
  No energy threshold for cells
Single KLong event
Event display: 1 GeV KL
Wang, Qian, et al. "High light yield Ce3+-doped dense scintillating glasses." Journal of alloys and compounds 581 (2013): 801-804.

## Slide 5: Simulation
Energy deposition
  Sampling ratio is around 30% while plastic scintillator AHCAL is 2%
Energy deposition: 10 and 80 GeV KL

## Slide 6: Simulation
Different Steel thickness
  Lineaity are all within
  Resolution has a statistical term around 30%
Energy resolution and linearity: different Steel thickness

## Slide 7: Simulation
Different glass thickness
  Lineaity are all within
  The statistical term for resolution changes obviously

## Slide 8: Scintillating Glass 5
Scintillating Glass 5 has the largest density
Differences are not obvious
scintillating glass 4
scintillating glass 5

## Slide 9: comparison
Total thickness fixed as 23mm(sensitive material+absorber)
Scintillator glass have advantage on the statistical fluctuation
Plastic scintillator AHCAL
scintillating glass AHCAL

## Slide 10: Plastic and glass
6mm glass + 17mm Fe VS 3mm plastic + 20mm Fe
The scintillating glass configuration is obviously better
It should be mentioned that the scintillating glass configuration hasn’t considered the birks effect and any thresholds
Resolution
Linearity

## Slide 11: Results from Yong Liu

## Slide 12: Summary and outlook
The scintillating glass ACHAL has better resolution
More simulation based on CEPC environment will be done to see the benefit on physics benchmarks

## Slide 13
backup

## Slide 14: comparison
The scintillating glass has advantage on statistical term
The scintillating glass’s constant term is not good especially the Birks effect is not considered for the scintillating glass
Plastic scintillator AHCAL
scintillating glass AHCAL

## Slide 15: comparison
The 3mm scintillating glass seems similar to plastic scintillator
Thicker scintilling glass has better performance but increases the total calorimeter thickness
Plastic scintillator AHCAL
scintillating glass AHCAL

## Slide 16: Plastic and glass
6mm glass + 17mm Fe VS 3mm plastic + 20mm Fe
Energy deposition is scaled
10 GeV KL
80 GeV KL