## Slide 1: Requirements on the CEPC SC sextupoles from accelerator physics
Yiwei Wang
for the CEPC Accelerator Physics Group
CEPC day, 21 May 2021

## Slide 2: Outline
  Distribution and strength of the SC sextupoles
  Why the distribution and strength?
  Summary

## Slide 3
  Distribution and strength of the SC sextupoles
Design parameters of sextupole magnets at Higgs operation
Field strength factor for tt/W/Z: 1.5/0.67/0.38
by Y. Zhu
HSIRU
HSIRU
VSIRU
VSIRU
HSIRD
HSIRD
VSIRD
VSIRD
IP

## Slide 4: Why the strength?
If lower strength:
Longer sextupole => larger tune shift => larger aberration after correction => smaller energy acceptance => short beam lifetime
Larger dispersion => larger synchrotron radiation power => lower luminosity or higher power cost
Actually, the strength of the sextupoles have been reduced with factors of 2 or 2.7 due to magnet technology which will hurt the beam lifetime.
Name | Quant | Ape[mm] | Fmax[T/m | Fop(tt)[ | Fop(H)[T | Fop(W)[T | Fop(Z)[T | Leff[mm] | Rgf[mm] | Harm.er | Ftip[T] | TwinAper | DbRing
VSIRD | 8 |  | -4769.04 | -4769.04 | -3270.2 | -2180.13 | -1239.95 | 300 | 8.5079 | 3.00E-04 |  | N | Y
HSIRD | 8 |  | 7315.734 | 7315.734 | 5016.503 | 3344.335 | 1902.09 | 300 | 14.9474 | 3.00E-04 |  | N | Y
VSIRU | 8 |  | 4555.833 | 4555.833 | 3124 | 2082.666 | 1184.516 | 300 | 8.5079 | 3.00E-04 |  | N | Y
HSIRU | 8 |  | -5829.14 | -5829.14 | -3997.12 | -2664.75 | -1515.57 | 300 | 15.4117 | 3.00E-04 |  | N | Y
Design parameters of sextupole magnets at Higgs operation
Field strength factor for tt/W/Z: 1.5/0.67/0.38

## Slide 5: Why the distribution?
Background of the detector: compacter IR => compacter final telescope => shorter final bend => stronger synchrotron radiation to the detector
  No bends in the last 70 m from upstream of IP. The SR critical energy is less than 45 keV within 150 m and 120 keV within 400 m.
  no bends in the last 50 m from downstream of IP. The critical energy is less than 97 keV within 100 m and 300 keV within 250 m.
(-1km,+0.7km)

## Slide 6: Why the distribution? (cont.)
Error tolerance: compacter IR => stronger magnets => more sensitive to errors => tighter requirement of magnet error and alignment
Component | x (mm) | y (mm) | z (mrad) | Field error
Dipole | 0.10 | 0.10 | 0.1 | 0.01%
Arc Quadrupole | 0.10 | 0.10 | 0.1 | 0.02%
IR Quadrupole | 0.10 | 0.10 | 0.10 | 
Sextupole | 0.10 | 0.10 | 0.1 | 
IR=100mm
by B. Wang, Y. Wei, Y. Wang

## Slide 7: Summary
The CEPC superconducting sextupoles locate at region of (-1.0km,+0.7km) around the interaction point with a pole-tip field up to 2.7 Tesla.
  The strength of the sextupoles have been reduced with factors of 2 or 2.7 due to magnet technology. Further widely reduction will hurt the energy acceptance significantly.
  A compacter sextupole distribution will lead to stronger synchrotron radiation to the detector and tighter error tolerances.

## Slide 8: backup

## Slide 9
Lattice design of Interaction region for colliders
SuperKEKB
LER
FCC-ee
Super Charm-Tau Factory
BINP
SuperB
High luminosity for circular colliders: local chromaticity correction + crab waist scheme

## Slide 10
Lattice design of Interaction region for colliders
High luminosity for linear colliders: local chromaticity correction + crab cavity
ILC 500GeV
βx/βy = 15/0.4 mm
CLIC

## Slide 11: Luminosity frontier
Crab waist collision: proposed and proved on DAFNE
Local chromaticity correction for the interaction region: FFTB proposed for linear collider and 1st applied to circular collider on KEKB
M. Zobov et al, PRL 104, 174801 (2010)
w/ crab waist
w/o crab waist
V. Balakin et al, Vol 74, Num 13 PRL, 1995
Bunch height 73nm
KEKB LER
KEKB DR
Flat beam + large Piwinski angle + crab sextupole

## Slide 12: FCC-ee
No CCX: risk of machine tuning
Even Stronger sextupole: magnet technology

## Slide 13
Magnets comparison
SC magnet in IR | Higgs (CDR) | Higgs (high lumi.)
SC QD0 and QF1 | L*=2.2m, d=0.6m, QD0: 2.0m, 136T/m QF1: 1.48m, 111T/m | L*=1.9m, d=0.3m, QD0: 2.5m, 142T/m, 96T/m QF1=1.5m, 56T/m
SC anti-solenoids | maximum 7.2T | maximum 6.8T
SC sextupoles | VSIRD: 0.6m, 1308 T/m^2 HSIRD: 0.8m, 1506 T/m^2 VSIRU: 0.6m, 1250 T/m^2 HSIRU: 0.6m, 1600 T/m^2 | VSIRD: 0.6m, 1209 T/m^2 HSIRD: 0.8m, 1679 T/m^2 VSIRU: 0.6m, 1548 T/m^2 HSIRU: 0.6m, 1130 T/m^2 (safety factor 20% for strength )