## Slide 1: Muon detector
XiaoLong Wang
Fudan University
东莞CEPC探测器与MDI机械设计研讨会
散列中子源园区， 10/22/2021

## Slide 2: Outline
Belle II Muon detector
G4 simulation on CEPC Muon detector
Status of hardware R&D

## Slide 3: Belle II muon detector -a good reference
H=7.1m, L=7.4m
W=1400t
B=1.5T
经验与教训
🙂 ☹

## Slide 7: 实验运行中发现的问题
运行费用的提升：电力消耗
  束团电流越大，消耗的电力越多。电费问题限制了运行时间。
2020b运行期间发现的问题：
  束团电流过大时引起的强烈的beam-beam相互作用，blowup的问题越严重。尝试办法：1）Crab waist方案；2）修改QCS，以减小其四极磁铁与Belle II探测器磁场的干扰。
  QCS系统的孔径(physical aperture)比较窄，不稳定束流的轰击会引起QCS淬火。解决办法：beam collimators, 但是在时会变得很困难。
  Belle II探测器中的本底较高。Belle II本底预期比Belle高20倍，但实际情况比预期还要高。原因是QCS中束流对束流管的轰击。
时()，在较高的束团电流区间，加速器的动力学孔径(dynamic aperture)会比较小，导致LER寿命从降到。

## Slide 8
Belle II运行的主要问题
探测器寿命，特别是iTOP
  需要维持MCP-PMT的量子效率： 直到获取数据；
  但是，Touschek和束流本底随，
  需要采取的措施：准直系统(collimators)，束流调试，更多的束流屏蔽(shielding)
Accidental huge beam loss对PXD和SVD造成的永久损害
高能环(HER)同步辐射对PXD造成的辐射损伤
加速器与探测器均在考虑升级。
  Partial RF power upgrade (2 stations) in 2026
  IR (QCS and its beam pipes etc.) upgrade in 2026

## Slide 9: Detector simulation
The detector simulation using Geant4 started in the early 2021.
CEPCSW installed, but G4 simulation has not been implemented yet.
  The implementation should be done recently.
The next step is testing with a high energy muon track.
The number of layers is not determined, 3 or 8?

## Slide 10
CEPCSW on cluster
$ git clone git@github.com:cepc/CEPCSW.git
$ cd CEPCSW
$ git checkout master # branch name
$ source setup.sh
$ ./build.sh
$ ./run.sh Examples/options/helloalg.py
check CVMFS
CEPCSW installed
Notes: 在高能所计算集群使用CernVM File System(CVMFS)安装新版本CEPCSW

## Slide 11
10cm
12m
9m
CEPC CDR 2018
superlayer
Magnetic field would be quite strong in muon detector.

## Slide 12: hits
Fast testing with is performed.
WLS fibre and SiPMs are not included yet.
Plan:
  A complete description of the scintillator-based muon detector.
  Implementation into the CEPCSW.
  Optimization according to CEPC physics goals.
Will be ready for G4 testing soon.

## Slide 13: Optical coupling
Get closer to improve the light collection.
Firm coupling to avoid the damage on the MPPC sensor surface.
Studying the coupling between scintillator strip and fibre with optical glue.
From Belle II

## Slide 14
LED
MPPC
Scintillator blocks
x
DT5725
Multiphoton spectrum from MPPC
Add scintillator between LED and MPPC
LED
light
scintillator
Pulse generator
Digital analyzer
MPPC
oscilloscope
Smooth surface
Trigger:
2 channel coincidence
reduce dark count
light
Attenuation length of Scintillator

## Slide 15: Attenuation length
Attenuation formula ：
With optical glue between blocks
Attenuation length should be optimized at the production.
Light lost between blocks is not taken into account…

## Slide 16: Photon collection and efficiency vs. length
2
3
1
Small strips for cosmic ray trigger: .
A good spatial resolution.

## Slide 17
Efficiency
Comparison of two method
Consistent results

## Slide 18
Efficiency
Efficiency of two scintillator with different reflective layer

## Slide 19
MSO 56 Oscilloscope
Signal 1
Black Box
with copper foil shielding
MPPC1
Signal 2
ZFL-1000LN+ Low Noise Amplifier 2
ZFL-1000LN+ Low Noise Amplifier 1
output circuit 1
output circuit 2
Set up for time resolution
Time resolution: scintillator+PCB+ MPPC+ZFL
Scintillator1+KURARAY1
Scintillator2+KURARAY2
MPPC2

## Slide 20: New pream for NDL SiPM
New pream designed for NDL SiPM
Good performance!
Gain~10.
Mad in China: scintillator and SiPM!!!
  How about WLS fibre in the future?

## Slide 21: Summary
Belle II detector is a good reference.
Preliminary work on G4 simulation for muon detector has been done.
There is a question of how many layers of CEPC muon detector?
R&D of muon detector is ongoing well.
  Made in China: scintillator+SiPM
  New FEE designed.
  Good efficiency: >90%
  Time resolution: < 2ns.
One comment: how about good time resolution in muon detector?
  Extend the performance to search for Long-Live Particle with the large size of muon detector.
Thank you!