## Slide 1: TaichuPix2—LDO测试
王 佳
jwang@nwpu.edu.cn
西北工业大学 计算机学院 微电子学研究所
2021.5.11

## Slide 2: 发现的版图问题
1. Bandgap内部的NPN阵列外隔离用的PWELL衬底接触，原来的接触点少，紧挨WN（WB）层上未连接触孔。

## Slide 3: 发现的版图问题
WN处(粉色边框)没有画和VDD的接触。
NPN管阵列
其余WN均接VDD2V
PMOS pass transistors

## Slide 4
WN处(粉色边框)没有画和VDD的接触。
LVS的extraction报错，错误器件。

## Slide 5: 发现的版图问题
2、最外层隔离环，VNN和WN之间有空隙，0.01um宽。

## Slide 6: TaichuPix3 design
Bandgap is replaced by the one designed by Liang ZHANG.

## Slide 7: Bandgap in DAC from Liang ZHANG
Vbg=0.989V

## Slide 8: BANDGAP T3 updating
Bipolar transistor are moved to connected with ground to prevent the diode between VBG and PWELL.

## Slide 9: Modified PAD
Vdd2V: PVDF_18_18_WB
VDDA: modified PVDF_18_18_WB
  All ESD have been removed. M6 is used for power distributing.

## Slide 10: Post-layout simulation with PAD
Load regulation: 160 mA (Maximum load current with all corners)

## Slide 11: Post-layout simulation
Line regulation @ iload=200mA
SLOW,FS:<1.8V. Since the output transistor is p-channel, the output decreases with slow PMOS transistors.

## Slide 12: TaichuPix2—LDO测试
王 佳
jwang@nwpu.edu.cn
西北工业大学 计算机学院 微电子学研究所
辐射探测材料与器件工信部重点实验室