## Slide 1: The Scintillating Glass AHCAL Simulation
Yukun Shi
USTC

## Slide 2: Simulation
Simulation Setup
  Stand Alone Geometry
  Sensitive material:Scintillating Glass S4
  Prototype Transverse size:
  Birks effect isn’t considered
  Incident particle: Klong(10 to 80GeV)
  Leakage cut: shower start before layer5
  No energy threshold for cells
Single KLong event
Event display: 1 GeV KL

## Slide 3: Simulation
Energy deposition
  Sampling ratio is around 30% while plastic scintillator AHCAL is 2%
Energy deposition: 10 and 80 GeV KL

## Slide 4: Simulation
Different Steel thickness
  Lineaity are all within
  Resolution has a statistical term around 30%

## Slide 5: Simulation
Different glass thickness
  Lineaity are all within
  The statistical term for resolution changes obviously

## Slide 6: comparison
The 3mm scintillating glass seems similar to plastic scintillator
Thicker scintilling glass has better performance but increases the total calorimeter thickness
Plastic scintillator AHCAL
scintillating glass AHCAL

## Slide 7: Scintillating Glass 5
Scintillating Glass 5 has the largest density
Differences are not obvious
scintillating glass 4
scintillating glass 5

## Slide 8: Plastic and glass
Total thickness fixed as 23mm(sensitive material+absorber)
Resolution is not just a matter of thickness, the compensation is also important
Plastic scintillator AHCAL
scintillating glass AHCAL

## Slide 9: Plastic and glass
6mm glass + 17mm Fe VS 3mm plastic + 20mm Fe
Energy deposition is scaled
Scintillating glass has more advantage at low energy
10 GeV KL
80 GeV KL

## Slide 10: Plastic and glass
The scintillating glass configuration is obviously better
It should be mentioned that the scintillating glass configuration hasn’t considered the birks effect and any thresholds
Resolution
Linearity

## Slide 11: Summary and outlook
The scintillating glass ACHAL has better resolution especially at low energy
More simulation based on CEPC environment will be done to see the benefit on physics benchmarks

## Slide 12
backup

## Slide 13: comparison
The scintillating glass has advantage on statistical term
The scintillating glass’s constant term is not good especially the Birks effect is not considered for the scintillating glass
Plastic scintillator AHCAL
scintillating glass AHCAL

## Slide 14: CALICE AHCAL
38 layers
  5.3 λ
  21mm Steel
  5mm plastic scintillator

## Slide 15: CALICE
Event selection
  Shower starts at the first 5 layers
  ECAL, TCMT energy limit