## Slide 1
Design of iRPC frond-end electronics emulator
Jia-ning Song*, Zhen-An Liu, Jingzhou Zhao, Hanjun Kou, Qingfeng Hou, Weizhuo Diao, Wenxuan Gong
Trigger and DAQ Group/ IHEP Beijing
2021 CLHCP 27th November

## Slide 2
  Background
  Emulator architecture
  Clock requirement and distribution study
  Data transmission mechanism and efficiency study
  FEE emulator to BEB test results in Beijing/CERN 904-lab
  Summary
Outline

## Slide 3
Difficulties
  How to develop and verify BEB functions in lab without test facility like detector, FEB, or GBTx chip ?
  What is the clock requirement of FEE and how to realize?
  What is the data transmission mechanism between the frontend and backend?
FEE Emulator GBT-FPGA
GBT link
BEB
（GBT-FPGA）
iRPC data source
Background
  iRPC software simulation
  Clock requirement and distribution study
  Data transmission mechanism and efficiency study

## Slide 4
r
Z
strip length L
t1
LR side
HR side
t2
r
2 2
r = 1 L − (t2 − t1) ∗ v
iRPC used in CMS Phase II upgrade
iRPC&FEB
Backend electronics system
iRPC&FEB
  One iRPC chamber covers 20°，read out by 2 FEBs through GBT link
  One FEB receives signals of 96 channels (48 strips* 2 ends)
Trigger/Backend electronics system (See Hanjun’s talk)
Hit position
  Each strip is read out from two ends and r is calculated by the time difference .
  Much improved hit localization along the strip can be achieved. –2cm

## Slide 5
Main components
  Software
    Using python to simulate the hits and generate the FEE TDC data
    Studying the data transmission efficiency
  Firmware
    Adopting GBT-FPGA to emulate GBTx chip on FEB
    Communicating with the backend to verify fast/slow control function
    Realizing the hit finding and data transmission algorithm
  Hardware
    An AMC card designed by the lab is chosen
    Providing as many as 36 links optical input/output
    Replicating the behavior of one or more real-working FEBs based on powerful V7 FPGA
Emulator architecture

## Slide 6: iRPC software simulation
  iRPC software simulation
    Three main parts
      Parameters setting
      Detector data generation
      FEE TDC emulator
    developed by python 3.7
parameters setting
data generation
FEB TDC emulator
. . .
96 strips
low radius cable
strip
high radius cable
. . .
FEB1
FEB2

## Slide 7: Parameters setting
Virtual RE3/1 iRPC Chamber
  For one RE3/1 chamber,=153cm,=319cm,Area=1.32m2,covers 20°
  contains 96 strips，read out by 2 GBT links.
  For one strip ,=166cm, pitch about 0.60cm at low radius(1.23cm at high radius)
  connect with a return line (kept as 244cm) within PCB.

## Slide 8: Detector data generation
Random hit point(r, φ) in the chamber
  r: generates the hit point along strip.
  φ: generates the strip number.
Smear of φ direction :
  Generates a consecutive set of strips as a cluster.
Cluster size randomization :
  1-8,mean is 2.35
  Reference : Shchablo Konstantin1 on behalf of the CMS Muon group, Front-End electronics for CMS iRPC detectors（RPC2020, Roma）
Number of clusters :
  1(75% probability),2(25% probability，keep the cluster size as 1)

## Slide 9: TDC emulator
TDC Data unit(32 bits)
devAddr | chanAddr | TDC data | 
 |  | Coarse time | Fine time
2 | 6 | 16 | 8
Digitization
    For each fired strip, there are always 2 constraint 32-bit TDC data constructed.
      Channel-HR Rising Edge (32bit) + Channel-LR Rising Edge (32bit)
    devAddr ：FPGA ID, totally 3 on 1 FEB chanAddr : channel number, 0~34
    Coarse time : the value of an internal counter at 400MHz which gives the coarse time (2.5ns step).
    Fine time: corresponding to the fractional part of the coarse time step, 2.5ns/256≈9.7ps

## Slide 10
For the final System
  The backend receives the LHC bunch clock from AMC13 then sends to FEE via GBT links.
  The LHC bunch or AMC13 clock is 40.0786MHz ± 0.0037MHz
BEB to FEB/FEE Emulator clock requirement
  No bunch clock
  GBT REFCLK ppm(parts per million) requirement : ±200 pm => 40MHz * 200/106= ± 0.0080MHz
  High accuracy 40.0786MHz oscillator is needed to communicate with FEB GBTx chip/FEE Emulator.
Verification
  At IHEP trigger lab
    Replace the on board OSC with high accuracy 40.0786MHz±0.002004MHz MHz OSC in IHEP.
    No error was found during a 96-hour test.
  At CERN
    Then we modified the BE boards in CERN with the help of electronics experts in CMS RPC collaboration.
    Already verified by joint test with FEB_V2(Lyon Group) .
Clock requirement and distribution study

## Slide 11
Clock requirement and distribution study
BEB to FEB clock distribution
GBT-FPGA TX
MGT TX
GBT-FPGA RX
MGT RX
CDR
Bunch clock or OSC
BEB
MiniPOD
MiniPOD
40.0786MHz
The system clock is sent to FEE via optical links.
The GBTx chip recovers the bunch clock from input data stream and uses it as system clock for FEE.
GBTx
SFP
FEB
GBT SERDES
E-LINK SERDES
CDR
E-LINK SERDES
Cyclone V
PLL

## Slide 12
The Check-Sort-Push (CSP) algorithm
  proposed by the IHEP trigger lab at first and widely discussed in the CMS RPC collaboration
  Became one of the solutions for FEE-BEE data transmission and adopted by FEE Emulator
Details
  Checking all the channels every BX (25ns) for new hits
  Sorting the new hits if Yes in time sequence with the remaining for transmission
  Transmitting them one-by-one in the consecutive BXs to the backend via GBT protocol
  An adjustable Tx Latency Window (TxLW) is applied to the transmitter side
    The value of the latency informs how many BX a given frame was delayed with respect to the BX from which the TDC data originates.
    Making it reliable for the transmission between FEE and BEE
    Preventing the buffer from overflowing and achieves system robustness if the hit rate exceeds designed values.) .
Data transmission mechanism and efficiency study

## Slide 13
Efficiency with different Tx Latency Windows(TxLw)
  TxLW width settings(BX): 4, 6, 8, 16
  hit rate( Hz/cm^2 ,safety factor 3):600, 800, 1000, 1200, 1500, 1800, 2000
  Including burst; Mean cluster size:2.35 ; Surface of half chamber :6600cm^2 (1 fiber)
  Size of 1 strip(2 channels) information: 64 bits
      For maximum rate 2000 Hz/cm^2,1 fiber data rate
= 2000rate*6600surface* 2.35cluster size *64 1 strip info
Gb/s
= 1.99 Gb/s(smaller than uplink data bandwidth 3.84Gbps)
The FEE original solution in TDR which sends both the rising and falling edge is replaced by the the collaboration based on our study.
A larger TxLW leads to increased efficiency.
100 % efficiency is measured with a 16-BX wide TxLW in our simulation.
Data transmission mechanism and efficiency study
Data bandwidth estimation

## Slide 14
Purpose：
  Understanding the basic requirement of FE Board
  Verifying back-end board function
System setup ：
  2 boards are used
  - one acts as FEB emulator
  - one acts as BEB
  Power supply
  Fan
  PC- desktop
  - 1Gb-link and 10Gb-link Hardware
  - Slow control software
  - DAQ software
  PC- laptop
  - Check firmware algorithm
FEE emulator to BEB test system
BEB
（GBT-FPGA）
FEE Emulator
GBT-FPGA
GBT link
12V-DC
Fiber(MPO-LC)
BEB
FEE emulator
Fan
1Gb-link,SC
10Gb-link,DAQ
Check Board status
SC-SW
DAQ-SW

## Slide 15
FEE emulator to BEB test results
Test List done in Beijing/CERN
  Check GBT link establish status between FEE emulator and BE board √
  GBT link Long time stability test( > 2 days) √
  Bit Error rate test between FEE emulator and BE board √
    FEE emulator send pseudo-random data and BE check the data
      BER is better than 8E-16.
  Slow control frame write and read check √
    Write and read a custom address
    Single frame mode
    Burst mode
  Slow control frame repeatedly write and read check √
  GBT SCA write/read test √
  Data process algorithm check √
    Check DEMUX, cluster finding, and angle conversion algorithm
    Check data package and upload algorithm

## Slide 16
Summary
Software simulation has been done.
  iRPC data source
Clock requirement of FEE has been researched and verified in emulator and joint test.
  High precision 40.0786MHz OSC
  Clock distribution
Data transmission mechanism and efficiency have been studied based on emulator and become one of the solutions.
Emulator system for iRPC backend system has been successfully tested in Beijing (May) and
CERN 904-Lab (June).

## Slide 17
Thanks!

## Slide 18
Joint test roadmap
  --Zhen-An Liu et al. Roadmap of Backend Electronics Test and Integration ,RPC Electronics Meeting ZooM,Dec. 22 2020
  Emulation test
  Board(BE) to Board(FE) Joint test
  Board(BE) to Boards(FE) joint test
  Moving to MTCA System –board(BE) to Boards(FE) (904)
  Moving to MTCA System –board(BE) to Boards(FE) (P5)
Backup

## Slide 19
The CDR state machine uses the data from both the edge and data samplers to determine the phase of the incoming data stream and to control the phase interpolators (PIs)
Alignment Block Finds Comma or Header
RXSlide
The data is shifted right by one bit for every RXSLIDE pulse issued. The GBT receiver searches for the Header in the incoming data and checks it. Link is established after GBT Rx receiving 24 successive Headers(0110/0101). Then use Header flag to align the Rx CDR clock.
Edge
Data sampler
Rx CDR clock introduction

## Slide 20
FEE emulator to BEB test results
GBT-link stability and bit error rate ：
  The link was established successfully and data
  are received correctly on FEB emulator and BEB.
  The long time test ( > 2 days) link is stable and
  there is no bit error.
  The BER is better than 8E-16.
FEE emulator
BEB

## Slide 21
FEE emulator to BEB test results
Clusterization algorithm：
  The firmware implementation of the Clusterization algorithm and the software simulation give the same results.
  Check the BE Clusterization algorithm step by step, and the result is correct.

## Slide 22
FEE emulator to BEB test results
Readout algorithm：
  The PC receives the DAQ data frame uploaded by BE and saves it into a file.
  The data in the DAQ file conforms to the custom DAQ data format.
DAQ file

## Slide 23
FEE emulator to BEB test results
Slow control：
Slow control of BE board
- Because the FEE emulator does not have a GBT-SCA chip, it cannot perform slow control readback operations.
- FEE emulator received slow control data is correct.
FEE slow control
BEE slow control repeat test
Write: address-0x0002, incremental data, repeat the test 1000 times; ok
Read back the last written data, the value is correct.
FEE slow control repeat test
Single frame mode and Burst mode;
Successfully read and write thousands of times;
GBT-SCA
Initial value=21,
21+3*1000=0xbcd