## Slide 1: CEPC new damping ring design status
Dou Wang, Cai Meng, Jingru Zhang, Xiaohao Cui, Yudong Liu, Jinhui Chen, Daheng Ji, Jie Gao, Chenghui Yu, Yuhui Li

## Slide 2: Damping ring layout (CDR)
Linac repetition: 100Hz
Only for positron beam
Storage time: 20 ms
Emittance (norm.): 2500 530 mm.mrad
e +

## Slide 3: Requirements update for the Damping ring
Emittance
  High luminosity of Higgs (lower emittance collider  lower emittance booster)
    Lower emittance Linac:10nm@20GeV  Norm. RMS emittance is 392mmmrad
    DR emittance requirement: < 200mmmrad
      Keep the margin for emittance growth
        -- high bunch charge
        -- C-band accelerating structure
      Could use C-band accelerating structure just after the Damping Ring (@1.1GeV)
Damping time
100Hz Linac & two-train scheme storage time: 20ms
Requirement for damping time: <13ms
Bunch length
  RMS bunch length after DR <1mm
    -- a bunch length compressor was introduced after the DR for electron and positron beam
Cai Meng

## Slide 4: Comparison of damping ring design requirement
 | CDR | New | remark
Energy (GeV) | 1.1 | 1.1 | 
Inj. Emittance (mmmrad) | 2500 | 2500 | 
Ext. emittance (mmmrad) | 530 | <200 | 1) Linac lower emittance: 10nm@20GeV, 2)use C band acc. structure as early as possible
Storage time (ms) | 20 | 20 | 
Damping time (ms) | 15 | <13 | 1) Smaller ext. emittance with same storage time
Circumference (expected) (m) | 75 | ~150 | 1) Smaller nature emittance for DR

## Slide 5: Design scheme for CEPC new damping ring
Option 1: damping with reversed bending magnet
Option 2: damping with wigglers

## Slide 6: Option 1: parameters
 | DR V3.0 | 
Energy (Gev) | 1.1 | 
Circumference (m) | 147 | 
Number of trains | 2 | 
Number of bunches/trian | 2 | 
Total current (mA) | 12.4 | 
Bending radius (m) | 2.87 | 
Dipole strength B0 (T) | 1.28 | 
U0 (kev/turn) | 94.6 | 
Damping time x/y/z (ms) | 11.4/11.4/5.7 | 
Phase/cell (degree) | 60/60 | 75/75
Momentum compaction | 0.013 | 0.007485
Storage time (ms) | 20 | 
0 (%) | 0.056 | 
0 (mm.mrad) | 94.4 | 56.7
injection z (mm) | 5 | 5
Extract z (mm) | 5.6 | 4.2
inj (mm.mrad) | 2500 | 2500
ext x/y (mm.mrad) | 166/75 | 123/68
inj /ext (%) | 0.18 /0.056 | 0.18 /0.056
Energy acceptance by RF(%) | 1.4 | 1.8
fRF (MHz) | 650 | 
VRF (MV) | 1.5 | 
Longitudinal tune | 0.0299 | 0.0224
Four-bunch storage scheme
Storage time: 20 ms
Emittance: 2500 166 (123) mm.mrad
Flexibility for extr. emittance

## Slide 7
Phase/cell: 60/60 ~ 90/90 FODO
Interleave sextupole scheme
2 sex. families
Option 1: optics
Arc
Straight

## Slide 8
Option 1: DA
Phase/cell: 60/60
Phase/cell: 75/75
Large trans. acceptance inj. efficiency
- DA > 5 inj. beam size

## Slide 9: Option 2: parameters
 | DR V4.0
Energy (Gev) | 1.1
Circumference (m) | 145
Number of trains | 2
Number of bunches/trian | 2
Total current (mA) | 12.4
Bending radius (m) | 3.44
Dipole strength B0 (T) | 1.07
U0 (kev/turn) | 98.0
Damping time x/y/z (ms) | 10.9/10.9/5.4
Momentum compaction | 0.015
Storage time (ms) | 20
0 (%) | 0.061
0 (mm.mrad) | 25.1
injection z (mm) | 5
Extract z (mm) | 5.7
inj (mm.mrad) | 2500
ext x/y (mm.mrad) | 87.3/62.8
inj /ext (%) | 0.18 /0.061
Energy acceptance by RF(%) | 1.5
fRF (MHz) | 650
VRF (MV) | 2.0
Longitudinal tune | 0.037
Four-bunch storage scheme
Storage time: 20 ms
Emittance: 2500 87 mm.mrad
Strong damping from wigglers

## Slide 10
Option 2: optics
Phase/cell: 60/60 FODO
Interleave sextupole scheme
Arc
Dis. suppressor
Straight

## Slide 11
Option 2: wiggler parameters
wiggler | value
Bw (T) | 1.8
w (m) | 2.0
w (m) | 0.16
Lw (m) | 1.5
Nw | 16
Fw (U0w/U0arc) | 1.6
Reduce horizontal beta in wiggler section to control emittance
- average x: 1.3m

## Slide 12
Option 2: DA
DA > 5 inj. beam size

## Slide 13: Injection/extraction scheme and time structure
J. H. Chen, D. Wang, X. H. Cui, C. H. Yu…
Double bunch
200Hz
Inj. scheme: two by two
Inj. scheme: bunch by bunch
Kicker repetition: 100Hz
Flat top: 87ns
Rise up/down: 168ns
Pulse duration: 423ns
Kicker repetition: 200Hz
Rise up/down: 125ns
Pulse duration: 250ns
High lum. Z mode: 4-bunch storage  most demanding case for DR Inj./ext.

## Slide 14: Impedance Instabilities
Resistive wall impedance was considered *.
Design bunch current: 3.1mA < threshold due to TMCI
Yudong Liu
* Circular Al pipe with 30mm inner diameter

## Slide 15: Transport lines between DR and Linac
LinacDR | EC
E0 (Gev) | 1.1
0 (%) | 0.6
z0 (mm) | 1.5
fRF (MHz) | 2860
VRF (MV) | 22.0
Length of acc. Structure (m) | 0.82
RF (degree) | 89.7
R56 (m) | -0.833
Ef (Gev) | 1.1
f (%) | 0.18
zf (mm) | 5
DRLinac | BC
E0 (Gev) | 1.1
0 (%) | 0.061
z0 (mm) | 5.7
fRF (MHz) | 2860
VRF (MV) | 16
Length of acc. Structure (m) | 0.6
RF (degree) | 89.6
R56 (m) | -1.15
Ef (Gev) | 1.1
f (%) | 0.50
zf (mm) | 0.7
Dou Wang, Xiaohao Cui

## Slide 16: Optics for the transport lines
LinacDR
DRLinac
Xiaohao Cui

## Slide 17: Damping ring cost estimation
Cost (ten thousand) | CDR | New (reversed bend) | New (wiggler)
Magnets | 1164 | 1750 (1.5) | 2910 (2.5)
RF | 800 | 800 | 800
RF Power Source | 385 | 385 | 385
Vacuum | 200 | 390 | 390
magnet supports | 237 | 360 (1.5) | 590 (2.5)
power supply | 313 | 470 (1.5) | 780 (2.5)
BI device | 600 | 800 | 1200
Injection & extraction | 160 | 160 | 160
wiggler | - | - | 8000
Total | 3859 | 5115 | 15215

## Slide 18: Summary
Damping ring update is the requirement of higher luminosity goal for TDR.
- lower emittance collider  lower emittance booster  lower emittance linac
New DR needs to damp the positron beam stronger and faster during 20ms storage
emittance: 530mmmrad (CDR)  under 200mmmrad (new)
Damping time: 15ms (CDR)  11ms (new)
So far, two kinds of DR were developed. Both can fulfill the requirement.
circumference: 150m, energy: 1.1GeV
Option 1: reversed bending, extracted emittance=120~166 mmmrad
Option 2: wigglers, extracted emittance=87mm mrad
Transport lines almost same as CDR