## Slide 1: Status of the MICROMEGAS semi-DHCAL
M. Chefdeville
LAPP, Annecy, France
LCWS, 27th March 2010, Beijing

## Slide 2: Overview
The 1 m3 semi-DHCAL project & MICROMEGAS
Simulation
Test beam and ASIC
DAQ
The 1 m2 MICROMEGAS prototype

## Slide 3: The 1 m3 semi-DHCAL
Calorimetry based on Particle Flow
  Granularity more important than resolution → digital option
  Loss of linearity at high energy (100 GeV/c) → 2 bit readout → semi-digital HCAL
1 m3 semi-DHCAL project in France
  Funded by CNRS/IN2P3 + “Agence Nationale de la Recherche” (ANR) + Rhone-Alpes region (chip development)
  Several labs involved LAL (Orsay) → HARDROC LLR (Palaiseau) → CALICE DAQ IPNL (Lyon) → RPC LAPP (Annecy) → MICROMEGAS
Choice of active media (required by ANR schedule)
  3 physicist committee
  RPC favored but production of MICROMEGAS m2 planes should be pursued

## Slide 4: The 1 m3 structure
Design proposed by CIEMAT group
  In collaboration with LAPP engineer
  2 different mechanical pieces minimum machine operation on each piece
  Deformation and stress simulation
From Enrique Calvo Alamillo talk, Madrid, 1st March 2010
Compatible with RPC and MICROMEGAS
  44 planes
  16 mm between absorbers 1 mm tolerances

## Slide 5: Detector planes
RPC VS MICROMEGAS
  Large VS small signals, low VS high rate capability
  Limited proportionality VS proportional mode → MICROMEGAS best suited for semi-DHCAL
Semi-digital readout
  HARDROC or DIRAC ASIC (3 thresholds)
  What should the threshold be? → detailed simulation

## Slide 6: Simulation (I)
Comparison analogue/digital readout for 1 m3 steel, applying 1 energy threshold
  Energy resolution, linearity, shower shapes → 2009 JINST 4 P11009
Digitization, from GEANT4 energy deposits in gas layers to hits, applying charge thresholds
Simulation for CLIC:
  Definition of HCAL;
  Definition of small prototype for beam test: → J. Blaha, CLIC Physics and Detector Meeting, 15 Sep. 2009, CERN
TB setup simulation and comparison with data → shower profile study to be published
TB: 2 GeV/c electron shower profile

## Slide 7: Simulation (II)
Implementation of MICROMEGAS DHCAL in CLIC and SiD detector geometry
Study of crack effects on HCAL performance
  Projective and tilted geometries

## Slide 8: TB and ASIC developments
Detector characterisation done with analogue readout prototype (GASSIPLEX)
  Carried out with Irfu collaborators
  → 2009 JINST 4 P11023
Signal MPV of 20 fC (with 10 % variations)
Sensitivity to P, T (2 % / K & -0.6 % / mbar)
At a threshold of 1.5 fC
  97 % efficiency with variations < 1 %
  Hit multiplicity below 1.12

## Slide 9: TB and ASIC developments
Now focus on test of digital readout prototypes with embedded electronics
  ASIC and spark protection components on PCB
  Bulk lamination on PCB using a mask at CERN workshop
  RD51 collaboration (http://rd51-public.web.cern.ch/RD51-Public) asked for a new location: increased production capability
2 different chips (64 channel each)
  HARDROC (LAL/Omega group), asynchronous functioning, shape signals
  DIRAC (IPNL/LAPP), synchronous functioning, integrate signals

## Slide 10: 2009 TB with HARDROC1
3 chambers of 32x8 cm2 (3 mm gas gap) 4 chips & 1 DIF / board
May 09 @ PS/T10
  Hard times with DAQ: DIF synchronicity no acquisition software expert available USB data readout problems…
  No quantitative study: beam profile → it works
Sep 09 @ PS/T10 (DAQ OK)
  Very low efficiency (5-10 %)
  Understood as too short shaping time
32x8 cm2 ASU with 4 HARDROC
Hadron beam profile in one chamber

## Slide 11: 2009 TB with HARDROC2
1 board of 48x32 cm2 (unit of future 1 m2) inside a gas test box with 3 cm gas gap, equipped with 24 chips & 1 DIF
Test with chamber (perpendicular and) // to beam
  Faster signals at the pads
  Larger signals (1 cm)
  Efficiency between 10-90 % depending on chip threshold

## Slide 12: 2008-09 TB with DIRAC
Synchronous chip functioning (ILC-like)
First chamber with embedded ASIC (ASU)
  8x8 cm2 tested in SPS beam in 2008
Stack of 4 chambers (8x8 cm2)
  PS/T9 in Nov. 2009
  Short life-time in beam → chip design improvement
  Small statistics but promising results → multiplicity 1.06-1.13 → efficiency 45-50 %
To be corrected for synchronous functioning

## Slide 13: Future plans for front end electronics
HR input stage not suited for the detection of MICROMEGAS signals
Promising results obtained with DIRAC chip
→Development of a new chip from existing ones, in collaboration with LAL/Omega group → Work on spark protection spark proofness test setup @ LAPP innovative solutions studied within RD51

## Slide 14: Contribution to CALICE DAQ
Detector Interface (DIF) developed at LAPP is ready for production
  A batch of 20 DIF should be available end of March
  150 board production planned for this summer, all available in Sept.
Important milestones
  8B/10B communication protocols validated (LAPP/LLR)
  CCC (Clock and Control Card) integration in work at LAPP

## Slide 15: The 1 m2 MICROMEGAS prototype
Features
  6 ASU of 48x32 cm2
  24 ASIC / ASU → 1536 * 6 = 9216 channels
  Dead areas < 10 %
  Total thickness of 1.15 cm (incl. steel covers)
  3 DIF boards
Test of each ASU separately
Assembly procedure validated

## Slide 16: Status and future plans
ASU test on-going
  Measurement of ASIC performance
    Noise, gain, uniformity, equalization
  Response to 55Fe X-rays and cosmics in gas box @ LAPP
4 ASU with HR2, 1 ASU with HR2b + 1 dummy Assembly foreseen in April Cosmics tests @ LAPP until June
2-3 weeks of beam in SPS/H4 end of June
  Efficiency, multiplicity, uniformity
  Spark study (beam intensity)

## Slide 17: Test inside W-structure
The LCD-CERN, CALICE-DESY and LAPP groups agreed to work together and construct a W-HCAL prototype starting 2010
  LAPP contribution on simulation + MICROMEGAS layers → see W. Klempt talk at CALICE meeting, Arlington, 12/03/10
Start with a small prototype
  20 W-layers of 81x81 cm2, 1 cm thick
2 weeks of beam inside W-structure with AHCAL in PS/T9 starting mid November 2010
  Test of scintillator layers + 1 or more MICROMEGAS planes

## Slide 18: Conclusions
MICROMEGAS, as proportional detector, is well suited for a semi-DHCAL
Very good basic performance for a DHCAL but strongly depends on electronics
  HARDROC input stage not optimized for MICROMEGAS signals Work on a new ASIC on-going
  Several options for spark protection are being investigated
First 1 m2 MICROMEGAS prototype available end of April 2010 and ready for beam test at the end of June
  Equipped with HR2, so limited performance expected However, a lot to learn for next 1 m2 prototypes
  Next prototypes should be equipped with a different chip
    One plane with DIRAC if spark protection issue solved
    Next planes with a new chip, probably resulting from the collaboration between LAL and LAPP

## Slide 19: Acknowledgments
Catherine Adloff
Jan Blaha
Jean-Jacques Blaising
Sébastien Cap
Maximilien Chefdeville
Alexandre Dalmaz
Cyril Drancourt
Ambroise Espargilière
Laurent Fournier
Renaud Gaglione
Nicolas Geffroy Jean Jacquemier Yannis Karyotakis Fabrice Peltier Julie Prast
Guillaume Vouters
David Attié
Enrique Calvo Alamillo
Paul Colas
Christophe Combaret
Mary-Cruz Fouz Iglesias
Wolfgang Klempt
Lucie Linsen
Rui de Oliveira
Dieter Schlatter
Nathalie Seguin
Christophe de la Taille
Wemxing Wang
the LAPP group
collaborators