## Slide 1: LHC Beam Operations Past, Present and Future
K. Foraz – CERN
(Acknowledgement : R. Bailey)

## Slide 2: LHC Beam Operation Operation envelope Progress with beam in 2009 2010-2011

## Slide 3: LHC nominal performance
Nominal settings | 
Beam energy (TeV) | 7.0
Number of particles per bunch | 1.15 1011
Number of bunches per beam | 2808
Crossing angle (rad) | 285
Norm transverse emittance (m rad) | 3.75
Bunch length (cm) | 7.55
Beta function at IP 1, 2, 5, 8 (m) | 0.55,10,0.55,10
Derived parameters | 
Luminosity in IP 1 & 5 (cm-2 s-1) | 1034
Luminosity in IP 2 & 8 (cm-2 s-1)* | ~5 1032
Transverse beam size at IP 1 & 5 (m) | 16.7
Transverse beam size at IP 2 & 8 (m) | 70.9
Stored energy per beam (MJ) | 362
* Luminosity in IP 2 and 8 optimized as needed
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 4: Instantaneous luminosity
Nearly all the parameters are variable (and not independent)
  Number of particles per bunch 
  Number of bunches per beam kb
  Relativistic factor (E/m0) 
  Normalized emittance n
  Beta function at the IP  *
  Crossing angle factor F
    Full crossing angle c
    Bunch length z
    Transverse beam size at the IP *
“Thus, to achieve high luminosity, all one has to do is make (lots of) high population bunches of low emittance to collide at high frequency at locations where the beam optics provides as low values of the amplitude functions as possible.” PDG 2005, chapter 25
Interaction Region
Energy
Intensity
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 5: LHC performance drivers
Intensity
Energy
Interconnects
Training
Machine protection
Injector chain
Electron cloud effect
Collimation
Machine protection
Optics
Aperture
Machine protection
Nominal
Operation envelope
Progress with beam in 2009
2010-2011
Interac. region (β*, F)

## Slide 6: Energy : Evolution of target
450 GeV
2 kA
1.18 TeV
When
7 TeV
12 kA
Operation envelope
Progress with beam in 2009
2010-2011
Why
2002-2007
Summer 2008
Winter 2008
Summer 2009
Autumn 2009
Design ….. Magnets commissioning
Detraining …. During hardware
Commissioning
Splices …. Sept. 08 incident
Stabilizers
QPS connectors
Breakdown at operational voltage
    Connector quality
5 TeV
9 kA
3.5 TeV
6 kA
R< 1n
R< 10
(after quench)

## Slide 7: Energy: the way back
450 GeV
3/26/2010
When
Operation envelope
Progress with beam in 2009
2010-2011
What
2014 ?
2013
2012
2010 – 2011
January 2010
Train magnets
Should be easy to get to 6TeV….
7 TeV will take time
Long shut-down:
Interconnections & completion
of pressure relief system
Run @ 3.5TeV
Connectors fixed
Commission nQPS system
Commission circuits to 6kA
3.5 TeV
6 TeV
7 TeV

## Slide 8: Intensity: limits 2010 2011
Fix Imax to 6 1013 protons per beam at 3.5TeV
(about 20% nominal intensity)
30MJ stored beam energy
0.2%/s assumed
Collimation system conceived as a staged system
  First stage to allow 40% of nominal intensity at 7 TeV
Imperfections bring this down
Machine stability and reproducibility also play a role
Cleaning gets easier at lower energies
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 9: Higher intensities
With experience assume that we can
  Move to tight settings
  Achieve 0.1% loss rates
Then need to install something more
  Proposal exists for next phase of collimation
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 10: β* and F: 2010 2011
Lower energy means bigger beams
  Less aperture margin
  Higher β*
> 150 bunches requires crossing angle
  Requires more aperture
  Higher β*
Targets for 3.5TeV
  2 m no crossing angle
  3m with crossing angle
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 11: β*: Evolution
As energy increases, lower β* gets easier
The squeeze is always going to be challenging
  Optics
  Collimator
With experience, should be easier, but still …
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 12: LHC performance drivers at start
Intensity
Energy
will start simple
&modest
Interconnects
Training
Machine protection
Collimation
Injector chain
Electron cloud effect
Machine protection
Optics
Aperture
Machine protection
Nominal
Start
Operation envelope
Progress with beam in 2009
2010-2011
will run at highest energy safely possible
will start low and simple
Interac. region (β*, F)

## Slide 13: Early beam operation
Energy limited to 3.5 TeV by the stabilizers
2010
  Intensity carefully increased to collimation limit
  β* pushed as low as possible
2011
  Run at established limits
Repair of Sector 34 | 1.18 TeV | nQPS 6kA | 3.5 TeV Isafe < I < 0.2 Inom β* > 2 m | Ions |  | 3.5 TeV ~ 0.2 Inom β* ~ 2 m | Ions | 
2009 | 2010 | 2011
No Beam | B |  | Beam |  | Beam | 
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 14: LHC Beam Operation Operation envelope Progress with beam in 2009 2010-2011

## Slide 15: Targets with beam 2009
Operation envelope
Progress with beam in 2009
2010-2011
Do this with SAFE BEAMS
1012 at 450 GeV → 2 1011 at 1.18 TeV
LIMITS
2 on 2 with 5 1010 per bunch at 1.18 TeV
4 on 4 with 2 1010 per bunch at 1.18 TeV
AIMS
450 GeV collisions
106 events
Ramp to 1.18 TeV
Collisions at 1.18 TeV

## Slide 16: Milestones reached
Date | Day | Achieved
Nov 20 | 1 | Each beam circulating. Key beam instrumentation working.
Nov 23 | 4 | First collisions at 450 GeV. First ramp (reached 560 GeV).
Nov 26 | 7 | Magnetic cycling established (reproducibility).
Nov 27 | 8 | Energy matching done.
Nov 29 | 10 | Ramp to 1.18 TeV.
Nov 30 | 11 | Experiment solenoids on.
Dec 04 | 15 | Aperture measurement campaign finished. LHCb and ALICE dipoles on.
Dec 05 | 16 | Machine protection (Injection, Beam dump, Collimators) ready for safe operation with pilots.
Dec 06 | 17 | First collisions with STABLE BEAMS, 4 on 4 pilots at 450 GeV, rates around 1Hz.
Dec 08 | 19 | Ramp colliding bunches to 1.18 TeV
Dec 11 | 22 | Collisions with STABLE BEAMS, 4 on 4 at 450 GeV, > 1010 per bunch, rates around 10Hz.
Dec 13 | 24 | Ramp 2 bunches per beam to 1.18 TeV. Collisions for 90mins.
Dec 14 | 25 | Collisions with STABLE BEAMS, 16 on 16 at 450 GeV, > 1010 per bunch, rates around 50Hz.
Dec 16 | 27 | Ramp 4 on 4 to 1.18 TeV. Squeeze to 7 m. Collisions.
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 17: Injection
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 18: Beam dump
IR6 H Beam2, extracted
IR6 H Beam2, circulating
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 19: Collimation after beam based set up (Ralph)
Efficiency: > 99.9%
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 20: Aperture scans – IR5 H shown
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 21: Beta-beat comparison 450 GeV and 1.18 TeV
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 22: Production !
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 23: Data recorded
“stage” Total hours
4x4 5e9 p/bch 16 hrs
4x4 1.5e10 p/bch 26 hrs
16x16 1e10 p/bch 1.5 hrs
43.5 hrs
Estimated numbers of pp interactions recorded by experiments
 | Not stable beams (detectors partly on) |  | Stable beams (full detector on)
 | 450GeV | 1.18 TeV | 450 GeV
ALICE | 40k | 33k | ~ 400k
ATLAS | ~ 320k | ~ 34k | ~ 540k
CMS | ~ 100k | ~18k | ~ 410k
LHCB |  | ~ 40k | ~ 250k
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 24: Experiments events
ALICE event at 900 GeV
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 25: Summary of progress with beam 2009
Excellent machine availability
Excellent performance of all accelerator systems
Huge amount achieved in 4 weeks
All targets met and more
All done with safe beams
Minimum changes made in the interest of expediency
Plenty to think about
Great collaboration between machine and experiments
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 26: LHC Beam Operation Operation envelope Progress with beam in 2009 2010-2011

## Slide 27: 2010 plan
  450 GeV phase 1 / Ramp to 3.5 TeV
  450 GeV phase II / Ramp to 3.5 TeV
  Collide / Squeeze / Collide
  Colliding, safe, stable, squeezed beams
  Increase intensity in steps x2
  Week of running after each step
  No crossing angle
  43 on 43 at 2m
  Increase stored energy in steps of 2MJ
  Week of running after each step
  Bunch trains and crossing angle
  1032 cm-2 s-1
  Ions (early scheme, 62 bunches per beam)
  Same magnetic machine as for protons
  2 weeks to switch
  4 weeks ion run
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 28: 2010 strategy
In 2009
  We corrected Q Q’ coupling orbit
  Otherwise optics were frozen
  Reference orbit established
  Protection devices set up and fixed
In 2010
  We correct everything we can with safe beams
  Then establish references
  Then set up protection devices
  Any further change will require another iteration
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 29: 2010 progress with safe beams
Some difficulties to get new QPS operational
450 GeV work completed to date
  Q Q’ coupling orbit measured and corrected
  Optics (beta-beating) measured and corrected
  Established references
  Collimation set up
  Injection and associated protection
  Extraction and associated protection
  RF
Ramp to 3.5 TeV done last week
  Optics
  Collimation set-up…
Target for first colliding stable 3.5 TeV beams March 30th
Operation envelope
Progress with beam in 2009
2010-2011
Chart: 
| Available | Unavailable | Technical stop
LHC availability | 0.66 | 0.17 | 0.17

## Slide 30: Rates in 2011
Energy | TeV | 3.50 | 3.50 | 3.50 | 3.50 | 3.50 | 3.50 | 3.50 | 3.50
Month |  | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
Bunch intensity | 1.E+10 | 7 | 9 | 9 | 9 | 9 | 9 | 9 | 9
Bunches / beam |  | 432 | 432 | 560 | 720 | 720 | 720 | 720 | 720
Emittance | µm | 3.75 | 3.75 | 3.75 | 3.75 | 3.75 | 3.75 | 3.75 | 3.75
β* | m | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Luminosity 1 & 5 | cm-2 s-1 | 9.2E+31 | 1.5E+32 | 2.0E+32 | 2.5E+32 | 2.5E+32 | 2.5E+32 | 2.5E+32 | 2.5E+32
Protons |  | 3.0E+13 | 3.9E+13 | 5.0E+13 | 6.5E+13 | 6.5E+13 | 6.5E+13 | 6.5E+13 | 6.5E+13
% nominal |  | 9.4 | 12.0 | 15.6 | 20.1 | 20.1 | 20.1 | 20.1 | 20.1
Current | mA | 54.4 | 70.0 | 90.7 | 116.6 | 116.6 | 116.6 | 116.6 | 116.6
Stored energy | MJ | 16.9 | 21.8 | 28.2 | 36.3 | 36.3 | 36.3 | 36.3 | 36.3
Beam size 1 & 5 | um | 44.8 | 44.8 | 44.8 | 44.8 | 44.8 | 44.8 | 44.8 | 44.8
Initial luminosity | cm-2s-1 | 9.17E+31 | 1.52E+32 | 1.97E+32 | 2.53E+32 | 2.53E+32 | 2.53E+32 | 2.53E+32 | 2.53E+32
Integrated/month | pb-1 | 52.37 | 86.58 | 112.23 | 144.30 | 144.30 | 144.30 | 144.30 | 144.30
Integrated | pb-1 | 52.37 | 138.95 | 251.18 | 395.48 | 539.78 | 684.07 | 828.37 | 972.66
Operation envelope
Progress with beam in 2009
2010-2011

## Slide 31: Summary
LHC is up and running with beam in 2009
  Excellent performance with safe beams
In 2010 & 2011
  Limited in energy due to interconnects …. Fixed in 2012
  Limited in intensity by collim. cleaning syst.…. Solution proposed
  Limited in β* because of lower energies …. target 2m
“Prudent step-by-step approach…. LHC is not a turnkey machine….” R. Heuer
“We can take satisfaction in what we have achieved to date, while reminding ourselves, that we are breaking new ground technologically as well as scientifically” . R. Heuer