## Slide 1
Zhang Junsong
Progress of CEPC detector Mechanical Design
2021.11.13

## Slide 2
Contents
1.Preliminary design of CEPC detector installation scheme
2.Iron yoke design
3.Heat transfer analysis of beampipe
4.Summry

## Slide 3: 1. Preliminary design of CEPC detector installation scheme
Overview

## Slide 4: 1.1 Weight Distribution
SN | Name | Total weight（ton） | Number | Weight of each（ton） | Boundary Dimension | mounting clearance
1 | Barrel iron yoke | 1200 | 12 | 100 | Φ8520，L:7660mm | /
2 | HCAL | 1200 | 12 | 100 | Φ7220，L:7660mm | 50mm
3 | Superconducting solenoid | 30 | 1 | 30 | Φ4960，L:7660mm | 50mm
3 | ECAL | 120 | 12 | 10 | Φ4400，L:4700mm | 50mm
4 | SET+TPC+SIT | ？ | Entirety | ？ | Φ3800，L:4700mm | /
5 | End-cap iron yoke | 500 | 5 | 100 | Φ8520，L:800mm | 180mm
6 | End-cap ECAL | 100 | 1 | 100 | Φ7220，L:1080mm | 50mm

## Slide 5
Installation at collision point, permanent guide, share the guide.
Reduce temporary installation tools.
1.2 General Installation Roadmap
Question：The weight of ECAL is about1200 tons, the gap is only 50mm, which guide can be use?
Low friction coefficient, easy installation.

## Slide 6: 1.3 The Survey of heavy duty guide
 | Friction coefficient | Permissible contact pressure（MPa） | Application area | Push Force for CEPC(KN)
roller guide | 0.01 | Maximum single load : 50ton | CNC | 120
Plastic coated guide（Teflon） | 0.05 | 1~2 | BESIII | 600
Cast iron rail | 0.15 | 1~2 | center lathe | 1800
Guide rail inlaid with metal composite board | 0.1 | 10~50 | Power tool | 1200
1） Rolling and sliding guide rails

## Slide 7: 1.3. The Survey of heavy duty guide
No contact, no friction.
The maximum load of single air pad is 4.8 tons, air gap is only 50 microns.
2）Air-pad bearing

## Slide 8: 1.3. The Survey of heavy duty guide
Max load：250ton/4MPa，385ton/5MPa.
Air gap：1mm.
Friction coefficient：0.01.
Total flatness requirements for guide rail:1mm.
Local flatness requirements for guide rail :0.2mm/m.
两组液压缸推动；
尺寸：1000×320mm;
3） Air pad of ATLAS/CMS

## Slide 9
The end yoke is supported separately from the mass.
The main part is supported by 10 sets of air pad, which is used for moving and horizontal fine-tuning. The single air pad capacity is 250 tons.
Use 6 sets of hydraulic cylinders to adjust the height, the capacity of which is 800 tons .
The final support adopts 8 sets of inclined iron support.
1.4 Preliminary design of installation scheme by air pad support
1）The overall layout

## Slide 10
Air pad with total load :250ton(40bar);
Diameter:1.1m，air gap:1mm;
800 ton grade jack, piston diameter 317mm, maximum working pressure 70MPa;
Outer diameter 530mm, stroke 50mm;
2） the support device
1.4 Preliminary design of installation scheme by air pad support

## Slide 11
3） Installation process
1.4 Preliminary design of installation scheme by air pad support
1. End yoke assembly
2. Yoke iron base assembly
3. Polygonal ion yoke assembly
4. Temporary mounting base assembly
5. HCAL is hoisted in
6. HCAL is pushed in
7. Superconducting magnet is hoisted in
8. Superconducting magnet is pushed in
9.ECAL is pushed in
10. Removal of temporary base
11. End yoke is push in
12.MDI docking

## Slide 12
1.4 Preliminary design of installation scheme by air pad support
4） Technical difficulties of sharing guide rail
1. External air pad can be shared, but the air pad in the yoke iron can not be shared 。
2. Each part must be pushed in, and the bottom height of each part is inconsistent, which make temporary tooling must be used。
3. The end yoke height is the lowest and the temporary mounting base must be lifted to push the end yoke next to the barrel yoke。
4. It is very difficult to push the HCAL into iron yoke with the weight of 1200Ton 。
Another idea: the end yoke is flat open, the difficulty is that the end yoke thickness is only 800mm

## Slide 13
1.4 Preliminary design of installation scheme by air pad support
4） Technical difficulties of sharing guide rail
Difficult：It is very difficult to push the HCAL into iron yoke with the weight of 1200Ton
Another idea: Open cover construction with iron yoke and HCAL.
Another idea: Iron yoke and HCAL form a whole and are divided into several parts.

## Slide 14
1.4 Preliminary design of installation scheme by air pad support
4） Technical difficulties of sharing guide rail
50mm
Difficult： There is not enough space for support and adjustment mechanism within 50mm clearance.
Another idea: CMS experience

## Slide 15: 2.Iron yoke design
Thickness: 600mm
Muon: 3 layer
Height: 9600mm
Weight: 920 t
Thickness: 1460mm
Muon: 4 layer
Height: 12120mm
Weight: 3180 t
Thickness: 600mm
Muon: 5 layers
Height: 8520mm
Weight: 760 t
Weight reduction
Save material costs
Other costs
Dec 26, 2018
Jan 16, 2020
March 23, 2021

## Slide 16: 2.Iron yoke design
Spiral structure
About 760 t
Dimension
Length: 8960mm
Outer height: 8520mm
Inner height: 7320mm
8960
In the direction of length,
six trapezoidal vertical plates
were added
Each unit is made up of six iron plates,
which can place five layers of muon detector

## Slide 17: 2.Iron yoke design
Calculation conditions:
Material --- T10
Load --- Self weight of yoke （760 t）
Stress cloud
Deformation cloud
Maximum deformation: 1.65mm
Maximum stress: 109MPa
Conclusion: Safety

## Slide 18: 2.Iron yoke design
Deformation and stress of yoke after installing all sub-detectors
Calculation conditions:
Material --- T10
Load --- Self weight of yoke + weight of the all sub-detectors
self weight of yoke : 760 t
weight of the all sub-detectors : 1600 t (estimate)
1600 tons uniformly loaded on
the upper surface of two guide rails
（Assuming: each rail is 200 mm wide）
Schematic diagram
of detector reloading
Stress cloud
Deformation cloud
Maximum deformation: 1.37mm
Maximum stress: 250MPa
Conclusion: Safety

## Slide 19: 2.1 Structural analysis of iron yoke under magnetic force
Loading of magnetic force
A unit of the yoke is combined to analyze the magnetic force structure；The magnetic field intensity is 3T；Gravitational field, calculating the maximum force in the vertical direction
A unit is divided into 7 pieces (divided according to the ribs)
Each piece has a total of 8 force surfaces, and the magnetic field forces are loaded separately. The magnetic field forces include radial and axial.

## Slide 20: 2.1Structural analysis of iron yoke under magnetic force
Loading conditions | Max deformation mm | Max stress Mpa
gravity and magnetic forces | 0.094 | 11
magnetic forces | 0.082 | 8.9
gravity | 0.012 | 2.8
The deformation of magnetic field force is small and needs further verification and calculation

## Slide 21
3. Heat transfer analysis of beampipe
Beam pipe:
High-order mode heat
Uniformly distributed
Total heat load：
1692W@Z;
5097W@HZ
Vertex detector：
chips：50mW/cm2
Electronic equipment: 412.1mW/cm2
Heat transfer of Be pipe
Analysis of flow characteristics in the detector cavity

## Slide 22
Heat transfer requirement：
Meet the pressure requirements.
The detector requires that the temperature difference between the two ends of the outer beryllium tube is less than 5 degrees.
The smaller the mass, the better.
3.1 Basic structure of beampipe Basic structure of beampipe
Be pipe
Extending AL pipe
Water inlet
Water outlet
Oil inlet
Oil outlet
Coolant: water
Inlet temperature: 23℃
Flow rate: 3.4L/min
Coolant: paraffin /water
Inlet temperature: 23℃
Flow rate: 1.3~2m/s
Critical dimension:
Be Length:240mm
Outer Be pipe: 0.25mm
Inner Be pipe: 0.35mm
Cooling channel: 0.5mm
Viscous model: Laminar

## Slide 23
(1) Results of paraffin cooling in Z mode(1692W)
Cooling well!
3.2 Heat transfer of Be pipe and extending AL pipe (Φ28mm)
Δp of paraffin: 23.3kPa
Δp of water: 14.8kPa
Paraffin flow parameters:
Flow rate: 1.7L/min
Inlet velocity: 1m/s
Velocity in ring pipe: 0.6m/s
Inlet temperature: 20℃
Max.t of outer Be: 24.3℃
Max.t of detector installation: 26.5℃
Max.t of AL: 42.4℃
Max.t of transition AL: 32.7℃
Δt of detector installation: 4.4℃
Max.t of extending AL: 31.8℃

## Slide 24
(2) Results of paraffin/water cooling for HZ mode(5097W)
Paraffin cooling for Be pipe:
Flow rate: 3.4L/min
Inlet velocity: 2m/s
Velocity in ring pipe: 1.2m/s
Δp=49.1kPa (Δp in BEPCII: ≤10kPa )
Temperature distribution
Max.t of outer Be: 24.6℃
Δt of detector installation: 5.3℃
High flow rate is required to meet the cooling requirements
High pressure drop
Will the high flow rate cause vibration exceeding the requirements?
Water cooling for Be pipe:
Flow rate: 1.7L/min
Inlet velocity: 1m/s
Velocity in ring pipe: 0.6m/s
Δp=13.4kPa
Max.t of outer Be: 24.5℃
Δt of detector installation: 4.4℃
Safety!
The corrosion of Beryllium by water？
Temperature distribution
3.2 Heat transfer of Be pipe and extending AL pipe (Φ28mm)

## Slide 25
inlet
outlet
chips
PCB
Carbon fiber
Simplify
Only carbon fiber
Hollow carbon fiber
Solid carbon fiber
Simplify
inlet
Detector cavity
Flow calculation model
Only doing flow calculation
Extracting fluid domain
Calculation model：K-Epsilon
outlet
u=15m/s
（1）calculation model
(1) Purpose: Determine the cooling flow rate of the vertex detector
(2) Difficulty: Complex structure
Limited by the configuration of the computer,
high quality grid can not be drawn.
Model simplification
3.3 Analysis of flow characteristics in the whole detector cavity

## Slide 26
0.98 m/s
0.41 m/s
0.40 m/s
（2）Velocity distribution
Streamline
Velocity distribution
Velocity distribution
(cross section)
The average velocity in detector cavity is very low.
0 m/s
3.3 Analysis of flow characteristics in the whole detector cavity
inlet u=15m/s

## Slide 27
tin=20℃
u=2.17m/s
Air average velocity: 0.4m/s
Section profile
inlet
outlet
Silicon strip in the first layer
Outer surface: 10 chips
Inner surface: 9 chips
50mW/cm2
412.1mW/cm2
t=20℃
t=25℃
①
②
⑦
Number | Material | thickness | density | Specific heat | Conductivity
 |  | μm | kg/m3 | J/(kg.K) | W/(m.K)
① | Si | 50 | 2419 | 713 | 148
② | Si | 50 | 2419 | 713 | 148
③ | PCB | 70 | 1417 | 1260 | 0.2
④ | glue | 25 | 1190 | 710 | 0.1
⑤ | graphene | 100 | 1810 | 710 | Kx=1000; Ky=1000; Kz=1
⑥ | glue | 25 | 1190 | 710 | 0.1
⑦ | carbon fiber | 100 | 1810 | 710 | 200
Material property
Problems left over from last year: PCB is insulated.
It means:
λpcb=0 W/(m.K), Ⅹ λpcb≈0.2 W/(m.K), √
Calculation model
(1) Calculation model and condition
3.4 Heat transfer analysis of Vertex Detector

## Slide 28
Surface temperature distribution
(2) Results
New calculation
The max. temperature of chip: 164.4℃.
The temperature difference in the chip is very large.
3.4 Heat transfer analysis of Vertex Detector

## Slide 29
Stress distribution
The maximum deformation:0.14mm
Deformation distribution
The maximum stress: 3MPa
(1)Case1： Cantilever installation ignoring detector load
3. Regardless of detector load
Calculation model and condition
1. Fixed support
2. Standard earth gravity
3.5 Stress analysis of beampipe structure
3. Ignore detector load

## Slide 30
The maximum deformation:0.002mm
Deformation distribution
Stress distribution
The maximum stress: 0.3MPa
(2)Case2： Working state, fixed at both ends
3. Adding detector load
1. Fixed support
2. Standard earth gravity
Calculation model and condition
4. Displacement:
Axial: free
Radial: fixed
3.5 Stress analysis of beampipe structure

## Slide 31
Stress distribution
The maximum deformation:0.015mm
Deformation distribution
The maximum stress: 13.9MPa
(3)Case3： Installation, adding 0.2MPa axial pressure
3. Adding detector load
1. Fixed support
2. Standard earth gravity
Calculation model and condition
4. Displacement:
Axial: free
Radial: fixed
5. pressure: 0.2MPa
3.5 Stress analysis of beampipe structure

## Slide 32
Stress analysis of the latest beam tube structure |  |  | 
Case | constraint | Deformation/mm | Stress/MPa
1 | Ignore detector load; Fixed at one end | 0.14 | 3
2 | Add detector load; One end is fixed; The other end is radial constrained | 0.002 | 0.3
3 | Add detector load ; One end is fixed; The other end is radial constrained and axial pressured 0.2MPa | 0.015 | 13.9
With carbon fiber tube, the overall structure is stable and safe.
(5) Summary of stress calculation
3.6 Stress analysis of beampipe structure

## Slide 33: 4.Summary
Air pad support installation scheme can be referred to .
Air pad support can achieve low friction coefficient, small driving force of detector movement .
At present, the air pad support scheme has not realized the idea of sharing guide rail, and no reduction in installation tooling.
        Iron yoke design: The results of magnetic field force analysis show that the deformation caused by magnetic field force can meet the requirements of use.
        The deformation of magnetic field force is small and needs further verification and calculation

## Slide 34
4. Summary
On Heat transfer analysis of beampipe
(1)Be pipe
Z mode: Safety!
HZ mode: Paraffin cooling requires high flow rate to meet the requirements, but it is unclear whether the flow rate causes vibration exceeding the requirements. Therefore, water cooling may be required, but the corrosion of Beryllium by water needs to be studied.
(Coolant velocity VS Vibration? Corrosion of Beryllium by water?)
(2)Vertex detector
Air cooling with remote heat conduction can not reduce the chip temperature to the engineering requirements.
(3) Beampipe structure stress
With carbon fiber tube, the overall structure is stable and safe.

## Slide 35
Thank you for your attention