## Slide 1: CEPC Injection/Extraction system including kicker technologies
Jinhui Chen, Lihua Huo , Yuwen Wu, Hua Shi , Guanjian Wu, Zilin Chen, Guanwen Wang, Lei Wang, X.H. Cui, D. Wang, Yiwei Wang
Injection group
2021-11-9
The 2021 international workshop on the CEPC，Nov. 8-12, 2021 on-line

## Slide 2: Outline
1
Overview of CEPC Inj./Ext. systems
2
Ferrite core kicker magnet systems
3
Kicker Ceramic vacuum chamber with coating
4
Summary

## Slide 3
Overview of the CEPC injection and extraction systems

## Slide 4: CEPC injection and extraction systems
DR injection and Extraction system(e+)
Booster LE injection system (e+,e-)
Booster Extraction system1 (e+,e-)
Collider off-axis injection system (e+,e-)
Booster Extraction system2 (e+,e-)
Booster HE injection system (e+,e-)
Collider swap out injection system (e+,e-)
Collider swap out extraction system (e+,e-)
Collider beam dump system(e+,e-)
In CEPC accelerator complex, there are 9 injection and extraction sub-systems, including:
Off-axis injection
(in W and Z mode)
On-axis injection
(only in Higgs mode)
Linac
DR
Booster
Collider
120GeV
1.1GeV
10~120GeV
dump
①
⑨
④
②
⑥
③
⑧
⑦
⑤

## Slide 5: Inj./ext. hardware type selection strategy
 | Sub-system | Kicker Type | Kicker waveform | Septa Type | Thickness of septum
1 | Damping ring inj./ext. | Slotted-pipe kicker | Half-sine/250ns | H. LMS | ф22/3.5mm
2 | Booster LE inj. | Strip-line kicker | Half-sine/50ns | H. LMS | ф55/5.5mm
3 | Booster ext. for CR off-axis inj. | Delay-line dipole kicker | Trapezoid /440-2420ns | V. LMS | Ф55/6mm
4 | Collider off-axis inj. | Delay-line NLK kicker | Trapezoid /440-2420ns | V. LMS | Ф75x56/2mm
5 | Booster ext. for CR on-axis inj. | Lumped parameter dipole kicker | Half-sine/1360ns | V. LMS | Ф55/6mm
6 | Booster HE inj. | NLK or Pulsed sextupole | Half-sine/0.333ms | V. LMS | Ф55/6mm
7 | Collider swap out inj. | Lumped parameter dipole kicker | Half-sine/1360ns | V. LMS | Ф75x56/6mm
8 | Collider swap out ext. | Lumped parameter dipole kicker | Half-sine/1360ns | V. LMS | Ф75x56/6mm
9 | Collider beam dump | Delay-line dipole kicker | Trapezoid /440-2420ns | V. LMS | Ф75x56/6mm
Septa:
Lambertson magnet is the first choice for CEPC because it is more reliable than other types of septa with typical septum wall width from 2mm to 10mm.
Kicker:
Which type of kicker to been chosen is determined by the injection scheme, the waveform of pulse and required kick strength. The waveform of kicker pulse is determined by injection scheme, filling pattern and revolution period.

## Slide 6: Hardware R&D activities towards TDR
In IHEP, one team is in charge of both HEPS and CEPC inj. & ext. system. A part of hardware R&D for 2 projects are overlapping. The experience of R&D could be shared.
Hardware R&D activities :
  Lambertson septa magnets
    In-air magnet: Septum thickness ≥3.5 mm
    Half in vacuum magnet: Septum thickness =2 mm
  Kicker systems
    Strip-line kicker and super fast pulser（PW=10~50ns）
    Slotted-pipe kicker and fast pulser（PW=250~300ns）
    Ferrite core kicker （in-air） and pusler
      Lumped parameter dipole kicker（half-sine PW=1.36us ）
      Distributed parameter dipole kicker（trapezoid PW=440~2420ns ）
      Distributed parameter Nonlinear kicker（trapezoid PW=440~2420ns ）
      Ceramic vacuum chamber and coating
Overlapping part
In prototyping phase
Initiate
Special for CEPC

## Slide 7
Ferrite core kicker magnet systems

## Slide 8: Ferrite core kicker design parameters
parameter | Unit | BST-ext.-kicker1 （for CR off-axis inj.） | BST-ext.-kicker2 （for CR on-axis inj.） | Collider-inj.-kcker1 (off-axis) | Collider-inj.&ext.-kcker2 (on-axis inj. & ext.)
Quantity | - | 2 | 2 | 2 | 2
Type | - | In-air delay-line dipole kicker | In-air lumped parameter dipole kicker | In-air delay-line NLK | In-air lumped parameter dipole kicker
Deflect direction | - | Horizontal | Horizontal | Horizontal | Horizontal
Beam Energy | GeV | 80 | 120 | 80 | 120
Deflect angle | mrad | 0.2 | 0.1 | 0.1 | 0.1
Magnetic effective length | m | 1.4 | 0.7 | 0.45 | 0.952
Magnetic strength | T | 0.06 | 0.06 | 0.06 | 0.042
Integral magnetic strength | T·m | 0.08 | 0.04 | 0.027 | 0.04
Beam pipe aperture(H×V) | mm | 55×55 | 55×55 | 75×56 | 75×56
Good field region(H×V) | mm | ? | ? | ? | ?
Field uniformity in good field region | - | ±1.5%？ | ±1.5%？ | ±1.5%？ | ±1.5%？
Repetition rate | Hz | 1k | 1k | 1k | 1k
Amplitude repeatability | - | ±0.5% | ±0.5% | ±0.5% | ±0.5%
Pulse jitter | ns | ≤5 | ≤5 | ≤5 | ≤5
Bottom width of pulse(5%-5%) | ns | Trapezoid：440~2420 | Half-sine：1360 | Trapezoid：440~2420 | Half-sine：1360
Tr/Tf(5%-95%) | ns | <200 | <680 | <200 | <680
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 9: Kicker magnet physics design consideration
h
w
L=
I=
U=I
Ferrite core kicker design parameters | BST | CR
Magnetic field B (T) | 0.06 | 0.042
Inner aperture of ceramic vacuum chamber (mm×mm) | 55×55 | 75×56
Ceramic vacuum chamber outer aperture (mm×mm) | 60×60 | 85×66
Magnet aperture w × h (mm×mm) | 68×64 | 100×80
Length of magnet l(m) | 1.4 | 0.952
Inductance of magnet L(μH) | 1.8683 | 1.496
Magnet exercitation current I (kA) | 3 | 2.67
Impedance Z(Ω) | 10 | 10/12.5
Voltage of magnet U(kV) | 30 | 26.7/33.4
Time constant τ (ns) | 187 | 149.6/120
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
Kicker magnet type | Pulse discharge mode | Magnetic field rise time Tr (5%-95%)
Lumped parameter | Shorted end | 3τ=561ns/448.8ns/360ns
Lumped parameter | Matching | 3τ/2=280.5ns/224.4ns/180ns
Distributed parameter (Delay-line) | Matching | τ=187ns/149.6ns/120ns
Ferrite core kicker

## Slide 10
1. Lumped parameter dipole kicker system
<1360ns,1kHz
Ferrite core
Ceramic vacuum chamber
Eddy current Shielding plate
HV conductor
The structure of in-air lumped parameter kicker is simpler.
For a half-sine kicker system, LC resonance discharge circuit is common. Here, the kicker magnet acts as a part of lumped inductor( L )in the pulse discharge circuit.

## Slide 11: Novel half-sine wave pulser
SIC 1200V SBD
IGBT
Considering the requirement of kicker repetition rate 1kHz, solid-state pulser is better for the CEPC.
A novel topology of pulser was proposed: LV LC resonance discharge circuit (IGBT+SBD) + Inductive adder
Imax=2326.5A(2500A)
L=194nH(250nH)
C=25nF
Tw=π√LC=248.4ns
Z=√L/C=3.16Ω
U=7357V(8000V)
IGBT quantity=10*4=40
920mm
510mm
564mm

## Slide 12: 2. Delay-line dipole kicker system
The structure of delay-line kicker is complicated, but helps to achieve ideal trapezoid waveform.
For a ideal trapezoid kicker system, the kicker magnet is a part of matched transmission line.
200ns
40~2000ns
200ns
1kHz
challenges
Pulser
Delay-line kicker
Lumped parameter kicker
PFN
Delay-line kicker magnet

## Slide 13: Dual-C type delay-line dipole kicker design
Chart: X/mm
| -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
BY/Gs | 421.5156 | 421.4332 | 421.3508 | 421.2684 | 421.1849 | 421.0998 | 421.0147 | 420.9296 | 420.8438 | 420.7576 | 420.6714 | 420.585 | 420.5008 | 420.4149 | 420.3291 | 420.2558 | 420.187 | 420.1147 | 420.054 | 420.0079 | 419.9554 | 419.905 | 419.8878 | 419.8703 | 419.8442 | 419.8445 | 419.8587 | 419.862 | 419.8795 | 419.9208 | 419.9549 | 419.9865 | 420.0458 | 420.1101 | 420.1744 | 420.2393 | 420.3206 | 420.4019 | 420.4862 | 420.5713 | 420.6574 | 420.7434 | 420.8295 | 420.9148 | 421.0008 | 421.0869 | 421.173 | 421.2588 | 421.3401 | 421.4168 | 421.4936
Parameters(unit) | value
Magnet aperture（mm） | 100×80
Length of cell （mm） | 36
Quantity of cell | 26
Characteristic impedance（Ω） | 12.5
Magnet effective length（mm） | 942
Magnet mechanical length（mm） | 1018
Inductance of cell（nH） | 56.6
Inductance of magnet（nH） | 1471.6
Capacitance of cell（pF） | 362
Capacitance of magnet（nF） | 9.412
Magnetic B field （Gs） | 425
Exciting current（A） | 2703
Operating voltage（V） | 33791
Zoom in
A little high for magnet in the air
2D model without metallic coating of ceramic vacuum chamber

## Slide 14: Structure mechanical design
Ferrite core
Base
Ceramic support
Eddy current Shielding plate
Ceramic Vacuum chamber
Capacitor plate@
High potential
Capacitor plate @
Ground potential
HV conductor
High potential Lead
ground potential Lead
Dual-C type delay-line dipole kicker

## Slide 15: Trapezoid wave pulser
Considering the requirements of 1kHz repetition rate, 200ns fast rise time and adjustable pulse width, the trapezoid waveform pulser is built based on SiC MOSFET
Energy storage component
  Capacitor ： Flat-top dropping compensate topology
  PFN ：low impedance, need 2 times of voltage of stored energy
Power stacking topology
  inductive adder: not fit for long pulse
  Marx generator: hard to control structure impedance
PFN
Delay-line kicker magnet
200ns
40~2000ns
200ns
1kHz
Solid-state switches（SIC MOSFET）
Marx generator
Or
Cap.
challenges
Inductive adder

## Slide 16: 3. Delay-line Nonlinear Kicker (NLK)
Differential mode exciting
Common mode exciting
Injected bunch
stored bunch
Dipole B field
Nonlinear B field
Thinking about if the nonlinear kicker injection is possible for CEPC, after all this kind of top-up injection scheme should loose the requirement of DA.
More physics parameter inputs are needed for the magnet design.
Extended eddy current Shielding plate

## Slide 17: Structure mechanical design
Capacitor plate@
High potential
HV conductor
Ferrite core
Base
Capacitor plate @
Ground potential
Ceramic Vacuum chamber
ground potential Lead
High potential Lead
Eddy current Shielding plate
Ceramic support
Delay-line NLK

## Slide 18
Kicker Ceramic vacuum chamber with coating

## Slide 19: Ceramic vacuum chamber fabrication
Chart: Wall thickness/mm
| 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2 | 1.5 | 1
octagon | 2.37 | 3.17 | 4.38 | 6.38 | 9.83 | 16.4 | 30.5 | 66.2 | 172
race track | 1.78 | 2.29 | 3.04 | 4.15 | 5.83 | 8.34 | 12 | 17.5 | 25.4
ellipse | 1.4 | 1.73 | 2.24 | 2.95 | 4.01 | 5.49 | 7.4 | 10.2 | 13.5
L=1.2m，thickness=5mm
Ceramic vacuum chamber with special pattern metallic coating is key component for in-air kicker magnet.
ellipse
octagon
Race track
Ceramic material: 99% AL2O3
√
Integrated sintering process

## Slide 20: Magnetron sputtering coating prepare
Movable solenoid
Solenoid coil
Inner diameter=208mm
Length =700mm
Good field region=500mm
According to the experience of coating, the cathode target discharge is unstable for long vacuum chamber more than 600mm and it is easy to cause ignition or local film formation failure.
So, sectional coating method by a movable solenoid is proposed for our ceramic vacuum chamber of 1.2m. The coating experiment shows uniform coating can be achieved in one antechamber of 1m for HEPS.
In order to obtain uniform coating on race-track shape vacuum chamber, a horizontal movable cathode wire target solution is proposed.
The antechamber for HEPS
(inner aperture=6mm)
1m
Cathode wire
Moving track
view window
Cathode pole
Graduated bellows is used to adjust the horizontal position of cathode wire (compression at one end and tension at the other end)

## Slide 21: Film pattern study
Strip film
Mesh film
Ladder film
Spiral film
Comb film
Metallic coating on the inner wall of ceramic vacuum chamber is provided for beam mirror current as a path.
The continuous uniform film can form large loop eddy current under fast pulse magnetic field, which has magnetic shielding effect.
An appropriate coating pattern can solve this contradiction at the same time.The design principles of coating pattern are as follows:
  The upstream and downstream of films are not connected to prevent the occurrence of large loop;
  The films should cross to form a capacitor structure as far as possible to provide a path for high-frequency beam mirror current.
√
×
×
√
√

## Slide 22: Eddy current shielding simulations
coil
ferrite
Ceramic vacuum chamber
Metallic film(spiral)
COMSOL 3D Model
Coil exciting current pulse
Central field deformation caused by different pattern films
3D model was built in COMSOL to simulate eddy current shielding effect.
  The film square resistance is set to 0.2 Ω (equivalent to 86nm copper film or 1.1 μm TiN film)
  Material conductivity is set to 5000S / m, and the corresponding thickness is 1mm.

## Slide 23: HF E-M field transmission simulations
SONNET is a kind of excellent 3D planar circuit and antenna simulation tools.
It is used to study the HF transmission characteristic of the metallic film on Al2O3 base with different patterns.
The simulation result of S21 shows that the metallic film with different pattern can transfer most HF signals from 50-2000MHz.
Al2O3 base
Metallic film
Box boundary
SONNET model
Comb film
air
Comb film
Ladder film
Spiral film
S21
S21
S21

## Slide 24: Summary
In CEPC accelerator complex，there are 9 inj. and ext. sub-systems. The types of all inj./ext. components are determined. The hardware designs towards TDR are being carried out.
One team is in charge of both HEPS and CEPC inj. & ext. system. A part of hardware R&D for 2 projects are overlapping. The experience of R&D could be shared.
In-air ferrite core kicker system R&D special for the CEPC is carrying out, including the lumped and distributed parameter dipole kicker, NLK and ceramic vacuum chamber with metallic coating.

## Slide 25
END
Thank you for attentions!!!

## Slide 26
Backup slides

## Slide 27: Layout of the accelerator complex
The CEPC accelerator complex consists of a Linac, which including a small damping ring for positron beams, several transport lines, a booster ring and 2 storage rings, all of which are in a single tunnel.
1.2km
10-120GeV
120GeV
120GeV
e+
e-
100km
Damping ring
Dump
Dump

## Slide 28: Booster Ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 10 | 120 |  | 10 | 80 | 10 | 45.5
Function | Injection （both） | Extraction （off-axis） | Inj./Ext. （on-axis） | Injection （off-axis） | Extraction （off-axis） | Injection （off-axis） | Extraction （off-axis）
Bunch number | 242（in half ring） |  | 7（in half ring） | 1524（uniform） |  | 6000 | 
Min. bunch spacing （ns） | 680 |  | 23800 | 220 |  | 25 | 
Bunch number per train× train number | - |  | - | - | - | 80×75 | 
Train spacing （ns） | - |  | - | - | - | 2460 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Bunch by bunch | Train by train
Kicker repetition rate (Hz) | 100 | 1000 |  | 100 | 1000 | 100 | 1000
Kicker pulse width (ns) | 1360 |  |  | 440 |  | 50 | <6900
Kicker flat top（ns） | - |  |  | - |  | - | >1980
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <25 | <2460
Timing delay(ns) | <680 |  | <23800 | <220 |  | <2460 | <4400
injection（extraction）period (s) | 2.42 | 0.242 | 0.007 | 15.24 | 1.5 | 60 | 0.075
Kick angle (mrad) | 0.11 | 0.2 | 0.1 | 0.11 | 0.2 | 0.11 | 0.2
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04 | 0.004 | 0.05 | 0.004 | 0.03
Beam pipe aperture Φ（mm） | 55 |  |  |  |  |  | 
Considering the compatibility of three operating modes:
Function | LE-Injection （both） | HE-Extraction （off-axis） | HE-Inj./Ext. （on-axis）
Kicker repetition rate (Hz) | 100 | 1000 | 1000
Kicker pulse width (ns) | 50 | 440~2420(Adjustable) | 1360
Kicker flat top（ns） | - | 0~1980(Adjustable) | -
Kicker rise（fall）time(ns) | <25 | <220 | <680
injection（extraction）period (s) | 60 | 1.5 | 0.007
Kick angle (mrad) | 0.11 | 0.2 | 0.1
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04
Beam pipe aperture Φ（mm） | 55 | 55 | 55
50ns,100Hz
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 29: Collider ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 120 |  |  | 80 |  | 45.5 | 
Function | Injection （off-axis） | Injection （on-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump）
Bunch number | 242（in half ring）- 7 |  |  | 1524（uniform） |  | 12000 | 
Min. bunch spacing （ns） | 680 |  |  | 220 |  | 25 | 
Bunch number per train× train number | - |  |  | - |  | 80×150 | 
Train spacing （ns） | - |  |  | - |  | 245 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Train by train | 
Kicker repetition rate (Hz) | 1000 |  |  | 1000 |  | 1000 | 
Kicker pulse width (ns) | 1360 |  |  | 440 |  | <2460 | 
Kicker flat top（ns） | - |  |  | - |  | >1980 | 
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <245 | 
Timing delay(ns) | <680 | <23800 | <680 | <220 |  | <4400 | 
injection（extraction）period (s) | 0.242 | 0.007 | 0.242 | 1.5 |  | 0.15 | 
Kick angle (mrad) | 0.1 | 0.2 | 0.2 | 0.1 | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.04 | 0.08 | 0.08 | 0.027 | 0.05 | 0.015 | 0.03
Beam pipe aperture HxV（mm） | 75×56 |  |  |  |  |  | 
Function | Injection （on-axis） | Injection （off-axis） | Extraction （dump）
Kicker repetition rate (Hz) | 1000 | 1000 | 1000
Kicker pulse width (ns) | 1360 | 440~2420(Adjustable) | 440~2420(Adjustable)
Kicker flat top（ns） | - | 0~1980(Adjustable) | 0~1980(Adjustable)
Kicker rise（fall）time(ns) | <680 | <220 | <220
injection（extraction）period (s) | 0.007 | 1.5 | 1.5
Kick angle (mrad) | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.08 | 0.04 | 0.08
Beam pipe aperture HxV（mm） | 75×56 | 75×56 | 75×56
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
Considering the compatibility of three operating modes:
200ns
40~2000ns
200ns
1kHz