## Slide 1: FCC-ee machine error correction
Tessa Charles 1,2, Bernhard Holzer 3, Katsunobu Oide 3, Frank Zimermann 3
and the FCC-ee optics team
1. University of Liverpool,
2. Cockcroft Institute
3. CERN
International workshop on the high energy CEPC, November 2021
FCCIS – The Future Circular Collider Innovation Study. This INFRADEV Research and Innovation Action project receives funding from the European Union’s H2020 Framework Programme under grant agreement no. 951754.

## Slide 2: FCC-ee Emittance Tuning: Challenges & Constraints
Challenges:
Large beta function values makes us sensitive to field and misalignment errors
Small beta* means strong FF magnets, which in turn requires strong sextupoles for local chromaticity correction.
Small emittance ratio makes us sensitive to any coupling between the horizontal and vertical motion.
Tessa Charles
CEPC workshop 2021
IP
Notes: I’ve shown a version of this slide before, at FCC weeks in the past, and I include it again here to briefly start by making the point that: FCC-ee presents quite a challenge when it comes to emittance tuning.
Beta* = 0.8 mm

## Slide 3: Natural chromaticities for a range of low emittance storage rings
Tessa Charles
Many thanks to:
Rohan Dowd (AS), Masamitsu Aiba (PSI), Katsunobu Oide (KEK), Thorsten Hellert (ALS), Ilya Agapov (DESY), Pedro Fernandes Tavares (MAX IV), Kent Wooton (APS), Bastian Härer (KIT), Liu Lin (LNLS), Simone Di Mitri (Elettra), Jeff Corbett (SLAC), Bernhard Holzer (CERN), Ian Martin (Diamond), David Amorim (SOLEIL)
CEPC workshop 2021
Notes: Here we compare FCC-ee to other low emittance SR around the world, including a number of existing and planned upgrades.
You can see that FCC-ee is pushing towards low emittance whilst battling high chromaticity.

## Slide 4: Correction tools
Tessa Charles
Orbit correction:
  MICADO & SVD from MAD-X
    Hor. corrector at each QF, Vert. corrector at each QD
  1598 vertical correctors / 1590 horizontal correctors
    BPM at each quadrupole
  1598 BPMs vertical / 1590 BPMs horizontal
Vertical dispersion and orbit:
  Orbit Dispersion Free Steering (DFS)
Linear coupling:
  Coupling resonant driving terms (RDT)
    1 skew at each sextupole
Beta beating correction & Horizontal dispersion via Response Matrix:
  Rematching of the phase advance at the BPMs
    1 trim quadrupole at each sextupole
CEPC workshop 2021

## Slide 5: Assigning misalignments
Tessa Charles
  - Misalignments are randomly distributed via a Gaussian distribution, truncated at 2.5 sigma.
CEPC workshop 2021
Notes: For these simulations we assign many misalignments. These figures define the various misalignment types.

## Slide 6: Assigning girder misalignments
Tessa Charles
  - 2 independent DX and DY misalignments for each end of the girder, and which can be used to calculate DTHETA and DPHI.
(not to scale)
dipole
girder
sextupoles/ quadrupoles
dipole
girder
CEPC workshop 2021
Notes: And actually we have misalignments on top of misalignments. Within the arcs, we have sextpoles and quadrupoels on a girder.

## Slide 7: Misalignments and field errors
Tessa Charles
  Misalignments are randomly distributed via a Gaussian distribution, truncated at 2.5 sigma.
CEPC workshop 2021
Notes: This table summarises the current set of misalignments. That’s not to say that this wont’ change. This talk is an update on going work.
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$DTHETA & $\Delta$DPHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 50 & 50 & 300 & 150 & 100 & 100 \\
Arc sextupoles* & 50 & 50 & 300 & 150 & 100 & 100 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 150 & 150 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 250 & 100 & 100 \\
IR sextupoles & 100 & 100 & 250 & 250 & 100 & 100 \\
\hline
BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 8: Correction Strategy (1/2)
Tessa Charles
Sextupoles strengths set to zero.
  Gradient errors applied
    Weighted beta-beat correction was performed and tune re-matched
    Sextupole and dipole field errors introduced
    Weighted beta-beat correction was performed and tune re-matched
  Misalignments applied to arc magnets and girders
    Tune re-matched to the nominal tune, and orbit correction performed
    Initial beta-beat correction and coupling correction
  Misalignments applied to IR magnets
    Tune re-matched to the nominal tune, and orbit correction performed
    Beta-beat correction applied, and if needed orbit corrected and tune rematched
    Coupling correction, followed by beta-beat correction and coupling correction
Sextupoles set to 10% of their design strength
(details on next slide)
Final correction (at 100% sextupole strength)
(details on next slide)
CEPC workshop 2021
Notes: We introduce the field errs and misalignments in two stages. Here we’re not trying to simulate the commission process from day 0. Instead we want to demonstrate that there is a set of corrector strengths, and magnet strengths, that result in a very well corrected lattice. It would be a different type of simulation to mimic the commissioning process.

## Slide 9: Correction Strategy (2/2)
Tessa Charles
Sextupoles strengths set to zero.
  (details on previous slide)
Sextupoles set to 10% of their design strength
  Orbit correction
  Combined coupling and dispersion correction
  Beta-beating correction applied.
  Sextupole strengths increased by 10%
Final correction (at 100% sextupole strength)
  Additional coupling, dispersion and beta-beating correction was applied.
  Step through corrections until beta beating threshold is reached (trade-off between beta beating and vertical emittance can be varied).
  Vary SV cut off values
These two steps repeated ~12 times.
Constant checking of the tunes and orbit avoids running into resonances, or failure to find the closed orbit.
CEPC workshop 2021

## Slide 10
Tessa Charles
ttbar (182.5 GeV) 4IP lattice,
after correction strategy:
FCC-ee emittance tuning results
RMS misalignment and field errors tolerances:
CEPC workshop 2021
Notes: Ttbar, 4IP lattice. These are the main results.
run_fccee_girs150_arcs50r400s150pt100_dip1000_IP100r250s250pt100_field_23b_3_gradual2
%$\epsilon_{x, \textrm{median}} = 2.276$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.242$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.011$ $\%$ \\

## Slide 11
Tessa Charles
ttbar (182.5 GeV) 4IP lattice,
after correction strategy:
FCC-ee emittance tuning results
RMS misalignment and field errors tolerances:
CEPC workshop 2021

## Slide 12
Tessa Charles
ttbar (182.5 GeV) 4IP lattice,
after correction strategy:
FCC-ee emittance tuning results
RMS misalignment and field errors tolerances:
CEPC workshop 2021

## Slide 13: Coupling matrix elements
Tessa Charles
Before correction
(without sextupoles)
After correction
(with sextupoles)
Before correction
(without sextupoles)
After correction
(with sextupoles)
CEPC workshop 2021

## Slide 14: Vertical dispersion
Tessa Charles
Before correction
(without sextupoles)
After full global correction
(with sextupoles)
Dy, rms = 3.90 mm
CEPC workshop 2021
After orbit correction, before full corrections (without sextupoles)
Notes: It can be quite informative to look at single seeds, to see how various properties vary around the ring. Here is one random seed, chosen at random, showing the vertical dispersion around the ring before and after correction.

## Slide 15
Tessa Charles
CEPC workshop 2021
After corrections, ttbar 4 IP lattice:
Notes: It can be quite informative to look at single seeds, to see how various properties vary around the ring. Here is one random seed, chosen at random, showing the vertical dispersion around the ring before and after correction.

## Slide 16: Misalignments of various magnet types
Tessa Charles
Notes: We undertook a simulation campaign to determine the influence of particular magnet type misalignment on the final results. We’re doing this in order guide alignment tolerance specifications.

## Slide 17
Tessa Charles
Girder misalignment
The girder misalignment has the strongest influence on horizontal emittance of all the parameters listed in the previous table.
All other misalignments are as defined on previous slide.
CEPC workshop 2021
Notes: Keeping all other misliagnmetns as previously defined in the table on the previous slide., we varied the RMS girder misalignment in X and Y

## Slide 18
Arc magnet misalignments
All other misalignments are as defined previously (i.e. girder DX and DY = 150 𝜇m).
Tessa Charles
CEPC workshop 2021
18

## Slide 19
Arc magnet roll angles
All other misalignments are as defined previously.
Arc magnet roll angles of up 400 𝜇rad can be handled by the correction strategy. This could be extended beyond 400 𝜇rad if necessary.
Tessa Charles
CEPC workshop 2021
19

## Slide 20: Interaction region
IR quads and sextupoles magnet
SY* sextupoles
QC1*, QC2* quadrupoles
Tessa Charles
CEPC workshop 2021

## Slide 21
IR magnets alignment - transverse misalignments (𝛥X and 𝛥Y)
Tessa Charles
21
  IR magnet alignment strongly influences global correction.
CEPC workshop 2021
Notes: 00_4IPttbar_IR_DXDY
\begin{table}[htb!]
\centering
\begin{tabular}{lccccccc}
\hline
Type & $\Delta$X ($\mu$m) & $\Delta$Y ($\mu$m) & $\Delta$PSI ($\mu$rad) & $\Delta$S ($\mu$m) & $\Delta$THETA ($\mu$rad) & $\Delta$PHI ($\mu$rad) & Field Errors \vspace{.1cm} \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
IR sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
All other magnets & \multicolumn{6}{c}{as listed in Table on slide 7} & \\
\hline
\end{tabular}
\end{table}
\vspace{-.45cm}

## Slide 22
Tessa Charles
22
IR magnets alignment - transverse misalignments (𝛥X and 𝛥Y)
  IR magnet alignment strongly influences global correction.
CEPC workshop 2021
Notes: 00_4IPttbar_IR_DXDY
\begin{table}[htb!]
\centering
\begin{tabular}{lccccccc}
\hline
Type & $\Delta$X ($\mu$m) & $\Delta$Y ($\mu$m) & $\Delta$PSI ($\mu$rad) & $\Delta$S ($\mu$m) & $\Delta$THETA ($\mu$rad) & $\Delta$PHI ($\mu$rad) & Field Errors \vspace{.1cm} \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
IR sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
All other magnets & \multicolumn{6}{c}{as listed in Table on slide 7} & \\
\hline
\end{tabular}
\end{table}
\vspace{-.45cm}

## Slide 23
IR magnets alignment - roll angle (𝛥PSI)
Tessa Charles
23
CEPC workshop 2021
Notes: 00_4IPttbar_IR_DPSI
\begin{table}[htb!]
\centering
\begin{tabular}{lccccccc}
\hline
Type & $\Delta$X ($\mu$m) & $\Delta$Y ($\mu$m) & $\Delta$PSI ($\mu$rad) & $\Delta$S ($\mu$m) & $\Delta$THETA ($\mu$rad) & $\Delta$PHI ($\mu$rad) & Field Errors \vspace{.1cm} \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
IR sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
All other magnets & \multicolumn{6}{c}{as listed in Table on slide 7} & \\
\hline
\end{tabular}
\end{table}
\vspace{-.45cm}

## Slide 24
IR magnets: longitudinal alignment (𝛥S)
Tessa Charles
24
CEPC workshop 2021
Notes: 00_4IPttbar_IR_DS
\begin{table}[htb!]
\centering
\begin{tabular}{lccccccc}
\hline
Type & $\Delta$X ($\mu$m) & $\Delta$Y ($\mu$m) & $\Delta$PSI ($\mu$rad) & $\Delta$S ($\mu$m) & $\Delta$THETA ($\mu$rad) & $\Delta$PHI ($\mu$rad) & Field Errors \vspace{.1cm} \\
\hline
IR quadrupole & 100 & 100 & varied & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
IR sextupoles & 100 & 100 & varied & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
All other magnets & \multicolumn{6}{c}{as listed in Table on slide 7} & \\
\hline
\end{tabular}
\end{table}
\vspace{-.45cm}

## Slide 25
SY* sextupole alignment: 𝛥X and 𝛥Y
Tessa Charles
25
CEPC workshop 2021
Notes: 00_4IPttbar_IPsext_DXDY
\begin{table}[htb!]
\centering
\begin{tabular}{lccccccc}
\hline
Type & $\Delta$X ($\mu$m) & $\Delta$Y ($\mu$m) & $\Delta$PSI ($\mu$rad) & $\Delta$S ($\mu$m) & $\Delta$THETA ($\mu$rad) & $\Delta$PHI ($\mu$rad) & Field Errors \vspace{.1cm} \\
\hline
QC1*, QC2* & 100 & 250 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
% IR sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
% IR quadrupole & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
SY sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
Other IR quads & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
Other IR sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
All other magnets & \multicolumn{6}{c}{as listed in Table on slide 7} & \\
\hline
\end{tabular}
\end{table}
\vspace{-.45cm}

## Slide 26
SY* sextupole roll angle: 𝛥PSI
Tessa Charles
26
CEPC workshop 2021
Notes: 00_4IPttbar_IPsext_DPSI

## Slide 27
SY* sextupole longitudinal alignment: 𝛥S
Tessa Charles
27
CEPC workshop 2021
Notes: 00_4IPttbar_IPsext_DS

## Slide 28
SY* sextupole alignment: 𝛥PHI
Tessa Charles
28
CEPC workshop 2021

## Slide 29
QC1* and QC2* quads alignment: 𝛥X and 𝛥Y
Tessa Charles
29
CEPC workshop 2021
Notes: 00_4IPttbar_FFquad_DXDY
\begin{table}[htb!]
\centering
\begin{tabular}{lccccccc}
\hline
Type & $\Delta$X ($\mu$m) & $\Delta$Y ($\mu$m) & $\Delta$PSI ($\mu$rad) & $\Delta$S ($\mu$m) & $\Delta$THETA ($\mu$rad) & $\Delta$PHI ($\mu$rad) & Field Errors \vspace{.1cm} \\
\hline
QC1*, QC2* & 100 & 250 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
% IR sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
% IR quadrupole & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
SY sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
Other IR quads & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
Other IR sextupoles & 100 & 100 & 250 & 200 & 100 & 100 & $\Delta k/k = 2\times 10^{-4}$ \\
\hline
All other magnets & \multicolumn{6}{c}{as listed in Table on slide 7} & \\
\hline
\end{tabular}
\end{table}
\vspace{-.45cm}

## Slide 30
QC1* and QC2* roll angle: 𝛥PSI
Whilst the equilibrium emittance after global correction is not strongly influenced by QC1 and QC2 roll angles, local corrections are needed which might require that these magnets are aligned to high precision.
Tessa Charles
30
CEPC workshop 2021
Notes: 00_4IPttbar_FFquad_DPSI

## Slide 31
QC1* and QC2* longitudinal alignment: 𝛥S
Whilst the equilibrium emittance after global correction is not strongly influenced by QC1 and QC2 misalignments, local corrections are needed which might require that these magnets are aligned to high precision.
Tessa Charles
31
Notes: 00_4IPttbar_FFquad_DS

## Slide 32
QC1* and QC2* alignment: 𝛥PHI
Tessa Charles
32

## Slide 33
Next steps include…
Include solenoid misalignment into simulations
Establish the most realistic modelling for BPM errors (e.g. non-linear responses, calibration measures for rotated BPMs, non-Gaussian BPM offset distributions)
Simulate optics measurements
Local corrections for vertical dispersion at the IP
Apply correction technique to low energy, Z lattice
Determine how to apply measure optics quickly
  LOCO is too slow on such a large machine
  AC dipole method may run into problems due to strong damping
Simulation of commissioning process
Tessa Charles
33

## Slide 34
Summary
In a simulation campaign, we systematically studied a wide combination of magnet tolerances for field errors, alignment of individual magnets as well as girders and the settings of the BPMs.
The correction algorithms developed in this context represent a powerful correction tools and lead to successful convergence for a large majority of the applied errors seeds. And, most importantly, the lead to values of coupling and emittances that lie within the requirements of the machine design. For a standard set of misalignments, the final median vertical emittance achieved is 0.410 pm rad and horizontal emittance of 2.277 nm rad.
Tessa Charles
34
Notes: %$\epsilon_{x, \textrm{rms}} = 2.271$ nm rad \\
%$\epsilon_{y, \textrm{rms}} = 0.180$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.0078$ $\%$ \\
Fontsize: 18

## Slide 35: Thank you for your attention.

## Slide 36
Dipole misalignments
Data from FCC week 2020.
Transverse dipole misalignments have little influence on final emittances achievable.
36
Tessa Charles

## Slide 37
Colors
Backgrounds
Radiant Blue
Flash
Energy
Green
Red
Deep Blue
Use for Layout
Background Blue
Background Purple
Background Yellow
Background Grey

## Slide 38
Graphical Elements
Badges
Infographics
Separation lines 1.5 pt
Arrows
Use light badges on dark backgrounds
Use blue badges on light backgrounds
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!